Source	MARKET NEWS
Date	11/17/2015
Time	05:52:05 AM

Company	 Scorpio Gold Corporation
Title	Final Results 
From 2015 Exploration Drilling At





    CDNX Symbol: SGN











Press Release	





SCORPIO GOLD CORP ("SGN-V;SRCRF-0")
- Final Results From 2015 Exploration Drilling At The Oromonte
- Satellite Deposit, Mineral Ridge Project, Nevada

Scorpio Gold Corporation ("Scorpio Gold" or the "Company") reports
final results from its 2015 exploration drilling program on the
Oromonte satellite deposit at the 70% owned Mineral Ridge project,
located in Nevada.

The Oromonte target occurs over a 300 x 500 meter area situated
between the Solberry and Wedge deposits. A small mineral resource
estimate containing almost entirely Indicated resources was reported
for Oromonte based on 53 reverse circulation ("RC") drill holes (see
July 21, 2014 news release).

Drilling in 2014-2015 has intersected significant mineralization
at vertical depths ranging from near surface to 80 meters depth across
the target area. A notably higher-grade zone of mineralization occurs
along the western edge of the target area, ranging in vertical depth
from 106 to 142 meters.

A geological interpretation of the mineralization at Oromonte is
that it represents a continuation of the mineralized horizon(s) between
the Solberry and Wedge deposits that have been offset by normal
faulting. The occurrence of a higher-grade zone of mineralization at
depth may be related to a synform axis, which concentrated
mineralization in the Oromonte area. This mineralized zone was
subsequently down-dropped by late-stage normal faulting. A generalized
geological model of the mineralization is presented here: Oromonte
Cross Section.

Although not accessible by open pit mining, the deeper
mineralization at Oromonte may be amenable to underground extraction
should further results support underground development. Historical
underground workings occur in the Wedge deposit area approximately 180
meters to the east.

Highlights from the final phase of the 2015 RC drilling program on
the Oromonte deposit include:

MR151671: 2.13 grams per tonne ("g/t") gold over 3.05 meters

MR151674: 5.18 g/t gold over 3.05 meters

MR151677: 8.28 g/t gold over 6.10 meters

MR151773: 7.58 g/t gold over 1.52 meters

MR151777: 8.58 g/t gold over 6.10 meters

MR151778: 7.95 g/t gold over 9.14 meters

MR151779: 2.85 g/t gold over 3.05 meters

MR151802: 40.40 g/t gold over 7.62 meters

MR151804: 2.22 g/t gold over 4.57 meters

MR151809: 12.29 g/t gold over 4.57 meters

MR151810: 2.58 g/t gold over 4.57 meters

MR151885: 39.15 g/t gold over 1.52 meters

MR151887: 2.83 g/t gold over 3.05 meters

A drill hole location map is available at: DH Plan

Table 1. Oromonte Deposit - Significant Drill Results

//st
Hole           Azm   Dip From   To Width   From     To Width  Gold  Gold
No.          (deg) (deg) (ft) (ft)  (ft)    (m)    (m)   (m) (OPT) (g/t)
MR151671         0   -90  220  230    10  67.06  70.10  3.05 0.062  2.13
245  250     5  74.68  76.20  1.52 0.018  0.60
255  260     5  77.72  79.25  1.52 0.022  0.77
MR151672-673     0   -90                          No Significant Results
MR151674         0   -90    5   10     5   1.52   3.05  1.52 0.018  0.62
165  175    10  50.29  53.34  3.05 0.151  5.18
200  205     5  60.96  62.48  1.52 0.022  0.76
245  250     5  74.68  76.20  1.52 0.030  1.03
MR151675         0   -90   20   35    15   6.10  10.67  4.57 0.050  1.70
110  130    20  33.53  39.62  6.10 0.033  1.14
MR151676         0   -90  100  105     5  30.48  32.00  1.52 0.035  1.19
MR151677         0   -90   30   35     5   9.14  10.67  1.52 0.031  1.06
65   85    20  19.81  25.91  6.10 0.242  8.28
incl                       70   75     5  21.34  22.86  1.52 0.888 30.45
MR151679         0   -90    5   10     5   1.52   3.05  1.52 0.028  0.96
MR151680         0   -90  160  165     5  48.77  50.29  1.52 0.015  0.51
MR151771         0   -90  290  295     5  88.39  89.92  1.52 0.131  4.49
325  330     5  99.06 100.58  1.52 0.018  0.62
MR151772         0   -90  215  225    10  65.53  68.58  3.05 0.036  1.22
320  325     5  97.54  99.06  1.52 0.045  1.54
MR151773         0   -90  245  250     5  74.68  76.20  1.52 0.221  7.58
375  380     5 114.30 115.82  1.52 0.016  0.55
MR151774         0   -90   10   15     5   3.05   4.57  1.52 0.015  0.51
MR151775         0   -90   35   40     5  10.67  12.19  1.52 0.100  3.43
130  135     5  39.62  41.15  1.52 0.018  0.62
230  235     5  70.10  71.63  1.52 0.032  1.10
260  265     5  79.25  80.77  1.52 0.030  1.03
MR151776         0   -90  305  315    10  92.96  96.01  3.05 0.016  0.53
MR151777         0   -90  380  385     5 115.82 117.35  1.52 0.022  0.75
400  410    10 121.92 124.97  3.05 0.062  2.11
445  465    20 135.64 141.73  6.10 0.250  8.58
incl                      445  450     5 135.64 137.16  1.52 0.503 17.25
480  485     5 146.30 147.83  1.52 0.019  0.65
MR151778         0   -90  190  200    10  57.91  60.96  3.05 0.025  0.86
330  340    10 100.58 103.63  3.05 0.260  8.90
385  400    15 117.35 121.92  4.57 0.022  0.74
405  435    30 123.44 132.59  9.14 0.232  7.95
incl                      410  420    10 124.97 128.02  3.05 0.582 19.95
495  500     5 150.88 152.40  1.52 0.017  0.58
MR151779         0   -90   80   85     5  24.38  25.91  1.52 0.020  0.69
190  195     5  57.91  59.44  1.52 0.045  1.54
440  450    10 134.11 137.16  3.05 0.083  2.85
MR151780         0   -90  185  190     5  56.39  57.91  1.52 0.032  1.10
275  285    10  83.82  86.87  3.05 0.031  1.05
300  305     5  91.44  92.96  1.52 0.020  0.69
MR151801         0   -90   95  100     5  28.96  30.48  1.52 0.034  1.17
200  225    25  60.96  68.58  7.62 0.014  0.49
255  260     5  77.72  79.25  1.52 0.019  0.65
335  340     5 102.11 103.63  1.52 0.033  1.13
350  360    10 106.68 109.73  3.05 0.016  0.53
375  395    20 114.30 120.40  6.10 0.052  1.77
MR151802         0   -90  205  215    10  62.48  65.53  3.05 0.024  0.82
270  275     5  82.30  83.82  1.52 0.016  0.55
310  315     5  94.49  96.01  1.52 0.068  2.33
370  375     5 112.78 114.30  1.52 0.038  1.30
420  445    25 128.02 135.64  7.62 1.178 40.40
incl                      420  430    10 128.02 131.06  3.05 2.799 95.97
MR151803         0   -90   55   60     5  16.76  18.29  1.52 0.024  0.82
365  370     5 111.25 112.78  1.52 0.024  0.82
400  405     5 121.92 123.44  1.52 0.019  0.65
MR151804         0   -90   60   65     5  18.29  19.81  1.52 0.033  1.13
250  265    15  76.20  80.77  4.57 0.065  2.22
MR151806         0   -90  255  260     5  77.72  79.25  1.52 0.030  1.03
MR151807         0   -90   50   55     5  15.24  16.76  1.52 0.130  4.46
120  125     5  36.58  38.10  1.52 0.016  0.55
205  210     5  62.48  64.01  1.52 0.049  1.68
220  230    10  67.06  70.10  3.05 0.015  0.50
MR151809         0   -90    5   20    15   1.52   6.10  4.57 0.015  0.51
145  160    15  44.20  48.77  4.57 0.358 12.29
incl                      145  150     5  44.20  45.72  1.52 1.034 35.45
MR151810         0   -90  155  170    15  47.24  51.82  4.57 0.075  2.58
180  190    10  54.86  57.91  3.05 0.021  0.72
MR151864         0   -90                          No Significant Results
MR151865         0   -90   15   25    10   4.57   7.62  3.05 0.034  1.15
85  100    15  25.91  30.48  4.57 0.027  0.94
120  135    15  36.58  41.15  4.57 0.057  1.95
MR151867         0   -90                          No Significant Results
MR151870         0   -90   20   25     5   6.10   7.62  1.52 0.015  0.51
55   65    10  16.76  19.81  3.05 0.018  0.63
MR151871         0   -90   65   70     5  19.81  21.34  1.52 0.017  0.58
MR151874         0   -90   75   85    10  22.86  25.91  3.05 0.023  0.77
100  120    20  30.48  36.58  6.10 0.022  0.74
MR151876         0   -90  150  155     5  45.72  47.24  1.52 0.108  3.70
190  195     5  57.91  59.44  1.52 0.028  0.96
MR151877         0   -90   75   80     5  22.86  24.38  1.52 0.020  0.69
135  140     5  41.15  42.67  1.52 0.016  0.55
230  235     5  70.10  71.63  1.52 0.056  1.92
MR151878         0   -90  195  200     5  59.44  60.96  1.52 0.039  1.34
205  210     5  62.48  64.01  1.52 0.017  0.58
MR151880         0   -90  185  190     5  56.39  57.91  1.52 0.014  0.48
245  250     5  74.68  76.20  1.52 0.033  1.13
MR151882         0   -90   15   20     5   4.57   6.10  1.52 0.027  0.93
MR151885         0   -90  240  245     5  73.15  74.68  1.52 1.142 39.15
MR151886         0   -90  240  245     5  73.15  74.68  1.52 0.066  2.26
MR151887         0   -90  115  120     5  35.05  36.58  1.52 0.024  0.82
190  200    10  57.91  60.96  3.05 0.083  2.83
MR151889         0   -90   75   90    15  22.86  27.43  4.57 0.014  0.49
240  245     5  73.15  74.68  1.52 0.017  0.58
MR151892         0   -90  180  185     5  54.86  56.39  1.52 0.039  1.34
MR151894         0   -90  330  335     5 100.58 102.11  1.52 0.014  0.48
//et

All holes presented in Table 1 were completed by reverse
circulation (RC) drilling. True width is estimated at 80-100% of
downhole width. Analytical results for the RC holes were performed by
American Assay Laboratory Inc. in Sparks, Nevada, an ISO/IEC 17025:2005
accredited facility. External check assays to verify lab accuracy are
routinely completed by ALS Chemex in Reno, Nevada, also an ISO/IEC
17025:2005 accredited facility. Further details are presented in the
Company's quality assurance and quality control program for the Mineral
Ridge project, available at: MR QAQC.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the producing Mineral Ridge
gold mining operation located in Esmeralda County, Nevada with joint
venture partner Elevon, LLC (30%). Mineral Ridge is a conventional open
pit mining and heap leach operation. The Mineral Ridge property is host
to multiple gold-bearing structures, veins and lenses at exploration,
development and production stages. Scorpio Gold also holds a 100%
interest in the advanced exploration-stage Goldwedge property in
Manhattan, Nevada, with a fully permitted underground mine and 400 ton
per day mill facility. The Goldwedge mill facility has been placed on a
care and maintenance basis and can be restarted immediately when
needed.

Scorpio Gold's President & CEO, Peter J. Hawley, P.Geo., is a
Qualified Person as defined by National Instrument 43-101 and has
reviewed and approved the content of this release.

ON BEHALF OF THE BOARD
SCORPIO GOLD CORPORATION
Peter J. Hawley, President & CEO

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

The Company relies on litigation protection for forward-looking
statements. This news release contains forward-looking statements that
are based on the Company's current expectations and estimates.
Forward-looking statements are frequently characterized by words such
as "plan", "expect", "project", "intend", "believe", "anticipate",
"estimate", "suggest", "indicate" and other similar words or statements
that certain events or conditions "may" or "will" occur, and include,
without limitation, statements regarding the Company's plans with
respect to the exploration, development and exploitation of its Mineral
Ridge project, including potential further exploration or development
of the Oromonte deposit. Such forward-looking statements involve known
and unknown risks, uncertainties and other factors that could cause
actual events or results to differ materially from estimated or
anticipated events or results implied or expressed in such
forward-looking statements, including risks involved in mineral
exploration and development programs, risks related to differences
between mineral reserve and resource estimates and actual operating
results and those risk factors outlined in the Company's Management
Discussion and Analysis as filed on SEDAR. Any forward-looking
statement speaks only as of the date on which it is made and, except as
may be required by applicable securities laws, the Company disclaims
any intent or obligation to update any forward-looking statement,
whether as a result of new information, future events or results or
otherwise. Forward-looking statements are not guarantees of future
performance and accordingly undue reliance should not be put on such
statements due to the inherent uncertainty thereof.

TSX Venture closing price for SGN-V
Date: 2015/11/16
Closing Price: 0.05

TEL:  (819) 825-7618  Peter J. Hawley, President & CEO
EMAIL:  phawley@scorpiogold.com
INTERNET:  www.scorpiogold.com
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1532000013TS11532000785-05494620151117