Source	MARKET NEWS
Date	11/18/2015
Time	05:31:30 AM

Company	 Independence Gold Corp.
Title	Intercepts 15.00 G/t Gold Across 3.05 M At The S





    CDNX Symbol: IGO











Press Release	





Intercepts 15.00 G/t Gold Across 3.05 M At The Sunrise Zone, Yukon --->@NEWS 
RELEASE
INDEPENDENCE GOLD CORP ("IGO-V;IEGCF-0")
- Intercepts 15.00 G/t Gold Across 3.05 M At The Sunrise Zone, Yukon

Independence Gold Corp. (the "Company") is pleased to announce
results from follow-up drilling at its Sunrise Zone on the Boulevard
Project. The best intercepts were 15.00 grams per tonne (g/t) gold
across 3.05 metres (m) and 0.94 g/t gold across 22.86 m. The Company
completed a total of 1,093 m (8 holes) of reverse circulation (RC)
drilling at the Sunrise Zone. The Boulevard Project is located 135
kilometers (km) south of Dawson City, Yukon and is contiguous to the
Coffee Gold Project owned by Kaminak Gold Corporation.

The fall 2015 RC drill program was designed to extend gold
mineralization at the Sunrise Zone, where 7.23 g/t gold across 12.2 m
was intercepted in hole BV15-31, the discovery hole, during the summer
2015 drill program (see news release dated August 24, 2015). The fall
follow-up drill program tested one of several northeast-trending multi-
element soil geochemical anomalies coincident with magnetic low
features. These anomalies are sub-parallel to mineralized trends at
Kaminak's Coffee Gold deposit located 9 km northeast of the Sunrise
Zone.

//st
Significant results from the fall 2015 RC drill program at the
Sunrise Zone are outlined below:
Drill Hole          From (m)    To (m)    Length (m)*    Au (g/t)
BV15-35                45.72     68.58          22.86        0.94
incl.                  53.34     54.86           1.52        2.78
&                      62.48     64.01           1.53        2.13
BV15-36                57.91     67.06           9.15        0.40
incl.                  57.91     59.44           1.53        1.04
BV15-37                73.15     89.92          16.77        0.30
131.06    137.20           6.10        0.49
BV15-39                74.68     80.77           6.09        0.63
BV15-40                24.38     27.43           3.05       15.00
incl.                  24.38     25.91           1.53       27.90
BV15-42                 3.05      4.57           1.52        2.10
91.44     96.01           4.57        1.63
//et

//st
*True thickness estimated to be 60-70% of drill intercepts
//et

The mineralized intercept in hole BV15-40 assayed 15.00 g/t gold
across 3.05 m. This intercept includes 27.90 g/t gold across 1.53 m in
weakly oxidized and sericite-altered quartzite, in combination with
2.10 g/t gold across 1.52 m in weakly oxidized, sericite-altered
quartz-biotite schist. The sulphide mineral and quartz vein content, as
well as the associated pathfinder element concentrations, within the
mineralized intercept in hole BV15-40 are unlike those associated with
the mineralized intercept in discovery hole BV15-31. These differences
imply that two separate, chemically distinct episodes of high grade
gold mineralization have occurred at the Sunrise Zone. Further drilling
is required to determine the relationship between these mineralized
intercepts.

Hole BV15-35 is an inclined "scissor" hole to hole BV15-31, and
was drilled in an attempt to determine the geometry and attitude of the
mineralized zone. The mineralized intercept in hole BV15-35 assayed
0.94 g/t gold across 22.86 m, hosted mainly within quartzite. Holes
BV15-36 and BV15-37 were drilled 25 m on either side of, and parallel
to, hole BV15-35; both of these holes intersected anomalous gold
mineralization. Gold mineralization at the Sunrise Zone appears to
occur within north-northeast striking, steeply dipping structures with
variable amounts of both sulphide minerals and vein quartz. To view the
latest drill map, please click here.

Additional northeast-trending multi-element soil geochemical
anomalies coincident with magnetic low features remain to be drill
tested in the Sunrise area. Further drilling will be required to better
understand the character and orientation of the mineralized structures
at the Sunrise Zone.

Thirteen km to the northwest of the Sunrise Zone is the Denali
Zone, the second new discovery identified during summer 2015 drilling
at the Boulevard Project (see news release dated August 24, 2015). The
best drill intercept to date at Denali is 4.25 g/t gold over 6.10
metres, with mineralization open both along strike and down-dip. Recent
re-interpretation of the geochemical and geophysical data from the
Denali area suggests that there is excellent potential for another,
similar mineralized structure to occur at Denali. This feature is a
high priority drill target.

David Pawliuk, P.Geo., the Company's Qualified Person as defined
by National Instrument 43-101 for the Boulevard Project, has reviewed
the technical information in this news release. Quality assurance and
quality control procedures include systematic insertion of blanks and
standards into the sample sequence. Samples are placed in sealed bags
and shipped directly to SGS Canada Inc.'s analytical facility in
Burnaby, BC for preparation, aqua regia inductively coupled plasma
(ICP) element analysis and fire assay analysis.

Independence Gold Corp. (TSX VENTURE:IGO) is a well-financed
mineral exploration company listed on the TSX Venture Exchange. With
multiple projects in the Yukon, and the 3Ts Project located in British
Columbia, the portfolio ranges from early stage grassroots exploration
to advanced-stage resource expansion. For additional information please
visit the Company's website www.ingold.ca.

INDEPENDENCE GOLD CORP.

Randy Turner, President & CEO

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TSX Venture closing price for IGO-V
Date: 2015/11/17
Closing Price: 0.07

TEL: 604-687-3959
FAX: 604-687-1448   Investor Relations
info@ingold.ca      INDEPENDENCE GOLD CORP.
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1532100002TS11532100644-05291920151118