Source	Marketwire
Date	11/18/2015
Time	04:01:03 AM

Company	 TERRAX MINERALS INC.
Title	TerraX Drills 10.26 m @ 3.61 g/t Au at Hebert-Brent Shear Area, 
Yellowknife City Gold Project





    CDNX Symbol: TXR











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: TerraX Minerals Inc.

TSX VENTURE SYMBOL: TXR
FRANKFURT SYMBOL: TX0
OTC PINK SYMBOL: TRXXF

November 18, 2015

TerraX Drills 10.26 m @ 3.61 g/t Au at Hebert-Brent Shear Area, Yellowknife 
City Gold Project


YELLOWKNIFE, NORTHWEST TERRITORIES--(Marketwired - Nov. 18, 2015) - TerraX 
Minerals Inc. (TSX VENTURE:TXR)(FRANKFURT:TX0)(OTC PINK:TRXXF) has received 
assay results from an initial six hole (953 m) drill program testing 
replacement style mineralization near surface in the Hebert-Brent Shear area on 
its Yellowknife City Gold Project ("YCG"), immediately north of Yellowknife in 
the Northwest Territories. Assay results for 42 holes drilled at Crestaurum 
this summer are pending and will be released once received and interpreted.

Highlights from the six holes reported today from the Hebert-Brent Shear 
include:

/T/

--  10.36 m @ 3.61 g/t Au, including 2.95 m @ 5.01 g/t Au and 2.58 m @ 6.45
g/t Au in hole TNB15-024, and
--  6.70 m @ 2.70 g/t Au, including 2.00 m @ 8.77 g/t Au in hole TNB15-025.

/T/

Drilling of the Hebert-Brent Shear was conducted to follow up on assays from 
cut channel sampling at surface that included 11.00 m @ 7.55 g/t Au (reported 
September 8, 2015) on the original Hebert-Brent Zone (H-B); 17.86 m @ 2.21 g/t 
Au on the Hebert-Brent East Zone (H-B East); 6.00 m @ 10.26 g/t Au on 
Hebert-Brent South Zone (reported September 8, 2015) and 4 m @ 13.89 g/t on the 
Brent Zone (reported October 28, 2015). This channel sampling interpreted 
multiple north to northeast striking shear zones intersecting steeply northeast 
dipping porphyry dykes that led us to expect north-easterly plunging zones of 
mineralization. These drill results, along with surface mapping that was 
carried out in conjunction with the drilling, reveal that the mineralization 
actually resides near the hinges of north to north-northeast trending fold axes 
plunging shallowly to the south. This new interpretation also shows that the 
mineralization in the H-B, Brent, and H-B East is the same zone of 
mineralization, located on a favourable gabbro and bleached mafic volcanics 
next to an identifiable sedimentary (mudstone) unit.

Holes TNB15-024 and TNB15-025 at the H-B zone and TNB15-028 at the H-B East 
successfully intersected the targeted mineralization, albeit at different 
down-hole distances than anticipated. Holes TNB15-026 and 027 failed to 
intersect the zone as they were well below the actual plunge direction, 
although TNB15-026 crossed the structure with minor anomalous gold. Hole 
TNB15-029, targeted on the H-B South, also failed to intersect the zone as it 
was well below and north of the expected south plunge direction. A map showing 
all drill collar locations reported in this news release is available on our 
web site at www.terraxminerals.com.

The shallow plunge directions on the zones make it ideal for follow-up drilling 
with short holes, which will be undertaken during the winter drill program in 
early 2016. In addition, the favourable stratigraphic horizon for the 
mineralization, with the necessary sericite and chlorite alteration, has been 
mapped over much larger areas to the northeast of the Hebert-Brent Shear. These 
areas will be explored during field programs in 2016.

The complete results of the drilling carried out at the Hebert-Brent Shear area 
are summarized below, by zone:

/T/

----------------------------------------------------------------------------
UTM Location
-----------------
(NAD 83)
-----------------
From   To   Interval  Au
Drill Hole   Dip  Azimuth Easting Northing        (m)   (m)    (m)     g/t
----------------------------------------------------------------------------
TNBI5-024   -47    266   636812  6941507        6.14  16.50  10.36   3.61
---------------------------------
incl. 7.14  10.09   2.95   5.01
---------------------------------
and
incl. 13.00 15.58   2.58   6.45
----------------------------------------------------------------------------
TNBI5-025   -87    266   636812  6941507        11.50 18.20   6.70   2.70
---------------------------------
incl. 11.50 13.50   2.00   8.77
----------------------------------------------------------------------------
TNB15-026   -45    269   636851  6942494        26.53 27.29   0.76   0.15
---------------------------------
and  30.00 31.00   1.00   0.23
----------------------------------------------------------------------------
TNB15-027   -45    225   636854  6942522                NSV
----------------------------------------------------------------------------
TNB15-028   -45    250   636847  6942478        3.58  12.00   8.42   1.37
----------------------------------------------------------------------------
TNB15-029   -45    250   636795  6942451                NSV
----------------------------------------------------------------------------

/T/

TerraX collected 804 samples for assay from the drilling reported here. Results 
ranged from below detection to a high of 15.2 g/t Au. Drill hole collar 
locations were surveyed to sub-meter accuracy. Down hole surveying (Easy Shot) 
was completed on all holes. TerraX inserts certified standards and blanks into 
the sample stream as a check on laboratory QC. Drill core samples are cut by 
diamond saw at TerraX's core facilities in Yellowknife. A halved core sample is 
left in the core box. The other half core is sampled and transported by TerraX 
personnel in securely sealed bags to ALS Chemex's (ALS) preparation laboratory 
in Yellowknife. After sample preparation, samples are shipped to ALS's 
Vancouver facility for gold and ICP analysis. Gold assays of greater than 3 g/t 
are re-assayed on a 30 gm split by fire assay with a gravimetric finish. ALS is 
a certified and accredited laboratory service. ALS routinely inserts certified 
gold standards, blanks and pulp duplicates, and results of all QC samples are 
reported.

TerraX and GeoVector Management Inc. were responsible for planning the drill 
holes. GeoVector was also responsible for the management and supervision of the 
drill program. The technical information contained in this news release has 
been approved by Joseph Campbell, the President of TerraX, who is a Qualified 
Person as defined in "National Instrument 43-101, Standards of Disclosure for 
Mineral Projects".

About the Yellowknife City Gold Project

The Yellowknife City Gold Project now encompasses approximately 116 sq km of 
contiguous land immediately north and now south of the City of Yellowknife in 
the Northwest Territories. Through a series of acquisitions, TerraX now 
controls one of the six major high-grade gold camps in Canada - and the least 
explored.

The project lies on the prolific Yellowknife greenstone belt and the combined 
Southbelt and Northbelt properties cover 23 km of strike length on the southern 
and northern extensions of the shear system that hosts the high-grade Con and 
Giant gold mines. The project area contains multiple shears that are the 
recognized hosts for gold deposits in the Yellowknife gold district, with 
innumerable gold showings and high grade drill results on the Northbelt 
property this past year that serve to indicate the project's potential as a 
world-class gold district. Since February 2013, TerraX has consolidated the 
project area by acquiring, optioning and staking numerous properties, 
including: Northbelt, Goodwin, Ryan Lake, Walsh Lake, U-Breccia and Southbelt, 
as well as staking additional contiguous lands. Being within 15 km of the City 
of Yellowknife, the YCG is close to vital infrastructure, including 
transportation, service providers, hydro-electric power and skilled 
tradespeople.

For more information on the Yellowknife City Gold Project, please visit our web 
site at www.terraxminerals.com.

On behalf of the Board of Directors

Joseph Campbell, President

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This news release contains forward-looking information, which involves known 
and unknown risks, uncertainties and other factors that may cause actual events 
to differ materially from current expectation. Important factors - including 
the availability of funds, the results of financing efforts, the completion of 
due diligence and the results of exploration activities - that could cause 
actual results to differ materially from the Company's expectations are 
disclosed in the Company's documents filed from time to time on SEDAR (see 
www.sedar.com). Readers are cautioned not to place undue reliance on these 
forward-looking statements, which speak only as of the date of this press 
release. The company disclaims any intention or obligation, except to the 
extent required by law, to update or revise any forward-looking statements, 
whether as a result of new information, future events or otherwise.

- 30 -

CONTACT INFO:

Contact: Paradox Public Relations
info@paradox-pr.ca
Phone: 514-341-0408
Toll Free: 1-866-460-0408

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=549776877