Source	MARKET NEWS
Date	11/24/2015
Time	05:32:05 AM

Company	 Troymet Exploration Corp.
Title	Targets The Rattler Breccia At Wildcat





    CDNX Symbol: TYE











Press Release	





Targets The Rattler Breccia At Wildcat --->@NEWS RELEASE
TROYMET EXPLORATION CORP ("TYE-V;TRYXF-0")
- Targets The Rattler Breccia At Wildcat

Troymet Exploration Corp. ("Troymet" or the Company") is pleased to
update exploration progress on its Wildcat gold-silver project located
in the Detroit Mining District, an historic gold producing region in
the northern Drum Mountains of central Utah. Troymet's exploration
focus is gold and silver mineralization in veins, stockworks, breccias
and bulk-tonnage deposits along the Joy Fault, and in
structural/stratigraphic hosts in Cambrian carbonate rocks.

As previously reported (news release dated July 27, 2015)
Troymet's initial exploration in the Southeast (SE) target area pointed
to the likelihood of untested precious metal mineralization at shallow
depths associated with anomalous soil and rock chip geochemistry (some
rock chip values are again reported below in summary form for the sake
of completion). Subsequently, Troymet completed detailed geological and
structural mapping, soil and rock geochemical sampling, hand trenching
and detailed bi-directional ground magnetic and EM surveys in order to
identify specific drill targets.

The Rattler Breccia (see Location Map) is developed in a
structurally complex location on the Joy Fault. Several significant
faults, either mapped in the field or interpreted from geophysics,
intersect at or near the breccia. As well, the detailed geophysical
survey suggests the possible existence of a step-over structure up to
200 meters wide in the hangingwall of the Joy Fault. The breccia and
adjacent carbonate host rocks are strongly anomalous in gold and other
trace elements associated with epithermal and carbonate-hosted gold
deposits. Three select rock chip samples of the breccia grade from
0.115 to 2.46 ppm gold (average 1.29 ppm), with tellurium (assayed in
two samples) concentrations of 15 ppm and )500 ppm. Adjacent variably
decalcified and silicified carbonate rocks range up to 3.94 ppm gold
(Au), )500 ppm tellurium (Te), 37 ppm mercury (Hg), 283 ppm antimony
(Sb), and 45 ppm thallium (Tl) - see table. The anomalous values of Au,
Ag, As, Sb, Te, Hg and Tl in carbonate rocks is notable and indicates
the potential for mineralization in feeders and as replacement deposits
in carbonates. The presence of Au and Te in the mineralization
indicates similarities with the mineralization on High Grade hill in
the Core target area approximately 2,700 metres to the northwest (news
release dated November 17, 2015).

//st

----------------------------------------------------------------------------
Rock        Sample             Au      Ag      As     Bi   Cu
Sample ID    Type        Type              ppm     ppm     ppm    ppm   ppm
----------------------------------------------------------------------------
RLDC6219_07  Jasperoid   Select rock
breccia     chips          1.290    1.60   259.0   4.00  21.0
----------------------------------------------------------------------------
MC13-WC001   Jasperoid   Select rock
breccia     chips          0.115    0.66    12.8   0.23   8.7
----------------------------------------------------------------------------
K DownesWC5  Jasperoid   Select rock
breccia     chips          2.460    1.44   332.0   5.74  16.0
----------------------------------------------------------------------------
GXD-1266     Decalcified Select rock
carbonate   chips          3.940    6.71    47.3   0.93   4.5
----------------------------------------------------------------------------
GXD-1253     Decalcified Select rock
carbonate   chips          2.180    0.57   391.0   0.19   8.8
----------------------------------------------------------------------------
MC15-WC100   Carbonate   Chip channel,
with FeOx   0.12m          0.347    0.09   387.0   1.32  15.8
----------------------------------------------------------------------------
MC15-WC101   Sanded      Chip channel,
carbonate   1.8m           0.016    0.02    50.8   0.05   3.6
----------------------------------------------------------------------------
GXD-1265     Volcanic    Select rock
tuff        chips          0.300    1.59    22.3   0.72  16.0
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Rock        Sample           Hg    Sb                  Te   Tl
Sample ID    Type        Type            ppm   ppm                 ppm  ppm
----------------------------------------------------------------------------
RLDC6219_07  Jasperoid   Select rock
breccia     chips         24.0  57.0                      8.0
----------------------------------------------------------------------------
MC13-WC001   Jasperoid   Select rock
breccia     chips                4.0                14.8  2.0
----------------------------------------------------------------------------
K DownesWC5  Jasperoid   Select rock
breccia     chips         37.4  99.6    greater than 500  5.3
----------------------------------------------------------------------------
GXD-1266     Decalcified Select rock
carbonate   chips               99.7                99.6 11.9
----------------------------------------------------------------------------
GXD-1253     Decalcified Select rock
carbonate   chips              283.0    greater than 500 20.0
----------------------------------------------------------------------------
MC15-WC100   Carbonate   Chip channel,
with FeOx   0.12m          0.4  45.8                 9.0 44.7
----------------------------------------------------------------------------
MC15-WC101   Sanded      Chip channel,
carbonate   1.8m           0.5  20.2                 0.3 12.6
----------------------------------------------------------------------------
GXD-1265     Volcanic    Select rock
tuff        chips                5.7                16.4  2.0
----------------------------------------------------------------------------

//et

The Rattler Breccia is exposed in Cambrian limestones in the
footwall of the Joy Fault adjacent to a large recessive zone along the
margin of the Thomas Caldera. Rounded clasts of probable Prospect
Mountain Quartzite indicate significant hydrothermal transport in the
breccia ()300 metres). The immediate target area is ~100 metres x 50
metres but may be larger.

Drilling will target structures and prospective calcareous
siltstone/sandstone beds of the Big Horse member of the Orr Formation,
which hosts most gold mineralization exposed elsewhere on the Wildcat
property. It is anticipated that multiple fault intersections could
have provided a broad zone of structural preparation in these favorable
host rocks to produce a significant zone of gold mineralization at
relatively shallow depths. There is no record of prior drilling on the
Rattler Breccia.

Troymet's rock and soil samples are analyzed by ALS Global in
Reno, Nevada, an ISO/IEC 17025:2005 accredited facility.

Kieran Downes, President and CEO of Troymet, comments: "The
Rattler Breccia offers significant discovery potential for previously
unrecognized precious metal targets in a new area."

Qualified Persons

All technical data, as disclosed in this press release, has been
verified by the Company's qualified persons Kieran Downes, Ph.D. P.Geo.
and Mark Coolbaugh, Ph.D., CPG. Both are Qualified Persons as defined
by National Instrument 43-101.

About Troymet Exploration Corp.

Troymet Exploration Corp. is a junior exploration company with a
solid treasury and with projects in British Columbia (Redhill and
Golden Eagle), Manitoba (McClarty Lake) and Utah (Wildcat). Troymet
operates the Wildcat, Redhill and Golden Eagle projects. Hudbay
Minerals Inc. is the operator of the McClarty Lake joint venture and
must contribute $1,151,052 in joint venture expenditures before Troymet
is required to fund its participating interest. Troymet retains a 2%
net smelter returns royalty (NSR) on the Key property, British
Columbia, which was sold to New Gold Inc. in 2013. Troymet is
continuing to evaluate mineral properties for acquisition.

TROYMET EXPLORATION CORP.

Kieran Downes, Ph.D., P.Geo., President, CEO & Director

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release.

This news release may contain certain forward-looking information.
All statements included herein, other than statements of historical
fact, are forward-looking information and such information involves
various risks and uncertainties. In particular, this news release
contains forward-looking information in respect of: the Wildcat
Project, including the exploration potential and analogous deposit
potential of the Wildcat Project; future data analysis, sampling plans
and exploration plans on the Wildcat Project; and exploration targets
and the potential of such exploration targets. There can be no
assurance that such information will prove to be accurate, and actual
results and future events could differ materially from those
anticipated in such information. This forward-looking information
reflects Troymet's current beliefs and is based on information
currently available to Troymet and on assumptions Troymet believes are
reasonable. These assumptions include, but are not limited to: the
current share price of Troymet's common shares and the ability to raise
future equity financing, if needed, at prices acceptable to Troymet;
Troymet's current and initial understanding and analysis of the Wildcat
Project; the ability of Troymet to discover viable exploration targets
and the results of exploration on the Wildcat Project; Troymet's
general and administrative costs remaining constant; and the market
acceptance of Troymet's business strategy. Forward-looking information
is subject to known and unknown risks, uncertainties and other factors
which may cause the actual results, level of activity, performance or
achievements of Troymet to be materially different from those expressed
or implied by such forward-looking information.             Such risks
and other factors may include, but are not limited to: the early stage
development of Troymet and its projects, and in particular, the Wildcat
Project; general business, economic, competitive, political and social
uncertainties; capital market conditions and market prices for
securities, junior market securities and mining exploration company
securities; commodity prices; the actual results of current exploration
and development or operational activities; competition; changes in
project parameters as plans continue to be refined; accidents and other
risks inherent in the mining industry; lack of insurance; delay or
failure to receive board or regulatory approvals; changes in
legislation, including environmental legislation, affecting Troymet;
timing and availability of external financing on acceptable terms;
conclusions of economic evaluations; and lack of qualified, skilled
labour or loss of key individuals. A description of other assumptions
used to develop such forward-looking information and a description of
other risk factors that may cause actual results to differ materially
from forward-looking information can be found in Troymet's disclosure
documents on the SEDAR website at www.sedar.com. Troymet does not
undertake to update any forward-looking information except in
accordance with applicable securities laws.



Troymet Exploration Corp.
Anthony Zelen



















TSX Venture closing price for TYE-V
Date: 2015/11/17
Closing Price: 0.02

TEL: 888-456-4952 or C: 778-388-5258
E-mail:   anthony@senergyir.com
Internet: www.troymet.com
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1532700009TS11532700622-05301620151124