Source	MARKET NEWS
Date	11/21/2016
Time	05:08:31 AM

Company	 Savary Gold Corp.
Title	Initiates The 
Largest Exploration Program in its





    CDNX Symbol: SCA











Press Release





SAVARY GOLD CORP ("SCA-V;SVVYF-0")
- Initiates The Largest Exploration Program in its History

Savary Gold Corp. ("Savary" or the "Company") is pleased to
announce that, along with partner Sarama Resources Ltd., it has
initiated its largest ever exploration program at its Karankasso JV
Project in southwestern Burkina Faso.

In late October, Savary, the operator of the Karankasso JV,
initiated an approximately US$2.6 million exploration program
consisting up to 21,000 metres of drilling (8,000 metres costing
~US$600,000, contingent on results), 12,000 metres of auger drilling,
approximately 275 line kilometres of gradient IP geophysical surveys
(see Figure 1) and collection of up to 3,000 soil samples. The initial
planned holes are designed to extend the in-pit inferred mineral
resources at the Karangosso, West Trend, Diosso South and Kueredougou
West Zones (see Figures 1 and 2). Priority will be given to extending
these zones along strike and to select in-fill holes which will add
confidence to the existing zone interpretations. Once the drill program
is completed, the Company plans to update the existing resource on the
back of this drill program in the second half of 2017.

Don Dudek, President and CEO of Savary states "The goal of this
work program is to materially increase our current in-pit inferred
mineral resource estimate and provide good visibility for additional
mineral resources with extensions to known zones and the discovery of
new zones. As well, we are also going to try some new things like
turning the drill 90 degrees, in areas like Serakoro 1 West, where
previous work has returned intercepts to 6.42 g/t gold over 15 metres
and Au-in-soil anomalies to 5,290 ppm gold, but follow-up drilling has
not been able to define a coherent zone. Recognition of
east-northeast-trending high grade zones on an adjacent property, make
this type of zone, a reasonable and compelling target. Management
believes that our current resource zones coupled with new exploration
opportunities, provide a compelling investment thesis. Our plan is to
hit this project hard with an aggressive combined drill, geophysical,
geochemical and geological program with a view to updating the mineral
resource estimate by the end of late Q3 or early Q4, 2017."

The new auger drilling, geophysical and soil sampling programs
started in late October, 2016. Phase 1 of the drilling will commence
during the week of November 21, as planned. Phase one consists
approximately 3,000 metres of RC and core drilling, in 22 holes,
pre-year end. This part of the program will comprise the following
goals;

--Drilling to test for extensions to in-pit mineral resources at
the Karangosso and Diosso South Zones, which combined, contain an
in-pit inferred mineral resource estimate of approximately 200,000
ounces of gold grading 2.77 g/t gold1,2,3,4,5,6 which form part of the
current in-pit inferred mineral resource estimate of 671,000 ounces
grading 2.28 g/t gold1,2,3,4,5,6;

--Follow-up testing of the Splay 2 Zone where the first hole
returned 9.75 g/t gold over 7 metres and 12.24 g/t gold over 4 metres;

--Start to test, with 200 to 400 metre spaced RC holes, the ~3.5
long, IP chargeability geophysical anomalies and new artisanal mining
zones that connect the Kueredougou West Zone to the Diosso South and
West Trend Zones (see Figure 2).

Phase 2 of the program consists of approximately 10,000 metres of
RC drilling and is scheduled to commence on or about January 20. This
portion of the program will focus on the following goals:

--Continued drilling to test for extensions to the Karangosso,
Kueredougou West, Diosso South and West Trend Zones;

--Continued testing, with 400 to 600 metre spaced drill holes, of
the geophysical anomalies that connect the Kueredougou West Zone with
the Diosso South and West Trend Zones;

--Follow-up of significant drill intercepts from the phase one
program;

--Test targets developed from current geophysical and auger
surveys;

--Follow-up on previous RAB and RC holes that have returned up to
2.80 g/t gold over 12 metres and RC holes that returned 2.66 g/t gold
over 10 metres in the Serakoro 1 West and Main Zones, respectively;

--Test for an alternative strike for gold zones at the Serakoro 1
West Zone where previous holes returned 6.42 g/t gold over 15 metres
and 18.72 g/t gold over 4 metres.

Phase 3 of the program, which is contingent on the results of the
first two phases of the program, would start at the beginning of May;
this portion of the program totals approximately 8,000 metres of RC
drilling.

Auger drilling is being carried out over five high priority target
areas along known gold-bearing structures, where shallow surficial
cover precludes fine tuning of drill targets.

To date, gradient IP survey conductivity data has proven to be
extremely effective at identifying the location of the
long-strike-length structures that are associated with gold
mineralization. During a recent trip to site, a new artisanal mining
area was discovered exactly where the gold bearing trend was predicted
and close to where an exploration hole was planned (see Figure 2).

The central, gold enriched corridor is a 45-kilometre long gold in
soil trend that is bracketed by the thick red dashed lines in Figure 1.
Figure 1 also presents the location of known gold zones along with the
strong geophysical IP gradient chargeability trend that links the
gold-bearing zones along with the central part of the Au-in-soil trend,
onto the Serakoro 1 concession. From this image, it appears that the
Serakoro 1 Main area lies along the likely southern continuation of the
structures that host most of the Zones with current resources, in the
northern part of the image. Along this trend, there is an
11.5-kilometre gap in the drilling between the furthest south hole on
the Diosso South Zone and the northern-most holes in the Serakoro 1
Main area. This drill and exploration gap exists due to the combination
of extensive laterite cover and local alluvium cover that masks the
surface expressions of the structures that are believed to be
gold-bearing. Augur drill surveys combined with gradient IP survey
data, will be used to refine drill targeting.

A second major, at least 29-kilometre long, anomalous gold-in-soil
bearing trend, lies along the western portion of the property and hosts
the Karangosso, NWQV and Serakoro 1 West Zones. This Au-in-soil trend
is up to 1.2 km wide, lies along the western margin of the Hounde Belt
and is dominantly hosted by felsic intrusions that intruded into the
volcanic and sedimentary rocks along the western margin of the Hounde
belt. Previous exploration has intersected significant gold
mineralization in both RC and AC (air core) holes along this trend. A
southern extension of this trend, which has returned AC holes
containing 2.80 g/t gold over 12 metres, have never been followed up.
Significant drill intercepts such as this require follow-up, however,
much of this western trend is covered by laterite which makes follow-up
more challenging. Both auger drilling and gradient IP geophysical
surveys are being carried out to support drill targeting.

1,2,3,4,5,6 Mineral Resource Estimate Notes

1.Mineral resources which are not mineral reserves do not have
demonstrated economic viability. The estimate of mineral resources may
be materially affected by environmental, permitting, legal, title,
taxation, sociopolitical, marketing, or other relevant issues.

2.The quantity and grade of reported inferred resources in this
estimation are uncertain in nature and there has been insufficient
exploration to define these Inferred resources as an Indicated or
Measured mineral resource and it is uncertain if further exploration
will result in upgrading them to an Indicated or Measured mineral
resource category.

3.The Karankasso Property Resource Estimates were prepared by
Eugene Puritch, P. Eng. and Antoine Yassa, P. Geo. from P&E Mining
Consultants Inc., Qualified Persons under NI 43-101 who are independent
of the Company.

4.The mineral resources were estimated using the Canadian
Institute of Mining, Metallurgy and Petroleum (CIM), CIM Standards on
Mineral Resources and Reserves, Definitions and Guidelines prepared by
the CIM Standing Committee on Reserve Definitions and adopted by CIM
Council.

5.The gold price used in this estimate was the Aug 31/15
approximate two year trailing average of US$1,250/oz. Gold recovery was
93% and mining costs were US$2.75/tonne. Processing and G&A costs
combined were US$18.50/tonne. Pit optimization slopes were 50 degrees.
Bulk densities used for the resource estimate were as follows;
Saprolite 1.98 t/m3, Sap Rock 2.45 t/m3 and Fresh Rock 2.80 t/m3.

6.The effective date of the Mineral Resource Estimate is October
7, 2015.

Figure 1 - Karankasso Property Surface Plan

Figure 2 - Detailed Compilation of Kueredougou West to Diosso
South Area

QA/QC information

Savary's procedures for handling reverse circulation drill chips
comprise initial riffle splitting of the rock chips from one metre
drill length samples into approximately 2.5 kilogram samples, as well
as description and logging into a database. A duplicate 2.5-kilogram
sample, prepared at the same time as the assay sample, is kept as a
reference for each sample. Assay standards, sample duplicates and assay
blanks were inserted sequentially every 14 samples resulting in an
assay standard inserted every 42 samples. This sampling procedure was
periodically reviewed by Savary's President and CEO, and the Company
QP, Don Dudek, P. Geo. All assay samples were collected at site by SGS
Laboratory staff from Ouagadougou, Burkina Faso. Sample preparation and
fire assays were performed by SGS Laboratories based in Ouagadougou.
Each sample was dried, crushed to 85% passing 2mm and then split to 1.5
kg by riffle splitter. The 1.5 kg, 2 mm split was pulverized to 95%
passing 106?m. Fifty grams of the pulverized material was analysed for
gold via fire assay with an atomic absorption spectroscopy (AAS)
finish. SGS Burkina Faso SA operates according to ISO 17025 standards
and institutes a full Quality Assurance/Quality Control (QA/QC) program
consisting of insertion of blanks, standard reference material, repeats
and reject splits which in total account for up to 25% of all
determinations conducted.

Sarama QAQC Statement (Sarama August 13, 2012 news release for
Serakoro 1 Concession)

Sarama undertook geological sampling and assaying in accordance
with its QA/QC program which includes the use of certified reference
materials and duplicates. Gold assay work was undertaken by SGS S.A.
("SGS") laboratories in Ouagadougou, Burkina Faso and Morila, Mali.
Assays are determined by the fire assay method using a 50-gram charge,
lead collection and an AAS finish with a 0.01 g/t Au lower detection
limit.

About Savary Gold

Savary Gold is a Canadian exploration company which, along with
partner Sarama Resources Limited, is focused on exploring and
developing the Karankasso Gold Project in Burkina Faso. At July 2016,
the Karankasso JV Project was approximately 69.5% owned by Savary and
30.5% owned by Sarama Resources Limited ("Sarama").The Project
properties lie within the Birimian age, Hounde Greenstone Belt, which
hosts Semafo's Mana mine, Roxgold's Yaramoko Mine and additional gold
deposits that are presently subject to production decisions and
extensive exploration efforts (including Endeavour Mining's Hounde
Project, Orezone's (acquired by Sarama) Bondi Project and
Sarama's/Acacia's South Hounde Project, which is adjacent to Savary
Gold's property). The Project contains an Inferred open pit constrained
mineral resource estimate of 9.16 million tonnes grading 2.28 g/t gold
(Savary news release November 24, 2015). For additional information
please visit our website at www.savarygold.com.

The Companies philosophy is to continue to keep corporate
overheads as low as practical so that most the funds raised flow back
into developing its projects.

Don Dudek, P.Geo., President and CEO of the Company and a
qualified person under National Instrument 43-101, has reviewed and
approved the scientific and technical information in this press
release.

SAVARY GOLD CORP.

On behalf of the Board

"Don Dudek"

President & Chief Executive Officer



Cautionary Notes

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

This news release may contain forward-looking statements. These
statements include statements regarding the details of the potential
value growth of the JV, the upside of the property, the drill program,
the company's exploration plans and the timing of results, the focus on
existing drill targets and new targets. These statements are based on
current expectations and assumptions that are subject to risks and
uncertainties. Actual results could differ materially because of
factors discussed in the management discussion and analysis section of
our interim and most recent annual financial statement or other reports
and filings with the TSX Venture Exchange and applicable Canadian
securities regulations. We do not assume any obligation to update any
forward-looking statements, except as required by applicable laws.
































TSX Venture closing price for SCA-V
Date: 2016/11/18
Closing Price: 0.09

TEL: 647-259-2097
E-mail: info@savarygold.com
Internet: www.savarygold.com
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1632500001TS11632500615-05054220161121