Source	MARKET NEWS
Date	11/08/2016
Time	05:48:21 AM

Company	 Kivalliq Energy Corporation
Title	Results 
From 2016 Exploration At Angilak; Yat Ch





    CDNX Symbol: KIV











Press Release




[200/News Release]KIVVKIVALLIQ ENERGY CORPNOV 08 2016  05:46 AMResults 
From 2016 Exploration At Angilak; Yat Channel Samples ReturnHigh grade 
Precious Metal And Uranium Values --->@NEWS RELEASE
KIVALLIQ ENERGY CORP ("KIV-V;KVLQF-0")
- Results From 2016 Exploration At Angilak; Yat Channel Samples
- Return High-grade Precious Metal And Uranium Values

Kivalliq Energy Corporation (Kivalliq) announced results from
Kivalliq's 2016 summer exploration program at the Yat and Dipole Target
areas of Kivalliq's 100% owned, 89,852 hectare Angilak Property in
Nunavut Territory, Canada.

"We are excited that the 2016 work at Yat has confirmed high grade
precious metal and uranium values from earlier programs are linked to
local bedrock occurrences, in addition to kilometer-scale geochemical
and geophysical signatures," stated Kivalliq President Jeff Ward.
"Furthermore, soil sampling around the recent Dipole uranium discovery
extended uranium anomalies to over 3.5 kilometres, thereby giving high
grade zones drilled at Dipole significant strike potential."

Highlights

//st
A trenching program at Yat collected rock samples from both bedrock and
frost heaved boulders. Results confirm high grade polymetallic U-Cu-Ag-Au
(Pt-Pd) mineralization identified in boulders are derived from localized
bedrock sources.

Highlight channel sample assays include:

2.50% U3O8, 16.2% Cu, 417 g/t Ag & 1.3 g/t Au across 0.5 m in Trench
Kiv-16-T03

0.32% U3O8, 373 g/t Ag, 2.9 g/t Au & 6.4 g/t Pd across 0.65 m in Trench
Kiv-PO-T05

Highlight frost heaved boulder sample assays include:

23.6% U3O8, 22.7% Cu, 879 g/t Ag & 5.3 g/t Au at Trench Kiv-16-T03

3.0% U3O8, 1.3% Cu, 3200 g/t Ag, 43.3 g/t Au, 7.8 g/t Pt & 56.3 g/t Pd at
Trench Kiv-PO-T05

Results from 704 enzyme leach (EL) soil samples collected in 2016 has
further outlined multiple anomalous uranium in soil trends at Yat and
Dipole.

At Yat, a pronounced uranium in soil anomaly has been defined along a
strike length of 1.6 km coincident to the Yat electromagnetic (EM)
conductor. A corroborating enzyme leach silver in soil anomaly occurs along
the same trend.

At Dipole, a strong uranium in soil anomaly has been defined along a strike
length of 0.6 km over a conductive trend parallel to the Dipole structure
and 1.5 km to 2.1 km northeast of the high grade uranium values drilled in
2015.
//et

Maps and images of the work performed in 2016 at the Yat Target and
the Dipole Trend can be viewed at:
http://www.kivalliqenergy.com/uranium/angilak/maps/.

Yat Target

The Yat Target is located near the northern margin of the Angikuni
Basin, 15 km southwest of Lac 50 and 10 km northeast of the high grade
uranium intercepts discovered by drilling at Dipole in 2015. Mineral
occurrences at Yat locally comprise a 100 m long string of
sulphide-bearing radioactive subcrops and historic pits in basin
conglomerate and sandstone. Yat is characterized by a strong 250 m wide
magnetic low with coincident high grade polymetallic U-Cu-Ag-Au (Pt-Pd)
mineralized zones. A discreet EM conductor strikes northeast at 045
through the centre of the magnetic response. Work in the late 1970's
and early 1980's included U-Cu-Mo-Ag-Pb soil surveys, trenching and
four drill holes. There is no historic record of rock analysis for Au,
Ag, or PGM's. Work by Kivalliq between 2007 and 2012 included ground
gravity, Mag-VLF surveys, and four shallow reverse circulation holes
nearby that did not intersect significant mineralization. A grab sample
from brecciated quartz-carbonate veined glacial float collected on the
south east margin of the Yat magnetic response returned the highest
precious metal assays ever reported from the Angilak Property with
1.82% U(sub)3(/sub)O(sub)8(/sub), 6.8% Cu, 211 g/t Au, 80,900 g/t Ag,
3.1 g/t Pt and 6.7 g/t Pd (See news release November 10, 2015)

In July 2016, a trenching program was undertaken in the area of the
high grade polymetallic boulders and historic pits using a
heli-portable excavator. The objective was to find a localized bedrock
source for the high grade boulder mineralization at a site with shallow
glacial till overburden. Trenches were excavated to bedrock with a
maximum depth of about 2.0 m, the depth limit of the excavator.
Radioactive, brecciated carbonate veining with sulphides, secondary
yellow uranium staining and malachite was identified in several trench
areas. Mineralization occurs as 1.0-1.5 m wide structural zones of
narrow veins and stringers in sandstone, conglomerate and Christopher
Island volcanics of the Proterozoic Angikuni Basin, striking northeast
and parallel to the larger Yat EM conductor. Mineralized veins within
these structural zones are generally narrow (( 5 cm wide) but in places
exceed widths of 20 cm. Veining and adjacent wall rocks were channel
sampled using a diamond rock saw. Mineralized subcrop and boulders
encountered while excavating were also sampled. A total of 100 samples
were collected with the 2016 Program.

Highlights include channel sample 18924 from Trench Kiv-16-T03
which assayed 2.50% U(sub)3(/sub)O(sub)8(/sub), 16.2% Cu, 417 g/t Ag
and 1.3 g/t Au over a width of 0.5 m that included a 15 cm wide
brecciated carbonate vein with strong malachite and channel sample
A00560 from Trench Kiv-PO-T05 which assayed 0.32%
U(sub)3(/sub)O(sub)8(/sub), 0.10% Cu, 373 g/t Ag, 2.9 g/t Au and 6.4
g/t Pd across a width of 0.65 m that included a 10 cm wide white
brecciated carbonate vein. Highlight grab samples collected from
boulders found while excavating the trenches include sample A00619 with
23.6% U(sub)3(/sub)O(sub)8(/sub), 22.7% Cu, 879 g/t Ag & 5.3 g/t Au
from till cover at Trench Kiv-16-T03 and sample 18939 with 3.0%
U(sub)3(/sub)O(sub)8(/sub), 1.3% Cu, 3200 g/t Ag, 43.3 g/t Au, 7.8 g/t
Pt & 56.3 g/t Pd from till cover at Trench Kiv-PO-T05.

TABLE 1: 2016 Yat Trenching Program -- Highlight Channel Sample
Assays and Rock Sample Assays

//st
Sample  Type % U3O8 % Cu Ag g/t Au g/t Pt g/t Pd g/t    Trench  Width
(cm)
18924  Channel  2.5 16.2    417   1.28  0.01   0.03 KIV-16-T03    50
18922  Channel  1.4 3.73   67.8   1.55  0.37    1.2 KIV-16-T03    55
18902  Channel 0.66 1.67   48.5   0.05     0      0  KIV-PO-T6    69
A00576 Channel 0.35 0.17   17.8   1.05  0.93   0.57  KIV-PO-T5    75
A00560 Channel 0.32 0.13    373   2.92  0.58   6.36  KIV-PO-T5    65
A00619    Rock 23.6 22.7    879   5.25  0.05   0.11 KIV-16-T03
cover Float
18939     Rock    3 1.28   3200  43.31   7.8  56.31  KIV-PO-T5
cover Float
18942     Rock 1.53 0.64   76.1   10.3  0.59   1.75 KIV-16-T06
cover Float
A00616    Rock 1.28 3.59   78.9    2.3  1.25      5 KIV-16-T05
cover Float
18907     Rock 0.21 0.46   15.4   53.6  1.21   6.03 KIV-16-T06
cover Float
//et

2016 Soil Geochemistry Program

The 2016 summer program included the collection of 704 soil samples
for enzyme leach (EL) analysis. The majority of these samples were
collected at 50 m intervals along sample lines spaced 100 m apart on a
1.2 km by 1.2 km grid centered over the Yat magnetic low and historic
trenches. The grid was also designed to cover 1.6 kms of the main Yat
conductor, an EM linear that strikes northeast at 045 through the
centre of the Yat magnetic feature, approximately 75 m northwest
(up-ice) and parallel to the structurally controlled high grade
polymetallic mineralization sampled by the 2016 Yat trenching program.
A pronounced EL uranium in soil anomaly (measured in ppb) has been
defined along the full 1.6 km strike length of the Yat EM conductor
covered by the 2016 soil grid. A silver in soil anomaly is also present
along this trend, corroborating the Ag-U association seen in the
mineralized trenches. Additionally, a distinctive EL uranium in soil
anomaly overlies a parallel conductor, approximately 0.5 km southeast
of the Yat EM conductor.

As part of the 2016 program, additional EL samples were collected
to extend the 2014 soil grid along the Dipole trend where drilling in
2015 discovered significant uranium mineralization associated with the
Dipole conductor and a pronounced EL uranium anomaly in soils. (See
news release July 30, 2015) Results from the 2016 samples have defined
a new EL uranium in soil anomaly with a strike length of 0.6 km that
overlies a parallel EM conductor 1.5 km to 2.1 km northeast of the
Dipole drill holes. These new results extend uranium in soil anomalies
to over 3.5 kilometres along the Dipole Trend.

Table 2. shows value ranges and anomalous thresholds for elements
of interest from the combined 2014-2016 EL soil sampling programs at
Yat and Dipole.

TABLE 2: 2014-2016 Yat and Dipole Enzyme Leach Soil Sampling --
Comparative Percentile Values

//st
Uranium          Copper       Molybdenum          Silver
Percen-   U     Percen-  Cu      Percen-  Mo     Percen-  Ag
tile  ppb    n  tile  ppb    n   tile  ppb    n  tile  ppb    n
75    9  247    75   73  237    75     2  246    75  0.8  262
85   14  147    85  108  143    85     3  150    85  1.2  142
90   18  100    90  136   96    90     4   95    90  1.5  104
95   30   48    95  190   48    95     5   62    95  2.5   49
Min  0.1    -   Min    3    -   Min     1    -   Min  0.2    -
Max  129    -   Max 2040    -   Max    21    -   Max 16.4    -
Avg  8.5    -   Avg   65    -   Avg   1.8    -   Avg  0.8    -
//et

The 2016 summer program confirmed Yat as a priority target by
identifying silver and uranium trends in soil along a 1.6 km long EM
conductor, and by confirming that high grade polymetallic prospecting
samples are locally derived and related to sub parallel structural
zones in trenches. The program also extended the strike potential of
uranium zones drilled at Dipole by identifying strong uranium in soil
values along trend and coincident to a parallel conductor 2.1 km
northeast of Dipole.

As demonstrated by the discovery of uranium at Dipole in 2015, the
integration of soil geochemical sampling and geophysical surveying has
proven to be effective for successfully targeting basement hosted
uranium mineralization at Angilak. Drill testing of the multiple
coincident geochemical-geophysical targets defined by the 2016
exploration program at both Yat and Dipole is warranted.

In addition to EL soil sampling and trenching, Kivalliq staff
collected 172 soil samples for conventional ICP geochemical comparative
analysis at Yat. Results showed similar results to the 2016 enzyme
leach sampling. Kivalliq staff also collected 41 twenty kilogram heavy
mineral samples located "down-ice" (south-southeast) from 13 circular
geophysical responses characteristic of kimberlitic intrusions. Heavy
mineral concentrates from these samples will be picked and analysed for
gold grains and kimberlite indicator mineral grains by CF Minerals in
Kelowna BC. Results from this work are pending.

QA/QC

Enzyme leach (EL) soil samples were sent to Activation Laboratories
Ltd. (Actlabs). The Actlabs facility is accredited to international
quality standards through the International Organization for
Standardization/International Electrotechnical Commission (ISO/IEC)
17025 (ISO/IEC 17025 includes ISO 9001 and ISO 9002 specifications)
with CAN-P-1578 (Forensics), CAN-P-1579 (Mineral Analysis) and
CAN-P-1585 (Environmental) for specific registered tests by the
Standards Council of Canada (SCC). For EL soil sample analysis, a 0.75
gram sample of B soil horizon is leached in an enzyme matrix for one
hour, where it reacts with amorphous MnO2 dissolving it. Metals complex
with the acid present and solutions are analyzed and reported in ppb
with a detection limit of ) 0.1 ppb U. QA/QC includes field standards,
blanks and duplicates, and those inserted by the Actlabs. All QA/QC
results were within expectations.

Rock samples and conventional soil samples were sent to the
Saskatchewan Research Council (SRC) for analysis. The SRC facility
operates in accordance with ISO/IEC 17025:2005 (CAN-P-4E), General
Requirements for the Competence of Mineral Testing and Calibration
laboratories and is accredited by the Standards Council of Canada.
Conventional soil samples undergo standard geochemical analysis using
ICP-MS. Rock samples are analyzed by SRC's ICP-OES multi-element
Uranium exploration ICP1 method. ICP results U ) 1,000 ppm are analyzed
using SRC's ISO/IEC 17025:2005-accredited U(sub)3(/sub)O(sub)8(/sub)
Assay method. Laboratory quality control (QC) includes a repeat
analysis on every 20th sample. Certain samples were also subject to
SRC's Au3 standard Fire Assay procedures for Au, Pt and Pd. All QA/QC
results for rocks samples and soil samples were within expectations.

Previous exploration results by Noranda Exploration Ltd. and Pan
Ocean Oil Ltd. reported herein are historic in nature and although not
verified by Kivalliq, this work was carried out by knowledgeable
explorers using acceptable industry practices at the time. Jeff Ward,
P.Geo., President of Kivalliq and a Qualified Person for Kivalliq, has
reviewed and approved the scientific and technical information
contained in this release.

About Kivalliq Energy Corporation

Kivalliq Energy Corporation (TSX VENTURE: KIV) is a Vancouver-based
company with a portfolio of high-quality uranium exploration projects
in Canada. Kivalliq holds Canada's highest-grade uranium resource
outside of Saskatchewan. The Company's flagship project, the 89,852
hectare Angilak Property in Nunavut Territory, hosts the Lac 50 Trend
with a NI 43-101 Inferred Resource of 2,831,000 tonnes grading 0.69%
U(sub)3(/sub)O(sub)8(/sub), totaling 43.3 million pounds
U(sub)3(/sub)O(sub)8(/sub). Kivalliq's comprehensive exploration
programs continue to demonstrate the "District Scale" potential of the
Angilak Property. For disclosure related to the inferred resource for
the Lac 50 Trend uranium deposits, please refer to Kivalliq's news
release of March 1, 2013.

In Saskatchewan, Kivalliq holds a 100% interest in the recently
acquired 13,711 hectare Hatchet Lake Property adjacent to the
north-eastern margin of the highly prolific uranium-producing Athabasca
Basin. Compilation of results from previous exploration by Hathor
Exploration Limited and Rio Tinto have identified multiple, priority
unconformity-related basement targets at Hatchet Lake that were
followed up in 2015.

Kivalliq also holds a 100% interest in the 200,909 hectare Genesis
Property located northeast of Saskatchewan's Athabasca Basin, with
Roughrider Exploration Limited funding the current exploration program
pursuant to an option to acquire up to an 85% interest in the property.
This highly prospective project is located along the Wollaston-Mudjatiktrend 
and extends 90 km northeast from Wollaston Lake to the Manitoba
border.

Kivalliq's team of northern exploration specialists has forged
strong relationships with sophisticated resource sector investors and
Angilak Property partner Nunavut Tunngavik Inc. (NTI). Kivalliq was the
first company to sign a comprehensive agreement to explore for uranium
on Inuit Owned Lands in Nunavut Territory, Canada and is committed to
building shareholder value while adhering to high levels of
environmental and safety standards and proactive local community
engagement.

On behalf of the Board of Directors

"Jim Paterson"

James R. Paterson, CEO

Kivalliq Energy Corporation

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Certain disclosures in this release constitute forward-looking
statements that are subject to numerous risks, uncertainties and other
factors relating to Kivalliq's operations as a mineral exploration
company that may cause future results to differ materially from those
expressed or implied in such forward-looking statements, including
risks as to the completion of the plans and projects. Readers are
cautioned not to place undue reliance on forward-looking statements.
Other than as required by applicable securities legislation, Kivalliq
expressly disclaims any intention or obligation to update or revise any
forward-looking statements whether as a result of new information,
future events, or otherwise.



















TSX Venture closing price for KIV-V
Date: 2016/11/07
Closing Price: 0.08

TEL: 1.888.331.2269
info@kivalliqenergy.com  Investor Relations
www.kivalliqenergy.com   Kivalliq Energy Corporation
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1631200007TS11631200690-05465520161108