Source	MARKET NEWS
Date	11/24/2016
Time	06:10:21 AM

Company	 Brixton Metals Corporation
Title	Expands The 
Outlaw Sediment Hosted Gold Zone





    CDNX Symbol: BBB











Press Release





BRIXTON METALS CORP ("BBB-V;BXTMF-0")
- Expands The Outlaw Sediment Hosted Gold Zone

Brixton Metals Corporation (the "Company" or "Brixton") is pleased
to announce that it has expanded the gold mineralization strike length
at the Outlaw Zone and has now released the remaining results from the
2016 program on its Thorn Project located in Northwest British
Columbia, Canada. The Company drilled five holes at the Outlaw Zone for
a total of 1,190 metres and four holes at the Aberlour Zone for a total
455 metres for a sum of 1,645 metres.

Highlights from the 2016 Exploration Program at the Thorn Project:

//st
Near surface gold mineralization confirmed along a 450m strike length and
remains open;
The Outlaw Zone gold-in-soils and the sedimentary unit has a strike of
greater than 5 km;
Delineated a new large gold-in-soils anomaly and a corresponding near
surface Induced Polarization chargeability high at the Chivas Zone;
The Chivas Zone has a strike length of 3.5km and is up to 2km in width. It
remains open ended based on the geochemical-geophysical surveys;
The Chivas Zone soil geochemical sampling program returned up to 16.7 g/t
Au.
//et

To view a stacked image of geology, drilling, and geochemistry,
click this link:



http://brixtonmetals.com/cn/wp-content/uploads/2013/08/Outlaw-stacked-view-
N2016.jpg

Chairman and CEO of Brixton, Gary R. Thompson stated, "The 2016
exploration work at Thorn was successful in expanding the near surface
gold mineralization at the Outlaw Gold Zone, which appears to have
significant scale potential. In addition the delineation of a new 7
square kilometre gold-in-soil anomaly associated with a near surface IP
chargeability high anomaly at the Chivas Gold Zone represents an
exciting drill target for 2017."

//st
Table of the 2016 Drilling Results:

Drill Hole    Zone   From     To Interval Weighted Average Weighted Average
ID                    (m)    (m)      (m)         Au (g/t)         Ag (g/t)
THN16-131*  Outlaw      0 121.00                        NA               NA
THN16-132*  Outlaw      0  18.00    18.00             1.61            12.31
including   Outlaw   1.00  12.75    11.75             2.23            14.56
THN16-132*  Outlaw  78.00 130.00    52.00             0.94             5.95
including   Outlaw 120.00 130.00    10.00             3.61            23.75
THN16-133*  Outlaw      0  13.00    13.00             1.73             7.25
including   Outlaw      0   6.00     6.00             3.41            12.49
THN16-133*  Outlaw 105.66 129.90    24.24             0.45             1.33
including   Outlaw 116.60 122.30     5.70             1.13             2.38
THN16-134   Outlaw  49.00  75.00    26.00             0.31               NA
Outlaw  83.00 148.60    65.60             0.63               NA
including   Outlaw  85.00 122.00    37.00             0.79               NA
including   Outlaw 103.00 122.00    19.00             1.02               NA
THN16-135   Outlaw  41.50  96.00    54.50             0.35               NA
including   Outlaw  51.50  57.50     6.00             1.68               NA
THN16-136 Aberlour  13.00  16.00     3.00             1.72               NA
including Aberlour  15.00  16.00     1.00             4.42               NA
THN16-137 Aberlour  22.50  24.00     1.50             0.58               NA
THN16-138 Aberlour  30.00  31.00     1.00             0.91            10.00
THN16-139 Aberlour  24.00  26.00     2.00             1.48               NA
including Aberlour  25.00  25.45     0.45             5.50            33.00
//et

//st
* results previously released Oct 31, 2016
//et

Drill hole THN16-134 was collared 289 metres east from hole 132-133
and 130 meters east from drill hole 128 (59.65m of 1.14 g/t Au
including 9.00m of 3.08 g/t Au). Hole 134 encountered two gold
mineralized zones within sediments. The upper zone in hole 134 from 49
metres depth returned 0.31 g/t Au over 26 meters. The lower zone from
83 metres depth returned 0.63 g/t Au over 65.60 metres (including 19 m
of 0.98 g/t Au). Drill hole THN16-135 was collared 740 metres east from
hole 134. Hole 135 had a target depth of 500 metres however,
encountered difficult ground conditions and was terminated at 195.07
meters depth, short of the target depth. Drill hole THN16-135 returned
6.00 metres of 1.68 g/t Au within 54.50 metres of 0.35 g/t Au.
Mineralization is hosted within interbedded siltstone and greywacke.
Primary sulphides are pyrrhotite and pyrite which occur as semi-massive
to disseminated mineralization and veinlets.

Drill holes THN16-136 to 139 were drilled at the Aberlour Zone from
the same pad where surface rock samples returned up to 57 g/t Au. Drill
hole 136 at the Aberlour Zone returned 3 metres of 1.72 g/t Au
including (4.42 g/t Au over 1.00m). Hole 139 returned 5.50 g/t Au over
0.45 metres (see table above).

To view the Aberlour drill location map, click this link:



http://brixtonmetals.com/cn/wp-content/uploads/2013/08/Aberlour-drill-map-N
2016.jpg

Quality Assurance & Quality Control

Sealed samples were shipped by the Company geologists to ALS
Minerals' preparation lab in Whitehorse, Yukon. ALS Minerals
Laboratories are registered to ISO 9001:2008 and ISO 17025
accreditations for laboratory procedures. Blank, duplicate and
certified reference materials were inserted into the sample stream.
Analysis for gold was done by Fire Assay with AA finish. All other
elements were analyzed by Aqua Regia Digest with ICP-AES finish. Gold
and Silver over-limits were analyzed by fire assay with gravimetric
finish. Base metal over-limits were analyzed with Aqua Regia Digest and
AES finish. A copy of the QAQC protocols can be viewed at the Company's
website.

All reported assays are uncut weighted averages. The true width of
reported mineralization is unknown at this time.

Mr. Sorin Posescu, P.Geo., VP Exploration, is a Qualified Person as
defined under National Instrument 43-101 standards and has reviewed and
approved this news release.

About Brixton Metals Corporation

Brixton Metals is a Canadian exploration company focused on the
advancement of its British Columbia and Ontario gold-silver projects
toward feasibility.

Brixton wholly owns 2 past producers of high-grade silver within
the Silver-Cobalt Camp of Ontario. The Langis mine produced 10.4Moz of
silver at 25 oz/t Ag and 358,340 pounds of cobalt, the Hudson Bay mine
produced 6.4Moz of silver at 123 oz/t. The projects are generally
located 500 km north of Toronto, Canada. The high-grade silver
mineralization occurs as moderate-steeply-dipping veins within any of
the three main rock types; Archean volcanics, Coleman Member sediments
and Nipissing diabase.

The 996 SQ/KM, wholly owned Thorn Project is located in
northwestern British Columbia, Canada, approximately 105 km ENE from
Juneau, AK. The Thorn project hosts a district scale gold-silver trend
associated with Triassic to Cretaceous volcano-plutonic complex. Many
styles of mineralization have been identified related to porphyry and
epithermal environments. Targets include high-grade gold-silver
underground targets and large-scale open pit gold type targets.

Brixton Metals Corporation shares trade on the TSX-V under the
ticker symbol BBB. For more information about Brixton please visit our
website at www.brixtonmetals.com.

On Behalf of the Board of Directors,

Mr. Gary R. Thompson, Chairman and CEO

Information set forth in this news release may involve
forward-looking statements under applicable securities laws.
Forward-looking statements are statements that relate to future, not
past, events. In this context, forward-looking statements often address
expected future business and financial performance, and often contain
words such as "anticipate", "believe", "plan", "estimate", "expect",
and "intend", statements that an action or event "may", "might",
"could", "should", or "will" be taken or occur, including statements
that address potential quantity and/or grade of minerals, potential
size and expansion of a mineralized zone, proposed timing of
exploration and development plans, or other similar expressions. All
statements, other than statements of historical fact included herein
including, without limitation, statements regarding the completion of
the acquisition, the anticipated closing of the acquisition, TSXV
approval, and the exploration potential of the property based on
resources estimates and forward looking statements. By their nature,
forward-looking statements involve known and unknown risks,
uncertainties and other factors which may cause our actual results,
performance or achievements, or other future events, to be materially
different from any future results, performance or achievements
expressed or implied by such forward-looking statements. Such factors
include, among others, the following risks: the need for additional
financing; operational risks associated with mineral exploration;
fluctuations in commodity prices; title matters; and the additional
risks identified in the annual information form of the Company or other
reports and filings with the TSXV and applicable Canadian securities
regulators. Forward-looking statements are made based on management's
beliefs, estimates and opinions on the date that statements are made
and the Company undertakes no obligation to update forward-looking
statements if these beliefs, estimates and opinions or other
circumstances should change, except as required by applicable
securities laws. Investors are cautioned against attributing undue
certainty to forward-looking statements.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Contact Information:

Brixton Metals Corporation
Mr. Gary R. Thompson
Chairman and CEO
604-630-9707
info@brixtonmetals.com
www.brixtonmetals.com
______________________________
_______________________________________________
TSX Venture closing price for BBB-V
Date: 2016/11/18
Closing Price: 0.37
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1632800008TS11632800369-06090220161124