Source	MARKET NEWS
Date	11/03/2017
Time	02:29:15 PM

Company	 First Mexican Gold Corp.
Title	Update 
on Guadalupe Property, Mexico





    CDNX Symbol: FMG











Press Release





FIRST MEXICAN GOLD CORP ("FMG-V;FMGXF-0")
- Update on Guadalupe Property, Mexico

First Mexican Gold Corp. (the 'Company' or 'FMG') is pleased to
announce, a resource estimate for the Karen Zone of the Guadalupe
property, State of Sonora, Mexico. This estimate is reported using a
recovered silver equivalent cut-off and reported in a conceptual pit
shell. The effective date of the resource is October 16, 2017.

Inferred Mineral Resource Estimate for The Karen Zone Reported
Inside Pit Shell

//st

---------------------------------------------------
|Cut-Off|Tonnes |Gold |Gold  |Silver|Silver|AgEQ**|
|AgEQ   |(000s)|Grade|(000s|Grade |(000s|Grade |
|(g/t)  |       |(g/t)|oz)   |(g/t) |oz)   |(g/t) |
|-------------------------------------------------|
|60.00  |193.8  |1.802|11.25 |144.8 |902   |229.2 |
|-------------------------------------------------|
|45.00  |221.7  |1.622|11.57 |131.0 |934   |206.9 |
|-------------------------------------------------|
|30.00  |262.6  |1.407|11.88 |114.9 |970   |180.6 |
|-------------------------------------------------|
|15.00  |280.1  |1.330|11.97 |108.8 |980   |170.9 |
---------------------------------------------------

//et

Equivalent calculations are based on three-year trailing average
metals prices of US$ 1214.94 per ounce

for gold and US$ 17.48 per ounce for silver. Metal recoveries used
were 81% for gold and 88% for silver

based on preliminary bottle roll tests. Interpolation by Inverse
Distance Methods.

*AuEQ = ((31.6386 x Au grade) + (0.4928 x Ag grade))/39.06

**AgEQ = ((0.4928 x Ag grade) + (31.6386 x Au grade))/0.56

1. A Mineral Resource is a concentration or occurrence of solid
material of economic interest in or on the Earth's crust in such form,
grade or quality and quantity that there are reasonable prospects for
eventual economic extraction.
An Inferred Mineral Resource is that part of a Mineral Resource
for which quantity and grade or quality are estimated on the basis of
limited geological evidence and sampling. Geological evidence is
sufficient to imply but not verify geological and grade or quality
continuity.

An Inferred Mineral Resource has a lower level of confidence than
that applying to an Indicated Mineral Resource and must not be
converted to a Mineral Reserve. It is reasonably expected that the
majority of Inferred Mineral Resources could be upgraded to Indicated
Mineral Resources with continued exploration.

2. Mineral resources, which are not mineral reserves, do not have
demonstrated economic viability. The estimate of mineral resources may
be materially affected by environmental, permitting, legal, title,
socio-political, marketing, or other relevant issues. There is no
guarantee that Cornelius Exploration or First Mexican will be
successful in obtaining any or all of the requisite consents, permits
or approvals, regulatory or otherwise for the project or that the
project will be placed into production.

3. The mineral resources in this study were estimated using the
Canadian Institute of Mining, Metallurgy and Petroleum ('CIM'), CIM
Standards on Mineral Resources and Reserves, Definitions and Guidelines
prepared by the Standing Committee on Reserve Definitions and adopted
by the CIM Council on May 10, 2014.

First Mexican Gold issued a News Release on October 28, 2014
disclosing a resource estimate for the Karen Zone and implied the
subsequent filing of a technical report. The resource reported in this
News Release is significantly smaller than the resource reported in
2014. These differences are attributable to a smaller overall footprint
to the deposit resulting from a more conservative, non-implicit,
modelling technique, the reporting of the resource in a conceptual pit
shell and the use of a recovered silver equivalent cut-off. The end
result being approximately one third of the volume from what was
reported earlier (600,000 versus 221,700 tonnes) where the resource now
contains 22% of the contained gold ounces and 11% of the contained
silver ounces, allowing for recoveries, compared to what was reported
previously. These differences are attributable to limiting the
projection of the mineralized envelope along strike and down dip and
reporting the resource in a conceptual pit shell. The resource is now
expressed using a silver equivalent cut-off to better reflect the gross
value of contained silver which is greater than the gross value of the
contained gold.

The company continues discussions with numerous other interested
parties to advance the Karen zone development including efforts to
close the existing agreement signed with Link resources FZC on October
10, 2015. The Company also plans exploration work to expand the
resource presently associated with the Karen zone from the various
mineralized areas.

The Company also intends to drill off the Diana zone which was
discovered through an extensive series of saw cut surface trenches and
three drill holes some 400 meters apart, suggesting potential for a
near surface lower grade open pit resource. As funds are available the
company plans a series of holes from the north side of the ridge with
the objective of defining a potential zone that crops out at surface
and has been further exposed some 125 meters below the ridge by a
bulldozer road cut into the lower mountainside. The Diana target
comprises a strongly altered near-vertical dipping vein breccia system
with widths near surface of 30 to 50 metres that has been traced along
strike for more than 700 metres. A faulted off extension of the vein
breccia system has been traced for an additional 400 meters at surface.


James McCrea, P.Geo, a qualified person pursuant to National
Instrument 43-101, has reviewed and approved the technical information
in this press release on behalf of the company.

The company has filed a NI 43-101 technical report supporting this
disclosure.

First Mexican Gold Corp is an active explorer for precious metals
in Mexico and controls a 100% interest in the Guadalupe property
package with the intention of becoming a gold and silver producer.

On behalf of the Board of Directors,

Jim Voisin

President & CEO

First Mexican Gold Corp.

519 699 5352
______________________________________
_______________________________________________
TSX Venture closing price for FMG-V
Date: 2017/10/17
Closing Price: 0.02
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1730600050TS11730601943-14265920171103