Source	Marketwire
Date	11/06/2017
Time	05:01:23 AM

Company	 WHITE GOLD CORP.
Title	White Gold Corp. Extends Gold Mineralization 125m Along Strike and 
Continues to Expand Mineralization Towards Surface and Down-Dip at Golden Saddle





    CDNX Symbol: WGO











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: White Gold Corp.

TSX VENTURE SYMBOL: WGO

November 6, 2017

White Gold Corp. Extends Gold Mineralization 125m Along Strike and Continues to 
Expand Mineralization Towards Surface and Down-Dip at Golden Saddle


TORONTO, ONTARIO--(Marketwired - Nov. 6, 2017) - White Gold Corp. (TSX 
VENTURE:WGO) (the "Company") is pleased to announce additional results from 
reverse circulation ("RC") and diamond drill ("DD") holes completed on the 
historical Golden Saddle deposit (the "Golden Saddle deposit", "deposit" or 
"resource")(5) located on the White Gold Property, Yukon. The results reported 
herein further define the extension of the Golden Saddle Main Zone ("GS Main") 
towards surface and the significant extension of mineralization associated with 
the Footwall Zone to the west and down-dip in undrilled and coarsely drilled 
portions of the deposit. Additional drill results are pending from the Golden 
Saddle deposit and historical Arc deposit (the "Arc deposit")(5) as well as the 
newly defined Golden Saddle East and Ulli's targets and will be released in due 
course. Detailed maps related to the drilling and additional information can be 
found at http://whitegoldcorp.ca/investors/exploration-highlights/.

Highlights include:

/T/

--  WHTGS17RC-012 intercepted 5.24 g/t Au over 6.10m and 6.10 g/t Au over
4.57m within a broader intercept of 1.33 g/t Au over 109.73m from 39.62m
depth, successfully extending the continuity and near surface projection
of the GS Main Zone


--  WHTGS17DD-171 extended Footwall Zone mineralization by 50m to the west;
intercepting 7.61 g/t Au over 2.0m from 222m depth and 3.45 g/t Au over
9.0m from 219m within a broader intercept of 1.19 g/t Au over 34m from
215m depth


--  WHTGS17DD-172 extended Footwall Zone mineralization by 125m to the west;
intercepting 5.66 g/t Au over 1.0m within a broader intercept of 1.8 g/t
Au over 7.0m from 205m depth


--  WHTGS17RC-016 extended Footwall Zone mineralization by 125m to the west
and 75m up-dip; intercepting 1.44 g/t Au over 16.76m within a broader
mineralized intercept from 134.11m depth


--  WHTGS17RC-011 intercepted 4.06 g/t Au over 65.53m from 48.768m depth
within a broader intercept of 2.61 g/t Au over 111.25m from 47.24m depth


--  WHTGS17RC-009 extended Footwall Zone down-dip continuity 125m
intercepting 5.37 g/t Au over 6.10m within a broader intercept of 1.31
g/t Au over 27.43m from 149.35m; and also extended GS Main Zone
continuity 50m up-dip


--  Overall significant extension of the subparallel Footwall Zone beneath
the GS Main Zone to the west, towards surface and down-dip;
demonstrating the potential for additional near surface mineralization
in undrilled and coarsely drilled portions of the deposit, as well as
increased continuity of the GS Main Zone and extension toward surface

/T/

Golden Saddle Exploration Update

Diamond Drill Results

WHTGS17DD-171 ("DD-171") was drilled on a 160 degrees azimuth and a -75 degrees 
dip to a total depth of 393m. It is located at the same site as historic 
diamond hole WGGS10D0136(1); approximately 50m outside of the historic resource 
area. The purpose of this hole was to step out 50m to the west from the 
historic resource area and infill a 150m gap between significant Footwall Zone 
intercepts in historic holes WGGS10D0121(1) (2.10 g/t Au over 36m from 173m 
depth) and WGGS10D0136(1) (2.00 g/t Au over 29.8m from 274.16m depth; including 
4.88 g/t Au over 6m from 284m depth). Results include 1.19 g/t Au over 34m from 
215m depth; including 3.45 g/t Au over 9.0m from 219m depth and 7.61 g/t Au 
over 2.0m from 222m depth. The results confirm continuity of Footwall Zone 
mineralization between the historic holes and add 50m of strike length to near 
surface mineralization within the Footwall Zone beyond the limits of the 
historic resource calculations(5).

/T/

(1)Reported in an Independent technical report for the White Gold Project,
Dawson Range, Yukon, Canada by Gilles Arseneau, P.Geo. dated Sept. 15, 2017
and available on SEDAR

/T/

WHTGS17DD-172 ("DD-172") was drilled on a 160 degrees azimuth and a -45 degrees 
dip to a total depth of 258m. It is located at the same site as historic 
diamond hole WGGS10D0153(1), approximately 110m to the NW of DD-171. The hole 
returned 1.8 g/t Au over 7.0m from 205m depth, including 5.66 g/t Au over 1.0m 
from 208m depth. On section, the intercept is a 75m extension of the 
mineralized Footwall Zone intercepted in DD-171 above; and extends 
mineralization 125m to the west of the historic resource area(5). Only results 
from the bottom of the hole have been received to date and results from the 
upper 184m of the hole are pending and will be reported in due course.

David D'Onofrio, Chief Executive Officer, commented: "We are very pleased to 
see that the results to date have successfully extended mineralization at the 
Golden Saddle and validate the Company's belief that the deposit remains open 
in multiple directions."

Significant results from the Golden Saddle 2017 drill program are detailed in 
the tables below.

/T/

----------------------------------------------------------------------------
Golden Saddle - 2017 Diamond Drill Holes
----------------------------------------------------------------------------
Hole ID                From (m)         To (m)   Interval (m)       Au (g/t)
----------------------------------------------------------------------------
WHTGS17DD-171               215            249             34           1.19
----------------------------------------------------------------------------
Including                   219            228              9           3.45
----------------------------------------------------------------------------
Including                   222            224              2           7.61
----------------------------------------------------------------------------
WHTGS17DD-172                                       Results Pending 0 - 184m
----------------------------------------------------------------------------
And                         205            212              7            1.8
----------------------------------------------------------------------------
Including                   208            209              1           5.66
----------------------------------------------------------------------------

True thickness is estimated to be between 65 - 95% of the reported
intercepts

/T/

RC Drill Results

WHTGS17RC-009 was drilled on a 160 degrees azimuth and -55 degrees dip to a 
total depth of 179.83m. The collar is located between historic diamond holes 
WD-020(2) & WD-092(3) and infills a 75m gap along the surface trace of the 
Golden Saddle Main zone between the historic holes and was extended to depth to 
test for continuity of the Footwall Zone to the east in an undrilled portion of 
the deposit. Three intercepts are noted in the hole and include 0.99 g/t Au 
over 7.62m from 12.192m depth and 1.12 g/t Au over 10.67m from 38.10m depth. 
Both intercepts are from the Golden Saddle Main Zone and add 50m of up-dip 
continuity from historic diamond hole WD-046(4). The third intercept consisted 
of a broader zone of alteration returning 1.31 g/t Au over 27.43m from 149.35m 
depth; including 5.37 g/t Au over 6.10m from 150.88m depth. The intercept was 
within and infilled a gap in the Footwall Zone, adding approximately 125m of 
down-dip continuity from surface, and demonstrates the potential for high grade 
(greater than 5 g/t Au) mineralization within the Footwall Zone.

/T/

(2)Reported in Underworld Resources Inc. ("UW") news release UW2008 - NR#11
dated Oct. 15, 2008 and available on SEDAR.
(3)Reported in Underworld Resources Inc. ("UW") news release UW2009 - NR#13
dated July 14, 2009 and available on SEDAR.
(4)Reported in Underworld Resources Inc. ("UW") news release UW2009 - NR#14
dated August 6, 2009 and available on SEDAR.

/T/

WHTGS17RC-011 was drilled on a 160 degrees azimuth and -72 degrees dip to a 
total depth of 163.07m. The hole was drilled adjacent to historic diamond hole 
WD-043(4) for QAQC purposes related to future resource modelling. The drilling 
returned 2.61 g/t Au over 111.25m from 47.24m depth; including 4.06 g/t Au over 
65.53m from 48.768m depth. The results compared favorably with the historic 
diamond hole which returned 2.29 g/t Au over 106m from 45m depth.

WHTGS17RC-012 was drilled on a 160 degrees azimuth and -55 degrees dip to a 
total depth of 169.21m. It was drilled from the same site as WHTGS17RC-011, and 
was designed to infill an approximately 65m gap between WD-043(4) and the 
surface projection of the GS Main. Results indicate a broad intercept of 1.33 
g/t Au over 109.73 from 39.62m depth; including 5.24 g/t Au over 6.10m from 
39.62m depth and 6.10 g/t Au over 4.57m from 74.68m depth.

WHTGS17RC-016 was drilled on a 160 degrees azimuth and -75 degrees dip to a 
total depth of 178.35m, and is located 155m to the SE of DD-172. Results 
include an intercept of 1.44 g/t Au over 16.76m from 134.11m within a broader 
intercept of 0.72 g/t Au over 38.1m from 134.11m depth. The intercept extends 
Footwall Zone mineralization approximately 75m up-dip from DD-172 reported 
above, and together extend mineralization 125m to the west of the historic 
resource area(5).

/T/

----------------------------------------------------------------------------
Golden Saddle - 2017 RC Drill Holes
----------------------------------------------------------------------------
Hole ID                   From (m)        To (m)  Interval (m)      Au (g/t)
----------------------------------------------------------------------------
WHTGS17RC-007                                                Results Pending
----------------------------------------------------------------------------
WHTGS17RC-008                                                Results Pending
----------------------------------------------------------------------------
WHTGS17RC-009               12.192        19.812          7.62          0.99
----------------------------------------------------------------------------
And                         32.004        48.768        16.764          0.82
----------------------------------------------------------------------------
Including                    38.10        48.768        10.668          1.12
----------------------------------------------------------------------------
And                        149.352       176.784        27.432          1.31
----------------------------------------------------------------------------
Including                  150.876       156.972         6.096          5.37
----------------------------------------------------------------------------
WHTGS17RC-010                                                Results Pending
----------------------------------------------------------------------------
WHTGS17RC-011               47.244       158.496       111.252          2.61
----------------------------------------------------------------------------
Including                   48.768         114.3        65.532          4.06
----------------------------------------------------------------------------
Including                   73.152        88.868        13.716          6.07
----------------------------------------------------------------------------
Including                   94.488         114.3        19.812          5.47
----------------------------------------------------------------------------
Including                    99.06        106.68          7.62          9.65
----------------------------------------------------------------------------
WHTGS17RC-012               39.624       149.352       109.728          1.33
----------------------------------------------------------------------------
Including                   39.624        79.248        39.624          2.12
----------------------------------------------------------------------------
Including                   39.624         45.72         6.096          5.24
----------------------------------------------------------------------------
Including                   74.676        79.248         4.572          6.10
----------------------------------------------------------------------------
WHTGS17RC-013                                                Results Pending
----------------------------------------------------------------------------
WHTGS17RC-014                                                Results Pending
----------------------------------------------------------------------------
WHTGS17RC-015                                                Results Pending
----------------------------------------------------------------------------
WHTGS17RC-016              134.112       172.212          38.1          0.72
----------------------------------------------------------------------------
Including                  134.112       150.846        16.764          1.44
----------------------------------------------------------------------------

/T/

True thickness is estimated to be between 65 - 95% of the reported intercepts.

The 2017 drilling campaign on the White Gold Property represents the first 
drilling program on the property since the previous operator Kinross Gold Corp. 
A total of 4,432m over 31 RC holes and 1,295m over 4 diamond holes have been 
completed by the Company in 2017 on the White Gold property to date. This 
includes 4,151m of drilling on the Golden Saddle deposit with additional 
drilling on the Arc deposit and newly identified Golden Saddle East and Ulli's 
target areas. Complete results have been reported for 10 of the RC holes and 2 
diamond drill holes to date. Assays for the additional holes will be reported 
in due course.

The Company encourages individuals interested in the Company to visit its 
website (www.whitegoldcorp.ca) to further understand the size and scope of the 
Company's projects in the White Gold District.
The analytical work for the 2017 program has been performed by Bureau Veritas 
Commodities Canada Ltd., an internationally recognized analytical services 
provider, at its Vancouver, British Columbia laboratory. Sample preparation was 
carried out at its Whitehorse, Yukon facility. All soil samples were using 
procedure SS80 (dry at 60 C and sieve 100g at -80 mesh) and analyzed by method 
AQ201 (aqua regia digestion and ICP-MS analysis). All rock, GT Probe, RAB, RC, 
and diamond core samples were prepared using procedure PRP70-250 (crush, split 
and pulverize 250 g to 200 mesh) and analyzed by method FA430 (30g fire assay 
with AAS finish) and AQ200 (0.5g, aqua regia digestion and ICP-MS analysis). 
Samples containing greater than 10g/t Au were reanalyzed using method FA530 
(30g Fire Assay with gravimetric finish). Metallic-screen analysis may also be 
utilized if coarse gold mineralization is encounter (FS600).

Qualified Person

Jodie Gibson, PGeo, VP, Exploration of the Company is a "qualified person" as 
defined under National Instrument 43-101 - Standards of Disclosure for Mineral 
Projects ("NI 43-101"), and has reviewed and approved the content of this news 
release. Potential quantity and grade is conceptual in nature. There has been 
insufficient exploration to define a mineral resource on any of the Company's 
properties to date, and it is uncertain if further exploration will result in 
any such target being delineated as a mineral resource.

The reported work was completed using industry standard procedures, including a 
quality assurance/quality control (QA/QC) program consisting of the insertion 
of certified standards, blanks, and field duplicates into the sample stream. 
The qualified person detected no significant QA/QC issues during review of the 
data.

(5)Information Regarding Historical Resources/Deposits

All historical scientific and technical information relating to the White Gold 
Properties is based on and derived from the 43-101 report titled "White Gold 
Property Dawson Range Yukon, Canada" dated March 3, 2010, prepared by Lars 
Weiershauser, P.Geo, Marek Nowak, P.Eng and Wayne Barnett, Pr.Sci.Nat. of SRK 
Consulting (Canada) Inc.) (the "Technical Report") available on Sedar and other 
information available to the Company as referenced herein. The property was 
historically explored by Underworld Resources from 2007 - 2009 and included the 
discovery of the Golden Saddle and Arc deposits. In 2010, Underworld reported a 
resource estimate of 1,004,570 ounces contained in 9.80 Mt at a grade of 3.19 
g/t Au in an Indicated category, with an additional 407,410 ounces contained in 
5.02 Mt at a grade of 2.5 g/t Au in an Inferred category for the Golden Saddle 
deposit. At the Arc deposit, the initial resource included 170,470 ounces 
contained within 4.37 Mt at a grade of 1.21 g/t Au in the inferred category 
(reported in Underworld Resources New Release UW2010-NR#2 dated January 19, 
2010 and the Technical Report. Kinross purchased Underworld shortly after the 
initial resource was released in 2010 and explored the property from 2010 - 
2012. In 2013, Kinross released the results of a resource estimate for the 
Golden Saddle deposit and reported a resource of 840,000 ounces within 9.79 Mt 
at a grade of 2.67 g/t Au in an Indicated category, with an additional 125,000 
ounces within 2.17 Mt at a grade of 1.8 g/t Au in an Inferred category 
(reported in Kinross Gold Corp.'s 2016 Mineral Reserves and Resource Statement).

Both Underworld's and Kinross' resource estimates are considered historical 
estimates and the Company is not treating them as current mineral resources. 
Although the Company believes these sources to be generally reliable, such 
information is subject to interpretation and cannot be verified with complete 
certainty due to limits on the availability and reliability of raw data, the 
voluntary nature of the data gathering process and other inherent limitations 
and uncertainties. In addition to the Golden Saddle and Arc deposits, there are 
numerous other targets known on the property that warrant follow-up work (for 
more information see Yukon Assessment Report #'s 095338, 096206, & 096207). The 
information contained herein is subject to all of the assumptions, 
qualifications and procedures set out in the Technical Report and reference 
should be made to the full details of the Technical Report which may be 
obtained from the Company by contacting dschmidt@whitegoldcorp.ca. Disclosure 
of the historical estimates in this news release is derived from the Technical 
Report and other information as set forth above previous press releases of the 
company as available on Sedar and has been judged to be relevant and therefore 
suitable for disclosure, however should not be relied upon. There are numerous 
uncertainties inherent in the historical estimates, which are subject to all of 
the assumptions, parameters and methods used to prepare such historical 
estimates and reference is made to the full text of the Technical Report with 
respect thereto. The historic estimates of mineral resources were estimated in 
conformity with generally accepted CIM "Estimation of Mineral Resource and 
Mineral Reserve Best Practices" Guidelines. Mineral resources are not mineral 
reserves and do not have demonstrated economic viability. There are no other 
recent estimates or data are available to the Company as at the date of this 
news release and a detailed exploration program is required to be conducted by 
the Company in order to verify or treat the historical estimate as a current 
mineral resource. A qualified person has not done sufficient work to classify 
the historical estimates as current mineral resources or mineral reserves and 
the Company is not treating the historical estimate as current mineral 
resources.

About White Gold Corp.

The Company owns a portfolio of 19,438 quartz claims across 30 properties 
covering over 390,000 hectares representing approximately 40% of the Yukon's 
White Gold district. Preliminary exploration work has produced several 
prospective targets. The claim packages are bordered by sizable gold 
discoveries including the Coffee project owned by Goldcorp Inc., Western Copper 
and Gold Corporation's Casino project, and the Golden Saddle and Arc deposits 
acquired by the Company in June 2017 from Kinross Gold Corp. The Company has 
outlined an aggressive exploration plan to further explore its properties. For 
more information visit www.whitegoldcorp.ca.

Cautionary Note Regarding Forward Looking Information

This news release contains "forward-looking information" and "forward-looking 
statements" (collectively, "forward-looking statements") within the meaning of 
the applicable Canadian securities legislation. All statements, other than 
statements of historical fact, are forward-looking statements and are based on 
expectations, estimates and projections as at the date of this news release. 
Any statement that involves discussions with respect to predictions, 
expectations, beliefs, plans, projections, objectives, assumptions, future 
events or performance (often but not always using phrases such as "expects", or 
"does not expect", "is expected", "anticipates" or "does not anticipate", 
"plans", "budget", "scheduled", "forecasts", "estimates", "believes" or 
"intends" or variations of such words and phrases or stating that certain 
actions, events or results "may" or "could", "would", "might" or "will" be 
taken to occur or be achieved) are not statements of historical fact and may be 
forward-looking statements. In this news release, forward-looking statements 
relate, among other things, to: the anticipated benefits to the Company and its 
shareholders respecting the Company's objectives, goals and exploration 
activities conducted and proposed to be conducted at the White Gold properties; 
future growth potential of the Company, including whether any mineral resource 
will be established in accordance with NI 43-101 at any of the Company's 
properties; exploration results; and future exploration plans.

These forward-looking statements are based on reasonable assumptions and 
estimates of management of the Company at the time such statements were made. 
Actual future results may differ materially as forward-looking statements 
involve known and unknown risks, uncertainties and other factors which may 
cause the actual results, performance or achievements of the Company to 
materially differ from any future results, performance or achievements 
expressed or implied by such forward-looking statements. Such factors, among 
other things, include: the expected benefits to the Company relating to the 
exploration conducted and proposed to be conducted at the White Gold 
properties; failure to identify mineral resources; the preliminary nature of 
metallurgical test results; uncertainties relating to the availability and 
costs of financing needed in the future, including to fund any exploration 
programs on the White Gold properties and the Company's other properties; 
business integration risks; fluctuations in general macroeconomic conditions; 
fluctuations in securities markets; fluctuations in spot and forward prices of 
gold, silver, base metals or certain other commodities; fluctuations in 
currency markets (such as the Canadian dollar to United States dollar exchange 
rate); change in national and local government, legislation, taxation, 
controls, regulations and political or economic developments; risks and hazards 
associated with the business of mineral exploration, development and mining 
(including environmental hazards, industrial accidents, unusual or unexpected 
formations pressures, cave-ins and flooding); inability to obtain adequate 
insurance to cover risks and hazards; the presence of laws and regulations that 
may impose restrictions on mining; employee relations; relationships with and 
claims by local communities and indigenous populations; availability of 
increasing costs associated with mining inputs and labour; the speculative 
nature of mineral exploration and development (including the risks of obtaining 
necessary licenses, permits and approvals from government authorities); the 
unlikelihood that properties that are explored are ultimately developed into 
producing mines; geological factors; actual results of current and future 
exploration; changes in project parameters as plans continue to be evaluated; 
soil sampling results being preliminary in nature and are not conclusive 
evidence of the likelihood of a mineral deposit; title to properties; and those 
factors described under the heading "Risks and Uncertainties" in the Company's 
most recently filed management's discussion and analysis.

Although the forward-looking statements contained in this news release are 
based upon what management of the Company believes, or believed at the time, to 
be reasonable assumptions, the Company cannot assure shareholders that actual 
results will be consistent with such forward-looking statements, as there may 
be other factors that cause results not to be as anticipated, estimated or 
intended. Accordingly, readers should not place undue reliance on 
forward-looking statements and information. There can be no assurance that 
forward-looking information, or the material factors or assumptions used to 
develop such forward-looking information, will prove to be accurate. The 
Company does not undertake any obligations to release publicly any revisions 
for updating any voluntary forward-looking statements, except as required by 
applicable securities law.

Neither the TSX Venture Exchange (the "Exchange") nor its Regulation Services 
Provider (as that term is defined in the policies of the Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

- 30 -

CONTACT INFO:

David D'Onofrio
Chief Executive Officer
White Gold Corp.
(416) 643-3880
ddonofrio@whitegoldcorp.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=600191545


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: White Gold Corp.

TSX VENTURE SYMBOL: WGO

November 6, 2017

White Gold Corp. Extends Gold Mineralization 125m Along Strike and Continues to 
Expand Mineralization Towards Surface and Down-Dip at Golden Saddle


TORONTO, ONTARIO--(Marketwired - Nov. 6, 2017) - White Gold Corp. (TSX 
VENTURE:WGO) (the "Company") is pleased to announce additional results from 
reverse circulation ("RC") and diamond drill ("DD") holes completed on the 
historical Golden Saddle deposit (the "Golden Saddle deposit", "deposit" or 
"resource")(5) located on the White Gold Property, Yukon. The results reported 
herein further define the extension of the Golden Saddle Main Zone ("GS Main") 
towards surface and the significant extension of mineralization associated with 
the Footwall Zone to the west and down-dip in undrilled and coarsely drilled 
portions of the deposit. Additional drill results are pending from the Golden 
Saddle deposit and historical Arc deposit (the "Arc deposit")(5) as well as the 
newly defined Golden Saddle East and Ulli's targets and will be released in due 
course. Detailed maps related to the drilling and additional information can be 
found at http://whitegoldcorp.ca/investors/exploration-highlights/.

Highlights include:

/T/

--  WHTGS17RC-012 intercepted 5.24 g/t Au over 6.10m and 6.10 g/t Au over
4.57m within a broader intercept of 1.33 g/t Au over 109.73m from 39.62m
depth, successfully extending the continuity and near surface projection
of the GS Main Zone


--  WHTGS17DD-171 extended Footwall Zone mineralization by 50m to the west;
intercepting 7.61 g/t Au over 2.0m from 222m depth and 3.45 g/t Au over
9.0m from 219m within a broader intercept of 1.19 g/t Au over 34m from
215m depth


--  WHTGS17DD-172 extended Footwall Zone mineralization by 125m to the west;
intercepting 5.66 g/t Au over 1.0m within a broader intercept of 1.8 g/t
Au over 7.0m from 205m depth


--  WHTGS17RC-016 extended Footwall Zone mineralization by 125m to the west
and 75m up-dip; intercepting 1.44 g/t Au over 16.76m within a broader
mineralized intercept from 134.11m depth


--  WHTGS17RC-011 intercepted 4.06 g/t Au over 65.53m from 48.768m depth
within a broader intercept of 2.61 g/t Au over 111.25m from 47.24m depth


--  WHTGS17RC-009 extended Footwall Zone down-dip continuity 125m
intercepting 5.37 g/t Au over 6.10m within a broader intercept of 1.31
g/t Au over 27.43m from 149.35m; and also extended GS Main Zone
continuity 50m up-dip


--  Overall significant extension of the subparallel Footwall Zone beneath
the GS Main Zone to the west, towards surface and down-dip;
demonstrating the potential for additional near surface mineralization
in undrilled and coarsely drilled portions of the deposit, as well as
increased continuity of the GS Main Zone and extension toward surface

/T/

Golden Saddle Exploration Update

Diamond Drill Results

WHTGS17DD-171 ("DD-171") was drilled on a 160 degrees azimuth and a -75 degrees 
dip to a total depth of 393m. It is located at the same site as historic 
diamond hole WGGS10D0136(1); approximately 50m outside of the historic resource 
area. The purpose of this hole was to step out 50m to the west from the 
historic resource area and infill a 150m gap between significant Footwall Zone 
intercepts in historic holes WGGS10D0121(1) (2.10 g/t Au over 36m from 173m 
depth) and WGGS10D0136(1) (2.00 g/t Au over 29.8m from 274.16m depth; including 4.88 g/t Au over 6m from 284m depth). Results 
include 1.19 g/t Au over 34m from 215m depth; including 3.45 g/t Au over 9.0m 
from 219m depth and 7.61 g/t Au over 2.0m from 222m depth. The results confirm 
continuity of Footwall Zone mineralization between the historic holes and add 
50m of strike length to near surface mineralization within the Footwall Zone 
beyond the limits of the historic resource calculations(5).

/T/

(1)Reported in an Independent technical report for the White Gold Project,
Dawson Range, Yukon, Canada by Gilles Arseneau, P.Geo. dated Sept. 15, 2017
and available on SEDAR

/T/

WHTGS17DD-172 ("DD-172") was drilled on a 160 degrees azimuth and a -45 degrees 
dip to a total depth of 258m. It is located at the same site as historic 
diamond hole WGGS10D0153(1), approximately 110m to the NW of DD-171. The hole 
returned 1.8 g/t Au over 7.0m from 205m depth, including 5.66 g/t Au over 1.0m 
from 208m depth. On section, the intercept is a 75m extension of the 
mineralized Footwall Zone intercepted in DD-171 above; and extends 
mineralization 125m to the west of the historic resource area(5). Only results 
from the bottom of the hole have been received to date and results from the 
upper 184m of the hole are pending and will be reported in due course.

David D'Onofrio, Chief Executive Officer, commented: "We are very pleased to 
see that the results to date have successfully extended mineralization at the 
Golden Saddle and validate the Company's belief that the deposit remains open 
in multiple directions."

Significant results from the Golden Saddle 2017 drill program are detailed in 
the tables below.

/T/

----------------------------------------------------------------------------
Golden Saddle - 2017 Diamond Drill Holes
----------------------------------------------------------------------------
Hole ID                From (m)         To (m)   Interval (m)       Au (g/t)
----------------------------------------------------------------------------
WHTGS17DD-171               215            249             34           1.19
----------------------------------------------------------------------------
Including                   219            228              9           3.45
----------------------------------------------------------------------------
Including                   222            224              2           7.61
----------------------------------------------------------------------------
WHTGS17DD-172                                       Results Pending 0 - 184m
----------------------------------------------------------------------------
And                         205            212              7            1.8
----------------------------------------------------------------------------
Including                   208            209              1           5.66
----------------------------------------------------------------------------

True thickness is estimated to be between 65 - 95% of the reported
intercepts

/T/

RC Drill Results

WHTGS17RC-009 was drilled on a 160 degrees azimuth and -55 degrees dip to a 
total depth of 179.83m. The collar is located between historic diamond holes 
WD-020(2) & WD-092(3) and infills a 75m gap along the surface trace of the 
Golden Saddle Main zone between the historic holes and was extended to depth to 
test for continuity of the Footwall Zone to the east in an undrilled portion of 
the deposit. Three intercepts are noted in the hole and include 0.99 g/t Au 
over 7.62m from 12.192m depth and 1.12 g/t Au over 10.67m from 38.10m depth. 
Both intercepts are from the Golden Saddle Main Zone and add 50m of up-dip 
continuity from historic diamond hole WD-046(4). The third intercept consisted 
of a broader zone of alteration returning 1.31 g/t Au over 27.43m from 149.35m 
depth; including 5.37 g/t Au over 6.10m from 150.88m depth. The intercept was 
within and infilled a gap in the Footwall Zone, adding approximately 125m of 
down-dip continuity from surface, and demonstrates the potential for high grade 
(greater than 5 g/t Au) mineralization within the Footwall Zone.

/T/

(2)Reported in Underworld Resources Inc. ("UW") news release UW2008 - NR#11
dated Oct. 15, 2008 and available on SEDAR.
(3)Reported in Underworld Resources Inc. ("UW") news release UW2009 - NR#13
dated July 14, 2009 and available on SEDAR.
(4)Reported in Underworld Resources Inc. ("UW") news release UW2009 - NR#14
dated August 6, 2009 and available on SEDAR.

/T/

WHTGS17RC-011 was drilled on a 160 degrees azimuth and -72 degrees dip to a 
total depth of 163.07m. The hole was drilled adjacent to historic diamond hole 
WD-043(4) for QAQC purposes related to future resource modelling. The drilling 
returned 2.61 g/t Au over 111.25m from 47.24m depth; including 4.06 g/t Au over 
65.53m from 48.768m depth. The results compared favorably with the historic 
diamond hole which returned 2.29 g/t Au over 106m from 45m depth.

WHTGS17RC-012 was drilled on a 160 degrees azimuth and -55 degrees dip to a 
total depth of 169.21m. It was drilled from the same site as WHTGS17RC-011, and 
was designed to infill an approximately 65m gap between WD-043(4) and the 
surface projection of the GS Main. Results indicate a broad intercept of 1.33 
g/t Au over 109.73 from 39.62m depth; including 5.24 g/t Au over 6.10m from 
39.62m depth and 6.10 g/t Au over 4.57m from 74.68m depth.

WHTGS17RC-016 was drilled on a 160 degrees azimuth and -75 degrees dip to a 
total depth of 178.35m, and is located 155m to the SE of DD-172. Results 
include an intercept of 1.44 g/t Au over 16.76m from 134.11m within a broader 
intercept of 0.72 g/t Au over 38.1m from 134.11m depth. The intercept extends 
Footwall Zone mineralization approximately 75m up-dip from DD-172 reported 
above, and together extend mineralization 125m to the west of the historic 
resource area(5).

/T/

----------------------------------------------------------------------------
Golden Saddle - 2017 RC Drill Holes
----------------------------------------------------------------------------
Hole ID                   From (m)        To (m)  Interval (m)      Au (g/t)
----------------------------------------------------------------------------
WHTGS17RC-007                                                Results Pending
----------------------------------------------------------------------------
WHTGS17RC-008                                                Results Pending
----------------------------------------------------------------------------
WHTGS17RC-009               12.192        19.812          7.62          0.99
----------------------------------------------------------------------------
And                         32.004        48.768        16.764          0.82
----------------------------------------------------------------------------
Including                    38.10        48.768        10.668          1.12
----------------------------------------------------------------------------
And                        149.352       176.784        27.432          1.31
----------------------------------------------------------------------------
Including                  150.876       156.972         6.096          5.37
----------------------------------------------------------------------------
WHTGS17RC-010                                                Results Pending
----------------------------------------------------------------------------
WHTGS17RC-011               47.244       158.496       111.252          2.61
----------------------------------------------------------------------------
Including                   48.768         114.3        65.532          4.06
----------------------------------------------------------------------------
Including                   73.152        88.868        13.716          6.07
----------------------------------------------------------------------------
Including                   94.488         114.3        19.812          5.47
----------------------------------------------------------------------------
Including                    99.06        106.68          7.62          9.65
----------------------------------------------------------------------------
WHTGS17RC-012               39.624       149.352       109.728          1.33
----------------------------------------------------------------------------
Including                   39.624        79.248        39.624          2.12
----------------------------------------------------------------------------
Including                   39.624         45.72         6.096          5.24
----------------------------------------------------------------------------
Including                   74.676        79.248         4.572          6.10
----------------------------------------------------------------------------
WHTGS17RC-013                                                Results Pending
----------------------------------------------------------------------------
WHTGS17RC-014                                                Results Pending
----------------------------------------------------------------------------
WHTGS17RC-015                                                Results Pending
----------------------------------------------------------------------------
WHTGS17RC-016              134.112       172.212          38.1          0.72
----------------------------------------------------------------------------
Including                  134.112       150.846        16.764          1.44
----------------------------------------------------------------------------

/T/

True thickness is estimated to be between 65 - 95% of the reported intercepts.

The 2017 drilling campaign on the White Gold Property represents the first 
drilling program on the property since the previous operator Kinross Gold Corp. 
A total of 4,432m over 31 RC holes and 1,295m over 4 diamond holes have been 
completed by the Company in 2017 on the White Gold property to date. This 
includes 4,151m of drilling on the Golden Saddle deposit with additional 
drilling on the Arc deposit and newly identified Golden Saddle East and Ulli's 
target areas. Complete results have been reported for 10 of the RC holes and 2 
diamond drill holes to date. Assays for the additional holes will be reported 
in due course.

The Company encourages individuals interested in the Company to visit its 
website (www.whitegoldcorp.ca) to further understand the size and scope of the 
Company's projects in the White Gold District.
The analytical work for the 2017 program has been performed by Bureau Veritas 
Commodities Canada Ltd., an internationally recognized analytical services 
provider, at its Vancouver, British Columbia laboratory. Sample preparation was 
carried out at its Whitehorse, Yukon facility. All soil samples were using 
procedure SS80 (dry at 60 C and sieve 100g at -80 mesh) and analyzed by method 
AQ201 (aqua regia digestion and ICP-MS analysis). All rock, GT Probe, RAB, RC, 
and diamond core samples were prepared using procedure PRP70-250 (crush, split 
and pulverize 250 g to 200 mesh) and analyzed by method FA430 (30g fire assay 
with AAS finish) and AQ200 (0.5g, aqua regia digestion and ICP-MS analysis). 
Samples containing greater than 10g/t Au were reanalyzed using method FA530 
(30g Fire Assay with gravimetric finish). Metallic-screen analysis may also be 
utilized if coarse gold mineralization is encounter (FS600).

Qualified Person

Jodie Gibson, PGeo, VP, Exploration of the Company is a "qualified person" as 
defined under National Instrument 43-101 - Standards of Disclosure for Mineral 
Projects ("NI 43-101"), and has reviewed and approved the content of this news 
release. Potential quantity and grade is conceptual in nature. There has been 
insufficient exploration to define a mineral resource on any of the Company's 
properties to date, and it is uncertain if further exploration will result in 
any such target being delineated as a mineral resource.

The reported work was completed using industry standard procedures, including a 
quality assurance/quality control (QA/QC) program consisting of the insertion 
of certified standards, blanks, and field duplicates into the sample stream. 
The qualified person detected no significant QA/QC issues during review of the 
data.

(5)Information Regarding Historical Resources/Deposits

All historical scientific and technical information relating to the White Gold 
Properties is based on and derived from the 43-101 report titled "White Gold 
Property Dawson Range Yukon, Canada" dated March 3, 2010, prepared by Lars 
Weiershauser, P.Geo, Marek Nowak, P.Eng and Wayne Barnett, Pr.Sci.Nat. of SRK 
Consulting (Canada) Inc.) (the "Technical Report") available on Sedar and other 
information available to the Company as referenced herein. The property was 
historically explored by Underworld Resources from 2007 - 2009 and included the 
discovery of the Golden Saddle and Arc deposits. In 2010, Underworld reported a 
resource estimate of 1,004,570 ounces contained in 9.80 Mt at a grade of 3.19 
g/t Au in an Indicated category, with an additional 407,410 ounces contained in 
5.02 Mt at a grade of 2.5 g/t Au in an Inferred category for the Golden Saddle 
deposit. At the Arc deposit, the initial resource included 170,470 ounces 
contained within 4.37 Mt at a grade of 1.21 g/t Au in the inferred category 
(reported in Underworld Resources New Release UW2010-NR#2 dated January 19, 
2010 and the Technical Report. Kinross purchased Underworld shortly after the 
initial resource was released in 2010 and explored the property from 2010 - 
2012. In 2013, Kinross released the results of a resource estimate for the 
Golden Saddle deposit and reported a resource of 840,000 ounces within 9.79 Mt 
at a grade of 2.67 g/t Au in an Indicated category, with an additional 125,000 
ounces within 2.17 Mt at a grade of 1.8 g/t Au in an Inferred category 
(reported in Kinross Gold Corp.'s 2016 Mineral Reserves and Resource Statement).

Both Underworld's and Kinross' resource estimates are considered historical 
estimates and the Company is not treating them as current mineral resources. 
Although the Company believes these sources to be generally reliable, such 
information is subject to interpretation and cannot be verified with complete 
certainty due to limits on the availability and reliability of raw data, the 
voluntary nature of the data gathering process and other inherent limitations 
and uncertainties. In addition to the Golden Saddle and Arc deposits, there are 
numerous other targets known on the property that warrant follow-up work (for 
more information see Yukon Assessment Report #'s 095338, 096206, & 096207). The 
information contained herein is subject to all of the assumptions, 
qualifications and procedures set out in the Technical Report and reference 
should be made to the full details of the Technical Report which may be 
obtained from the Company by contacting dschmidt@whitegoldcorp.ca. Disclosure 
of the historical estimates in this news release is derived from the Technical 
Report and other information as set forth above previous press releases of the 
company as available on Sedar and has been judged to be relevant and therefore 
suitable for disclosure, however should not be relied upon. There are numerous 
uncertainties inherent in the historical estimates, which are subject to all of 
the assumptions, parameters and methods used to prepare such historical 
estimates and reference is made to the full text of the Technical Report with 
respect thereto. The historic estimates of mineral resources were estimated in 
conformity with generally accepted CIM "Estimation of Mineral Resource and 
Mineral Reserve Best Practices" Guidelines. Mineral resources are not mineral 
reserves and do not have demonstrated economic viability. There are no other 
recent estimates or data are available to the Company as at the date of this 
news release and a detailed exploration program is required to be conducted by 
the Company in order to verify or treat the historical estimate as a current 
mineral resource. A qualified person has not done sufficient work to classify 
the historical estimates as current mineral resources or mineral reserves and 
the Company is not treating the historical estimate as current mineral 
resources.

About White Gold Corp.

The Company owns a portfolio of 19,438 quartz claims across 30 properties 
covering over 390,000 hectares representing approximately 40% of the Yukon's 
White Gold district. Preliminary exploration work has produced several 
prospective targets. The claim packages are bordered by sizable gold 
discoveries including the Coffee project owned by Goldcorp Inc., Western Copper 
and Gold Corporation's Casino project, and the Golden Saddle and Arc deposits 
acquired by the Company in June 2017 from Kinross Gold Corp. The Company has 
outlined an aggressive exploration plan to further explore its properties. For 
more information visit www.whitegoldcorp.ca.

Cautionary Note Regarding Forward Looking Information

This news release contains "forward-looking information" and "forward-looking 
statements" (collectively, "forward-looking statements") within the meaning of 
the applicable Canadian securities legislation. All statements, other than 
statements of historical fact, are forward-looking statements and are based on 
expectations, estimates and projections as at the date of this news release. 
Any statement that involves discussions with respect to predictions, 
expectations, beliefs, plans, projections, objectives, assumptions, future 
events or performance (often but not always using phrases such as "expects", or 
"does not expect", "is expected", "anticipates" or "does not anticipate", 
"plans", "budget", "scheduled", "forecasts", "estimates", "believes" or 
"intends" or variations of such words and phrases or stating that certain 
actions, events or results "may" or "could", "would", "might" or "will" be 
taken to occur or be achieved) are not statements of historical fact and may be 
forward-looking statements. In this news release, forward-looking statements 
relate, among other things, to: the anticipated benefits to the Company and its 
shareholders respecting the Company's objectives, goals and exploration 
activities conducted and proposed to be conducted at the White Gold properties; 
future growth potential of the Company, including whether any mineral resource 
will be established in accordance with NI 43-101 at any of the Company's 
properties; exploration results; and future exploration plans.

These forward-looking statements are based on reasonable assumptions and 
estimates of management of the Company at the time such statements were made. 
Actual future results may differ materially as forward-looking statements 
involve known and unknown risks, uncertainties and other factors which may 
cause the actual results, performance or achievements of the Company to 
materially differ from any future results, performance or achievements 
expressed or implied by such forward-looking statements. Such factors, among 
other things, include: the expected benefits to the Company relating to the 
exploration conducted and proposed to be conducted at the White Gold 
properties; failure to identify mineral resources; the preliminary nature of 
metallurgical test results; uncertainties relating to the availability and 
costs of financing needed in the future, including to fund any exploration 
programs on the White Gold properties and the Company's other properties; 
business integration risks; fluctuations in general macroeconomic conditions; 
fluctuations in securities markets; fluctuations in spot and forward prices of 
gold, silver, base metals or certain other commodities; fluctuations in 
currency markets (such as the Canadian dollar to United States dollar exchange 
rate); change in national and local government, legislation, taxation, 
controls, regulations and political or economic developments; risks and hazards 
associated with the business of mineral exploration, development and mining 
(including environmental hazards, industrial accidents, unusual or unexpected 
formations pressures, cave-ins and flooding); inability to obtain adequate 
insurance to cover risks and hazards; the presence of laws and regulations that 
may impose restrictions on mining; employee relations; relationships with and 
claims by local communities and indigenous populations; availability of 
increasing costs associated with mining inputs and labour; the speculative 
nature of mineral exploration and development (including the risks of obtaining 
necessary licenses, permits and approvals from government authorities); the 
unlikelihood that properties that are explored are ultimately developed into 
producing mines; geological factors; actual results of current and future 
exploration; changes in project parameters as plans continue to be evaluated; 
soil sampling results being preliminary in nature and are not conclusive 
evidence of the likelihood of a mineral deposit; title to properties; and those 
factors described under the heading "Risks and Uncertainties" in the Company's 
most recently filed management's discussion and analysis.

Although the forward-looking statements contained in this news release are 
based upon what management of the Company believes, or believed at the time, to 
be reasonable assumptions, the Company cannot assure shareholders that actual 
results will be consistent with such forward-looking statements, as there may 
be other factors that cause results not to be as anticipated, estimated or 
intended. Accordingly, readers should not place undue reliance on 
forward-looking statements and information. There can be no assurance that 
forward-looking information, or the material factors or assumptions used to 
develop such forward-looking information, will prove to be accurate. The 
Company does not undertake any obligations to release publicly any revisions 
for updating any voluntary forward-looking statements, except as required by 
applicable securities law.

Neither the TSX Venture Exchange (the "Exchange") nor its Regulation Services 
Provider (as that term is defined in the policies of the Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

- 30 -

CONTACT INFO:

David D'Onofrio
Chief Executive Officer
White Gold Corp.
(416) 643-3880
ddonofrio@whitegoldcorp.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=600191545