Source	MARKET NEWS
Date	11/07/2017
Time	05:47:37 AM

Company	 BTU Metals Corp.
Title	Commences 
Ground Program Aimed at Defining Drill





    CDNX Symbol: BTU











Press Release





BTU METALS CORP ("BTU-V")
- Commences Ground Program Aimed at Defining Drill Targets at
- Galway, Ireland

BTU Metals Corp. ("BTU" or the "Company") reports it has commenced
work at its Galway Gold property located in County Galway, Republic of
Ireland.

The company is targeting orogenic and low-sulphidation
mineralization based on the following factors:

//st

* Location within the Caledonian (Lower Paleozoic) orogenic zone.
* Favourable lithologies for metal precipitation (chemical traps) within
the Dalradian Supergroup metasediments, e.g., graphitic schist, marble.
* Favourable source rocks for gold, e.g., arc volcanics and numerous
cross-cutting faults, evidence for post-collision rifting and volcanism
in the Silurian/Devonian in Ireland and neighbouring terranes.
* Known gold occurrences related to late cross-cutting fault structures,
some of which shows textural evidence for near-surface boiling that
affects precipitation of metals from solution, e.g., Bohaun Gold
occurrence.

//et

About the Lee Occurrence

The Lee occurrence lies within Prospecting Licence 2295 and is
located 10km west of the Bohaun epithermal gold occurrence. A series of
mineralized boulders were discovered by Ovoca Gold Exploration in the
late 1980s. These boulders returned values of up to 195 g/t Au and 240
g/t Ag. Deep overburden sampling outlined a 1km long, NW trending
lead-zinc-arsenic-silver-gold anomaly. Subsequent trenching located a
tectonic breccia containing sulphides and gold values up to 12 g/t. The
mineralized breccia is associated with a lamprophyre dyke intruded
along a pre-existing shear zone (Ovoca Gold Exploration PLC, 1988).

Additionally, Ovoca identified a second separate hydrothermal
system on PL2295. In this system, gold values are associated with
quartz porphyry intrusions in Dalradian rocks. Outcrop sampling of an
exposed fault system yielded gold values between 3 and 5 g/t Au. Float
samples of comparable material assayed up to 24.5 g/t Au (Ovoca Gold
Exploration PLC, 1987).

About the Dooros Occurrence

The Dooros occurrence lies within Prospecting Licence 3145 and
gold is reported from massive pyrrhotite mineralization hosted in an
amphibolite unit. An historical sample taken from this area assayed by
Anglo United Development Ltd. returned 1.3 g/t Au.  Ennex reported the
discovery of a 3000' (914.4 meter) long zone containing anomalous gold
values. Trenching has identified seven bedrock copper-gold occurrences,
with the best historical showing having a strike length of 120' (36.6
meters) averaging 1.1% copper and 0.2 ounces (6.86 g/t) gold per short
ton. Historical trench samples include:

//st

* 1.7 metres of 11.2 g/t Au
* 1.2 metres of 7.12 g/t Au
* 2.7 metres of 12.6 g/t Au
* 4.2 metres of 6.2 g/t Au

//et

(Source - Irish Base Metals / Aquatine Mining Data).

Five of the occurrences were tested by drilling and all holes
intersected mineralization including 15.0 feet of 0.17 ounces gold per
short ton (Aurum Mineral Resources Limited 2009, Exploration Work
Report PL3145).

The 2017 work program will consist of mapping, sampling, and
geophysics to follow up on this and other historic work as well as more
recent work performed by BTU which garnered samples assaying up to 49.6
g/t Au (see PR dated July 27, 2017) from the Lee showing. A diamond
drill program is expected to follow.

Andris Kikauka , P. Geo, is a qualified person as defined by
National Instrument 43-101 and is responsible for reviewing and
approving the technical contents of this press release.

ON BEHALF OF THE BOARD

"Paul Wood"

Paul Wood, CEO, Director

FOR FURTHER INFORMATION, PLEASE CONTACT:

Telephone: 1-604-683-3995

Toll Free: 1-888-945-4770

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

FORWARD LOOKING STATEMENTS: This news release contains
forward-looking statements, which relate to future events or future
performance and reflect management's current expectations and
assumptions. Such forward-looking statements reflect management's
current beliefs and are based on assumptions made by and information
currently available to the Company. Investors are cautioned that these
forward looking statements are neither promises nor guarantees, and are
subject to risks and uncertainties that may cause future results to
differ materially from those expected. These forward -looking
statements are made as of the date hereof and, except as required under
applicable securities legislation, the Company does not assume any
obligation to update or revise them to reflect new events or
circumstances. All of the forward-looking statements made in this press
release are qualified by these cautionary statements and by those made
in our filings with SEDAR in Canada (available at WWW.SEDAR.COM).
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1731000013TS11731000908-05460120171107