Source	MARKET NEWS
Date	11/20/2017
Time	02:28:59 PM

Company	 Great Thunder Gold Corp.
Title	Receives Urban Thunder Soil Survey Results





    CDNX Symbol: GTG











Press Release





Receives Urban Thunder Soil Survey Results --->@NEWS RELEASE
GREAT THUNDER GOLD CORP ("GTG-V")
- Receives Urban Thunder Soil Survey Results

Great Thunder Gold Corp. completed a soil geochemistry survey
between October 9 and October 16, 2017 on its 100%-owned Urban Thunder
property located in the Windfall Lake gold camp of Quebec. The survey
was undertaken on GPS lines 400 metres apart with sampling every 100
metres. A total of 301 samples were drawn, to the extent possible, from
the B soil horizon and were sent for analysis at ALS Canada's
laboratory in Val d'Or, Quebec.
The samples were analyzed using ALS codes Au-ICP-21 and ME-ICP41.
Au-ICP21 consists of analysis of gold by fire assay with an ICP-AES
finish on 30-gram samples. The detection limits of this method are from
0.001 g/t to 10 g/t gold. The samples were then submitted to the second
analytical method - ME-ICP41 - where elements are estimated using aqua
regia digestion followed by analysis using ICP-AES. Included in this
package of 35 elements are silver, arsenic, copper, nickel and zinc.
Results from the laboratory have only just been received, but a
preliminary evaluation revealed several gold anomalous results up to 24
ppb, mainly obtained on the northern part of the property. Further
analytical verification is required with the laboratory before
proceeding with the final evaluation of all the data obtained. A full
report will follow in the coming weeks.
The technical contents of this release were approved by Donald
Thberge, P.Eng., MBA, an independent Qualified Person as defined by
National Instrument 43-101.

ON BEHALF OF THE BOARD

Signed "Kevin C. Whelan"
Kevin C. Whelan, President
Direct line: (250) 474-6640

Neither TSX Venture Exchange nor its Regulation Services Provider (as that
term is defined in the policies of the TSX Venture Exchange) accepts

TEL:  (604) 682-3701
FAX:  (604) 682-3600
Website: www.greatthundergold.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1732300098TS11732302965-14250120171120