Source	MARKET NEWS
Date	11/21/2017
Time	06:38:04 AM

Company	 Happy Creek Minerals Ltd.
Title	Drills 
19.4 Metres of 0.93% WO3 Including 2.6 Me





    CDNX Symbol: HPY











Press Release




[200/News Release]HPYVHAPPY CREEK MINERALS LTDNOV 21 2017  06:37 AMDrills 
19.4 Metres of 0.93% WO3 Including 2.6 Metres of 5.8% W03 AtRidley Creek and 
Makes a Discovery at South Grid on the Fox TungstenProperty --->@NEWS RELEASE
HAPPY CREEK MINERALS LTD ("HPY-V;HPYCF-0")
- Drills 19.4 Metres of 0.93% WO3 Including 2.6 Metres of 5.8% W03
- At Ridley Creek and Makes a Discovery at South Grid on the Fox
- Tungsten Property

Happy Creek Minerals Ltd. (the "Company") is pleased to announce
the remaining results from drilling on its 100% owned Fox tungsten
property, located 90 km northeast of the town of 100 Mile House, in
south central B.C., Canada. During 2017, 11,429 metres of diamond core
drilling in 66 holes was performed on the BN, Ridley Creek and
Nightcrawler-South Grid zones.

Further to the news release October 24, 2017 for the BN zone
drilling results, results for the Ridley Creek, South Grid and Creek
zones are reported here for drill holes F17-39 to F17-66, along with a
summary of surface trench and rock sampling. Refer to the Tables below,
and maps will be posted to the website shortly. On January 26, 2017 the
Company announced the Ridley Creek and BN zones contain 486,000 tonnes
indicated grading 0.818% W03 (tungsten trioxide) and 361,000 tonnes
inferred grading 1.568% WO3. This includes 329,000 tonnes of 0.729% WO3
indicated within an open pit. Resources have not yet been estimated for
the South Grid, Nightcrawler, Creek, BK and North zones.

In 2017, drilling at Ridley Creek was focused on the outward
expansion of the current resource area and collecting data to better
delimit the deposit around the periphery of the current open pit shell.
Distances are relative to the current resource area or pit shell
perimeter. True widths are estimated to be 75-95% of reported drill
intervals, and trenches are rock-saw cut channel and chip samples.

Highlights

DDH F17-44: Starting at 46.0 metres, 19.4 metres of 0.927% WO3,
including 2.59 metres of 5.824% that expands the Ridley Creek zone
approximately 35 metres to the northwest and this high-grade zone
remains open.

DDH F17-48: Starting at 62.6 metres, 0.72 metres of 4.653% WO3
that expands the Ridley Creek zone 100 metres north of the current
resource area.

DDH F17-56: Starting at 11.45 metres, 0.85 metres of 4.160% WO3 at
Ridley Creek south and,

DDH F17-57: starting at 21.2 metres, 4.82 metres of 0.516% WO3
that expands Ridley Creek 45 metres further southeast of the current
resource area where it is open to the west and southeast.

Trench 17RCS-1: Rock saw cut 3.3 metres containing 0.91% WO3 that
is located 45 metres northeast of F17-57 and connects to the
mineralized zones in drill holes F17-56 and F17-57.

DDH F17-61: Starting at 12.6 metres below surface, 3.07 metres of
0.496% WO3 at the South Grid. This is considered a discovery of
potentially economic grade in this new, road accessible target that is
underlain by a 1.5 km by 500 metre tungsten in soil anomaly.

DDH F17-64: Starting at the top of the hole, 0.7m of 0.991% WO3 in
the first sample at the Creek zone, and the mineralized zone remains
open in several directions.

David Blann, President and C.E.O. of Happy Creek states: "Drilling
at Ridley Creek has improved geological modelling of the deposit,
collected data for more advanced studies, and expanded the area of
excellent grade mainly to the northwest and southeast. Another top-tier
result in F17-44 with 2.6 metres of 5.8% WO3 and 3.1 metres of 0.919%
WO3 provides a clear vector to continue expanding this high-grade
material to the northwest. To the southeast, drill holes F17-56 and
F17-57 include 0.9 metres of 4.160% WO3 and 4.8 metres of 0.516% WO3
respectively, that connect with a new trench containing 3.3 metres of
0.913% WO3, and together should add to the existing shallow open pit
resource. In addition, new outcrop containing 0.698% WO3 over 0.7
metres (open in width) and grab samples up to 2.383% WO3 are located up
to 200 metres further southeast and provide an exciting opportunity to
increase near-surface resources along the 750 metre un-explored gap
between the Ridley Creek and BN zone.

At the South Grid, the drilling discovery of 3.0 metres with
0.496% WO3 near surface is an excellent result that elevates the
importance of this new 1.5 km by 500 metre geochemical target that is
all within recent logging clear-cuts and numerous roads and trails.

We look forward to evaluating all the new results from 2017 to
formulate a plan for the next steps and deliver an updated resource in
Q1 2018. The Fox continues to increase in merit and advance as an
important new high-grade tungsten discovery in the western world."

Details

The Fox tungsten property covers an area with positive tungsten in
rock, soil and drill core that is 10 km by 3 km in dimension.
Tabular-shaped and flat or gently dipping layers of calc-silicate
(skarn) hosts the tungsten mineral scheelite, and are cut by varying
thickness of intrusive rocks. The BN, Ridley Creek and BK zones are
within one of the calc-silicate layers that outcrops for three
kilometres along the east side of Deception Mountain. This layer is
gently dipping in orientation, extending west beneath Deception
Mountain and may connect with mineralized calc-silicate layers that
occur on the other side of the mountain to the northwest, a one
kilometre distance. Between four and eight km south, the Nightcrawler
and South Grid zones respectively, contain multiple calc-silicate
layers traced by drilling for over three km east-west and extend south
of an intrusive contact for two km and is open to the south.

Ridley Creek

Drill holes F17-39 to F17-42 are located approximately 200 metres
northeast of the current Ridley Creek resource, where a 1.5 metre chip
sample with 3.44% WO3 occurs at the base of a 20 metre cliff of
calc-silicate. Drill holes tested the extent of this showing to the
west, northwest and southwest of the outcrop, and returned 30 metres of
calc-silicate containing intervals of variable thickness with low grade
tungsten.

Drill hole F17-43 is located 35 metres north of the current
resource area and returned 1.0 metre of 0.594% WO3 starting at 22.35
metres down the hole. Drill holes F17-44 to F17-49 are located
northwest and north of the current resource area and drilled westward.
F17-44 averaged 19.4 metres of 0.927% WO3 including 2.59 metres of
5.824% WO3 and 3.13 metres of 0.919% WO3 starting at 46.0 metres.
Results of this drill hole extend the mineralized intercept in F13-19
(26.0 metres of 1.19% WO3) by 35 metres and this high-grade zone is
open to the northwest. Drill holes F17-45 to F17-49 are located to the
north of F17-44 and drilled westward but appear to have not reached the
thickest part of this high-grade northwest trending zone, the best
being F17-48 containing 0.72 metres of 4.653% WO3. Additional drilling
to the northwest of the Ridley Creek deposit is required to expand the
very high-grade mineralization to the northwest with potential for the
zone to continue one kilometre to where mineralized outcrop occurs on
the other side of Deception Mountain.

Drill holes F17-50 to F17-55 are located around the southern side
of the current resource open pit shell and contain locally moderate
grade intervals. F17-51 contains 13.1 metres of 0.124% WO3 starting at
15.3 metres, including 0.8 metres of 0.764% WO3. The Ridley Creek zone
remains open to the southwest beyond drill hole F16-9 containing 3.0
metres of 0.52% WO3.

Drill holes F17-56 to F17-59 are located to the southeast of any
previous drilling in the Ridley Creek zone and demonstrate the deposit
remains open in this direction. F17-56 is an angle drill hole and
contains a 0.85 metre interval with 4.161% WO3 starting at 11.45 metres
down the hole, or 8.1 metres vertically below surface. F17-57 is
located 35 metres south of F17-56 and contains 4.82 metres of 0.516%
WO3 starting at 21.44 metres down the hole, or 16.4 metres vertically
below surface. The positive grade occurring near-surface in this area
is thought to add to the open-pit resource potential and it remains
open to the west and 750 metres southeast toward the BN zone.

In 2017, new hand-dug pits and trenches around the Ridley Creek
zone exposed outcrop containing positive to high grade tungsten values.
Approximately 35 metres to the south of the main Ridley Creek trenches
a one-metre chip sample returned 2.82% WO3 that is open in thickness
and along strike. This result demonstrates good continuity of the
high-grade surface zone and that it extends further than previously
thought.

In the southeastern area of Ridley Creek, hand trenching exposed
outcrop which returned a saw-cut channel sample of 3.3 metres of 0.913%
WO3 that connects with the mineralized zone in F14-56 and F17-57. Hand
clearing, trenching and rock sampling further south of this area was
successful in partially exposing this calc-silicate layer with samples
returning 0.70 metres of 0.698% WO3, and 0.45 metres of 0.559% WO3 that
are open in width. A grab sample located 200 metres to the south
contains 2.383% WO3. These surface results support the potential to
connect the Ridley Creek with the BN zone, and a gap of approximately
750 metres remains unexplored between them.

South Grid

Drill holes F17-60 to F17-63 are located at the South Grid target,
a 1.5 km by 500 metre tungsten in soil geochemical anomaly with limited
outcrop exposure and excellent road access. The 2017 drill holes are
located to the west and east of the three shallow and incomplete 2016
drill holes.

Drill hole F17-61 (-60 degrees to the northeast) returned 3.07
metres of 0.496% WO3 starting at 14.6 metres, or 12.6 metres vertically
below surface. This result is open for expansion and confirms
significant grade occurs near surface in this large geochemical target.
Drill hole F17-60 is located 150 metres southwest of F17-61 and
contains mainly biotite schist and minor calc-silicate with one metre
and 1.8 metre intervals containing 0.181% WO3 and 0.149% WO3,
respectively. Approximately 350 metres to the east-northeast of F17-61,
drill hole F17-62 intersected approximately 60 metres of calc-silicate
with eight intervals of 2.0 metres containing elevated tungsten, the
best including 4.0 metres of 0.239% WO3 starting at 99 metres. F17-63
is located approximately 50 metres north of F17-62 and similarly
contains approximately 60 metres of calc-silicate with multiple
intervals of elevated tungsten, the best being 1.8 metres of 0.192% WO3
starting at 58.75 metres, and 0.90 metres of 0.282% WO3. This drill
hole is on the edge of a slope down to the north and the mineralized
zones are expected to continue to surface, and the grade-thickness of
mineralized intervals appear to increase to the south. Results from
drilling at the South Grid in 2017 are thought to demonstrate excellent
potential and additional trenching and drilling is required to better
define the geology and extent of this quality new prospect.

Creek zone

Three drill holes were collared on the north side of the
interpreted mineralized trend at the Creek zone and drilled towards the
south. Drill hole F17-64 intersected 0.7 metres of 0.991% WO3 in the
casing at the top of the hole, and F17-65 (vertical) intersected 0.7
metres of 0.831% WO3 at 89 metres. In 2015, drill hole F15-2, is
located 100 metres south of F17-64 and angled to the north and returned
5.0 metres of 1.00% WO3.
The drill intercepts in F17-64 and F17-65 are located
approximately 35 metres northeast of saw-cut channel samples at the
Creek zone. In 2017, four saw cut channel samples were collected from
intermittently exposed rock at the northern end of the prospect and
returned 1.0 metre of 1.165% WO3, 0.9 metres of 0.716% WO3, 1.1 metres
of 1.10% WO3 and 0.8 metres of 0.163% WO3. A boulder located on the
other side of the creek returned 1.87% WO3. Further testing is required
to resolve geological controls of the high-grade mineralization at the
Creek zone and this zone remains open in several directions.

Mapping

In 2017 the Company engaged ARC-Geoscience Group Inc. to perform
geological mapping mainly around Deception Mountain and the South Grid
areas. Several layers of calc-silicate located at higher elevations
above the BN, Ridley Creek and BK zones were mapped and locally sampled
returning positive tungsten values. The North zone was traced for over
500 metres south and a grab sample returned 0.349% WO3. In addition,
scientific studies, funded in part by government research grants, are
being conducted by the University of British Columbia, and final
reporting of this as well as geological work completed by ARC and the
Company will be reported when completed.

2017 Ridley Creek, South Grid and Creek Zone Drilling Results

//st

------------------------------------------------------
2017       From   To     Interval WO3
----------------------------------------------------
Zone         Drill hole Metres Metres Metres   %
----------------------------------------------------
Ridley Creek F17-39                         NSV
----------------------------------------------------
Ridley Creek F17-40     24.00  24.80  0.80     0.100
----------------------------------------------------
Ridley Creek F17-41     5.18   7.20   2.00     0.083
----------------------------------------------------
Ridley Creek F17-42                         NSV
----------------------------------------------------
Ridley Creek F17-43     14.35  16.35  2.00     0.116
----------------------------------------------------
Ridley Creek And        22.35  23.35  1.00     0.594
----------------------------------------------------
Ridley Creek F17-44     46.00  65.40  19.40    0.927
----------------------------------------------------
Ridley Creek Includes   46.00  48.59  2.59     5.824
----------------------------------------------------
Ridley Creek And        62.27  65.40  3.13     0.919
----------------------------------------------------
Ridley Creek F17-45     27.70  28.20  0.50     0.339
----------------------------------------------------
Ridley Creek And        48.08  49.07  0.99     0.608
----------------------------------------------------
Ridley Creek F17-46     18.93  19.51  0.58     0.274
----------------------------------------------------
Ridley Creek And        73.93  74.43  0.50     0.213
----------------------------------------------------
Ridley Creek And        76.72  77.33  0.61     0.106
----------------------------------------------------
Ridley Creek And        78.15  79.00  0.85     0.113
----------------------------------------------------
Ridley Creek F17-47     15.93  17.40  1.47     0.078
----------------------------------------------------
Ridley Creek And        53.65  55.55  1.90     
0.054----------------------------------------------------
Ridley Creek F17-48     62.63  63.35  0.72     4.653
----------------------------------------------------
Ridley Creek F17-51     15.30  28.35  13.05    0.124
----------------------------------------------------
Ridley Creek Includes   20.25  21.05  0.80     0.764
----------------------------------------------------
Ridley Creek F17-53     15.60  17.35  1.75     0.175
----------------------------------------------------
Ridley Creek F17-54     42.74  43.74  1.00     0.074
----------------------------------------------------
Ridley Creek F17-55     NSV
----------------------------------------------------
Ridley Creek F17-56     11.45  12.30  0.85     4.161
----------------------------------------------------
Ridley Creek F17-57     21.44  26.26  4.82     0.516
----------------------------------------------------
Ridley Creek F17-58     20.72  21.85  1.13     0.108
----------------------------------------------------
Ridley Creek F17-59     22.50  23.50  1.00     0.227
----------------------------------------------------

----------------------------------------------------
South Grid   F17-60     41.00  42.00  1.00     0.181
----------------------------------------------------
South Grid   And        186.30 187.80 1.50     0.149
----------------------------------------------------
South Grid   F17-61     14.58  17.65  3.07     0.496
----------------------------------------------------
South Grid   And        26.48  27.30  0.82     0.111
----------------------------------------------------
South Grid   F17-62     99.00  103.00 4.00     0.239
----------------------------------------------------
South Grid   And        122.00 124.40 2.40     0.129
----------------------------------------------------
South Grid   F17-63     36.50  37.00  0.50     0.141
----------------------------------------------------
South Grid   And        57.10  57.60  0.50     0.153
----------------------------------------------------
South Grid   And        58.75  60.55  1.80     0.192
----------------------------------------------------
South Grid   And        80.00  80.90  0.90     0.282
----------------------------------------------------
South Grid   And        87.72  88.30  0.58     0.168
----------------------------------------------------

----------------------------------------------------
Creek Zone   F17-64     0.00   0.70   0.70     0.991
----------------------------------------------------
Creek Zone   And        65.90  67.15  1.25     0.197
----------------------------------------------------
Creek Zone   F17-65     89.05  89.75  0.70     0.831
----------------------------------------------------
Creek Zone   F17-66     3.54   5.00   1.46     0.112
------------------------------------------------------

//et

2017 Fox Surface Trench Summary

//st

---------------------------------------------------
Zone       Trench  From To   Width W03   Comment
-------------------------------------------------
(m)  (m)  (m)   %     On width
-------------------------------------------------
Creek Zone 17CZ-1  0.00 1.00 1.00  1.165
-------------------------------------------------
Creek Zone 17CZ-1  4.70 5.60 0.90  0.716
-------------------------------------------------
Creek Zone 17CZ-1  6.00 7.10 1.10  1.100
-------------------------------------------------
Creek Zone 17CZ-1  8.90 9.70 0.80  0.163
-------------------------------------------------
RC south   17RCS-1 1.00 4.30 3.30  0.913 Open
-------------------------------------------------
RC south   17RCS-2 0.00 0.35 0.35  0.438 Open
-------------------------------------------------
RC south   17RCS-3 0.00 0.70 0.70  0.698 Open
-------------------------------------------------
RC south   17RCS-4 0.00 1.65 1.65  0.236 Open
-------------------------------------------------
RC south   17RCS-5 0.00 0.45 0.45  0.559 Open
-------------------------------------------------
RC Main    17RC-2  0.00 1.00 1.00  2.282 Open
---------------------------------------------------

//et

On Deception Mountain, substantially unexplored gaps occur between
the two high grade resource areas at the BN and Ridley Creek deposits,
between Ridley Creek and the BK zones, and further northwest of the BK.
The Nightcrawler and South Grid are within a 3 km by 2 km area
containing surface rock and drill core results indicating a large-scale
mineral system occurs and potentially economic drill intercepts that
warrant follow-up.

The Fox property contains seven zones in a 10 km by 3 km area,
with current resources within two deposits having among the highest
tungsten grade. The Company will be updating the resource for the
project in Q1 2018 and results of geological work and other base metal
analyses are pending.

On behalf of the Board of Directors,

"David E Blann"

David E Blann, P.Eng.

President, CEO

FOR FURTHER INFORMATION PLEASE CONTACT:

David Blann, President, CEO

Corporate Office:

Phone: 604.662.8310
Email: Info@happycreekminerals.com

Website: www.happycreekminerals.com

Corporate Communications

Ron Birch: Phone: 250.545.0383

Toll Free: 1.800.910.7711

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release. David Blann, P.Eng. is a Qualified Person as defined by
National Instrument 43-101 and is responsible for the preparation and
approval of the technical information disclosed in the news release.

Samples are derived from 1/2 core cut by rock saw and shipped to,
prepared and analyzed at SGS Laboratories in Burnaby, British Columbia.
SGS Burnaby is ISO 9001:2008 certified. Drill core samples of all calc
silicate are digested and analyzed by aqua regia and ICP-MS and if
greater than 40 ppm W (tungsten) they are re-analyzed by peroxide
fusion and ICP-AES for percent tungsten (W), respectively. Over limit
samples greater than 4% W are re-analyzed for tungsten by XRF. W is
multiplied by 1.261 to obtain WO3 (tungsten trioxide) the compound for
which tungsten prices are quoted. The Company routinely inserts blanks,
certified standards and duplicate samples within the submitted drill
core batches submitted for assay as part of its quality control
procedures.

This press release contains "forward-looking information" within
the meaning of applicable securities laws, including statements that
address capital costs, recovery, grade, and timing of work or plans at
the Company's mineral projects. Forward-looking information may be, but
not always, identified by the use of words such as "seek",
"anticipate", "plan", "planned", "continue", "expect", "thought to",
"project", "predict", "potential", "targeting", "intends", "believe",
"opportunity", "further" and others, or which describes a goal or
action, event or result such as "may", "should", "could", "would",
"might" or "will" be undertaken, occur or achieved. Statements also
include those that address future mineral production, reserve
potential, potential size or scale of a mineralized zone, potential
expansion of mineralization, potential type(s) of mining, potential
grades as well as to Happy creek's ability to fund ongoing expenditure,
or assumptions about future metal or mineral prices, currency exchange
rates, metallurgical recoveries and grades, favorable operating
conditions, access, political stability, obtaining or renewal of
existing or required mineral titles, licenses and permits, labour
stability, market conditions, availability of equipment, accuracy of
any mineral resources, anticipated costs and expenditures. Assumptions
may be based on factors and events that are not within the control of
Happy creek and there is no assurance they will prove to be correct.
Such forward-looking information involves known and unknown risks,
which may cause the actual results to materially differ, and/or any
future results expressed or implied by such forward-looking
information. Additional information on risks and uncertainties can be
found within Financial Statements, Prospectus and other materials found
on the Company's SEDAR profile at www.sedar.com. Although Happy creek
has attempted to identify important factors that could cause actual
actions, events or results to differ materially from those described in
forward-looking information, there can be no assurance that such
information will prove to be accurate as actual results and future
events could differ materially from those anticipated in such
statements. Happy creek withholds any obligation to update or revise
any forward-looking information, whether as a result of new
information, future events or otherwise, unless required by law.
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1732400030TS11732401117-06371320171121


[200/News Release]HPYVHAPPY CREEK MINERALS LTDNOV 21 2017  06:37 AMDrills 
19.4 Metres of 0.93% WO3 Including 2.6 Metres of 5.8% W03 AtRidley Creek and 
Makes a Discovery at South Grid on the Fox TungstenProperty --->@NEWS RELEASE
HAPPY CREEK MINERALS LTD ("HPY-V;HPYCF-0")
- Drills 19.4 Metres of 0.93% WO3 Including 2.6 Metres of 5.8% W03
- At Ridley Creek and Makes a Discovery at South Grid on the Fox
- Tungsten Property

Happy Creek Minerals Ltd. (the "Company") is pleased to announce
the remaining results from drilling on its 100% owned Fox tungsten
property, located 90 km northeast of the town of 100 Mile House, in
south central B.C., Canada. During 2017, 11,429 metres of diamond core
drilling in 66 holes was performed on the BN, Ridley Creek and
Nightcrawler-South Grid zones.

Further to the news release October 24, 2017 for the BN zone
drilling results, results for the Ridley Creek, South Grid and Creek
zones are reported here for drill holes F17-39 to F17-66, along with a
summary of surface trench and rock sampling. Refer to the Tables below,
and maps will be posted to the website shortly. On January 26, 2017 the
Company announced the Ridley Creek and BN zones contain 486,000 tonnes
indicated grading 0.818% W03 (tungsten trioxide) and 361,000 tonnes
inferred grading 1.568% WO3. This includes 329,000 tonnes of 0.729% WO3
indicated within an open pit. Resources have not yet been estimated for
the South Grid, Nightcrawler, Creek, BK and North zones.

In 2017, drilling at Ridley Creek was focused on the outward
expansion of the current resource area and collecting data to better
delimit the deposit around the periphery of the current open pit shell.
Distances are relative to the current resource area or pit shell
perimeter. True widths are estimated to be 75-95% of reported drill
intervals, and trenches are rock-saw cut channel and chip samples.

Highlights

DDH F17-44: Starting at 46.0 metres, 19.4 metres of 0.927% WO3,
including 2.59 metres of 5.824% that expands the Ridley Creek zone
approximately 35 metres to the northwest and this high-grade zone
remains open.

DDH F17-48: Starting at 62.6 metres, 0.72 metres of 4.653% WO3
that expands the Ridley Creek zone 100 metres north of the current
resource area.

DDH F17-56: Starting at 11.45 metres, 0.85 metres of 4.160% WO3 at
Ridley Creek south and,

DDH F17-57: starting at 21.2 metres, 4.82 metres of 0.516% WO3
that expands Ridley Creek 45 metres further southeast of the current
resource area where it is open to the west and southeast.

Trench 17RCS-1: Rock saw cut 3.3 metres containing 0.91% WO3 that
is located 45 metres northeast of F17-57 and connects to the
mineralized zones in drill holes F17-56 and F17-57.

DDH F17-61: Starting at 12.6 metres below surface, 3.07 metres of
0.496% WO3 at the South Grid. This is considered a discovery of
potentially economic grade in this new, road accessible target that is
underlain by a 1.5 km by 500 metre tungsten in soil anomaly.

DDH F17-64: Starting at the top of the hole, 0.7m of 0.991% WO3 in
the first sample at the Creek zone, and the mineralized zone remains
open in several directions.

David Blann, President and C.E.O. of Happy Creek states: "Drilling
at Ridley Creek has improved geological modelling of the deposit,
collected data for more advanced studies, and expanded the area of
excellent grade mainly to the northwest and southeast. Another top-tier
result in F17-44 with 2.6 metres of 5.8% WO3 and 3.1 metres of 0.919%
WO3 provides a clear vector to continue expanding this high-grade
material to the northwest. To the southeast, drill holes F17-56 and
F17-57 include 0.9 metres of 4.160% WO3 and 4.8 metres of 0.516% WO3
respectively, that connect with a new trench containing 3.3 metres of
0.913% WO3, and together should add to the existing shallow open pit
resource. In addition, new outcrop containing 0.698% WO3 over 0.7
metres (open in width) and grab samples up to 2.383% WO3 are located up
to 200 metres further southeast and provide an exciting opportunity to
increase near-surface resources along the 750 metre un-explored gap
between the Ridley Creek and BN zone.

At the South Grid, the drilling discovery of 3.0 metres with
0.496% WO3 near surface is an excellent result that elevates the
importance of this new 1.5 km by 500 metre geochemical target that is
all within recent logging clear-cuts and numerous roads and trails.

We look forward to evaluating all the new results from 2017 to
formulate a plan for the next steps and deliver an updated resource in
Q1 2018. The Fox continues to increase in merit and advance as an
important new high-grade tungsten discovery in the western world."

Details

The Fox tungsten property covers an area with positive tungsten in
rock, soil and drill core that is 10 km by 3 km in dimension.
Tabular-shaped and flat or gently dipping layers of calc-silicate
(skarn) hosts the tungsten mineral scheelite, and are cut by varying
thickness of intrusive rocks. The BN, Ridley Creek and BK zones are
within one of the calc-silicate layers that outcrops for three
kilometres along the east side of Deception Mountain. This layer is
gently dipping in orientation, extending west beneath Deception
Mountain and may connect with mineralized calc-silicate layers that
occur on the other side of the mountain to the northwest, a one
kilometre distance. Between four and eight km south, the Nightcrawler
and South Grid zones respectively, contain multiple calc-silicate
layers traced by drilling for over three km east-west and extend south
of an intrusive contact for two km and is open to the south.

Ridley Creek

Drill holes F17-39 to F17-42 are located approximately 200 metres
northeast of the current Ridley Creek resource, where a 1.5 metre chip
sample with 3.44% WO3 occurs at the base of a 20 metre cliff of
calc-silicate. Drill holes tested the extent of this showing to the
west, northwest and southwest of the outcrop, and returned 30 metres of
calc-silicate containing intervals of variable thickness with low grade
tungsten.

Drill hole F17-43 is located 35 metres north of the current
resource area and returned 1.0 metre of 0.594% WO3 starting at 22.35
metres down the hole. Drill holes F17-44 to F17-49 are located
northwest and north of the current resource area and drilled westward.
F17-44 averaged 19.4 metres of 0.927% WO3 including 2.59 metres of
5.824% WO3 and 3.13 metres of 0.919% WO3 starting at 46.0 metres.
Results of this drill hole extend the mineralized intercept in F13-19
(26.0 metres of 1.19% WO3) by 35 metres and this high-grade zone is
open to the northwest. Drill holes F17-45 to F17-49 are located to the
north of F17-44 and drilled westward but appear to have not reached the
thickest part of this high-grade northwest trending zone, the best
being F17-48 containing 0.72 metres of 4.653% WO3. Additional drilling
to the northwest of the Ridley Creek deposit is required to expand the
very high-grade mineralization to the northwest with potential for the
zone to continue one kilometre to where mineralized outcrop occurs on
the other side of Deception Mountain.

Drill holes F17-50 to F17-55 are located around the southern side
of the current resource open pit shell and contain locally moderate
grade intervals. F17-51 contains 13.1 metres of 0.124% WO3 starting at
15.3 metres, including 0.8 metres of 0.764% WO3. The Ridley Creek zone
remains open to the southwest beyond drill hole F16-9 containing 3.0
metres of 0.52% WO3.

Drill holes F17-56 to F17-59 are located to the southeast of any
previous drilling in the Ridley Creek zone and demonstrate the deposit
remains open in this direction. F17-56 is an angle drill hole and
contains a 0.85 metre interval with 4.161% WO3 starting at 11.45 metres
down the hole, or 8.1 metres vertically below surface. F17-57 is
located 35 metres south of F17-56 and contains 4.82 metres of 0.516%
WO3 starting at 21.44 metres down the hole, or 16.4 metres vertically
below surface. The positive grade occurring near-surface in this area
is thought to add to the open-pit resource potential and it remains
open to the west and 750 metres southeast toward the BN zone.

In 2017, new hand-dug pits and trenches around the Ridley Creek
zone exposed outcrop containing positive to high grade tungsten values.
Approximately 35 metres to the south of the main Ridley Creek trenches
a one-metre chip sample returned 2.82% WO3 that is open in thickness
and along strike. This result demonstrates good continuity of the
high-grade surface zone and that it extends further than previously
thought.

In the southeastern area of Ridley Creek, hand trenching exposed
outcrop which returned a saw-cut channel sample of 3.3 metres of 0.913%
WO3 that connects with the mineralized zone in F14-56 and F17-57. Hand
clearing, trenching and rock sampling further south of this area was
successful in partially exposing this calc-silicate layer with samples
returning 0.70 metres of 0.698% WO3, and 0.45 metres of 0.559% WO3 that
are open in width. A grab sample located 200 metres to the south
contains 2.383% WO3. These surface results support the potential to
connect the Ridley Creek with the BN zone, and a gap of approximately
750 metres remains unexplored between them.

South Grid

Drill holes F17-60 to F17-63 are located at the South Grid target,
a 1.5 km by 500 metre tungsten in soil geochemical anomaly with limited
outcrop exposure and excellent road access. The 2017 drill holes are
located to the west and east of the three shallow and incomplete 2016
drill holes.

Drill hole F17-61 (-60 degrees to the northeast) returned 3.07
metres of 0.496% WO3 starting at 14.6 metres, or 12.6 metres vertically
below surface. This result is open for expansion and confirms
significant grade occurs near surface in this large geochemical target.
Drill hole F17-60 is located 150 metres southwest of F17-61 and
contains mainly biotite schist and minor calc-silicate with one metre
and 1.8 metre intervals containing 0.181% WO3 and 0.149% WO3,
respectively. Approximately 350 metres to the east-northeast of F17-61,
drill hole F17-62 intersected approximately 60 metres of calc-silicate
with eight intervals of 2.0 metres containing elevated tungsten, the
best including 4.0 metres of 0.239% WO3 starting at 99 metres. F17-63
is located approximately 50 metres north of F17-62 and similarly
contains approximately 60 metres of calc-silicate with multiple
intervals of elevated tungsten, the best being 1.8 metres of 0.192% WO3
starting at 58.75 metres, and 0.90 metres of 0.282% WO3. This drill
hole is on the edge of a slope down to the north and the mineralized
zones are expected to continue to surface, and the grade-thickness of
mineralized intervals appear to increase to the south. Results from
drilling at the South Grid in 2017 are thought to demonstrate excellent
potential and additional trenching and drilling is required to better
define the geology and extent of this quality new prospect.

Creek zone

Three drill holes were collared on the north side of the
interpreted mineralized trend at the Creek zone and drilled towards the
south. Drill hole F17-64 intersected 0.7 metres of 0.991% WO3 in the
casing at the top of the hole, and F17-65 (vertical) intersected 0.7
metres of 0.831% WO3 at 89 metres. In 2015, drill hole F15-2, is
located 100 metres south of F17-64 and angled to the north and returned
5.0 metres of 1.00% WO3.
The drill intercepts in F17-64 and F17-65 are located
approximately 35 metres northeast of saw-cut channel samples at the
Creek zone. In 2017, four saw cut channel samples were collected from
intermittently exposed rock at the northern end of the prospect and
returned 1.0 metre of 1.165% WO3, 0.9 metres of 0.716% WO3, 1.1 metres
of 1.10% WO3 and 0.8 metres of 0.163% WO3. A boulder located on the
other side of the creek returned 1.87% WO3. Further testing is required
to resolve geological controls of the high-grade mineralization at the
Creek zone and this zone remains open in several directions.

Mapping

In 2017 the Company engaged ARC-Geoscience Group Inc. to perform
geological mapping mainly around Deception Mountain and the South Grid
areas. Several layers of calc-silicate located at higher elevations
above the BN, Ridley Creek and BK zones were mapped and locally sampled
returning positive tungsten values. The North zone was traced for over
500 metres south and a grab sample returned 0.349% WO3. In addition,
scientific studies, funded in part by government research grants, are
being conducted by the University of British Columbia, and final
reporting of this as well as geological work completed by ARC and the
Company will be reported when completed.

2017 Ridley Creek, South Grid and Creek Zone Drilling Results

//st

------------------------------------------------------
2017       From   To     Interval WO3
----------------------------------------------------
Zone         Drill hole Metres Metres Metres   %
----------------------------------------------------
Ridley Creek F17-39                         NSV
----------------------------------------------------
Ridley Creek F17-40     24.00  24.80  0.80     0.100
----------------------------------------------------
Ridley Creek F17-41     5.18   7.20   2.00     0.083
----------------------------------------------------
Ridley Creek F17-42                         NSV
----------------------------------------------------
Ridley Creek F17-43     14.35  16.35  2.00     0.116
----------------------------------------------------
Ridley Creek And        22.35  23.35  1.00     0.594
----------------------------------------------------
Ridley Creek F17-44     46.00  65.40  19.40    0.927
----------------------------------------------------
Ridley Creek Includes   46.00  48.59  2.59     5.824
----------------------------------------------------
Ridley Creek And        62.27  65.40  3.13     0.919
----------------------------------------------------
Ridley Creek F17-45     27.70  28.20  0.50     0.339
----------------------------------------------------
Ridley Creek And        48.08  49.07  0.99     0.608
----------------------------------------------------
Ridley Creek F17-46     18.93  19.51  0.58     0.274
----------------------------------------------------
Ridley Creek And        73.93  74.43  0.50     0.213
----------------------------------------------------
Ridley Creek And        76.72  77.33  0.61     0.106
----------------------------------------------------
Ridley Creek And        78.15  79.00  0.85     0.113
----------------------------------------------------
Ridley Creek F17-47     15.93  17.40  1.47     0.078
----------------------------------------------------
Ridley Creek And        53.65  55.55  1.90     
0.054----------------------------------------------------
Ridley Creek F17-48     62.63  63.35  0.72     4.653
----------------------------------------------------
Ridley Creek F17-51     15.30  28.35  13.05    0.124
----------------------------------------------------
Ridley Creek Includes   20.25  21.05  0.80     0.764
----------------------------------------------------
Ridley Creek F17-53     15.60  17.35  1.75     0.175
----------------------------------------------------
Ridley Creek F17-54     42.74  43.74  1.00     0.074
----------------------------------------------------
Ridley Creek F17-55     NSV
----------------------------------------------------
Ridley Creek F17-56     11.45  12.30  0.85     4.161
----------------------------------------------------
Ridley Creek F17-57     21.44  26.26  4.82     0.516
----------------------------------------------------
Ridley Creek F17-58     20.72  21.85  1.13     0.108
----------------------------------------------------
Ridley Creek F17-59     22.50  23.50  1.00     0.227
----------------------------------------------------

----------------------------------------------------
South Grid   F17-60     41.00  42.00  1.00     0.181
----------------------------------------------------
South Grid   And        186.30 187.80 1.50     0.149
----------------------------------------------------
South Grid   F17-61     14.58  17.65  3.07     0.496
----------------------------------------------------
South Grid   And        26.48  27.30  0.82     0.111
----------------------------------------------------
South Grid   F17-62     99.00  103.00 4.00     0.239
----------------------------------------------------
South Grid   And        122.00 124.40 2.40     0.129
----------------------------------------------------
South Grid   F17-63     36.50  37.00  0.50     0.141
----------------------------------------------------
South Grid   And        57.10  57.60  0.50     0.153
----------------------------------------------------
South Grid   And        58.75  60.55  1.80     0.192
----------------------------------------------------
South Grid   And        80.00  80.90  0.90     0.282
----------------------------------------------------
South Grid   And        87.72  88.30  0.58     0.168
----------------------------------------------------

----------------------------------------------------
Creek Zone   F17-64     0.00   0.70   0.70     0.991
----------------------------------------------------
Creek Zone   And        65.90  67.15  1.25     0.197
----------------------------------------------------
Creek Zone   F17-65     89.05  89.75  0.70     0.831
----------------------------------------------------
Creek Zone   F17-66     3.54   5.00   1.46     0.112
------------------------------------------------------

//et

2017 Fox Surface Trench Summary

//st

---------------------------------------------------
Zone       Trench  From To   Width W03   Comment
-------------------------------------------------
(m)  (m)  (m)   %     On width
-------------------------------------------------
Creek Zone 17CZ-1  0.00 1.00 1.00  1.165
-------------------------------------------------
Creek Zone 17CZ-1  4.70 5.60 0.90  0.716
-------------------------------------------------
Creek Zone 17CZ-1  6.00 7.10 1.10  1.100
-------------------------------------------------
Creek Zone 17CZ-1  8.90 9.70 0.80  0.163
-------------------------------------------------
RC south   17RCS-1 1.00 4.30 3.30  0.913 Open
-------------------------------------------------
RC south   17RCS-2 0.00 0.35 0.35  0.438 Open
-------------------------------------------------
RC south   17RCS-3 0.00 0.70 0.70  0.698 Open
-------------------------------------------------
RC south   17RCS-4 0.00 1.65 1.65  0.236 Open
-------------------------------------------------
RC south   17RCS-5 0.00 0.45 0.45  0.559 Open
-------------------------------------------------
RC Main    17RC-2  0.00 1.00 1.00  2.282 Open
---------------------------------------------------

//et

On Deception Mountain, substantially unexplored gaps occur between
the two high grade resource areas at the BN and Ridley Creek deposits,
between Ridley Creek and the BK zones, and further northwest of the BK.
The Nightcrawler and South Grid are within a 3 km by 2 km area
containing surface rock and drill core results indicating a large-scale
mineral system occurs and potentially economic drill intercepts that
warrant follow-up.

The Fox property contains seven zones in a 10 km by 3 km area,
with current resources within two deposits having among the highest
tungsten grade. The Company will be updating the resource for the
project in Q1 2018 and results of geological work and other base metal
analyses are pending.

On behalf of the Board of Directors,

"David E Blann"

David E Blann, P.Eng.

President, CEO

FOR FURTHER INFORMATION PLEASE CONTACT:

David Blann, President, CEO

Corporate Office:

Phone: 604.662.8310
Email: Info@happycreekminerals.com

Website: www.happycreekminerals.com

Corporate Communications

Ron Birch: Phone: 250.545.0383

Toll Free: 1.800.910.7711

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release. David Blann, P.Eng. is a Qualified Person as defined by
National Instrument 43-101 and is responsible for the preparation and
approval of the technical information disclosed in the news release.

Samples are derived from 1/2 core cut by rock saw and shipped to,
prepared and analyzed at SGS Laboratories in Burnaby, British Columbia.
SGS Burnaby is ISO 9001:2008 certified. Drill core samples of all calc
silicate are digested and analyzed by aqua regia and ICP-MS and if
greater than 40 ppm W (tungsten) they are re-analyzed by peroxide
fusion and ICP-AES for percent tungsten (W), respectively. Over limit
samples greater than 4% W are re-analyzed for tungsten by XRF. W is
multiplied by 1.261 to obtain WO3 (tungsten trioxide) the compound for
which tungsten prices are quoted. The Company routinely inserts blanks,
certified standards and duplicate samples within the submitted drill
core batches submitted for assay as part of its quality control
procedures.

This press release contains "forward-looking information" within
the meaning of applicable securities laws, including statements that
address capital costs, recovery, grade, and timing of work or plans at
the Company's mineral projects. Forward-looking information may be, but
not always, identified by the use of words such as "seek",
"anticipate", "plan", "planned", "continue", "expect", "thought to",
"project", "predict", "potential", "targeting", "intends", "believe",
"opportunity", "further" and others, or which describes a goal or
action, event or result such as "may", "should", "could", "would",
"might" or "will" be undertaken, occur or achieved. Statements also
include those that address future mineral production, reserve
potential, potential size or scale of a mineralized zone, potential
expansion of mineralization, potential type(s) of mining, potential
grades as well as to Happy creek's ability to fund ongoing expenditure,
or assumptions about future metal or mineral prices, currency exchange
rates, metallurgical recoveries and grades, favorable operating
conditions, access, political stability, obtaining or renewal of
existing or required mineral titles, licenses and permits, labour
stability, market conditions, availability of equipment, accuracy of
any mineral resources, anticipated costs and expenditures. Assumptions
may be based on factors and events that are not within the control of
Happy creek and there is no assurance they will prove to be correct.
Such forward-looking information involves known and unknown risks,
which may cause the actual results to materially differ, and/or any
future results expressed or implied by such forward-looking
information. Additional information on risks and uncertainties can be
found within Financial Statements, Prospectus and other materials found
on the Company's SEDAR profile at www.sedar.com. Although Happy creek
has attempted to identify important factors that could cause actual
actions, events or results to differ materially from those described in
forward-looking information, there can be no assurance that such
information will prove to be accurate as actual results and future
events could differ materially from those anticipated in such
statements. Happy creek withholds any obligation to update or revise
any forward-looking information, whether as a result of new
information, future events or otherwise, unless required by law.
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1732400030TS11732401117-06371320171121