Source	CANADA NEWSWIRE
Date	11/16/2017
Time	07:04:38 AM

Company	 Hannan Metals Ltd.
Title	Hannan commences 41 line kilometre seismic survey in Ireland





    CDNX Symbol: HAN











Press Release




" BC-HannanSeismicSurvey   11-16 1112
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Hannan commences 41 line kilometre seismic survey in Ireland@

VANCOUVER, Nov. 16, 2017 /CNW/ - Hannan Metals Limited ("Hannan" or the
"Company") (TSX.V: HAN) (OTCPK: HANNF) is pleased to announce the commencement
of a 40.6 line kilometre 2D seismic survey at the 100%-owned County Clare
exploration license, which hosts the Kilbricken zinc-lead-silver deposit,
Ireland. The survey will cover the most prospective areas within the 32,223 Ha
prospecting licence area, and is designed to identify and map the geological
structures that host and control base metal mineralization.
Key Points:
<<

--  A 40.6 line kilometre 2D seismic survey has commenced across Hannan's
County Clare 100% owned prospecting licence area, employing the latest
seismic geophysical exploration techniques used by the oil and gas
industry;
--  The survey will extend from the Kilbricken zinc-lead-silver resource
area and will extend over an area of 12 kilometre by 14 kilometre within
the Clare Basin where potential is very high for additional base metals
discoveries (Figure 1);
--  Seismic is not a technique commonly used in hard rock mining and is more
popular in the oil and gas industry. Hannan is one of only a handful of
exploration companies to use the method globally;
--  The survey has the potential to propel understanding of the regional
geology of the Clare Basin in a technological way, not previously
possible. The survey aims to map subsurface structures that may host
mineral deposits, allowing for highly effective drill targeting when
used in combination with other data.
>>
Mr. Michael Hudson, CEO and Chairman, states: "The application of an
innovative technology such as seismic to our exploration program provides
Hannan the opportunity to greatly accelerate discovery rate at our County
Clare zinc project. Hannan is one of few hard rock companies to apply seismic
surveying to mineral exploration globally. The geological data collected will
allow our geological experts to identify structures that may host base metal
deposits in the both the local area surrounding the Kilbricken resource, and
beyond over a large regional area."
The seismic survey was designed by Hannan, together with its geophysical
consultants and is being carried out by Gallego Technic Geophysics and Rees
Onshore Seismic Ltd. A total of 34 people are currently at site in Ireland
performing the survey. The operations have been permitted by the Clare County
Council and comply with all relevant central and local government regulations.
Three north-south lines and one east-west tie line is planned to test for
structures in multiple orientations (Figure 1). The survey will run until the
end of November.
Seismic surveys use sound waves to map features beneath the earth's
surface. A convoy of specialized vehicles (Vibrators) (Photo 1) generate the
sound waves which travel through the earth and are reflected back to surface
from geological layers. These faint echoes are recorded by sensors (geophones
- Photo 2), which are then processed to produce images of the underlying
geological layers and structures. The seismic technique has advanced rapidly
over the recent years as researchers adapt and introduce new methods,
algorithms and approaches with increasing computing power (Photo 3).
About Hannan Metals Limited (TSX.V:HAN) (OTCPK: HANNF)Hannan Metals
Limited has 100% ownership of the County Clare Zn-Pb-Ag-Cu project in Ireland,
which consists of 9 prospecting licences for 32,223 hectares. Zinc remains in
tight supply amidst rising demand and stagnant supply. Ireland is a leading
global jurisdiction for zinc mining and exploration. In 2015, Ireland was the
world's 10th largest zinc producing nation with 230,000 tonnes produced.
The maiden mineral resource, dated July 10, 2017, immediately ranked
Kilbricken as one of the top ten base metal deposits discovered in Ireland by
tonnes and grade. Total indicated mineral resources were calculated as 2.7
million tonnes at 8.8% zinc equivalent ("ZnEq"), including 1.4 million tonnes
at 10.8% Zneq and total inferred mineral resources of 1.7 million tonnes at
8.2% ZnEq, including 0.6 million tonnes at 10.4% ZnEq.
Over the last decade, the team behind Hannan has forged a long and
successful record of financing and discovering mineral projects in Europe.
Additionally, the team holds extensive zinc experience, gained from the
world's largest integrated zinc producer of the time, Pasminco Ltd.
Mr. Michael Hudson FAusIMM, Hannan's Chairman and CEO, a Qualified Person
as defined in National Instrument 43-101, has reviewed and approved the
technical disclosure contained in this news release.
NI 43-101 Technical Report:On August 22, 2017, Hannan filed an
independent National Instrument 43-101 Technical Report (the "NI 43-101
Technical Report") on The Mineral Resource Estimate for the Kilbricken
Zinc-Silver-Lead-Copper Project Co. Clare, Ireland For Hannan Metals Ltd in
support of the Company's news release dated July 10, 2017. The NI 43-101
Technical Report was authored by Mr. Geoff Reed of Reed Leyton Consultants and
Dr. John Colthurst who are independent "qualified persons" as defined by
National Instrument 43-101. The NI 43-101 Technical Report may be found under
the Company's profile on SEDAR at www.sedar.com and on the Company's website
at www.hannanmetals.com.
On behalf of the Board,

"Michael Hudson" Michael Hudson, Chairman & CEO
Forward Looking Statements
Certain information set forth in this news release contains
"forward-looking statements", and "forward- looking information" under
applicable securities laws. Except for statements of historical fact, certain
information contained herein constitutes forward-looking statements, which
include the Company's expectations regarding future performance based on
current results, expected cash costs based on the Company's current internal
expectations, estimates, projections, assumptions and beliefs, which may prove
to be incorrect. These statements are not guarantees of future performance and
undue reliance should not be placed on them. Such forward-looking statements
necessarily involve known and unknown risks and uncertainties, which may cause
the Company's actual performance and financial results in future periods to
differ materially from any projects of future performance or results expressed
or implied by such forward-looking statement. These risks and uncertainties
include, but are not limited to: The Company's expectations regarding the
current drill program, liabilities inherent in mine development and
production, geological risks, the financial markets generally, and the ability
of the Company to raise additional capital to fund future operations. There
can be no assurance that forward-looking statements will prove to be accurate,
and actual results and future events could differ materially from those
anticipated in such statements. The Company undertakes no obligation to update
forward-looking statements if circumstances or management's estimates or
opinions should change except as required by applicable securities laws. The
reader is cautioned not to place undue reliance on forward-looking statements.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this news release.
SOURCE Hannan Metals Ltd.



View original content with multimedia:
http://www.newswire.ca/en/releases/archive/November2017/16/c7161.html

-0-                           11/16/2017
/For further information: www.hannanmetals.com, 1305 - 1090 West Georgia
St., Vancouver, BC, V6E 3V7, Mariana Bermudez, Corporate Secretary, +1 (604)
685 9316, info(at)hannanmetals.com/
(HANNF HAN.)

CO:  Hannan Metals Ltd.
ST:  British Columbia
IN:  MIN MNG
SU:

-30-