Source	MARKET NEWS
Date	11/16/2017
Time	07:07:52 AM

Company	 Independence Gold Corp.
Title	Intersects Gold Mineralization on Boulevard, Yuk





    CDNX Symbol: IGO











Press Release





Intersects Gold Mineralization on Boulevard, Yukon --->@NEWS RELEASE
INDEPENDENCE GOLD CORP ("IGO-V")
- Intersects Gold Mineralization on Boulevard, Yukon

Independence Gold Corp. ("Independence" or "the Company") is
pleased to announce drill results from four of nine diamond drill holes
completed this summer on the Company's 100% owned Boulevard Project,
contiguous to Goldcorp Incs Coffee Gold Deposit in the White Gold
District, Yukon. The best intercept in these four holes is 3.10 grams
per tonne ("g/t") gold over 1.5 metres ("m") including 76.2 g/t gold in
the coarse fraction (24.1 g) of a 875 grams ("g") sample over the same
interval.
A total of 977.5 m of diamond drilling was completed in 9 holes
within the Sunrise/Sunset Zone, located 8.5 kilometres (km) southwest
of the Coffee deposit.  Drilling focused primarily on the intersection
of the Sunrise and Sunset trends which have been identified as
multi-element soil geochemical anomalies and were confirmed by reverse
circulation ("RC") drilling in previous years.  Significant intercepts
from this year's diamond drilling program are presented in the table
below.  A table of all 2017 drill results and a map showing the drill
hole locations is posted on the Company's website.
//st

Drill    From To   Length Au (g/t) Au (g/t)  Au (g/t) by
hole      (m) (m)  (m)    by Fire  by        Screen
Assay    Screen    Metallics
Metallics (Fine Fraction
(Coarse   )106 microns)
Fraction
)106
microns)
BV17-58 53.5  55.0 1.5    3.10*    76.20    1.01
And     91.5  95.0 3.5    0.40     -        -
BV17-60 13.0  17.5 4.5    2.97*    14.03    2.56
BV17-61 81.0  88.0 7.0    0.47     -        -
BV17-62 41.0  42.0 1.0    0.61     -        -
And     92.0  99.0 7.0    0.10     -        -
//et

Length represents the apparent thickness of the mineralization and
should not be considered as the true width *Fire Assay by Screen
Metallic  weighted average of the coarse and fine fractions of the
Screen Metallic analysis

Samples from this year's program have exhibited a nugget effect in
the gold mineralization. Therefore, all samples from this program with
fire assay results greater than 1 g/t gold have been further analysed
by screen metallics to determine the amount of gold in the coarse
fraction (greater than 106 microns) and the amount of gold in the fine
fraction (less than 106 microns).

Drill holes BV17-58 and 62 were follow-up drill holes to RC hole
BV16-54 which intersected 1.58 g/t gold over 39.6 m including 7.73 g/t
gold over 6.1 m.  BV17-58 and 62 both ended in minimally anomalous gold
zones, suggesting that mineralization remains open and may continue at
depth. Drill hole BV17-58 intersected 1.5m wide interval of quartz
biotite schist with moderate to strong silica alteration associated
with multiple 0.5-4.0 centimetre wide cross-cutting quartz veins.
Disseminated pyrite was observed throughout the interval while stibnite
was observed in association with the cross-cutting quartz veins.
Drill hole BV17-60 and 61 were follow-up drill holes to RC hole
BV15-40 which intersected 15.00 g/t gold over 3.1 m including 27.90 g/t
gold over 1.5 m. BV17-60 intersected a 4.5 m wide interval of quartz
biotite schist intruded by white massive quartz veining with
disseminated pyrite. This intercept exhibited a nugget effect which
resulted in 14.03 g/t gold found in the coarse fraction during a screen
metallic analysis
All four holes have azimuths that vary from 070 to 080 degrees
with dips of -45 to -55 degrees.  Results from the remaining fives
holes, including three holes that followed-up on BV15-31 which
intercepted 3.21 g/t gold over 29 m including 7.23 g/t gold over 12.2
m, are still pending.
All samples were submitted to SGS Minerals Services in Burnaby, BC
for sample preparation by crushing to 75% less than 2 millimetres,
creation of a 250 g split, and then pulverizing to 85% passing 75
microns.  Sample pulps were submitted for a 52 element analysis using
an aqua regia digest and ICP-AES and ICPMS analysis (GE-ICM14B) and for
gold analysis with a 30 g fire assay and AAS finish (code GE-FAA313).
Samples resulting in greater than 1 g/t of gold were then re-submitted
for analysis by screen metallics. A 1,000 g sample was taken from the
reject, crushed to 2 mm and split. A representative sample of
approximately 100 g was taken.  This sample was pulverized and screened
to 106 microns. The plus 106 micron fraction was submitted for fire
assay, the minus fraction was split and two 30 g aliquots were
submitted for fire assay.  Final assays were weight ratioed back to the
representative sample weight (code FAS51K).  Control samples
(accredited gold standards and blanks) were inserted into the sample
sequence on a regular basis to monitor precision of results.  No QAQC
concerns were identified.
About Independence
Independence Gold Corp. (TSX.V:IGO) is a mineral exploration
company listed on the TSX Venture Exchange.  With a portfolio of
projects in the Yukon and the 3Ts Project in British Columbia, the
Companys holdings range from early-stage grassroots exploration to
advanced-stage resource expansion.  For additional information, visit
the Company's website www.ingold.ca.
Kendra Johnston, P.Geo., the Companys Qualified Person as defined
by National Instrument 43-101 for the White Gold District projects, has
reviewed the technical information in this news release.

ON BEHALF OF THE BOARD of Independence Gold Corp.

"Michael McPhie"

Interim Chairman, CEO and Director

For more information, contact:



Kendra Johnston, Interim President
T: 604-687-3959
E: kjohnston@ingold.ca
W: www.ingold.ca

Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.

All statements in this press release, other than statements of historical
fact, are "forward-looking information" with respect to Independence within
the meaning of applicable securities laws, including statements with
respect to the Companys planned drilling and exploration activities. The
Company provides forward-looking statements for the purpose of conveying
information about current expectations and plans relating to the future and
readers are cautioned that such statements may not be appropriate for other
purposes. By its nature, this information is subject to inherent risks and
uncertainties that may be general or specific and which give rise to the
possibility that expectations, forecasts, predictions, projections or
conclusions will not prove to be accurate, that assumptions may not be
correct and that objectives, strategic goals and priorities will not be
achieved. These risks and uncertainties include but are not limited to
those identified and reported in Independences public filings under
Independence Gold Corp.s SEDAR profile at www.sedar.com.  Although
Independence has attempted to identify important factors that could cause
actual actions, events or results to differ materially from those described
in forward-looking information, there may be other factors that cause
actions, events or results not to be as anticipated, estimated or intended.
There can be no assurance that such information will prove to be accurate
as actual results and future events could differ materially from those
anticipated in such statements.  Independence disclaims any intention or
obligation to update or revise any forward-looking information, whether as
a result of new information, future events or otherwise unless required by
law.
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1731900047TS11731901434-07041420171116