Source	Marketwire
Date	11/14/2017
Time	05:01:01 AM

Company	 STRIKEPOINT GOLD INC.
Title	StrikePoint Gold Inc. Releases Results from PDM Property and Discovery of 
'Seven Wonders Trend', a New Regional-Scale Structural Corridor





    CDNX Symbol: SKP











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: StrikePoint Gold Inc.

TSX VENTURE SYMBOL: SKP
OTCQB SYMBOL: STKXF

November 14, 2017

StrikePoint Gold Inc. Releases Results from PDM Property and Discovery of 
'Seven Wonders Trend', a New Regional-Scale Structural Corridor


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Nov. 14, 2017) - StrikePoint Gold 
Inc. (TSX VENTURE:SKP)(OTCQB:STKXF) is pleased to provide surface results from 
its PDM Property in the Yukon Territory, and its implications in a new 
regional-scale structural trend that links the PDM, Golden-Oly and Nordic 
properties.

Highlights

/T/

--  Surface grab samples at PDM returned grades of up to 9.8g/t gold, 2.8%
copper and 245g/t silver.
--  Samples collected from area of sheeted veins within intrusive material
with visible copper mineralization, including native copper.
--  Sheeted veins observed occurring throughout an area of 350m by 350m,
with a maximum density of 30 veins over a 10m natural exposure
--  Geological observations at PDM tie in to an overall structural trend
that stretches for 78km and incorporates the Golden-Oly and Nordic
properties, termed the "Seven Wonders Trend".
--  New model will help focus future targeting within a large project area.

/T/

Strikepoint Gold was active on the project between August 11th and August 19th 
2017. Extensive mapping and surface sampling focused in the center of the 
property around the Spearhead showing, identified by the Yukon Geological 
Survey. A total of 159 grab samples were collected from the area, mainly from 
obviously mineralized zones, but also from further out to gather additional 
geochemical data.

The mineralogy observed in the field was primarily copper-based, including 
chalcopyrite, malachite, bornite, chrysocolla and native copper, along with 
other sulphides such as pyrite, arsenopyrite and pyrhottite. These mineralized 
samples returned from trace to 2.8% copper (with 15% of all surface samples 
collected returning greater than 0.2% copper), and from trace to 9.8g/t gold 
(with 10% of all surface samples returning greater than 0.5g/t gold). Silver 
was also found in samples, ranging from trace to 245g/t, with 13% of all 
samples returning grades more than 20g/t silver).

Geologists on site focused on an area of sheeted veins within a granodioritic 
stock that had densities up to 30 veins over a 10m exposure oriented between 50 
to 60 degrees. The veins ranged from the millimeter to centimeter thickness and 
contained a variety of sulphides with quartz. The intrusive host rock also 
contains additional sulphide mineralization although at a lower rate of 
occurrence than within the veins.

The PDM property has had a history of exploration going back to 1967, although 
most of this has been basic soils and mapping with little consistency. 
Strategic Metals held the property between 2007 and 2008 and undertook a 
diamond drilling program, but it appears that each of the three holes missed 
the target area (see maps). The current land package is also more extensive 
than held in the past, so the additional data collected across a larger area 
has assisted in a broader understanding of the potential.

Mapping on the property shows that the veins are regularly orientated, at 
around 58 degrees (roughly northeast to southwest).

The "Seven Wonders" Trend

Post-season compilation of data has highlighted the existence of a structural 
trend that passes through PDM, Golden-Oly and the Nordic properties, for a 
total of 78km by 16km, and helps to explain certain mineralized features 
observed during the 2017 program.

These features fall within a model known as a 'Strain Ellipse' which shows how 
an area will deform when compressed through a regional event such as the 
accretional formation of the western coast of North America. This model is well 
understood, demonstrable and therefore predictable.

During compression of an area, the rocks are put under pressure forming a 
variety of faults, folds and other structures, some of which can become traps 
and fluid conduits. This model is showing the intrusions observed across the 
three properties have filled anticlinal folds within the sedimentary rocks, and 
then sympathetic off-shooting structures, known as Riedel Shears, have allowed 
mineralizing fluids to pass through them. These manifest as the sheeted veins 
observed at the Babylon and Colossus targets, the latter of which returned 
assays to 10.65g/t gold and 364g/t silver (refer to press release dated 10th 
October 2017).

The identification of the Seven Wonders Trend will help with future targeting, 
including any drilling, on the property, as only certain structures that 
develop will also promote fluid flow and therefore mineralization. This is a 
key finding for the 2017 season as it will help focus work across a collection 
of large land packages and ensure exploration funds are spent the most wisely.

Shawn Khunkhun, CEO Strikepoint, says "This is another major step forwards by 
the Strikepoint team on this newly acquired portfolio. The discovery of 
mineralization at PDM is significant, but being able to tie this in to a larger 
geological model that covers additional company properties confirms our view 
that this area warrants further systematic exploration."

QA/QC

The Company maintains a rigorous QA/QC program with respect to the preparation, 
shipping, analysis and checking of all samples and data from the properties. 
Quality control for field sampling and drill samples at the Company's projects 
covers the complete chain of custody of samples, including sample handling 
procedures and analytical-related work, plus the insertion of standard and 
blank materials. The QA/QC program also includes data verification procedures. 
ALS Laboratories in Vancouver, Canada (ISO 17025:2005 accreditation) assayed 
all grab samples from the current field program using fire assay and ICP Mass 
Spectroscopy methods. Drill samples were processed by Bureau Veritas Labs in 
Vancouver, Canada (ISO9001:2008 accreditation).

The technical information contained in this news release has been approved by 
Andy Randell, P. Geo., Vice President, Exploration of StrikePoint Gold. Mr. 
Randell is a qualified person as defined in NI 43-101.

For further information, please review the Corporate Presentation on the 
StrikePoint Gold Inc. website for a more detailed, comprehensive review of the 
2017 exploration program: 
http://www.strikepointgold.com/images/Yukon-Properties-Presentation.pdf

ON BEHALF OF THE BOARD of STRIKEPOINT GOLD INC.

Shawn Khunkhun CEO and Director

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

To view the maps associated with this release, please visit the following links:

http://media3.marketwire.com/docs/1104748_map1.JPG

http://media3.marketwire.com/docs/1104748_map2.JPG

http://media3.marketwire.com/docs/1104748_map3.JPG

http://media3.marketwire.com/docs/1104748_map4.JPG

http://media3.marketwire.com/docs/1104748_map5.JPG

- 30 -

CONTACT INFO:

Shawn Khunkhun
604-602-1440
sk@strikepointgold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=600464451


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: StrikePoint Gold Inc.

TSX VENTURE SYMBOL: SKP
OTCQB SYMBOL: STKXF

November 14, 2017

StrikePoint Gold Inc. Releases Results from PDM Property and Discovery of 
'Seven Wonders Trend', a New Regional-Scale Structural Corridor


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Nov. 14, 2017) - StrikePoint Gold 
Inc. (TSX VENTURE:SKP)(OTCQB:STKXF) is pleased to provide surface results from 
its PDM Property in the Yukon Territory, and its implications in a new 
regional-scale structural trend that links the PDM, Golden-Oly and Nordic 
properties.

Highlights

/T/

--  Surface grab samples at PDM returned grades of up to 9.8g/t gold, 2.8%
copper and 245g/t silver.
--  Samples collected from area of sheeted veins within intrusive material
with visible copper mineralization, including native copper.
--  Sheeted veins observed occurring throughout an area of 350m by 350m,
with a maximum density of 30 veins over a 10m natural exposure
--  Geological observations at PDM tie in to an overall structural trend
that stretches for 78km and incorporates the Golden-Oly and Nordic
properties, termed the "Seven Wonders Trend".
--  New model will help focus future targeting within a large project area.

/T/

Strikepoint Gold was active on the project between August 11th and August 19th 
2017. Extensive mapping and surface sampling focused in the center of the 
property around the Spearhead showing, identified by the Yukon Geological 
Survey. A total of 159 grab samples were collected from the area, mainly from 
obviously mineralized zones, but also from further out to gather additional 
geochemical data.

The mineralogy observed in the field was primarily copper-based, including 
chalcopyrite, malachite, bornite, chrysocolla and native copper, along with 
other sulphides such as pyrite, arsenopyrite and pyrhottite. These mineralized 
samples returned from trace to 2.8% copper (with 15% of all surface samples 
collected returning greater than 0.2% copper), and from trace to 9.8g/t gold 
(with 10% of all surface samples returning greater than 0.5g/t gold). Silver 
was also found in samples, ranging from trace to 245g/t, with 13% of all 
samples returning grades more than 20g/t silver).

Geologists on site focused on an area of sheeted veins within a granodioritic 
stock that had densities up to 30 veins over a 10m exposure oriented between 50 
to 60 degrees. The veins ranged from the millimeter to centimeter thickness and 
contained a variety of sulphides with quartz. The intrusive host rock also 
contains additional sulphide mineralization although at a lower rate of 
occurrence than within the veins.

The PDM property has had a history of exploration going back to 1967, although 
most of this has been basic soils and mapping with little consistency. 
Strategic Metals held the property between 2007 and 2008 and undertook a 
diamond drilling program, but it appears that each of the three holes missed 
the target area (see maps). The current land package is also more extensive 
than held in the past, so the additional data collected across a larger area 
has assisted in a broader understanding of the potential.

Mapping on the property shows that the veins are regularly orientated, at 
around 58 degrees (roughly northeast to southwest).

The "Seven Wonders" Trend

Post-season compilation of data has highlighted the existence of a structural 
trend that passes through PDM, Golden-Oly and the Nordic properties, for a 
total of 78km by 16km, and helps to explain certain mineralized features 
observed during the 2017 program.

These features fall within a model known as a 'Strain Ellipse' which shows how 
an area will deform when compressed through a regional event such as the 
accretional formation of the western coast of North America. This model is well 
understood, demonstrable and therefore predictable.

During compression of an area, the rocks are put under pressure forming a 
variety of faults, folds and other structures, some of which can become traps 
and fluid conduits. This model is showing the intrusions observed across the 
three properties have filled anticlinal folds within the sedimentary rocks, and 
then sympathetic off-shooting structures, known as Riedel Shears, have allowed 
mineralizing fluids to pass through them. These manifest as the sheeted veins 
observed at the Babylon and Colossus targets, the latter of which returned 
assays to 10.65g/t gold and 364g/t silver (refer to press release dated 10th 
October 2017).

The identification of the Seven Wonders Trend will help with future targeting, 
including any drilling, on the property, as only certain structures that 
develop will also promote fluid flow and therefore mineralization. This is a 
key finding for the 2017 season as it will help focus work across a collection 
of large land packages and ensure exploration funds are spent the most wisely.

Shawn Khunkhun, CEO Strikepoint, says "This is another major step forwards by 
the Strikepoint team on this newly acquired portfolio. The discovery of 
mineralization at PDM is significant, but being able to tie this in to a larger 
geological model that covers additional company properties confirms our view 
that this area warrants further systematic exploration."

QA/QC

The Company maintains a rigorous QA/QC program with respect to the preparation, 
shipping, analysis and checking of all samples and data from the properties. 
Quality control for field sampling and drill samples at the Company's projects 
covers the complete chain of custody of samples, including sample handling 
procedures and analytical-related work, plus the insertion of standard and 
blank materials. The QA/QC program also includes data verification procedures. 
ALS Laboratories in Vancouver, Canada (ISO 17025:2005 accreditation) assayed 
all grab samples from the current field program using fire assay and ICP Mass 
Spectroscopy methods. Drill samples were processed by Bureau Veritas Labs in 
Vancouver, Canada (ISO9001:2008 accreditation).

The technical information contained in this news release has been approved by 
Andy Randell, P. Geo., Vice President, Exploration of StrikePoint Gold. Mr. 
Randell is a qualified person as defined in NI 43-101.

For further information, please review the Corporate Presentation on the 
StrikePoint Gold Inc. website for a more detailed, comprehensive review of the 
2017 exploration program: 
http://www.strikepointgold.com/images/Yukon-Properties-Presentation.pdf

ON BEHALF OF THE BOARD of STRIKEPOINT GOLD INC.

Shawn Khunkhun CEO and Director

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

To view the maps associated with this release, please visit the following links:

http://media3.marketwire.com/docs/1104748_map1.JPG

http://media3.marketwire.com/docs/1104748_map2.JPG

http://media3.marketwire.com/docs/1104748_map3.JPG

http://media3.marketwire.com/docs/1104748_map4.JPG

http://media3.marketwire.com/docs/1104748_map5.JPG

- 30 -

CONTACT INFO:

Shawn Khunkhun
604-602-1440
sk@strikepointgold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=600464451