Source	MARKET NEWS
Date	11/14/2017
Time	10:31:23 AM

Company	 Taranis Resources Inc.
Title	Extends 
Gold Pit at Depth, Samples 2.04 m of Bon





    CDNX Symbol: TRO











Press Release





TARANIS RESOURCES INC.  ("TRO-V")
- Extends Gold Pit at Depth, Samples 2.04 m of Bonanza-Grade
- Material 26.6 g/t Gold, 1,246 g/t Silver, 3.1% Lead, 4.3% Zinc
- & 0.55% Copper

Taranis Resources Inc. ("Taranis") is pleased to update
exploration activity related to its 100%-owned Thor mine (MX-5-602).




Taranis has received assay results from a zone located 700m
southeast of the high-grade SIF gold zone where mining activity was
initiated at Thor this summer. Gold Pit channel sampling was undertaken
after Taranis further excavated the zone at depth in August of 2017,
and extended the highest-grade mineral occurrence known on the Thor
project. Mechanical excavation made another important model-building
discovery at Thor in 2017, and this will be released in a subsequent
news release.




2017 Gold Pit Excavation




Contrary to what was previously thought about the Gold Pit Area,
the continued excavation of the zone at depth showed that the plunge of
the mineralization is steeply to the southeast. It was formerly thought
that the mineralization plunged shallowly to the northwest.




A channel sample across the zone at the bottom of the 2017 trench
returned the following results, and a photograph of the outcrop showing
the channels sample locations has been posted on
www.taranisresources.com




From (m) To (m) True Thickness (m) Gold (g/t) Silver (g/t) Lead
(%) Zinc (%) Copper (%) 1.53 3.57 2.04 26.6 1,245.7 3.08 4.32 0.55

* Includes 0.64 m of 72.81 g/t Au, 1,716 g/t Ag, 3.6 % Pb, 6.0 %
Zn, 0.78% Cu & 0.42% Sb



Sampling undertaken in 2015 at the top of the currently exposed
outcrop (January 14, 2015) reported similar, but lower-grade results.
These results are duplicated here for the sake of comparison, but were
all located above the 2017 sampling.

Table is available at
https://www.jjgmining.com/2017-news-releases.html



Geological mapping of the outcrop appears to show that the zone is
widening at depth, and the high-grade gold and silver is moving onto a
structural contact under a quartz-rich zone into the Sharon Creek
Formation.




Comparison and Implications for Gold Pit Zone and SIF /
SIF-Extension Zones




The Gold Pit Zone occurs about 700 m southeast of the newly
discovered SIF-Extension zone that was bulk sampled in 2017, and
recently yielded high-grade gold including 28.79 g/t gold over 3.72
meters true thickness. SIF Extension is primarily a coarse-gold in
quartz deposit, while high-grade gold, silver and base metals are
hosted in the conventional sulphide occurrence at Gold Pit.




The mineralogy of the two zones differs considerably, but a
coherent picture is starting to form that may indicate that the zones
are connected. Both zones occur west of the known Thor deposit in a
complex area of faulting within the Thor Anticline, and both have a
unique dip to the southwest. All other known areas of mineralization at
Thor dip moderately to the northeast and return lower-grade gold
assays. Also, both areas of high-grade gold mineralization lie directly
on the contact between the underlying Sharon Creek formation and the
overlying Broadview Formation. This suggests that the high-grade gold
is likely stratiform in nature, and has been subjected to
remobilization along the contact by folding and faulting. What is known
is that this receptive contact connects the two areas separated by
700m, and it is possible that the gold mineralization is contiguous.
Further exploration is necessary to prove this concept.




John Gardiner, President and CEO remarks "Grades and a very unique
metal content like those seen at Gold Pit are approaching what defined
the unique Eskay Creek Mine in British Columbia that was mined by
Barrick Gold from 1993-2008. Eskay Creek also had a very small
footprint (1.5 M tonnes), and careful exploration is required to define
these types of zones. Eskay Creek produced over 3 M Oz. of gold
(grading 48.4g/t Au) and 160 M Oz. of silver (grading 2,221g/t Ag),
making it one of the highest-grade mines in Canada. One of the common
threads between Thor and Eskay Creek apart from the metal grades is the
volcanogenic massive sulphide model that has been advocated for both
deposits. While the extent of Gold Pit's exploration is in its infancy,
we think the potential to extend this bonanza-grade area over distance
is very real".




Quality Control and Analytical Procedures




Samples were analyzed by MS-Analytical in Vancouver, Canada. Fire
Assay was completed on a 30g sample for gold content and the remaining
analytical data was completed using ICP analytical methods. Silver
content over 100 g/t was determined using gravimetric methods.




All sampling and gold determinations are subject to a rigorous
quality control program that includes the placement of standards and
blanks a minimum of every tenth sample in addition to a rigorous
internal control instituted by MS-Analytical.




Qualified Person - Exploration activities at Thor were overseen by
John Gardiner (P. Geol.) who is a Qualified Person under the meaning of
Canadian National Instrument 43-101.

About Taranis Resources Inc.




Taranis is an exploration and mining company focused on the
development of its 100%-owned Thor project in southeast British
Columbia. In 2017, Taranis undertook a fully permitted mining operation
on the property aimed at recovering gold and gaining a better
understanding of the newly discovered gold zones at Thor. Taranis is
pursuing two parallel and distinct strategies at Thor: one focused on
continuing to mine the deposit in a series of three steps, and the
other is the continued growth and expansion of the existing deposit.
Please visit our website at www.taranisresources.com for more
information.




Taranis currently has 55,951,716 shares issued and outstanding
(63,376,716 shares on a fully-diluted basis).




TARANIS RESOURCES INC.

Per:    John J. Gardiner (P. Geol.),

President and CEO

For further information contact:




John J. Gardiner

14247 West Iliff Avenue

Lakewood, Colorado

Phone: (303) 716-5922

Cell: (720) 209-3049

johnjgardiner@earthlink.net

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
NEWS RELEASE.




This News Release may contain forward looking statements based on
assumptions and judgments of management regarding future events or
results that may prove to be inaccurate as a result of factors beyond
its control, and actual results may differ materially from expected
results.
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1731700045TS11731702271-10300820171114