Source	MARKET NEWS
Date	11/15/2017
Time	06:22:28 AM

Company	 Triumph Gold Corp.
Title	Discovery of 
High Grade Gold in Least Explored P





    CDNX Symbol: TIG











Press Release





TRIUMPH GOLD CORP ("TIG-V;NFRGF-0")
- Discovery of High-Grade Gold in Least-Explored Portion
- of the Revenue

Triumph Gold Corp., ("Triumph Gold" or the "Company") is pleased
to announce that exploration drilling in an underexplored portion of
the Revenue soil anomaly intersected high-grade gold mineralization in
granite south of the Revenue diatreme.  Highlights from diamond drill
hole RVD17-14 include:

//st

* Visible gold over a 5-metre interval (129 - 134 m).
* Contained within a 7-metre interval (129 - 136 m) of gold-silver-copper
mineralization with a length*** weighted grade of 15.0 grams/tonne (g/t)
gold (see below).
* Including a 1-metre interval (129 - 130 m), re-assayed three times,
grading between 45.0 and 81.3 g/t gold.
* The drill hole was collared in the immediate catchment of a renowned
placer creek (Revenue Creek), and the mineral association, coarse gold
with bismuthinite, is the same as the placer gold.

//et

RVD17-14 (Table 1) was drilled within a 1.2 X 0.5 kilometre
multi-element, gold-rich, soil anomaly on a broad ridge that separates
Whirlwind Pup and Revenue Creeks on the southern side of the Revenue
diatreme. It is in the immediate catchment of the Revenue Creek placer
gold deposit, renowned for having had one of the most gold-rich
channels in the Dawson Range. Historical exploration within the anomaly
documented two gold showings, suggesting that the entire area is
prospective for high-grade lode gold, and may be the source for much of
the abundant placer gold found in Revenue Creek:

//st

* the Klaus Zone which is immediately above the historical (pre-placer
mining) confluence of Whirlwind Pup and Revenue Creek; and
* the Guder Zone, which is approximately 400 metres past the confluence, up
the ridge to the south.

//et

Historical assay results for the two zones are noted below and in
Table 3.

RVD17-14, the first modern drill hole in the area, was collared in
the Guder Zone, 200 metres away from any historical trenching or
drilling, within an outstanding and previously untested portion of the
gold-in-soil anomaly, which includes four high grade samples (3.37 g/t,
2.26 g/t, 0.83 g/t and 0.88 g/t).  The drill hole intersected a
seven-metre-long interval (129 - 134 m) of strong gold-silver-copper
mineralization with gold disseminated within intergrown
pyrite-arsenopyrite-chalcopyrite-bismuthinite and carbonate veins. The
interval includes a 5-metre section with visible gold.

The tenor of gold mineralization in RVD17-14 is high as confirmed
by repeated assay results, however, the results indicate a pronounced
nugget effect.  To reduce the nugget effect Table 2 includes the
averaged results from repeat fire assays (with gravimetric finishes for
Au)10 g/t)  See the bottom of the news release for a table of all gold
results from the high-grade interval.

For location maps and photographs of visible gold in core see
Triumph Gold Corp.'s website
at:http://www.triumphgoldcorp.com/projects/freegold-mountain/revenue-deposi
t/maps/

Table 1: Location and Orientation of 2017 Diamond Drill Holes
Testing the Guder Zone

//st

Hole #     Easting**   Northing**   Azimuth   Inclination   Depth (m)

RVD17-14   382201      6913044      000       -50           341.38

RVD17-15   382201      6913044      000       -60           245.16

//et

Table 2: Results from high-grade gold intercept in RVD17-14

//st

From (m)             To (m)   Length (m)***   Au (g/t)   Ag (g/t)   Cu (%)

129.00               130.00   1.00            63.67      21.4       0.006

130.00               130.88   0.88            2.85       0.6        0.002

130.88               132.00   1.12            0.92       2.8        0.204

132.00               134.00   2.00            5.03       6.1        0.067

134.00               136.00   2.00            2.74       6.6        0.208

Length Weighted Average over 7m               15.04      7.2        0.113

//et

Historical Exploration in the Vicinity of RVD17-14

The 1.2 X 0.5 km soil anomaly between Whirlwind Pup and Revenue
Creek has seen less drilling that any other area near the Revenue
diatreme. Limited historical exploration documented significant
concentrations of gold in the Klaus and Guder zones (Main and Duke
1987), including:

//st

* trench samples in the Klaus Zone grading up to 32.98 g/t Au over 20 cm;
14.3 g/t over 1 m, and 3.67 g/t over 1 m;
* trench samples in the Guder Zone grading up to 20.24 g/t Au over 6.1 m;
and
* high-grade gold in drill intersections from the Guder Zone (Table 3).

//et

Table 3: Historical drill intersections in the Guder Zone

//st

Hole #      From      To (m)   Length***     Au (g/t)   Ag        Cu (%)
(m)                (m)                      (g/t)

GRS84-09    51.82     53.34    1.52          24.858     4.3       Not
tested

Including   51.82     52.73    0.91          39.086     6.2       Not
tested

GRD68-05    80.16     81.38    1.22          11.657     69.3      6.800

GRD69-01    38.22     39.60    1.38          5.486      37.03     1.680

//et

Other Notable Intersections in RVD17-14

In addition to the high-grade gold intersection in RVD17-14 there
were also two other notable mineralized intervals (Table 4):

//st

* 29.79 metres (185.00 - 214.79m) of 0.46 g/t AuEq* in rocks with polyphase
porphyry veining and potassic alteration at the contact between granite
country rock and the Revenue diatreme.
* 6 metres (331.00 - 337.00 m) of 0.73 g/t AuEq* in sulfide-matrix
hydrothermal breccia within the Revenue diatreme.

//et

The 29.79 metres of porphyry mineralization on the margin of the
diatreme add to the body of evidence (see PR17-12, PR17-13) that show a
broad, at least 2.85 km long, mineralized porphyry at Revenue, which is
cored, and cross-cut, by the Revenue diatreme.

Table 4: Full table of Significant Results - Guder Zone Diamond
Drilling 2017

Table is available at
http://www.triumphgoldcorp.com/triumph-gold-announces-discovery-of-high-gra
de-gold-in-least-explored-portion-of-the-revenue-deposit-including-a-7-metr
e-interval-grading-15-0-gramstonne-gold/



//st

Note: The average of tests 1 and 2 are calculated by first averaging test
1 FA1 and FA2, and then averaging that result with test 2.

//et

Methods and Qualified Person

Drill core samples ranged between 1 and 2 meters length and were
cut at Triumph's core logging facility on the Freegold Mountain
Property.  The samples were analyzed by ALS Global of North Vancouver,
British Columbia. They were prepared for analysis according to ALS
method PREP35: each sample was crushed to 70% passing 2mm and a 250g
split was pulverized to better than 95% passing 106 micron mesh.  Gold
was tested by fire assay with atomic absorption finish on a 30g nominal
sample (method Au-AA23), and samples that tested over 10 g/t Au were
retested using fire assay with a gravimetric finish (method Au-GRA21).
An additional 35 elements were tested by ICP-AES using an Aqua Regia
digestion (method ME-ICP41), over limit samples for copper were
retested using the same technique but with assay grade Aqua Regia
digestion and a higher range of detection (method ME-OG46).  Quality
assurance and control (QAQC) is maintained at the lab through rigorous
use of internal standards, blanks and duplicates.  An additional QAQC
program was administered by Triumph Gold: at minimum one in ten samples
submitted by Triumph Gold was a blank or certified reference standard.
QAQC samples that returned unacceptable values triggered
investigations into the results and reanalyses of the samples that were
tested in the batch with the failed QAQC sample. Where contamination or
analytical error were suspected the original data were discarded and
superseded by the results of the reanalyses.

The five samples reported in Table 5 were part of a 19-sample
batch that included six QAQC samples.  The samples were delivered by
Triumph Gold personnel directly to the ALS prep-lab in Whitehorse.  All
of the samples were tested by the methods discussed in the previous
paragraph and the five samples listed in Table 5 were also tested using
the gold screen metallic technique (method Au-SCR24).  For this
technique the sample was prepared by passing up to 1000g of pulp though
a 100 micron mesh and testing both the material that passed through the
screen ("-" fraction) and the material that remained on the screen ("+"
fraction). The entire + fraction was tested by fire assay with a
gravimetric finish, and the - fraction was homogenized and two 50g
splits were tested by fire assay with AAS finish and the results were
averaged.  The gold values of the + and - fractions were combined in a
weighted average to give the total gold content of the sample.

Some technical information contained in this release is historical
in nature and has been compiled from sources believed to be accurate.
This technical information has not been verified by Triumph Gold and
may in some instances be unverifiable.

The technical content of this news release has been reviewed and
approved by Tony Barresi, Ph.D., P.Geo., VP Exploration for the
company, and qualified person as defined by National Instrument 43-101.


Reference

Main, C.A., Duke, J.L., (1988): Revenue Trenching and Geophysics.
Assessment Report # 092131, Yukon Department of Energy, Mines and
Resources.

About Triumph Gold Corp.

Triumph Gold Corp. is a growth oriented Canadian-based precious
metals exploration and development company.  Triumph Gold Corp. is
focused on creating value through the advancement of the district scale
Freegold Mountain project in Yukon.  For maps and more information,
please visit our website www.triumphgoldcorp.com

On behalf of the Board of Directors

Signed "Paul Reynolds" Paul Reynolds, President & CEO

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release contains forward-looking information, which
involves known and unknown risks, uncertainties and other factors that
may cause actual events to differ materially from current expectation.
Important factors - including the availability of funds, the results of
financing efforts, the completion of due diligence and the results of
exploration activities - that could cause actual results to differ
materially from the Company's expectations are disclosed in the
Company's documents filed from time to time on SEDAR (see
www.sedar.com). Readers are cautioned not to place undue reliance on
these forward-looking statements, which speak only as of the date of
this press release.  The company disclaims any intention or obligation,
except to the extent required by law, to update or revise any
forward-looking statements, whether as a result of new information,
future events or otherwise.

For further information:  John Anderson, Chairman, Triumph Gold
Corp., (604) 218-7400, janderson@triumphgoldcorp.com; Nancy Massicotte,
IR Pro Communications Inc., (604)-507-3377,
nancy@irprocommunications.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1731800029TS11731801187-06220220171115