Source	MARKET NEWS
Date	11/15/2017
Time	07:58:29 AM

Company	 Genesis Metals Corp.
Title	Intersects 
Near Surface Interval of 24.33 Meters





    CDNX Symbol: GIS











Press Release





GENESIS METALS CORP ("GIS-V")
- Intersects Near-Surface Interval of 24.33 Meters True Width
- Averaging 1.94 g/t Gold at Chevrier Project

Genesis Metals Corp ("Genesis" or the "Company") is pleased to
announce the results from the remaining holes from the first phase of
drilling completed at the Chevrier gold project near Chibougamau,
Quebec. A second phase of 5,000 m of drilling is ongoing and expected
to continue until early December. It is anticipated that a total of
10,000 meters of core drilling in approximately 50 drill holes will be
completed during the 2017 program.
Assay results received to-date continue to demonstrate continuity
of near-surface gold mineralization within the Chevrier Main Zone.
Drilling by previous operators have traced continuous gold
mineralization for a minimum of 1,000 meters along strike.
The Company is targeting near-surface mineralization potentially
amenable to open pit mining, as well as deeper extensions potentially
amenable to bulk underground mining methods.
Highlights of Results (true widths)
Hole GM-17-15 returned 1.94 g/t Au over 24.33 m (starting at 49.50
m down hole) including 2.66 g/t Au over 16.53 m
Hole GM-17-20 returned 2.00 g/t Au over 20 m within a zone that
graded 0.93 g/t Au over 54.3 m starting at 91.5 m down hole
Hole GM-17-21 returned 1.13 g/t Au over 18.04 m including 2.21 g/t
Au over 6.01 m.
Hole GM-17-22 returned 1.06 g/t Au over 16.22 m starting at 19.15
m down hole.
Hole GM-17-16 returned 1.06 g/t Au over 14.22 m including: 3.50
g/t Au over 3.22 m.
Hole GM-17-17 returned 1.06 g/t Au over 7.63 m
Holes GM-17-23 to GM-17-25 were designed to evaluate an IP
response 150 m from and to the north of the Main Zone. These holes did
not return significant assays.
Hole GM-17-26 evaluated the source of an IP anomaly 225 m north of
the Main Zone and returned 0.5 g/t Au over 1.55 m
Previously released results from the Chevrier Main Zone include
(see NR GIS NR#16, October 3rd 2017): Hole GM17-09 returned 2.94 g/t
gold Au over a true width of 37.40 meters (starting at 74.60 m
downhole) including 14.01 g/t Au over a true width of 4.07 m.
Drill hole location plans from Main Zone are available at the
company's website
http://www.genesismetalscorp.com/projects/chevrier/exploration/.
The Company plans, subject to results of Phase 1 and 2 drill
programs, to complete additional drilling with the objective of
estimating a NI 43 -101 compliant resource in 2018.
The South Zone and up to ten other untested zones within the 120
square kilometer property remain to be evaluated. Additional mapping,
sampling and mechanical trenching will be completed on other targets on
the Property, with possible follow-up diamond drilling.
Discussion of Results
A summary of significant assay results is presented in the
following Table.
Assays presented continue to confirm the results from previous
drilling within the Main Zone The results allow the Company to refine
the geological model for the Main Zone
//st

SIGNIFICANT ASSAYS FOR CHEVRIER MAIN ZONE - PHASE 1 - 2017
HOLES          FROM          TO    LENGTH CORE  TRUE WIDTH  Au GRADE
(g/t)
GM-17-10                         No significant result
GM-17-11        224.35        233.9      9.55        5.62     0.5
Including  233.05   233.9      0.85         0.5     1.79
GM-17-12         85.5         93.2       7.7         2.47     0.66
Including   89.95   91.8       1.85        0.59     2.39
GM-17-13         94.1         130.8      36.7       19.19    0.52
146.3         205.5      59.2        31.52     0.5

GM-17-14        30.05         47.5       17.45        11.66    0.52
55.75         57.5        1.75        1.17     0.65

GM-17-15        49.5          92.5        43         24.33     1.94
Including   63.35   92.5      29.15        16.53     2.66
Including   63.35   73.2       9.85        5.57      3.02
Including   77.05   92.5      15.45        8.78      3.06
Including   81.15    89        7.85        4.46      4.6
GM-17-16          21          31.35     10.35        5.18      0.57
106.6       143       36.4        18.77      0.88

Including  112.15   139.7     27.55        14.22     1.06
Including   133.5   139.7      6.2         3.22      3.5
GM-17-17        186.1         211.6      25.5        15.37     0.65
Including   195.9  208.55     12.65        7.63      1.06
GM-17-18        273.1        278.35      5.25        2.23      0.73
GM-17-19                              No significant result
GM-17-20         91.5         186.4      94.9        54.3      0.93
Including    95     133.4      38.4        21.82     1.89
Including   96.15  131.35      35.2         20       2
Including   103.9   106.1      2.2         1.25      4.89
Including   125.4  131.35      5.95        3.39      3.8
GM-17-21         40.1         52.75     12.65        5.67      0.26
221.45         259.5     38.05       18.04      1.13

Including   231.8   244.5      12.7        6.01      2.21
GM-17-22        19.15         49.5      30.35        16.22     1.06
Including   19.15   43.6      24.45        13.05     1.23
Including   26.15   28.25      2.1         1.12      3.58
Including   40.05   43.6       3.55         1.9      3.29
GM-17-26              78.85   81.9       3.05        1.55      0.5
//et

Genesis anticipates the receipt of all assays from the current
program by January, 2018.

Quality Control and Quality Assurance
The Company maintains a rigorous QA/QC program with respect to the
preparation, shipping, analysis and checking of all samples and data
from the Property. Quality control for field sampling and drill samples
at the Company's projects covers the complete chain of custody of
samples, including sample handling procedures and analytical-related
work, plus the insertion of standard and blank materials. The QA/QC
program also includes data verification procedures. Actlabs in
Ancaster, Ontario, Canada (ISO 17025 certification) assayed all rock
and core samples from the current field program using fire assay and
atomic absorption finish for gold and gravimetric finish if gold grades
exceeded 5 g/t Au.

Mr. Andre Liboiron, P. Geo, Exploration Manager for the Company
and the Qualified Person as defined within National Instrument 43-101
for the Chevrier Project, has reviewed the contents of this news
release.

About Genesis Metals
The Company is focused on advancing the Chevrier Gold Project
located 35 km southwest of Chibougamau, Quebec. The Project is located
along the Fancamp Deformation Zone, 15 km northeast of the high-grade
Monster Lake gold discovery and 15 km northwest of the past producing
Joe Mann gold mine.
Genesis also owns 100% the 203 km2 October Gold project located in
the southern Swayze greenstone belt in Benton Township, Ontario. This
project is located 35 km northwest of IAMGold and Sumitomo Mining's
Cote Lake deposit and 50km southeast of Goldcorp's Borden gold deposit.


ON BEHALF OF THE BOARD

"Brian Groves"

Brian Groves
CEO and Director

"Jeff Sundar"

Jeff Sundar
President and Director

Suite 1500, 409 Granville Street, Vancouver, BC V6C 1T2
Telephone: 604-646-8356 Fax: 604-484-7155
Email: js@genesismetalscorp.com
Website: www.genesismetalscorp.com



Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.

Certain disclosure in this release, including statements regarding the
intended use of proceeds from the private placement, constitute
forward-looking information or statements (collectively, "forward-looking
statements") for the purpose of applicable securities laws. In making the
forward-looking statements, the Company has applied certain factors and
assumptions that are based on the Company's current beliefs as well as
assumptions made by and information currently available to the Company,
including that the Company is able to obtain any government or other
regulatory approvals required to complete the Company's planned exploration
and development activities, that the Company is able to procure personnel,
equipment and supplies required for its exploration and development
activities in sufficient quantities and on a timely basis and that actual
results of exploration activities are consistent with management's
expectations. Although the Company considers these assumptions to be
reasonable based on information currently available to it, they may prove
to be incorrect, and the forward-looking statements in this release are
subject to numerous risks, uncertainties and other factors that may cause
future results to differ materially from those expressed or implied in such
forward-looking statements. Such risk factors include, among others, that
the Company will be unable to obtain required regulatory approvals on a
timely basis or at all, that actual results of the Company's exploration
activities will be different than those expected by management and that the
Company will be unable to obtain or will experience delays in obtaining any
required government approvals or be unable to procure required equipment
and supplies in sufficient quantities and on a timely basis. Readers are
cautioned not to place undue reliance on forward-looking statements. The
Company does not intend, and expressly disclaims any intention or
obligation to, update or revise any forward-looking statements whether as a
result of new information, future events or otherwise, except as required
by law.
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1731800041TS11731801734-07575120171115