Source	MARKET NEWS
Date	11/15/2017
Time	08:13:30 AM

Company	 Orford Mining Corporation
Title	Multiple 
High grade Gold and Copper Intersection





    CDNX Symbol: ORM











Press Release





ORFORD MINING CORP ("ORM-V")
- Multiple High-grade Gold and Copper Intersections at the
- Esperance Zone on the Qiqavik Property

Orford Mining Corporation ("Orford") is pleased to announce that
it has received the base metal assay results that were outstanding from
the Summer 2017 drilling and prospecting program at its 100% controlled
Qiqavik Project in northern Quebec. These results show that high-grade
copper is associated with the gold mineralization intersected in
drilling at the Esperance West Zone and previously reported on October
26, 2017.

Highlights from the new results include:

//st

* 2.37 g/t Au and 2.19% Cu over 7.0m core length in QK-17-022,
including 5.58g/t Au and 3.06% Cu over 1.0m
* 1.58 g/t Au and 1.28% Cu over 7.1m core length in QK-17-021,
including 3.62 g/t Au and 2.04%Cu over 1.1m.

//et

David Christie, President and CEO of Orford, commented, "We are
very encouraged by these new results, which highlight the polymetallic
nature of the western portion of the Qiqavik trend. At current prices,
these new copper results more than double the gold equivalent grades of
the mineralization intersected in these holes at Esperance West,
yielding gold equivalents of up to 6.1g/t over 7m core length. These
results further support the tremendous potential of this new gold belt
located in a previously unexplored region of Canada."

Multi-element results from holes QK-17-017, -019, -020, -021,
-022, -028 and -029, and from 116 grab samples that were noted as
pending in Orford Mining's news release dated October 26, 2017 have
been received. A summary of significant new copper assays is presented
below. A table of the complete results can be accessed at Table 2. Note
that drill intervals reported in this news release are down-hole core
lengths as true thicknesses cannot be determined with available
information. Also note that grab samples are selective by nature and
values reported may not be representative of mineralized zones.

These new drilling results continue to support the subsurface
extent of the structures and the Au-Cu-Co mineralization discovered at
Esperance West.

Work completed during the 2017 program demonstrates that gold and
copper is associated with secondary splay structures located along the
district-scale Qiqavik Break Shear Zone, which extends the full 40 km
length of the Qiqavik Property. Geological data indicate that gold
mineralization at Qiqavik is structurally controlled and associated
with porphyry intrusions in places. Typically, in structurally
controlled gold deposits, the intensity of mineralization varies along
the length of the structures with ore shoots focused in zones of
dilation. Orford is currently analyzing airborne magnetic and field
mapping data collected during the Summer 2017 program to identify and
locate sites of dilation along structures that were active at the time
of gold mineralization in order to target significant gold
mineralization accumulations.

The Qiqavik Break is part of the Cape Smith Belt event which is of
Paleoproterozoic age (1.8-1.9 billion years). This geologic era is
marked by its significant metal endowment as illustrated by the
important gold districts that occur worldwide related to geological
events of Paleoproterozoic age. These include the Flin Flon-Snow Lake
Belt, the Ashanti Gold Fields of West Africa, the Tapajos-Parima Belt
of Brazil, and the Tanami Region in Australia.

Table 1: Highlights of new Cu results from 2017 Exploration
Drilling at Esperance West1

//st

Hole         From   To     Core     Au*    Cu %   Co %    Au       Cu
Length   g/t                   equiv.   equiv.
(m)                            g/t      %

QK-17-021   32     39.1   7.1      1.59   1.28   0.03    3.78     2.21

Including   33     34.1   1.1      3.62   2.04   0.02    7.12     4.15

And         45     46.5   1.5      4.65   0.15   0       4.91     2.86

And         62     63     1        1.58   0.14   0.01    1.82     1.06

QK-17-022   28     35     7        2.37   2.19   0.02    6.12     3.57

Including   29     30     1        5.21   2.67   0.01    9.79     5.71

And         33     34     1        5.58   3.06   0.02    10.83    6.32
including

And         39.5   40     0.5      4.26   0.26   0.02    4.71     2.75

And         41     42     1        2.31   0.09   0.01    2.46     1.44

And         59     60     1        4.75   0.10   0.06    4.92     2.87

And         62     63     1        0.94   0.33   0.01    1.51     0.88

And         84     85     1        1.07   0.04   0.06    1.14     0.66

QK-17-019   94     95     1        1.05   0.14   0.005   1.06     0.62

//et

//st

*   Au Results Previously Reported News Release Dated October 26, 2017.

1   Indicated lengths are reported as apparent thickness along the core
and do not represent true thickness of the mineralized intersections. True
thicknesses are unknown. Au equivalent and Cu equivalent values calculated
using a Au price of US$1,200/oz and a Cu price of US$3.00/lb. Drill hole
location and orientation details available in the 43-101 Technical Report
on the Qiqavik Property filed under Orford's profile on SEDAR and on
Orford's website

//et

Esperance

At Esperance, drilling has outlined two Au-Cu-Co sulphide-rich
mineralized zones, Esperance and Esperance West, that extend over a
known strike length of 300m and 650m respectively (Figure 2; see also
Orford Mining news release dated October 26, 2017). New copper results
in drilling from Esperance West include 2.37 g/t Au and 2.19% Cu over
7.0m core length in QK-17-022, including 5.58g/t Au and 3.06% Cu over
1.0m, and 1.58 g/t Au and 1.28% Cu over 7.1m core length in QK-17-021,
including 3.62 g/t Au and 2.04%Cu over 1.1m. Holes QK-17-021 and
QK-17-022 were drilled from the same set-up on the same section. The
intersection in QK-17-022 is approximately 20 m down-dip from the
intersection in QK-17-021.

The polymetallic mineralized trend continues West of Esperance
along the Qiqavik Shear Zone where the new Horizon discovery has
yielded 5.67 g/t Au and 0.38% Cu over 0.9m in a channel sample at a
distance of 1.8 km west of QK-17-021 and -022.

Qualified Person and Quality Assurance and Quality Control

The disclosure of scientific and technical information contained
in this news release has been approved by Alger St-Jean, P.Geo, Vice
President, Exploration of Orford, a Qualified Person under NI 43-101.

The work program at Qiqavik was supervised by Michelle Sciortino,
Senior Project Geologist who is responsible for all aspects of the
work, including the quality control/quality assurance program. On-site
personnel at the project log and weigh all samples prior to sealing and
shipping. Sample shipments are sealed and shipped to Techni-Lab,
Sainte-Germaine-Boule, Quebec. All gold assays reported were obtained
by either 350-g screen fire assay or standard 50-gram fire-assaying-AA
finish or gravimetric finish (method 1A2-5 and 1A3-50) at Techni-Lab,
Sainte-Germaine-Boule, Quebec. The 350-g screen assay method is
selected by the site geologist or the lab when samples contain coarse
gold or higher percentage of sulfide mineralization that may be
associated with gold relative to surrounding intervals. All samples are
also analyzed for multi-elements, including copper and silver, using a
four-acid method with an ICP-EOS and ICP-MS finish at Techi-labs
affiliated Actlabs in Ancaster, Ontario. Overlimits were analyzed by
peroxide fusion with ICP-EOS finish. Drill program design, Quality
Assurance/Quality Control ("QA/QC") and interpretation of results is
performed by qualified persons employing a QA/QC program consistent
with NI 43-101 and industry best practices. Standards and blanks are
inserted at a minimum of 10% and 5% for core and grab samples
respectively for QA/QC purposes in addition to those inserted by the
lab. A subset of samples has not yet been sent for a verification assay
at another lab.

Techni-Lab Laboratory, is a subsidiary of Act Labs, is accredited
(n. 707) by the Standards Council of Canada and found to comply with
the requirements of ISO/IEC 17025:2005 (CAN-P-4E) and CAN-P-1579.

About Orford Mining Corporation

Orford Mining is a mineral explorer focused on highly prospective
and underexplored areas of Northern Quebec and the Carolina Gold Belt
in United States. Orford's principal assets are the Qiqavik and West
Raglan projects comprising of a land package totaling over 70,000
hectares in the Cape Smith Belt of Northern Quebec and properties in
the U.S. Carolina Gold Belt. The Qiqavik Project hosts several new
high-grade gold discoveries along a mineralized trend in excess of 40
km. Orford's common shares trade on the TSX Venture Exchange under the
symbol ORM.

Cautionary Statement Concerning Forward-Looking Statements

Neither the TSXV nor its Regulation Services Provider (as that
term is defined in the policies of the TSXV) accepts responsibility for
the adequacy or accuracy of this release.

This news release contains "forward-looking information" including
without limitation statements relating to the liquidity and capital
resources of Orford and potential of one or more of the Qiqavik, West
Raglan, Jones-Keystone Loflin and Landrum-Faulkner exploration
properties.

Forward-looking statements involve known and unknown risks,
uncertainties and other factors which may cause the actual results,
performance or achievements of Orford to be materially different from
any future results, performance or achievements expressed or implied by
the forward-looking statements. Factors that could affect the outcome
include, among others: future prices and the supply of metals; the
results of drilling; inability to raise the money necessary to incur
the expenditures required to retain and advance the properties;
environmental liabilities (known and unknown); general business,
economic, competitive, political and social uncertainties; accidents,
labour disputes and other risks of the mining industry; political
instability, terrorism, insurrection or war; or delays in obtaining
governmental approvals, failure to obtain regulatory or shareholder
approvals. For a more detailed discussion of such risks and other
factors that could cause actual results to differ materially from those
expressed or implied by such forward-looking statements, refer to
Orford's filings with Canadian securities regulators available on SEDAR
at www.sedar.com.

Although Orford has attempted to identify important factors that
could cause actual actions, events or results to differ materially from
those described in forward-looking statements, there may be other
factors that cause actions, events or results to differ from those
anticipated, estimated or intended. Forward-looking statements
contained herein are made as of the date of this news release and
Orford disclaims any obligation to update any forward-looking
statements, whether as a result of new information, future events or
results or otherwise, except as required by applicable securities laws.


The TSXV has neither approved nor disapproved the contents of this
news release.

Contact Information:
David Christie, President and CEO, T: (647) 253-1144, www.orfordmining.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1731800044TS11731801802-08123820171115