Source	MARKET NEWS
Date	11/15/2017
Time	11:34:34 AM

Company	 Osisko Metals Incorporated
Title	Intersects 7.5 
Metres Assaying 13.4 % Zinc+lead





    CDNX Symbol: OM











Press Release





OSISKO METALS INC ("OM-V")
- Intersects 7.5 Metres Assaying 13.4 % Zinc+lead At The Gilmour
- South Project

Osisko Metals Incorporated (the "Company" or "Osisko Metals")
is pleased to announce initial results from its Gilmour South Project
located 35 km south west of Bathurst, New Brunswick. Drill hole
GS-00-22W1 intersected 11.31% Zn; 2.10% Pb; 0.16% Cu; 20.95g/t Ag and
0.21 g/t Au over 7.55 metres.

This drill hole provided insight into the massive
sulphide-bearing geological trends present in the Gilmour South area
and guided the design of subsequent stepout drilling described below.
This drill hole was a close- proximity wedge cut, up-dip from the
original drill hole GS-99-22 and was designed to confirm previously-
obtained massive sulphide grades for NI43-101 regulation compliance:

//st

Location  Angle /               Core
Length
DDH NB        Direction From  To    (m)   Zn %  Pb %  Cu % Ag    Au
Stereographic                                          g/t   g/t

GS-99-22W1**
2550547E, -76/ 091  592.8 600.4 7.55* 11.31 2.10  0.16 20.95 0.21
7591396N

Original                597.8 605.4 7.98  9.61  1.02  0.20 32.28 NA
GS-99-22

//et

//st

*True width of the intersection is estimated at 6.80 metres.

** Wedge cut from original drillhole; 194 metres is the length drilled
from wedge cut to end of hole (EOH).

//et

Drill hole GS-17-02 was drilled 59 metres to the south of
GS-99-22W1 where it extended the zone and intersected 12.0 metres of
massive sulphides containing sphalerite, galena and pyrite; assays are
pending.

Drill hole GS-17-03 was drilled 70 metres up-dip from
GS-99-22W1 and intersected stringer and disseminated sulphides at the
target horizon. Assays are pending.

Approximately 450 metres to the north, a close-proximity wedge
cut adjacent to historical drill hole GS-00-33 was drilled to sample
the sulphide mineralization. The sulfide intersection in this new hole,
GS-00-33W1, is similar to the original hole and assays are pending.
Drill hole GS-17-01 is in progress and will investigate the
continuation of the sulphide horizon approximately 50 metres to the
north of GS-00-33W1 where mineralization is open.

Jeff Hussey, President and CEO of Osisko Metals, commented:
"These are the first drill results from Gilmour South project as we
investigate the periphery of the deposit to potentially expand
resources. Our exploration team has acquired recent airborne
geophysical datasets and has combined them with historical data to
develop new interpretations and targets as we move forward."

The initial objective of the drill program is to increase and
upgrade historical resources to comply with NI43-101 regulations (see
news releases dated October 19, 2017). A key part of this effort will
be to investigate the potential for structural thickening of the
high-grade sulphide mineralization that is typically associated to the
major deposits in the Bathurst Mining Camp.

Mr. Robin Adair is the Qualified Person responsible for the
technical data reported in this news release, he is a Professional
Geologist registered in New Brunswick and is the President of Osisko
Metals Incorporated.

Quality Assurance / Quality Control

Osisko Metals adheres to a strict Quality Assurance and Quality
Control program with regard to core handling, sampling, transportation
of samples and lab analyses. Drill core samples from Osisko Metals New
Brunswick projects were securely transported to its core facility in
Bathurst where they were logged and sampled. Samples selected for assay
were shipped via secure transportation to Activation Laboratories
preparation facility in Fredericton, New Brunswick. Pulps were analyzed
at Activation Laboratories facility in Ancaster Ontario. Zinc, lead and
copper were analyzed by assay grade peroxide fusion (total digestion)
with ICP-AES finish. Silver was analyzed by gravimetric fire assay and
gold by fire assay-atomic absorption.

About Gilmour South

The Gilmour South project hosts the "Brunswick Horizon", and is
located 20km south of the former Brunswick No. 12 mine and 7 km south
of the former Brunswick No. 6 Mine. These mines produced approximately
150 million tonnes of +12% zinc equivalent. Brunswick No. 12 was the
largest underground zinc mine for nearly 50 years, processing 10,500
tonnes per day on average. Both mines occurred in structural corridors
that enhanced the thickness and grade of the sulphide horizon.

The Brunswick Horizon is present at Gilmour South over 1.4
kilometers and is characterized by sulphide mineralization, host-rock
types and alteration similar to the Brunswick Mines stratiform
zinc-lead sulphide mineralization otherwise known as the "Brunswick
Horizon". Mineralization has not been well-delineated and has been
investigated by relatively sparse historical drilling at approximately
200 metre centres.

About Osisko Metals

Osisko Metals is a Canadian exploration and development company
creating value in the base metal space with an emphasis on zinc. In
2017, the Company acquired over 63,000 hectares in the Bathurst Mining
Camp ("BMC"). The objective is to develop a multi-deposit asset base
that could feed a central concentrator. In parallel, Osisko Metals is
monitoring several base metal oriented peers for projects and
acquisition opportunities. In Quebec, the Company acquired 42,000
hectares that cover 12 grass-root zinc targets that will be selectively
advanced through exploration. Osisko Gold Royalties Ltd. (TSX/NYSE:OR)
and Osisko Mining Inc. (TSX:OSK) are significant shareholders of the
Company.

For further information on Osisko Metals, visit
www.osiskometals.com

Neither TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Cautionary Note Regarding Forward-Looking Information

This news release contains "forward-looking information" within
the meaning of applicable Canadian securities legislation based on
expectations, estimates and projections as at the date of this news
release. Forward-looking information involves risks, uncertainties and
other factors that could cause actual events, results, performance,
prospects and opportunities to differ materially from those expressed
or implied by such forward-looking information. Forward-looking
information in this news release includes, but is not limited to, the
use of proceeds of the Offering; the timing and ability of the
Corporation, if at all, to obtain final approval of the Offering from
the TSX Venture Exchange; an exemption being available under MI 61-101
and Policy 5.9 of the TSX Venture Exchange from the minority
shareholder approval and valuation requirements for each related party
transaction; objectives, goals or future plans; statements regarding
exploration results and exploration plans. Factors that could cause
actual results to differ materially from such forward-looking
information include, but are not limited to, capital and operating
costs varying significantly from estimates; the preliminary nature of
metallurgical test results; delays in obtaining or failures to obtain
required governmental, environmental or other project approvals;
uncertainties relating to the availability and costs of financing
needed in the future; changes in equity markets; inflation;
fluctuations in commodity prices; delays in the development of
projects; the other risks involved in the mineral exploration and
development industry; and those risks set out in the Corporation's
public documents filed on SEDAR at www.sedar.com. Although the
Corporation believes that the assumptions and factors used in preparing
the forward- looking information in this news release are reasonable,
undue reliance should not be placed on such information, which only
applies as of the date of this news release, and no assurance can be
given that such events will occur in the disclosed time frames or at
all. The Corporation disclaims any intention or obligation to update or
revise any forward-looking information, whether as a result of new
information, future events or otherwise, other than as required by law.


Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release. No stock exchange, securities commission or other
regulatory authority has approved or disapproved the information
contained herein.

Contact Information:

Jeff Hussey
President & CEO
Osisko Metals Incorporated
(514) 861-4441
info@osiskometals.com
www.osiskometals.com

Christina Lalli
Director, Investor Relations
Osisko Metals Incorporated
(514) 861-4441
info@osiskometals.com
www.osiskometals.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1731800055TS11731802389-11312820171115