Source	CANADA NEWSWIRE
Date	11/20/2017
Time	05:03:02 AM

Company	 Triumph Gold Corp.
Title	Triumph Gold Announces Definition of a 1.8 X 0.75 km Soil Anomaly along
Strike of the Tinta Au-Ag Deposit and Discovery of Gold Bearing Quartz
Veins in Six Trenches Over 700 metres Strike Length within the Anomaly





    CDNX Symbol: TIG











Press Release




" BC-TriumphGoldTintaAuAg   11-20 1835
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Triumph Gold Announces Definition of a 1.8 X 0.75 km Soil Anomaly along
Strike of the Tinta Au-Ag Deposit and Discovery of Gold Bearing Quartz
Veins in Six Trenches Over 700 metres Strike Length within the Anomaly@

TSX.V: TIGOTCMKTS: NFRGFFrankfurt: 8N61
VANCOUVER, Nov. 20, 2017 /CNW/ - Triumph Gold Corp., (TSX-V: TIG)
(OTCMKTS: NFRGF) ("Triumph Gold" or the "Company") is pleased to announce that
recent soil sampling has defined a 1.8 X 0.75 km multi-element (Au, Cu, Pb,
Zn, As, Bi, Sb) soil anomaly, extending the Tinta Au-Ag vein system to the
northwest. The anomaly is northwest-southeast trending, open to the northwest
and begins 500 metres northwest, along strike, of the Tinta Au-Ag-Cu-Pb-Zn
deposit, in an area tested by only one historical drill hole (see below). Six
of seven trenches dug over 700 metres strike length, within the anomaly,
uncovered multiple clay-altered or silicified zones up to 2.6 metres wide that
contain strongly weathered quartz-chalcedony-carbonate-sulphide vein networks.
Sulphide contents are highly variable due to surface weathering and boxwork
after leached sulphides are common. Where sulphides are preserved they include
up to 15% coarse pyrite and variable amounts of galena, sphalerite and
chalcopyrite. Highlights of exploration at Tinta include:
<<

--  A 1.8-km-long multi-element soil anomaly, open to the northwest, along
strike of the Tinta Au-Ag deposit has been defined.

--  The anomaly has a higher concentration of samples with elevated
pathfinder elements (As, Sb, Bi) than the area surrounding the Tinta
vein deposit and a similar concentration of samples with elevated gold,
but over an area twice the size.

--  Within the 1.8-km-long soil anomaly, a 700-metre-long section was tested
with seven trenches. Six exposed multiple clay-altered or silicified
zones with mineralized quartz-chalcedony-carbonate-sulphide vein
networks. Highlights of assay results include:
o 2.21 grams/tonne (g/t) Au and 11.3 g/t Ag over 1.5m in a chip sample from
Trench 3
o 0.666 g/t Au and 13.7 g/t Ag over 1.5m in a chip sample from Trench 3
o 1.9 g/t Au and 40.9 g/t Ag in a grab sample from Trench 4.
o 4.9 g/t Ag, 1.5% Zn and 0.4% Pb in a grab sample from Trench 4
o 0.793 g/t Au and 3.7 g/t Ag over 0.4m in a chip sample from Trench 5.
>>
Exploration in the vicinity of the Tinta vein deposit in 2016 comprised a
1.1 sq. km (414 sample) soil geochemistry grid and VLF-EM and magnetic
geophysical surveys covering 9.0 sq. km. These surveys defined a number of
coincident multi-element soil and geophysical anomalies, the most prominent of
which was along strike of the Tinta Au-Ag-Cu-Pb-Zn deposit (see PR17-04, Feb.
27 2017), which has an inferred resource of 2.16 million tonnes grading 1.89
g/t Au, 54.9 g/t Ag, 0.27% Cu, 0.99% Pb and 1.41% Zn (December 15, 2014).
Follow-up exploration in 2017 included:
<<

1. an expanded soil geochemistry grid with 993 samples collected over 8 sq.
km, and

2. 560 metres of excavator trenching within the coincident anomalies defined
by the 2016 survey.
>>
The 2017 soil grid expanded the length of the 2016 soil anomaly from 900
to 1,800 metres. In addition, the 2017 soil survey covered the area around the
Tinta vein to provide a better basis for comparison between geochemistry of
soils in the new anomaly and soils surrounding the existing deposit.
The 2017 trenches uncovered granite with numerous broad
hematite-epidote-chlorite-altered intervals, the same host rock and alteration
that surrounds productive veins in the Tinta deposit. Within these zones there
are multiple discrete strongly weathered, clay-altered or silicified zones up
to 2.6 metres wide that contain quartz-chalcedony-carbonate-sulphide vein
networks that appear to be hosted in faulted zones which are parallel to the
Tinta vein trend; similar zones are also observed in the Tinta deposit. The
trenches were mapped and sampled; a total of ninety-two samples were collected
including eighteen grab samples and seventy-three chip samples (collected over
107.2 metres). Table 1 contains significant results from the trench sampling
and Figure 1 below (or see Triumph Gold website) shows the locations of the
trenches and samples.
http://www.triumphgoldcorp.com/projects/freegold-mountain/tinta-hill-depo
sit/
Table 1: Significant assay results from trenching within the Tinta
Extension Soil Anomaly. These data represent highlights of 2017 trench
sampling that included 18 grab and 73 chip samples.
Trench  From                 To             Length             Sample  
Au             Ag          Cu           Pb            Zn
------  ----                ---             ------             ------  
---           ---          ---          ---          ---

(m)                (m)               (m)               Type  (ppm)         
(ppm)        (ppm)        (ppm)        (ppm)
---                ---               ---               ----  ----           
----        ----         ----          ----

TT17-01      16.00                18.00            2.00   CHIP                
0.177         36.9           31          234           139
-------      -----                -----            ----   ----                
-----         ----          ---          ---           ---


TT17-02        No Significant Assay Results
-------        ----------------------------


TT17-03      12.00                13.50            1.50   CHIP                
2.210         11.3          232          117           269
-------      -----                -----            ----   ----                
-----         ----          ---          ---           ---

TT17-03      74.00                                      GRAB                
0.759          7.1           69          246           504
-------      -----                                      ----                
-----          ---          ---          ---           ---

TT17-03      75.50                77.00            1.50   CHIP                
0.666         13.7          700          815           911
-------      -----                -----            ----   ----                
-----         ----          ---          ---           ---


TT17-04       2.70                                      GRAB                
1.900         40.9           99          910           199
-------       ----                                      ----                
-----         ----          ---          ---           ---

TT17-04       3.50                                      GRAB                
0.100         15.3         1785         1810          1760
-------       ----                                      ----                
-----         ----         ----         ----          ----


TT17-05      24.40                                      GRAB                
0.194          6.2           91          714           519
-------      -----                                      ----                
-----          ---          ---          ---           ---


TT17-06      21.50                                      GRAB                
0.400         25.5          229          451           201
-------      -----                                      ----                
-----         ----          ---          ---           ---

TT17-06      30.00                                      GRAB                
0.171         15.3           77           50            94
-------      -----                                      ----                
-----         ----          ---          ---           ---

TT17-06      71.50                72.50            1.00   CHIP                
0.022          1.1           16          734          1910
-------      -----                -----            ----   ----                
-----          ---          ---          ---          ----

TT17-06      73.00                                      GRAB                
0.068          4.9           97         4020         15050
-------      -----                                      ----                
-----          ---          ---         ----         -----


TT17-07      18.00                                      GRAB                
0.050          9.2         1045         1885          2500
-------      -----                                      ----                
-----          ---         ----         ----          ----

TT17-07      20.10                20.50            0.40   CHIP                
0.793          3.7          905           47           448
-------      -----                -----            ----   ----                
-----          ---          ---          ---           ---

TT17-07      20.30                                      GRAB                
0.891          4.5           62         1550            50
-------      -----                                      ----                
-----          ---          ---         ----           ---
Historical drilling within the newly defined soil anomaly is limited to a
single 152 m diamond drill hole (TH07-06; Figure 1), which was collared
between trench 4 and trench 6 (Figure 1). The drill hole was not well situated
to test the mineralized structures identified in 2017 trenches, but it did
intersect two approximately 50 cm quartz veins surrounded by networks of
quartz-calcite stringers. Assay results include 0.355 g/t Au and 5.9 g/t Ag
over 1.1 m (45.06-46.16 m) and 0.310 g/t Au and 12.7 g/t Ag over 0.45 m
(40.8-41.25 m).
Discussion of results:
Results from the 2016 and 2017 soil sampling survey show a strong
multi-element anomaly along strike of the Tinta vein deposit, with an
approximately 500 metre gap between the vein and the newly defined 1.8-km-long
anomaly. The geological model of a pinching and swelling vein structure may
adequately explain the absence and then re-occurrence of the soil anomaly
along strike of the Tinta vein. The new soil anomaly covers twice the area of
the one defined around the Tinta vein. It has a greater concentration of
samples with elevated gold pathfinder elements (e.g. As, Sb and Bi) and
similar concentration of samples with elevated gold compared to the samples
surrounding the Tinta vein. The geochemical signature within the new anomaly
is suggestive of a higher-level portion of the vein which may be more
prospective for precious metals.
Trenching within the soil anomaly tested less than half of the total
length of the anomaly, and uncovered altered, veined and mineralized rock in
six of seven trenches. Trench 2, which did not uncover mineralized rock, is
interpreted to have been dug too far to the southwest to have encountered the
same mineralized structures identified in the other trenches. Mineralization
in the trenches is associated with faulted alteration zones, which are also
observed in the Tinta deposit. Sulphide leaching has likely reduced the
overall base metal grades of the trench samples.
President's Comment:
Paul Reynolds, Triumph Gold Corp.'s President and CEO comments: "The
Tinta Au-Ag deposit is one of Triumph Gold's higher grade and underexplored
resources. Identifying an along-strike soil anomaly that is twice the size of
the anomaly surrounding the current resource area is very exciting. If it is
an extension of the Tinta vein system, it could dramatically affect the size
of the resource. We look forward to testing the new anomaly with more
trenching and follow-up drilling in 2018 and exploring to the northwest where
the anomaly remains open."
Methods and Qualified Person
Soil samples were collected at predetermined locations identified using a
global positioning system. Samples were collected from B-horizon, or below the
top layer of volcanic ash where B-horizon could not be sampled. The samples
were characterized, dried, and delivered to ALS Minerals Preparation
Laboratory in Whitehorse. Samples were analyzed by ALS Global of North
Vancouver, British Columbia using Au-ST43 (super trace Au determination via
25.0 g Aqua Regia digestion and ICP-MS analysis) and ME-MS41 (51 element
analysis via 0.5 g Aqua Regia digestion and ICP-MS analysis).
Trench samples were collected from locations determined by a global
positioning system. The samples were analyzed by ALS Global of North
Vancouver, British Columbia. They were prepared for analysis according to ALS
method PREP35: each sample was crushed to 70% passing 2mm and a 250g split was
pulverized to better than 95% passing 106 micron mesh. Gold was tested by fire
assay with atomic absorption finish on a 30g nominal sample (method Au-AA23),
and samples that tested over 10 g/t Au were retested using fire assay with a
gravimetric finish (method Au-GRA21). An additional 35 elements were tested by
ICP-AES using an Aqua Regia digestion (method ME-ICP41), over limit samples
for copper were retested using the same technique but with assay grade Aqua
Regia digestion and a higher range of detection (method ME-OG46). Quality
assurance and control (QAQC) is maintained at the lab through rigorous use of
internal standards, blanks and duplicates.
Some technical information contained in this release is historical in
nature and has been compiled from sources believed to be accurate. This
technical information has not been verified by Triumph Gold and may in some
instances be unverifiable.
The reported geochemical sampling program was carried out by TerraLogic
Exploration Inc. under the supervision of Michael McCuaig (P.Geo). The
reported trenching program was conducted under the supervision of Jesse Halle
(P.Geo). The technical content of this news release has been reviewed and
approved by Tony Barresi, Ph.D., P.Geo., VP Exploration for the company, and
qualified person as defined by National Instrument 43-101.
About Triumph Gold Corp.
Triumph Gold Corp. is a growth oriented Canadian-based precious metals
exploration and development company. Triumph Gold Corp. is focused on creating
value through the advancement of the district scale Freegold Mountain project
in Yukon. For maps and more information, please visit our website
www.triumphgoldcorp.com
On behalf of the Board of Directors
Signed "Paul Reynolds" Paul Reynolds, President & CEO
For further information please contact:
John Anderson, Chairman                 Nancy Massicotte
Triumph Gold Corp.                      IR Pro Communications Inc.
(604) 218-7400                          (604)-507-3377
janderson(at)triumphgoldcorp.com           nancy(at)irprocommunications.com
Neither the TSX Venture Exchange nor its Regulation Services Provider (asthat 
term is defined in policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
This news release contains forward-looking information, which involves
known and unknown risks, uncertainties and other factors that may cause actual
events to differ materially from current expectation. Important factors -
including the availability of funds, the results of financing efforts, the
completion of due diligence and the results of exploration activities - that
could cause actual results to differ materially from the Company's
expectations are disclosed in the Company's documents filed from time to time
on SEDAR (see www.sedar.com). Readers are cautioned not to place undue
reliance on these forward-looking statements, which speak only as of the date
of this press release. The company disclaims any intention or obligation,
except to the extent required by law, to update or revise any forward-looking
statements, whether as a result of new information, future events or
otherwise.
SOURCE Triumph Gold Corp.



View original content with multimedia:

 securities in any state in
which such offer, solicitation or sale would be unlawful.
Completion of the Proposed Transaction is subject to a number of
conditions, including but not limited to, Exchange acceptance. There can be no
assurance that the Proposed Transaction will be completed as proposed or at
all.
Investors are cautioned that, except as disclosed in the filing statement
to be prepared in connection with the Transaction, any information released or
received with respect to the Proposed Transaction may not be accurate or
complete and should not be relied upon. Trading in the securities of a capital
pool company should be considered highly speculative.
The TSX Venture Exchange Inc. has in no way passed upon the merits of the
Proposed Transaction and has neither approved nor disapproved the contents of
this press release.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this press release.
SOURCE Soleil Capital Corp.



View original content:
http://www.newswire.ca/en/releases/archive/November2017/20/c3826.html

-0-                           11/20/2017
/For further information: Michael Thomson, Email: cpc.thomson(at)icloud.com,
Phone: (604) 312-4777/
(SOLE.P.)

CO:  Soleil Capital Corp.
ST:  Alberta
IN:  FIN
SU: 

" BC-TriumphGoldTintaAuAg   11-20 1835
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Triumph Gold Announces Definition of a 1.8 X 0.75 km Soil Anomaly along
Strike of the Tinta Au-Ag Deposit and Discovery of Gold Bearing Quartz
Veins in Six Trenches Over 700 metres Strike Length within the Anomaly@

TSX.V: TIGOTCMKTS: NFRGFFrankfurt: 8N61
VANCOUVER, Nov. 20, 2017 /CNW/ - Triumph Gold Corp., (TSX-V: TIG)
(OTCMKTS: NFRGF) ("Triumph Gold" or the "Company") is pleased to announce that
recent soil sampling has defined a 1.8 X 0.75 km multi-element (Au, Cu, Pb,
Zn, As, Bi, Sb) soil anomaly, extending the Tinta Au-Ag vein system to the
northwest. The anomaly is northwest-southeast trending, open to the northwest
and begins 500 metres northwest, along strike, of the Tinta Au-Ag-Cu-Pb-Zn
deposit, in an area tested by only one historical drill hole (see below). Six
of seven trenches dug over 700 metres strike length, within the anomaly,
uncovered multiple clay-altered or silicified zones up to 2.6 metres wide that
contain strongly weathered quartz-chalcedony-carbonate-sulphide vein networks.
Sulphide contents are highly variable due to surface weathering and boxwork
after leached sulphides are common. Where sulphides are preserved they include
up to 15% coarse pyrite and variable amounts of galena, sphalerite and
chalcopyrite. Highlights of exploration at Tinta include:
<<

--  A 1.8-km-long multi-element soil anomaly, open to the northwest, along
strike of the Tinta Au-Ag deposit has been defined.

--  The anomaly has a higher concentration of samples with elevated
pathfinder elements (As, Sb, Bi) than the area surrounding the Tinta
vein deposit and a similar concentration of samples with elevated gold,
but over an area twice the size.

--  Within the 1.8-km-long soil anomaly, a 700-metre-long section was tested
with seven trenches. Six exposed multiple clay-altered or silicified
zones with mineralized quartz-chalcedony-carbonate-sulphide vein
networks. Highlights of assay results include:
o 2.21 grams/tonne (g/t) Au and 11.3 g/t Ag over 1.5m in a chip sample from
Trench 3
o 0.666 g/t Au and 13.7 g/t Ag over 1.5m in a chip sample from Trench 3
o 1.9 g/t Au and 40.9 g/t Ag in a grab sample from Trench 4.
o 4.9 g/t Ag, 1.5% Zn and 0.4% Pb in a grab sample from Trench 4
o 0.793 g/t Au and 3.7 g/t Ag over 0.4m in a chip sample from Trench 5.
>>
Exploration in the vicinity of the Tinta vein deposit in 2016 comprised a
1.1 sq. km (414 sample) soil geochemistry grid and VLF-EM and magnetic
geophysical surveys covering 9.0 sq. km. These surveys defined a number of
coincident multi-element soil and geophysical anomalies, the most prominent of
which was along strike of the Tinta Au-Ag-Cu-Pb-Zn deposit (see PR17-04, Feb.
27 2017), which has an inferred resource of 2.16 million tonnes grading 1.89
g/t Au, 54.9 g/t Ag, 0.27% Cu, 0.99% Pb and 1.41% Zn (December 15, 2014).
Follow-up exploration in 2017 included:
<<

1. an expanded soil geochemistry grid with 993 samples collected over 8 sq.
km, and

2. 560 metres of excavator trenching within the coincident anomalies defined
by the 2016 survey.
>>
The 2017 soil grid expanded the length of the 2016 soil anomaly from 900
to 1,800 metres. In addition, the 2017 soil survey covered the area around the
Tinta vein to provide a better basis for comparison between geochemistry of
soils in the new anomaly and soils surrounding the existing deposit.
The 2017 trenches uncovered granite with numerous broad
hematite-epidote-chlorite-altered intervals, the same host rock and alteration
that surrounds productive veins in the Tinta deposit. Within these zones there
are multiple discrete strongly weathered, clay-altered or silicified zones up
to 2.6 metres wide that contain quartz-chalcedony-carbonate-sulphide vein
networks that appear to be hosted in faulted zones which are parallel to the
Tinta vein trend; similar zones are also observed in the Tinta deposit. The
trenches were mapped and sampled; a total of ninety-two samples were collected
including eighteen grab samples and seventy-three chip samples (collected over
107.2 metres). Table 1 contains significant results from the trench sampling
and Figure 1 below (or see Triumph Gold website) shows the locations of the
trenches and samples.
http://www.triumphgoldcorp.com/projects/freegold-mountain/tinta-hill-depo
sit/
Table 1: Significant assay results from trenching within the Tinta
Extension Soil Anomaly. These data represent highlights of 2017 trench
sampling that included 18 grab and 73 chip samples.
Trench  From                 To             Length             Sample  
Au             Ag          Cu           Pb            Zn
------  ----                ---             ------             ------  
---           ---          ---          ---          ---

(m)                (m)               (m)               Type  (ppm)         
(ppm)        (ppm)        (ppm)        (ppm)
---                ---               ---               ----  ----           
----        ----         ----          ----

TT17-01      16.00                18.00            2.00   CHIP                
0.177         36.9           31          234           139
-------      -----                -----            ----   ----                
-----         ----          ---          ---           ---


TT17-02        No Significant Assay Results
-------        ----------------------------


TT17-03      12.00                13.50            1.50   CHIP                
2.210         11.3          232          117           269
-------      -----                -----            ----   ----                
-----         ----          ---          ---           ---

TT17-03      74.00                                      GRAB                
0.759          7.1           69          246           504
-------      -----                                      ----                
-----          ---          ---          ---           ---

TT17-03      75.50                77.00            1.50   CHIP                
0.666         13.7          700          815           911
-------      -----                -----            ----   ----                
-----         ----          ---          ---           ---


TT17-04       2.70                                      GRAB                
1.900         40.9           99          910           199
-------       ----                                      ----                
-----         ----          ---          ---           ---

TT17-04       3.50                                      GRAB                
0.100         15.3         1785         1810          1760
-------       ----                                      ----                
-----         ----         ----         ----          ----


TT17-05      24.40                                      GRAB                
0.194          6.2           91          714           519
-------      -----                                      ----                
-----          ---          ---          ---           ---


TT17-06      21.50                                      GRAB                
0.400         25.5          229          451           201
-------      -----                                      ----                
-----         ----          ---          ---           ---

TT17-06      30.00                                      GRAB                
0.171         15.3           77           50            94
-------      -----                                      ----                
-----         ----          ---          ---           ---

TT17-06      71.50                72.50            1.00   CHIP                
0.022          1.1           16          734          1910
-------      -----                -----            ----   ----                
-----          ---          ---          ---          ----

TT17-06      73.00                                      GRAB                
0.068          4.9           97         4020         15050
-------      -----                                      ----                
-----          ---          ---         ----         -----


TT17-07      18.00                                      GRAB                
0.050          9.2         1045         1885          2500
-------      -----                                      ----                
-----          ---         ----         ----          ----

TT17-07      20.10                20.50            0.40   CHIP                
0.793          3.7          905           47           448
-------      -----                -----            ----   ----                
-----          ---          ---          ---           ---

TT17-07      20.30                                      GRAB                
0.891          4.5           62         1550            50
-------      -----                                      ----                
-----          ---          ---         ----           ---
Historical drilling within the newly defined soil anomaly is limited to a
single 152 m diamond drill hole (TH07-06; Figure 1), which was collared
between trench 4 and trench 6 (Figure 1). The drill hole was not well situated
to test the mineralized structures identified in 2017 trenches, but it did
intersect two approximately 50 cm quartz veins surrounded by networks of
quartz-calcite stringers. Assay results include 0.355 g/t Au and 5.9 g/t Ag
over 1.1 m (45.06-46.16 m) and 0.310 g/t Au and 12.7 g/t Ag over 0.45 m
(40.8-41.25 m).
Discussion of results:
Results from the 2016 and 2017 soil sampling survey show a strong
multi-element anomaly along strike of the Tinta vein deposit, with an
approximately 500 metre gap between the vein and the newly defined 1.8-km-long
anomaly. The geological model of a pinching and swelling vein structure may
adequately explain the absence and then re-occurrence of the soil anomaly
along strike of the Tinta vein. The new soil anomaly covers twice the area of
the one defined around the Tinta vein. It has a greater concentration of
samples with elevated gold pathfinder elements (e.g. As, Sb and Bi) and
similar concentration of samples with elevated gold compared to the samples
surrounding the Tinta vein. The geochemical signature within the new anomaly
is suggestive of a higher-level portion of the vein which may be more
prospective for precious metals.
Trenching within the soil anomaly tested less than half of the total
length of the anomaly, and uncovered altered, veined and mineralized rock in
six of seven trenches. Trench 2, which did not uncover mineralized rock, is
interpreted to have been dug too far to the southwest to have encountered the
same mineralized structures identified in the other trenches. Mineralization
in the trenches is associated with faulted alteration zones, which are also
observed in the Tinta deposit. Sulphide leaching has likely reduced the
overall base metal grades of the trench samples.
President's Comment:
Paul Reynolds, Triumph Gold Corp.'s President and CEO comments: "The
Tinta Au-Ag deposit is one of Triumph Gold's higher grade and underexplored
resources. Identifying an along-strike soil anomaly that is twice the size of
the anomaly surrounding the current resource area is very exciting. If it is
an extension of the Tinta vein system, it could dramatically affect the size
of the resource. We look forward to testing the new anomaly with more
trenching and follow-up drilling in 2018 and exploring to the northwest where
the anomaly remains open."
Methods and Qualified Person
Soil samples were collected at predetermined locations identified using a
global positioning system. Samples were collected from B-horizon, or below the
top layer of volcanic ash where B-horizon could not be sampled. The samples
were characterized, dried, and delivered to ALS Minerals Preparation
Laboratory in Whitehorse. Samples were analyzed by ALS Global of North
Vancouver, British Columbia using Au-ST43 (super trace Au determination via
25.0 g Aqua Regia digestion and ICP-MS analysis) and ME-MS41 (51 element
analysis via 0.5 g Aqua Regia digestion and ICP-MS analysis).
Trench samples were collected from locations determined by a global
positioning system. The samples were analyzed by ALS Global of North
Vancouver, British Columbia. They were prepared for analysis according to ALS
method PREP35: each sample was crushed to 70% passing 2mm and a 250g split was
pulverized to better than 95% passing 106 micron mesh. Gold was tested by fire
assay with atomic absorption finish on a 30g nominal sample (method Au-AA23),
and samples that tested over 10 g/t Au were retested using fire assay with a
gravimetric finish (method Au-GRA21). An additional 35 elements were tested by
ICP-AES using an Aqua Regia digestion (method ME-ICP41), over limit samples
for copper were retested using the same technique but with assay grade Aqua
Regia digestion and a higher range of detection (method ME-OG46). Quality
assurance and control (QAQC) is maintained at the lab through rigorous use of
internal standards, blanks and duplicates.
Some technical information contained in this release is historical in
nature and has been compiled from sources believed to be accurate. This
technical information has not been verified by Triumph Gold and may in some
instances be unverifiable.
The reported geochemical sampling program was carried out by TerraLogic
Exploration Inc. under the supervision of Michael McCuaig (P.Geo). The
reported trenching program was conducted under the supervision of Jesse Halle
(P.Geo). The technical content of this news release has been reviewed and
approved by Tony Barresi, Ph.D., P.Geo., VP Exploration for the company, and
qualified person as defined by National Instrument 43-101.
About Triumph Gold Corp.
Triumph Gold Corp. is a growth oriented Canadian-based precious metals
exploration and development company. Triumph Gold Corp. is focused on creating
value through the advancement of the district scale Freegold Mountain project
in Yukon. For maps and more information, please visit our website
www.triumphgoldcorp.com
On behalf of the Board of Directors
Signed "Paul Reynolds" Paul Reynolds, President & CEO
For further information please contact:
John Anderson, Chairman                 Nancy Massicotte
Triumph Gold Corp.                      IR Pro Communications Inc.
(604) 218-7400                          (604)-507-3377
janderson(at)triumphgoldcorp.com           nancy(at)irprocommunications.com
Neither the TSX Venture Exchange nor its Regulation Services Provider (asthat 
term is defined in policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
This news release contains forward-looking information, which involves
known and unknown risks, uncertainties and other factors that may cause actual
events to differ materially from current expectation. Important factors -
including the availability of funds, the results of financing efforts, the
completion of due diligence and the results of exploration activities - that
could cause actual results to differ materially from the Company's
expectations are disclosed in the Company's documents filed from time to time
on SEDAR (see www.sedar.com). Readers are cautioned not to place undue
reliance on these forward-looking statements, which speak only as of the date
of this press release. The company disclaims any intention or obligation,
except to the extent required by law, to update or revise any forward-looking
statements, whether as a result of new information, future events or
otherwise.
SOURCE Triumph Gold Corp.



View original content with multimedia:
http://www.newswire.ca/en/releases/archive/November2017/20/c6466.html

-0-                           11/20/2017
/For further information:/
(NFRGF TIG.)

CO:  Triumph Gold Corp.
ST:  British Columbia
IN:  MNG MIN
SU:

-30-



 securities in any state in
which such offer, solicitation or sale would be unlawful.
Completion of the Proposed Transaction is subject to a number of
conditions, including but not limited to, Exchange acceptance. There can be no
assurance that the Proposed Transaction will be completed as proposed or at
all.
Investors are cautioned that, except as disclosed in the filing statement
to be prepared in connection with the Transaction, any information released or
received with respect to the Proposed Transaction may not be accurate or
complete and should not be relied upon. Trading in the securities of a capital
pool company should be considered highly speculative.
The TSX Venture Exchange Inc. has in no way passed upon the merits of the
Proposed Transaction and has neither approved nor disapproved the contents of
this press release.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this press release.
SOURCE Soleil Capital Corp.



View original content:
http://www.newswire.ca/en/releases/archive/November2017/20/c3826.html

-0-                           11/20/2017
/For further information: Michael Thomson, Email: cpc.thomson(at)icloud.com,
Phone: (604) 312-4777/
(SOLE.P.)

CO:  Soleil Capital Corp.
ST:  Alberta
IN:  FIN
SU: