Source	Marketwire
Date	11/20/2017
Time	05:54:29 AM

Company	 WHITE GOLD CORP.
Title	White Gold Extends Historical Arc Deposit Strike Length by 250m and 
Continues to Extend and Define the Golden Saddle Footwall Zone Beyond 
Historical Resource Limits





    CDNX Symbol: WGO











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: White Gold Corp.

TSX VENTURE SYMBOL: WGO

November 20, 2017

White Gold Extends Historical Arc Deposit Strike Length by 250m and Continues 
to Extend and Define the Golden Saddle Footwall Zone Beyond Historical Resource 
Limits


TORONTO, ONTARIO--(Marketwired - Nov. 20, 2017) - White Gold Corp. (TSX 
VENTURE:WGO) (the "Company") is pleased to announce additional results from 
reverse circulation ("RC") holes completed along trend with the historical Arc 
deposit (the "Arc deposit")(1) and the historical Golden Saddle deposit (the 
"Golden Saddle deposit" or "Golden Saddle resource")(1) located on the White 
Gold Property, Yukon. The results reported herein further define a significant 
extension of the Arc deposit 250m along strike and also extend the Golden 
Saddle Footwall Zone along strike and towards surface. Additional drill results 
are pending from the Golden Saddle and Arc deposits as well as the newly 
defined Golden Saddle East and Ulli's targets and will be released in due 
course. Detailed maps related to the drilling and additional information can be 
found at http://whitegoldcorp.ca/investors/exploration-highlights/.

/T/

(1) See information regarding historical resources/deposits below

/T/

Highlights include:

/T/

--  Strike length of gold mineralization at Arc deposit extended by 29%
(250m) along trend to the west from previous limit of historic drilling.


--  Golden Saddle Footwall Zone further defined along a 300m mineralized
zone with mineralization also being further extended 50m along strike
length.


--  Golden Saddle RC drilling continued to validate historical drilling
within the historical Golden Saddle resource area with WHTGS17RC-010
intersecting 10.67m of 10.09 g/t Au within a broader intercept of 28.96m
of 3.99g/t Au from 59.44m depth and WHTGS17RC-013 intersecting 6.1m of
9.52 g/t Au within a broader intercept 13.12m of 7.47 g/t Au from 68.58m
depth.

/T/

Arc Exploration Update

The Arc deposit occurs adjacent to the Golden Saddle deposit, approximately 
400m to the south. Historic drilling on the Arc was limited and widely spaced 
(typically greater than 100m between drill collars), but defined an east-west 
trending, north dipping zone of mineralization over 850m of strike and 
extending 400m down dip. Historic estimates of inferred mineral resources on 
the Arc include 170,470 ounces contained within 4.37Mt at a grade of 1.21 g/t 
Au(1). In addition to the continuation of the mineralization along trend, there 
appears to be strong potential for subparallel zones of mineralization below 
the historic resource area based on historic drilling and revised geologic 
interpretation of the Arc deposit.

WHTARR17RC-001 to 003 RC holes were drilled as shallow reconnaissance holes to 
approximately 100m depth to evaluate for near surface continuation of Arc Zone 
mineralization to the west and to potentially identify near surface projects of 
subparallel zones of mineralization to the Arc. The holes were placed as a 
fence along a north-south oriented ridge approximately 250m west of the Arc 
deposit area with collar locations approximately 100m apart and all three holes 
directed at an azimuth of 180 degrees and dip of -60 degrees. RC hole 
WHTARR17RC-002 successfully intercepted 1.52 g/t Au over 12.19m from 79.25m 
depth with the hole ending in mineralization at 91.44m. This intersection 
corresponds to the projection of the Arc Zone and extends mineralization 
approximately 250m to the west. True thickness is estimated to be between 65 - 
95% of the reported intercepts. Assay results range from trace to 4.19g/t Au. 
Significant results are detailed in the table below.

Jodie Gibson, VP, Exploration of the Company commented: "The results of the 
2017 drill program received to date confirm the potential to significantly 
expand both the Golden Saddle and Arc deposits, and I look forward to receiving 
the additional drill results from the Arc as well as initial drill results from 
the Ulli's and Golden Saddle East targets. Furthermore, new geologic mapping 
and geophysical interpretation on the property indicate the potential for 
additional sub-parallel zones of mineralization that will be the focus of 
future exploration programs on the property as well as the newly identified 
and/or other undrilled targets."

/T/

----------------------------------------------------------------------------
Arc - 2017 RC Drill Holes
----------------------------------------------------------------------------
Hole ID                       From (m)      To (m)  Interval (m)    Au (g/t)
----------------------------------------------------------------------------
WHTARR17RC-002(i)               79.248       91.44        12.192        1.52
----------------------------------------------------------------------------
Including                       80.772      82.296         1.524        4.19
----------------------------------------------------------------------------
WHTARR17RC-003                  50.292      57.912          7.62        1.28
----------------------------------------------------------------------------
(i) Hole Ended in Mineralization

/T/

Golden Saddle Exploration Update

RC Holes WHTGS17RC-014 & 015 were drilled in close proximity to historic 
diamond hole WGGS10D0121(2) ("Hole 121") and infill a 150m gap in the footwall 
zone between Hole 121 and hole WGGS10D0138(2). The holes are on section with 
previously reported diamond hole WHTGS17DD-0171(3) and together define 300m of 
mineralization along the Footwall Zone that is a 50m step-out beyond the limits 
of historic resource estimates.

RC hole WHTGS17RC-014 was drilled at an azimuth of 160 degrees, dip of -60, and 
to a depth of 186m, and intercepted a 12.19m zone averaging 1.83 g/t Au from 
128.02m depth. This intercept corresponds to the Footwall Zone and extends 
mineralization 95m up-dip from Hole 121.

RC hole WHTGS17RC-015 was drilled from the same site as WHTGS17RC-014 at an 
azimuth of 160 degrees, dip of -77, and to a depth of 189m. The hole returned 
an upper intercept of 4.57m averaging 1.22 g/t Au from 21.34m depth and a lower 
intercept of 21.34m averaging 0.95 g/t Au from 135.64m depth; including 10.67m 
of 1.59 g/t Au from 138.68m depth. The lower intercept corresponds to the 
Footwall Zone and extends mineralization 50m up-dip from Hole 121.

RC holes WHTGS17RC-010 and 013 were drilled in close proximity to historic 
diamond holes at a dip of -90 for QA/QC purposes. Both intercepts were 
equivalent or slightly higher grade than the historic diamond holes. 
WHTGS17RC-010 was drilled in close proximity to historic diamond hole WD-009(4) 
for QA/QC purposes and returned 3.99 g/t Au over 28.96m from 59.44m depth; 
including 10.09 g/t Au over 10.67m from 62.48m depth. WHTGS17RC-013 was drilled 
in close proximity to historic diamond hole WD-013(4) for QA/QC purposes and 
returned 7.47 g/t Au over 13.12m from 68.58m depth; including 21.5 g/t Au over 
1.52m from 68.58m depth and 9.52 g/t Au over 6.096m from 74.68m depth.

True thickness is estimated to be between 65 - 95% of the reported intercepts. 
Assay results range from trace to 21.5g/t Au. Significant results are detailed 
in the table below.

/T/

(2) Reported in the Independent Technical Report for the White Gold Project,
Dawson Range, Yukon, Canada by Gilles Arseneau, P.Geo. dated Sept. 15th,
2017 and is available on SEDAR
(3) Reported in the Company's news release dated Nov. 6, 2017, and is
available on SEDAR
(4) Reported in Underworld Resources Inc. ("UW") news release UW2008 - NR#6
dated Aug. 6, 2008 and is available on SEDAR


----------------------------------------------------------------------------
Golden Saddle - 2017 RC Drill Holes
----------------------------------------------------------------------------
Hole ID                       From (m)      To (m)  Interval (m)    Au (g/t)
----------------------------------------------------------------------------
WHTGS17RC-010                   59.436      88.392        28.956        3.99
----------------------------------------------------------------------------
Including                       62.484      73.152        10.668       10.09
----------------------------------------------------------------------------
Including                       67.056      71.628         4.572       14.63
----------------------------------------------------------------------------
WHTGS17RC-013                    68.58      82.296        13.716        7.47
----------------------------------------------------------------------------
Including                        68.58      70.104         1.524        21.5
----------------------------------------------------------------------------
Including                       74.676      80.772         6.096        9.52
----------------------------------------------------------------------------
WHTGS17RC-014                  128.016     140.208        12.192        1.83
----------------------------------------------------------------------------
WHTGS17RC-015                   21.336       22.86         4.572        1.22
----------------------------------------------------------------------------
And                            135.636     156.972        21.336        0.95
----------------------------------------------------------------------------
Including                      138.684     149.352        10.668        1.59
----------------------------------------------------------------------------

/T/

The 2017 drilling campaign on the White Gold Property represents the first 
drilling program on the property since the previous operator, Kinross Gold 
Corp. A total of 4,432m over 31 RC holes and 1,295m over 4 diamond holes have 
been completed by the Company in 2017 on the White Gold property. This includes 
4,151m of drilling on the Golden Saddle deposit with additional drilling on the 
Arc deposit and newly identified Golden Saddle East and Ulli's target areas. 
Complete results have been reported for 18 of the RC holes and 4 diamond drill 
holes to date. Assays for the additional holes will be reported in due course.

(1) Information Regarding Historical Resources/Deposits

All historical scientific and technical information relating to the White Gold 
Properties is based on and derived from the 43-101 report titled "White Gold 
Property Dawson Range Yukon, Canada" dated March 3, 2010, prepared by Lars 
Weiershauser, P.Geo, Marek Nowak, P.Eng and Wayne Barnett, Pr.Sci.Nat. of SRK 
Consulting (Canada) Inc.) (the "Technical Report") available on Sedar and other 
information available to the Company as referenced herein. The property was 
historically explored by Underworld Resources from 2007 - 2009 and included the 
discovery of the Golden Saddle and Arc deposits. In 2010, Underworld reported a 
resource estimate of 1,004,570 ounces contained in 9.80 Mt at a grade of 3.19 
g/t Au in an Indicated category, with an additional 407,410 ounces contained in 
5.02 Mt at a grade of 2.5 g/t Au in an Inferred category for the Golden Saddle 
deposit. At the Arc deposit, the initial resource included 170,470 ounces 
contained within 4.37 Mt at a grade of 1.21 g/t Au in the inferred category 
(reported in Underworld Resources New Release UW2010-NR#2 dated January 19, 
2010 and the Technical Report. Kinross purchased Underworld shortly after the 
initial resource was released in 2010 and explored the property from 2010 - 
2012. In 2013, Kinross released the results of a resource estimate for the 
Golden Saddle deposit and reported a resource of 840,000 ounces within 9.79 Mt 
at a grade of 2.67 g/t Au in an Indicated category, with an additional 125,000 
ounces within 2.17 Mt at a grade of 1.8 g/t Au in an Inferred category 
(reported in Kinross Gold Corp.'s 2016 Mineral Reserves and Resource 
Statement). Both Underworld's and Kinross' resource estimates are considered 
historical estimates and the Company is not treating them as current mineral 
resources. Although the Company believes these sources to be generally 
reliable, such information is subject to interpretation and cannot be verified 
with complete certainty due to limits on the availability and reliability of 
raw data, the voluntary nature of the data gathering process and other inherent 
limitations and uncertainties. In addition to the Golden Saddle and Arc 
deposits, there are numerous other targets known on the property that warrant 
follow-up work (for more information see Yukon Assessment Report #'s 095338, 
096206, & 096207).

The information contained herein is subject to all of the assumptions, 
qualifications and procedures set out in the Technical Report and reference 
should be made to the full details of the Technical Report which may be 
obtained from the Company by contacting dschmidt@whitegoldcorp.ca. Disclosure 
of the historical estimates in this news release is derived from the Technical 
Report and other information as set forth above previous press releases of the 
company as available on Sedar and has been judged to be relevant and therefore 
suitable for disclosure, however should not be relied upon. There are numerous 
uncertainties inherent in the historical estimates, which are subject to all of 
the assumptions, parameters and methods used to prepare such historical 
estimates and reference is made to the full text of the Technical Report with 
respect thereto. The historic estimates of mineral resources were estimated in 
conformity with generally accepted CIM "Estimation of Mineral Resource and 
Mineral Reserve Best Practices" Guidelines. Mineral resources are not mineral 
reserves and do not have demonstrated economic viability. There are no other 
recent estimates or data are available to the Company as at the date of this 
news release and a detailed exploration program is required to be conducted by 
the Company in order to verify or treat the historical estimate as a current 
mineral resource. A qualified person has not done sufficient work to classify 
the historical estimates as current mineral resources or mineral reserves and 
the Company is not treating the historical estimate as current mineral 
resources.

The Company encourages individuals interested in the Company to visit its 
website (www.whitegoldcorp.ca) to further understand the size and scope of the 
Company's projects in the White Gold District.
The analytical work for the 2017 program has been performed by Bureau Veritas 
Commodities Canada Ltd., an internationally recognized analytical services 
provider, at its Vancouver, British Columbia laboratory. Sample preparation was 
carried out at its Whitehorse, Yukon facility. All soil samples were using 
procedure SS80 (dry at 60 C and sieve 100g at -80 mesh) and analyzed by method 
AQ201 (aqua regia digestion and ICP-MS analysis). All rock, GT Probe, RAB, RC, 
and diamond core samples were prepared using procedure PRP70-250 (crush, split 
and pulverize 250 g to 200 mesh) and analyzed by method FA430 (30g fire assay 
with AAS finish) and AQ200 (0.5g, aqua regia digestion and ICP-MS analysis). 
Samples containing greater than 10g/t Au were reanalyzed using method FA530 
(30g Fire Assay with gravimetric finish). Metallic-screen analysis may also be 
utilized if coarse gold mineralization is encounter (FS600).

Qualified Person

Jodie Gibson, PGeo, VP, Exploration of the Company is a "qualified person" as 
defined under National Instrument 43-101 - Standards of Disclosure for Mineral 
Projects ("NI 43-101"), and has reviewed and approved the content of this news 
release. Potential quantity and grade is conceptual in nature. There has been 
insufficient exploration to define a mineral resource on any of the Company's 
properties to date, and it is uncertain if further exploration will result in 
any such target being delineated as a mineral resource.

The reported work was completed using industry standard procedures, including a 
quality assurance/quality control (QA/QC) program consisting of the insertion 
of certified standards, blanks, and field duplicates into the sample stream. 
The qualified person detected no significant QA/QC issues during review of the 
data.

About White Gold Corp.

The Company owns a portfolio of 19,438 quartz claims across 30 properties 
covering over 390,000 hectares representing approximately 40% of the Yukon's 
White Gold district. Preliminary exploration work has produced several 
prospective targets. The claim packages are bordered by sizable gold 
discoveries including the Coffee project owned by Goldcorp Inc., Western Copper 
and Gold Corporation's Casino project, and the Golden Saddle and Arc deposits 
acquired by the Company in June 2017 from Kinross Gold Corp. The Company has 
outlined an aggressive exploration plan to further explore its properties. For 
more information visit www.whitegoldcorp.ca.

Cautionary Note Regarding Forward Looking Information

This news release contains "forward-looking information" and "forward-looking 
statements" (collectively, "forward-looking statements") within the meaning of 
the applicable Canadian securities legislation. All statements, other than 
statements of historical fact, are forward-looking statements and are based on 
expectations, estimates and projections as at the date of this news release. 
Any statement that involves discussions with respect to predictions, 
expectations, beliefs, plans, projections, objectives, assumptions, future 
events or performance (often but not always using phrases such as "expects", or 
"does not expect", "is expected", "anticipates" or "does not anticipate", 
"plans", "budget", "scheduled", "forecasts", "estimates", "believes" or 
"intends" or variations of such words and phrases or stating that certain 
actions, events or results "may" or "could", "would", "might" or "will" be 
taken to occur or be achieved) are not statements of historical fact and may be 
forward-looking statements. In this news release, forward-looking statements 
relate, among other things, to: the anticipated benefits to the Company and its 
shareholders respecting the Company's objectives, goals and exploration 
activities conducted and proposed to be conducted at the White Gold properties; 
future growth potential of the Company, including whether any mineral resource 
will be established in accordance with NI 43-101 at any of the Company's 
properties; exploration results; and future exploration plans.

These forward-looking statements are based on reasonable assumptions and 
estimates of management of the Company at the time such statements were made. 
Actual future results may differ materially as forward-looking statements 
involve known and unknown risks, uncertainties and other factors which may 
cause the actual results, performance or achievements of the Company to 
materially differ from any future results, performance or achievements 
expressed or implied by such forward-looking statements. Such factors, among 
other things, include: the expected benefits to the Company relating to the 
exploration conducted and proposed to be conducted at the White Gold 
properties; failure to identify mineral resources; the preliminary nature of 
metallurgical test results; uncertainties relating to the availability and 
costs of financing needed in the future, including to fund any exploration 
programs on the White Gold properties and the Company's other properties; 
business integration risks; fluctuations in general macroeconomic conditions; 
fluctuations in securities markets; fluctuations in spot and forward prices of 
gold, silver, base metals or certain other commodities; fluctuations in 
currency markets (such as the Canadian dollar to United States dollar exchange 
rate); change in national and local government, legislation, taxation, 
controls, regulations and political or economic developments; risks and hazards 
associated with the business of mineral exploration, development and mining 
(including environmental hazards, industrial accidents, unusual or unexpected 
formations pressures, cave-ins and flooding); inability to obtain adequate 
insurance to cover risks and hazards; the presence of laws and regulations that 
may impose restrictions on mining; employee relations; relationships with and 
claims by local communities and indigenous populations; availability of 
increasing costs associated with mining inputs and labour; the speculative 
nature of mineral exploration and development (including the risks of obtaining 
necessary licenses, permits and approvals from government authorities); the 
unlikelihood that properties that are explored are ultimately developed into 
producing mines; geological factors; actual results of current and future 
exploration; changes in project parameters as plans continue to be evaluated; 
soil sampling results being preliminary in nature and are not conclusive 
evidence of the likelihood of a mineral deposit; title to properties; and those 
factors described under the heading "Risks and Uncertainties" in the Company's 
most recently filed management's discussion and analysis.

Although the forward-looking statements contained in this news release are 
based upon what management of the Company believes, or believed at the time, to 
be reasonable assumptions, the Company cannot assure shareholders that actual 
results will be consistent with such forward-looking statements, as there may 
be other factors that cause results not to be as anticipated, estimated or 
intended. Accordingly, readers should not place undue reliance on 
forward-looking statements and information. There can be no assurance that 
forward-looking information, or the material factors or assumptions used to 
develop such forward-looking information, will prove to be accurate. The 
Company does not undertake any obligations to release publicly any revisions 
for updating any voluntary forward-looking statements, except as required by 
applicable securities law.

Neither the TSX Venture Exchange (the "Exchange") nor its Regulation Services 
Provider (as that term is defined in the policies of the Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

- 30 -

CONTACT INFO:

White Gold Corp.
David D'Onofrio
Chief Executive Officer
(416) 643-3880
ddonofrio@whitegoldcorp.ca
www.whitegoldcorp.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=600723085


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: White Gold Corp.

TSX VENTURE SYMBOL: WGO

November 20, 2017

White Gold Extends Historical Arc Deposit Strike Length by 250m and Continues 
to Extend and Define the Golden Saddle Footwall Zone Beyond Historical Resource 
Limits


TORONTO, ONTARIO--(Marketwired - Nov. 20, 2017) - White Gold Corp. (TSX 
VENTURE:WGO) (the "Company") is pleased to announce additional results from 
reverse circulation ("RC") holes completed along trend with the historical Arc 
deposit (the "Arc deposit")(1) and the historical Golden Saddle deposit (the 
"Golden Saddle deposit" or "Golden Saddle resource")(1) located on the White 
Gold Property, Yukon. The results reported herein further define a significant 
extension of the Arc deposit 250m along strike and also extend the Golden 
Saddle Footwall Zone along strike and towards surface. Additional drill results 
are pending from the Golden Saddle and Arc deposits as well as the newly 
defined Golden Saddle East and Ulli's targets and will be released in due 
course. Detailed maps related to the drilling and additional information can be 
found at http://whitegoldcorp.ca/investors/exploration-highlights/.

/T/

(1) See information regarding historical resources/deposits below

/T/

Highlights include:

/T/

--  Strike length of gold mineralization at Arc deposit extended by 29%
(250m) along trend to the west from previous limit of historic drilling.


--  Golden Saddle Footwall Zone further defined along a 300m mineralized
zone with mineralization also being further extended 50m along strike
length.


--  Golden Saddle RC drilling continued to validate historical drilling
within the historical Golden Saddle resource area with WHTGS17RC-010
intersecting 10.67m of 10.09 g/t Au within a broader intercept of 28.96m
of 3.99g/t Au from 59.44m depth and WHTGS17RC-013 intersecting 6.1m of
9.52 g/t Au within a broader intercept 13.12m of 7.47 g/t Au from 68.58m
depth.

/T/

Arc Exploration Update

The Arc deposit occurs adjacent to the Golden Saddle deposit, approximately 
400m to the south. Historic drilling on the Arc was limited and widely spaced 
(typically greater than 100m between drill collars), but defined an east-west 
trending, north dipping zone of mineralization over 850m of strike and 
extending 400m down dip. Historic estimates of inferred mineral resources on 
the Arc include 170,470 ounces contained within 4.37Mt at a grade of 1.21 g/t 
Au(1). In addition to the continuation of the mineralization along trend, there 
appears to be strong potential for subparallel zones of mineralization below 
the historic resource area based on historic drilling and revised geologic 
interpretation of the Arc deposit.

WHTARR17RC-001 to 003 RC holes were drilled as shallow reconnaissance holes to 
approximately 100m depth to evaluate for near surface continuation of Arc Zone 
mineralization to the west and to potentially identify near surface projects of 
subparallel zones of mineralization to the Arc. The holes were placed as a 
fence along a north-south oriented ridge approximately 250m west of the Arc 
deposit area with collar locations approximately 100m apart and all three holes 
directed at an azimuth of 180 degrees and dip of -60 degrees. RC hole 
WHTARR17RC-002 successfully intercepted 1.52 g/t Au over 12.19m from 79.25m 
depth with the hole ending in mineralization at 91.44m. This intersection 
corresponds to the projection of the Arc Zone and extends mineralization 
approximately 250m to the west. True thickness is estimated to be between 65 - 
95% of the reported intercepts. Assay results range from trace to 4.19g/t Au. 
Significant results are detailed in the table below.

Jodie Gibson, VP, Exploration of the Company commented: "The results of the 
2017 drill program received to date confirm the potential to significantly 
expand both the Golden Saddle and Arc deposits, and I look forward to receiving 
the additional drill results from the Arc as well as initial drill results from 
the Ulli's and Golden Saddle East targets. Furthermore, new geologic mapping 
and geophysical interpretation on the property indicate the potential for 
additional sub-parallel zones of mineralization that will be the focus of 
future exploration programs on the property as well as the newly identified 
and/or other undrilled targets."

/T/

----------------------------------------------------------------------------
Arc - 2017 RC Drill Holes
----------------------------------------------------------------------------
Hole ID                       From (m)      To (m)  Interval (m)    Au (g/t)
----------------------------------------------------------------------------
WHTARR17RC-002(i)               79.248       91.44        12.192        1.52
----------------------------------------------------------------------------
Including                       80.772      82.296         1.524        4.19
----------------------------------------------------------------------------
WHTARR17RC-003                  50.292      57.912          7.62        1.28
----------------------------------------------------------------------------
(i) Hole Ended in Mineralization

/T/

Golden Saddle Exploration Update

RC Holes WHTGS17RC-014 & 015 were drilled in close proximity to historic 
diamond hole WGGS10D0121(2) ("Hole 121") and infill a 150m gap in the footwall 
zone between Hole 121 and hole WGGS10D0138(2). The holes are on section with 
previously reported diamond hole WHTGS17DD-0171(3) and together define 300m of 
mineralization along the Footwall Zone that is a 50m step-out beyond the limits 
of historic resource estimates.

RC hole WHTGS17RC-014 was drilled at an azimuth of 160 degrees, dip of -60, and 
to a depth of 186m, and intercepted a 12.19m zone averaging 1.83 g/t Au from 
128.02m depth. This intercept corresponds to the Footwall Zone and extends 
mineralization 95m up-dip from Hole 121.

RC hole WHTGS17RC-015 was drilled from the same site as WHTGS17RC-014 at an 
azimuth of 160 degrees, dip of -77, and to a depth of 189m. The hole returned 
an upper intercept of 4.57m averaging 1.22 g/t Au from 21.34m depth and a lower 
intercept of 21.34m averaging 0.95 g/t Au from 135.64m depth; including 10.67m 
of 1.59 g/t Au from 138.68m depth. The lower intercept corresponds to the 
Footwall Zone and extends mineralization 50m up-dip from Hole 121.

RC holes WHTGS17RC-010 and 013 were drilled in close proximity to historic 
diamond holes at a dip of -90 for QA/QC purposes. Both intercepts were 
equivalent or slightly higher grade than the historic diamond holes. 
WHTGS17RC-010 was drilled in close proximity to historic diamond hole WD-009(4) 
for QA/QC purposes and returned 3.99 g/t Au over 28.96m from 59.44m depth; 
including 10.09 g/t Au over 10.67m from 62.48m depth. WHTGS17RC-013 was drilled 
in close proximity to historic diamond hole WD-013(4) for QA/QC purposes and 
returned 7.47 g/t Au over 13.12m from 68.58m depth; including 21.5 g/t Au over 
1.52m from 68.58m depth and 9.52 g/t Au over 6.096m from 74.68m depth.

True thickness is estimated to be between 65 - 95% of the reported intercepts. 
Assay results range from trace to 21.5g/t Au. Significant results are detailed 
in the table below.

/T/

(2) Reported in the Independent Technical Report for the White Gold Project,
Dawson Range, Yukon, Canada by Gilles Arseneau, P.Geo. dated Sept. 15th,
2017 and is available on SEDAR
(3) Reported in the Company's news release dated Nov. 6, 2017, and is
available on SEDAR
(4) Reported in Underworld Resources Inc. ("UW") news release UW2008 - NR#6
dated Aug. 6, 2008 and is available on SEDAR


----------------------------------------------------------------------------
Golden Saddle - 2017 RC Drill Holes
----------------------------------------------------------------------------
Hole ID                       From (m)      To (m)  Interval (m)    Au (g/t)
----------------------------------------------------------------------------
WHTGS17RC-010                   59.436      88.392        28.956        3.99
----------------------------------------------------------------------------
Including                       62.484      73.152        10.668       10.09
----------------------------------------------------------------------------
Including                       67.056      71.628         4.572       14.63
----------------------------------------------------------------------------
WHTGS17RC-013                    68.58      82.296        13.716        7.47
----------------------------------------------------------------------------
Including                        68.58      70.104         1.524        21.5
----------------------------------------------------------------------------
Including                       74.676      80.772         6.096        9.52
----------------------------------------------------------------------------
WHTGS17RC-014                  128.016     140.208        12.192        1.83
----------------------------------------------------------------------------
WHTGS17RC-015                   21.336       22.86         4.572        1.22
----------------------------------------------------------------------------
And                            135.636     156.972        21.336        0.95
----------------------------------------------------------------------------
Including                      138.684     149.352        10.668        1.59
----------------------------------------------------------------------------

/T/

The 2017 drilling campaign on the White Gold Property represents the first 
drilling program on the property since the previous operator, Kinross Gold 
Corp. A total of 4,432m over 31 RC holes and 1,295m over 4 diamond holes have 
been completed by the Company in 2017 on the White Gold property. This includes 
4,151m of drilling on the Golden Saddle deposit with additional drilling on the 
Arc deposit and newly identified Golden Saddle East and Ulli's target areas. 
Complete results have been reported for 18 of the RC holes and 4 diamond drill 
holes to date. Assays for the additional holes will be reported in due course.

(1) Information Regarding Historical Resources/Deposits

All historical scientific and technical information relating to the White Gold 
Properties is based on and derived from the 43-101 report titled "White Gold 
Property Dawson Range Yukon, Canada" dated March 3, 2010, prepared by Lars 
Weiershauser, P.Geo, Marek Nowak, P.Eng and Wayne Barnett, Pr.Sci.Nat. of SRK 
Consulting (Canada) Inc.) (the "Technical Report") available on Sedar and other 
information available to the Company as referenced herein. The property was 
historically explored by Underworld Resources from 2007 - 2009 and included the 
discovery of the Golden Saddle and Arc deposits. In 2010, Underworld reported a 
resource estimate of 1,004,570 ounces contained in 9.80 Mt at a grade of 3.19 
g/t Au in an Indicated category, with an additional 407,410 ounces contained in 
5.02 Mt at a grade of 2.5 g/t Au in an Inferred category for the Golden Saddle 
deposit. At the Arc deposit, the initial resource included 170,470 ounces 
contained within 4.37 Mt at a grade of 1.21 g/t Au in the inferred category 
(reported in Underworld Resources New Release UW2010-NR#2 dated January 19, 
2010 and the Technical Report. Kinross purchased Underworld shortly after the 
initial resource was released in 2010 and explored the property from 2010 - 
2012. In 2013, Kinross released the results of a resource estimate for the 
Golden Saddle deposit and reported a resource of 840,000 ounces within 9.79 Mt 
at a grade of 2.67 g/t Au in an Indicated category, with an additional 125,000 
ounces within 2.17 Mt at a grade of 1.8 g/t Au in an Inferred category 
(reported in Kinross Gold Corp.'s 2016 Mineral Reserves and Resource 
Statement). Both Underworld's and Kinross' resource estimates are considered 
historical estimates and the Company is not treating them as current mineral 
resources. Although the Company believes these sources to be generally 
reliable, such information is subject to interpretation and cannot be verified 
with complete certainty due to limits on the availability and reliability of 
raw data, the voluntary nature of the data gathering process and other inherent 
limitations and uncertainties. In addition to the Golden Saddle and Arc 
deposits, there are numerous other targets known on the property that warrant 
follow-up work (for more information see Yukon Assessment Report #'s 095338, 
096206, & 096207).

The information contained herein is subject to all of the assumptions, 
qualifications and procedures set out in the Technical Report and reference 
should be made to the full details of the Technical Report which may be 
obtained from the Company by contacting dschmidt@whitegoldcorp.ca. Disclosure 
of the historical estimates in this news release is derived from the Technical 
Report and other information as set forth above previous press releases of the 
company as available on Sedar and has been judged to be relevant and therefore 
suitable for disclosure, however should not be relied upon. There are numerous 
uncertainties inherent in the historical estimates, which are subject to all of 
the assumptions, parameters and methods used to prepare such historical 
estimates and reference is made to the full text of the Technical Report with 
respect thereto. The historic estimates of mineral resources were estimated in 
conformity with generally accepted CIM "Estimation of Mineral Resource and 
Mineral Reserve Best Practices" Guidelines. Mineral resources are not mineral 
reserves and do not have demonstrated economic viability. There are no other 
recent estimates or data are available to the Company as at the date of this 
news release and a detailed exploration program is required to be conducted by 
the Company in order to verify or treat the historical estimate as a current 
mineral resource. A qualified person has not done sufficient work to classify 
the historical estimates as current mineral resources or mineral reserves and 
the Company is not treating the historical estimate as current mineral 
resources.

The Company encourages individuals interested in the Company to visit its 
website (www.whitegoldcorp.ca) to further understand the size and scope of the 
Company's projects in the White Gold District.
The analytical work for the 2017 program has been performed by Bureau Veritas 
Commodities Canada Ltd., an internationally recognized analytical services 
provider, at its Vancouver, British Columbia laboratory. Sample preparation was 
carried out at its Whitehorse, Yukon facility. All soil samples were using 
procedure SS80 (dry at 60 C and sieve 100g at -80 mesh) and analyzed by method 
AQ201 (aqua regia digestion and ICP-MS analysis). All rock, GT Probe, RAB, RC, 
and diamond core samples were prepared using procedure PRP70-250 (crush, split 
and pulverize 250 g to 200 mesh) and analyzed by method FA430 (30g fire assay 
with AAS finish) and AQ200 (0.5g, aqua regia digestion and ICP-MS analysis). 
Samples containing greater than 10g/t Au were reanalyzed using method FA530 
(30g Fire Assay with gravimetric finish). Metallic-screen analysis may also be 
utilized if coarse gold mineralization is encounter (FS600).

Qualified Person

Jodie Gibson, PGeo, VP, Exploration of the Company is a "qualified person" as 
defined under National Instrument 43-101 - Standards of Disclosure for Mineral 
Projects ("NI 43-101"), and has reviewed and approved the content of this news 
release. Potential quantity and grade is conceptual in nature. There has been 
insufficient exploration to define a mineral resource on any of the Company's 
properties to date, and it is uncertain if further exploration will result in 
any such target being delineated as a mineral resource.

The reported work was completed using industry standard procedures, including a 
quality assurance/quality control (QA/QC) program consisting of the insertion 
of certified standards, blanks, and field duplicates into the sample stream. 
The qualified person detected no significant QA/QC issues during review of the 
data.

About White Gold Corp.

The Company owns a portfolio of 19,438 quartz claims across 30 properties 
covering over 390,000 hectares representing approximately 40% of the Yukon's 
White Gold district. Preliminary exploration work has produced several 
prospective targets. The claim packages are bordered by sizable gold 
discoveries including the Coffee project owned by Goldcorp Inc., Western Copper 
and Gold Corporation's Casino project, and the Golden Saddle and Arc deposits 
acquired by the Company in June 2017 from Kinross Gold Corp. The Company has 
outlined an aggressive exploration plan to further explore its properties. For 
more information visit www.whitegoldcorp.ca.

Cautionary Note Regarding Forward Looking Information

This news release contains "forward-looking information" and "forward-looking 
statements" (collectively, "forward-looking statements") within the meaning of 
the applicable Canadian securities legislation. All statements, other than 
statements of historical fact, are forward-looking statements and are based on 
expectations, estimates and projections as at the date of this news release. 
Any statement that involves discussions with respect to predictions, 
expectations, beliefs, plans, projections, objectives, assumptions, future 
events or performance (often but not always using phrases such as "expects", or 
"does not expect", "is expected", "anticipates" or "does not anticipate", 
"plans", "budget", "scheduled", "forecasts", "estimates", "believes" or 
"intends" or variations of such words and phrases or stating that certain 
actions, events or results "may" or "could", "would", "might" or "will" be 
taken to occur or be achieved) are not statements of historical fact and may be 
forward-looking statements. In this news release, forward-looking statements 
relate, among other things, to: the anticipated benefits to the Company and its 
shareholders respecting the Company's objectives, goals and exploration 
activities conducted and proposed to be conducted at the White Gold properties; 
future growth potential of the Company, including whether any mineral resource 
will be established in accordance with NI 43-101 at any of the Company's 
properties; exploration results; and future exploration plans.

These forward-looking statements are based on reasonable assumptions and 
estimates of management of the Company at the time such statements were made. 
Actual future results may differ materially as forward-looking statements 
involve known and unknown risks, uncertainties and other factors which may 
cause the actual results, performance or achievements of the Company to 
materially differ from any future results, performance or achievements 
expressed or implied by such forward-looking statements. Such factors, among 
other things, include: the expected benefits to the Company relating to the 
exploration conducted and proposed to be conducted at the White Gold 
properties; failure to identify mineral resources; the preliminary nature of 
metallurgical test results; uncertainties relating to the availability and 
costs of financing needed in the future, including to fund any exploration 
programs on the White Gold properties and the Company's other properties; 
business integration risks; fluctuations in general macroeconomic conditions; 
fluctuations in securities markets; fluctuations in spot and forward prices of 
gold, silver, base metals or certain other commodities; fluctuations in 
currency markets (such as the Canadian dollar to United States dollar exchange 
rate); change in national and local government, legislation, taxation, 
controls, regulations and political or economic developments; risks and hazards 
associated with the business of mineral exploration, development and mining 
(including environmental hazards, industrial accidents, unusual or unexpected 
formations pressures, cave-ins and flooding); inability to obtain adequate 
insurance to cover risks and hazards; the presence of laws and regulations that 
may impose restrictions on mining; employee relations; relationships with and 
claims by local communities and indigenous populations; availability of 
increasing costs associated with mining inputs and labour; the speculative 
nature of mineral exploration and development (including the risks of obtaining 
necessary licenses, permits and approvals from government authorities); the 
unlikelihood that properties that are explored are ultimately developed into 
producing mines; geological factors; actual results of current and future 
exploration; changes in project parameters as plans continue to be evaluated; 
soil sampling results being preliminary in nature and are not conclusive 
evidence of the likelihood of a mineral deposit; title to properties; and those 
factors described under the heading "Risks and Uncertainties" in the Company's 
most recently filed management's discussion and analysis.

Although the forward-looking statements contained in this news release are 
based upon what management of the Company believes, or believed at the time, to 
be reasonable assumptions, the Company cannot assure shareholders that actual 
results will be consistent with such forward-looking statements, as there may 
be other factors that cause results not to be as anticipated, estimated or 
intended. Accordingly, readers should not place undue reliance on 
forward-looking statements and information. There can be no assurance that 
forward-looking information, or the material factors or assumptions used to 
develop such forward-looking information, will prove to be accurate. The 
Company does not undertake any obligations to release publicly any revisions 
for updating any voluntary forward-looking statements, except as required by 
applicable securities law.

Neither the TSX Venture Exchange (the "Exchange") nor its Regulation Services 
Provider (as that term is defined in the policies of the Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

- 30 -

CONTACT INFO:

White Gold Corp.
David D'Onofrio
Chief Executive Officer
(416) 643-3880
ddonofrio@whitegoldcorp.ca
www.whitegoldcorp.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=600723085