Source	MARKET NEWS
Date	11/27/2017
Time	05:44:07 AM

Company	 BTU Metals Corp.
Title	BTU Galway Gold 
Update Exploration Team Discover





    CDNX Symbol: BTU











Press Release





BTU METALS CORP ("BTU-V")
- BTU Galway Gold Update - Exploration Team Discovers New Vein At
- Lee Target, Galway, Ireland

BTU METALS CORP. ("BTU" or the "Company") reports the following
exploration program update for the Company's Galway Gold property. The
Exploration Team is currently conducting geological mapping, sampling,
prospecting, as well as Magnetometer, and Ground Penetrating Radar
(GPR) surveys at the Lee, Teernakill, Fooey, and Glenlusk target areas.


At the Lee area, a new vein has been discovered approximately 250
meters from the Lee vein. The vein is trending northwest at right
angles to the Lee vein and is associated with a fault structure that
cuts the foliated schist. The mineralogy of the vein is similar to
samples taken in the southeast portion of the Lee Valley which contains
several locations where multi-gram gold samples have been found (see PR
dated July 27, 2017).

"The discovery of a new vein at Lee is very encouraging. We look
forward to obtaining assays and the interpretation of geophysics from
this current program in order to define drill targets for 2018." stated
Paul Wood, CEO of BTU.

A 20 line kilometer grid has been surveyed over and extending from
the previously identified areas of high-grade gold mineralization.
Ground magnetometer surveys have been completed over the grid and a
programme of high-density deep-overburden soil sampling is currently
being carried out. Preliminary magnetometer results suggest an
east-west trending lithology contact occurs parallel to Lee Creek and
adjacent to the Lee vein showing, as well as several fault structures
which coincide with north-south trending creek gullies.

A ground penetrating radar survey has been permitted by the EMD on
the Lee grid, and Terravision UK will begin this survey on November
27th, 2017. Terravision's GPRPlus system is a state of the art method
of overburden and bedrock surveying which is useful in identifying vein
and fault structures in the Dalradian Group gold-bearing metamorphic
rocks of Ireland.

The historic Teernakill mine site is also undergoing further
exploration.  Ground magnetics surveys as well as geological mapping
and sampling have been completed. At Teernakill, sulphide replacement
zones consisting of massive and semi-massive pyrrhotite and
chalcopyrite occur intermittently over a strike-length of approximately
500 meters and widths ranging between 1-4 meters.  Several new areas of
mineralization located outside of the historical mine workings have
been discovered.

At the Glenlusk target area, angular float samples taken in 2015
returned 930 ppb, 2370 ppb, and 5066 ppb gold respectively (Gold Note
Minerals, 2015).  For the 2017 programme, extensive geological mapping
and rock sampling (including bedrock), as well as magnetometer surveys
have been carried out over the primary area of interest.  This work has
traced a north-south fault structure that cuts the east-west trend of
the country rock. The geological setting is similar to the Bohaun Gold
Occurrence located 4.5km to the north.  Bohaun is a north-northeast
trending, steeply dipping quartz breccia zone that has seen extensive
exploration for epithermal gold mineralization.

Fooey Target Area: In the summer of 2016, a fixed wing high
resolution aeromagnetic survey conducted by Sander Geophysics Ltd (on
behalf of the Geological Survey of Ireland) identified a 0.5 X 7
kilometer, east-west trending high strength positive anomaly that
correlates with surface exposures of Bencorragh Formation metamorphosed
pillow lava located south of Lough Nafooy.  Geological mapping,
geochemical rock sampling, and ground magnetometer geophysics were
carried out over this formation.  Widespread jasper-bearing chert
horizons occur as late-stage layers and fragmental zones within the
formation.  Localized high order positive magnetometer anomalies
correlate with layered and fragmental bright red coloured ferruginous
chert, as well as increased amounts of disseminated pyrite, pyrrhotite,
and minor chalcopyrite.  Ground magnetometer geophysics and geological
mapping has identified several prospective zones.  Additionally, vuggy
crystalline quartz veins with saccharoidal-crustiform textures and
sparse sulphide mineralization occur as late stage infillings,
suggesting potential for low sulphidation, epithermal deposit types
similar to Bohaun located 3.5 km to the south-east.

Andris Kikauka, P.Geo, is a qualified person as defined by
National Instrument 43-101 who has examined and described the mineral
occurrences within BTU Metals Corp Irish prospecting licenses and is
responsible for reviewing and approving the technical contents of this
press release.

About BTU Metals Corp

BTU Metals is a Canadian-based junior exploration company focused
on developing its Galway Gold project located in Ireland and the
Shakespeare Gold project in Ontario. For more information on BTU Metals
Corp. please visit our website located at www.btumetals.com.

ON BEHALF OF THE BOARD
"Paul Wood"
Paul Wood, CEO, Director

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

FORWARD LOOKING STATEMENTS: This news release contains
forward-looking statements, which relate to future events or future
performance and reflect management's current expectations and
assumptions. Such forward-looking statements reflect management's
current beliefs and are based on assumptions made by and information
currently available to the Company. Investors are cautioned that these
forward looking statements are neither promises nor guarantees, and are
subject to risks and uncertainties that may cause future results to
differ materially from those expected. These forward -looking
statements are made as of the date hereof and, except as required under
applicable securities legislation, the Company does not assume any
obligation to update or revise them to reflect new events or
circumstances. All of the forward-looking statements made in this press
release are qualified by these cautionary statements and by those made
in our filings with SEDAR in Canada (available at WWW.SEDAR.COM).


TEL:  1-604-683-3995

TEL:  1-888-945-4770
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1733000010TS11733001156-05421020171127