Source	Marketwire
Date	11/28/2017
Time	04:32:52 AM

Company	 MONUMENT MINING LIMITED
Title	Monument Announces Encouraging Results from Recent Drilling at New Gold 
Field Peranggih Project





    CDNX Symbol: MMY











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Monument Mining Limited

TSX VENTURE SYMBOL: MMY
FRANKFURT SYMBOL: D7Q1

November 28, 2017

Monument Announces Encouraging Results from Recent Drilling at New Gold Field 
Peranggih Project


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Nov. 28, 2017) - Monument Mining 
Limited (TSX VENTURE:MMY)(FRANKFURT:D7Q1) "Monument" or the "Company" is 
pleased to report significant results from its recently completed drilling 
program at the Peranggih Gold Prospect, located approximately 10 km North of 
the Selinsing Gold Mine (Figure 1). A close spaced 5m x 5m Rotary Air Blast 
(RAB) drilling program together with previous exploration has successfully 
delineated a zone of higher grade gold material, indicating that the 
mineralization occurs in the same regional shearing structure hosting Selinsing 
and Buffalo Reef deposits.

Highlights of Significant Intercepts

The recent 2017 close spaced RAB drilling program was carried out at an 
historic mining site to test 150m strike length x 80m width of the 
mineralization. This allowed the accurate identification of several high grade 
gold (HG) zones surrounded by a main low grade (LG) halo. The significant drill 
intersections (Au greater than 2.0 g/t & greater than 5m length) within a more 
consistent high grade gold area are presented in Table 1.The full set of drill 
results for the holes intercepting this HG gold mineralization occurrence are 
listed in Appendix A and Appendix B.

The Peranggih Prospect has been identified as a new Gold Field that has the 
potential to host a significant mineralized hydrothermal breccia system.

Figure 1 - Local Geology of the Peranggih Area is available at the following 
address: http://media3.marketwire.com/docs/Figure1MMY.jpg

/T/

Table 1: Highlight of the best intercepts at Peranggih - Close Spaced RAB
Drilling in 2017
----------------------------------------------------------------------------
Drilled Width  approx. True
HOLE ID(i)         From(m)    To (m)           (m)     Width (m)      Au g/t
----------------------------------------------------------------------------
1_PGC006                 2         8           6.0           4.3        3.07
1_PGC007                 0        10          10.0           6.7        2.94
1_PGC019                 0        10          10.0           7.7        2.28
1_PGC020                 0         5           5.0           3.9        2.68
1_PGC428                 1        10           9.0           6.6        3.14
1_PGC429                 1        10           9.0           8.0        2.34
1_PGC430                 0        10          10.0           8.7        2.49
----------------------------------------------------------------------------
(i)all vertical holes

/T/

The low and high grade gold mineralization is hosted in both matrix supported 
and clast supported quartz breccia. Significant coarse free gold was observed 
hosted in the breccia matrix. The matrix is friable and loose material 
composing clay minerals and small rock fragments, as well as mixed ore and/or 
gangue minerals (Figure 2).

Figure 2 - Exposure of highly fractured quartz breccia on the old pit wall is 
available at the following address: 
http://media3.marketwire.com/docs/Figure2MMY.jpg

This leads to a nugget effect on the gold distribution throughout the deposit. 
The presence of well crystallized coarse free disseminated gold in the matrixes 
was not well recognized during the earlier exploration campaigns. This key 
finding had changed the perspective and approach facilitate better and more 
appropriate sampling and analysis methods to be applied to future exploration 
programs which include comparative work between traditional fire assay, screen 
fire assay as well as reconciliation of grade by way of bulk sampling.

The close spaced shallow drilling can be used as a cost effective tool to 
define shallow and broad gold mineralization within the breccia matrix that 
occur at this site

Peranggih

Peranggih was historically mined in the late 1980's and into the early 1990's 
by local artisanal miners. Gold was recovered by traditional sluicing and 
residual tailings and other evidence indicates substantial work was undertaken 
throughout this period.

In 2014 the company conducted exploration drilling with encouraging results, 
followed by soil sampling, trenching and other reconnaissance mapping to 
understand the extent and boundaries of the system at Peranggih. The recent 
work determined that the gold mineralization is associated with a hydrothermal 
breccia system which is distinct from the hydrothermal veins system that occurs 
at Selinsing and Buffalo Reef, but still related to the same regional shearing 
structuring.

Previous activities plus more recent exploration works, totaling 1,700m for 21 
trenches, 2,900m of Diamond Drilling (DD) and Reverse Circulation (RC) drilling 
for 35 drill holes, and 2,800m of close spaced RAB drilling for approximately 
300 drill holes (completed in 2017) have been used to outline an exploration 
target of 20,000 to 30,000 oz Au contained within 1 to 2 Mt @ 0.3 to 2.0 g/t 
Au. The potential tonnages and grades are conceptual in nature and are based on 
historical and recent drill and trench results that defined the approximate 
length, thickness, depth and grade of the portion of the internal resource 
estimate. There has been insufficient exploration to define a current resource, 
and the Company cautions that there is a risk that further exploration will not 
completely result in the delineation of a current mineral resource.

Sampling, assaying and cyanide leach test work to date shows that recoveries 
exceed 80% ranging up to 98%. The system extends over a distance of 
approximately 1.2 kilometers in length with varying widths of between 25 to 50 
meters with identified areas of high gold grade mineralization surrounded by a 
halo of lower grade mineralization. The system is open down dip and along 
strike.

Follow up Exploration Programs

Further exploration work primarily aims to carry out resource definition 
drilling around an area selected for bulk sample testwork. Regional exploration 
should also identify other target areas within the same Peranggih oxide system, 
eventually adding oxide mill feed sources to the Company.

The Company plans to mine a bulk sample of up to 50,000 tonnes, feed it to the 
existing Selinsing oxide gold processing plant to establish the average grade 
of the close spaced drilled area; and test the metallurgical performance at 
plant scale. This work can commence as soon as the access road has been 
prepared which is estimated to be in the beginning of 2018.

Roger Stangler, Chief Managing Geologist of the Company, MEng, MAusIMM, MAIG, 
has prepared, reviewed, supervised the preparation and approved the scientific 
and technical disclosure in this news release as a Qualified Person under 
NI43-101 standards.

About Monument

Monument Mining Limited (TSX VENTURE:MMY)(FRANKFURT:D7Q1) is an established 
Canadian gold producer that owns and operates the Selinsing Gold Mine in 
Malaysia. Its experienced management team is committed to growth and is 
advancing several exploration and development projects including the Mengapur 
Polymetallic Project, in Pahang State of Malaysia, and the Murchison Gold 
Projects comprising Burnakura, Gabanintha and Tuckanarra in the Murchison area 
of Western Australia. The Company employs approximately 190 people in both 
regions and is committed to the highest standards of environmental management, 
social responsibility, and health and safety for its employees and neighboring 
communities.

/T/

Robert F. Baldock, President and CEO
Monument Mining Limited
Suite 1580 -1100 Melville Street
Vancouver, BC V6E 4A6

/T/

FOR FURTHER INFORMATION visit the company web site at www.monumentmining.com.

"Neither TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release."

Forward-Looking Statement

This news release includes statements containing forward-looking information 
about Monument, its business and future plans ("forward-looking statements"). 
Forward-looking statements are statements that involve expectations, plans, 
objectives or future events that are not historical facts and include the 
Company's plans with respect to its mineral projects and the timing and results 
of proposed programs and events referred to in this news release. Generally, 
forward-looking information can be identified by the use of forward-looking 
terminology such as "plans", "expects" or "does not expect", "is expected", 
"budget", "scheduled", "estimates", "forecasts", "intends", "anticipates" or 
"does not anticipate", or "believes", or variations of such words and phrases 
or state that certain actions, events or results "may", "could", "would", 
"might" or "will be taken", "occur" or "be achieved". The forward-looking 
statements in this news release are subject to various risks, uncertainties and 
other factors that could cause actual results or achievements to differ 
materially from those expressed or implied by the forward-looking statements. 
These risks and certain other factors include, without limitation: risks 
related to general business, economic, competitive, geopolitical and social 
uncertainties; uncertainties regarding the results of current exploration 
activities; uncertainties in the progress and timing of development activities; 
foreign operations risks; other risks inherent in the mining industry and other 
risks described in the management discussion and analysis of the Company and 
the technical reports on the Company's projects, all of which are available 
under the profile of the Company on SEDAR at www.sedar.com.

Material factors and assumptions used to develop forward-looking statements in 
this news release include: expectations regarding the estimated cash cost per 
ounce of gold production and the estimated cash flows which may be generated 
from the operations, general economic factors and other factors that may be 
beyond the control of Monument; assumptions and expectations regarding the 
results of exploration on the Company's projects; assumptions regarding the 
future price of gold of other minerals; the timing and amount of estimated 
future production; the expected timing and results of development and 
exploration activities; costs of future activities; capital and operating 
expenditures; success of exploration activities; mining or processing issues; 
exchange rates; and all of the factors and assumptions described in the 
management discussion and analysis of the Company and the technical reports on 
the Company's projects, all of which are available under the profile of the 
Company on SEDAR at www.sedar.com. Although the Company has attempted to 
identify important factors that could cause actual results to differ materially 
from those contained in forward-looking statements, there may be other factors 
that cause results not to be as anticipated, estimated or intended. There can 
be no assurance that such statements will prove to be accurate, as actual 
results and future events could differ materially from those anticipated in 
such statements. Accordingly, readers should not place undue reliance on 
forward-looking statements. The Company does not undertake to update any 
forward-looking statements, except in accordance with applicable securities 
laws.

/T/

Appendix A
- Peranggih Close Spaced RAB Drilling Campaign 2017: collar coordinates in
Kertau MRSO Coordinate System

----------------------------------------------------------------------------
End of Hole
Hole ID      Depth (m)        East       North          RL     Dip   Azimuth
----------------------------------------------------------------------------
1_PGC005            10    422963.2    480242.3     130.438     -90         0
----------------------------------------------------------------------------
1_PGC006            10    422967.8    480242.3     130.179     -90         0
----------------------------------------------------------------------------
1_PGC007            10    422973.1    480242.3     124.445     -90         0
----------------------------------------------------------------------------
1_PGC008             2    422978.2    480242.3     123.833     -90         0
----------------------------------------------------------------------------
1_PGC016            10    422955.7    480247.3     132.874     -90         0
----------------------------------------------------------------------------
1_PGC017            10    422960.5    480247.3     130.778     -90         0
----------------------------------------------------------------------------
1_PGC018            10    422965.6    480247.3     129.522     -90         0
----------------------------------------------------------------------------
1_PGC019            10    422971.3    480247.3     125.017     -90         0
----------------------------------------------------------------------------
1_PGC020            10    422975.6    480247.3     124.231     -90         0
----------------------------------------------------------------------------
1_PGC021            10    422980.7    480247.3     123.698     -90         0
----------------------------------------------------------------------------
1_PGC022            10    422985.6    480247.4     122.141     -90         0
----------------------------------------------------------------------------
1_PGC027            10    422948.2    480252.4     135.437     -90         0
----------------------------------------------------------------------------
1_PGC028            10    422953.1    480252.3     134.800     -90         0
----------------------------------------------------------------------------
1_PGC029            10    422958.3    480252.3     130.241     -90         0
----------------------------------------------------------------------------
1_PGC030            10    422963.2    480252.3     129.090     -90         0
----------------------------------------------------------------------------
1_PGC031            10    422968.2    480252.3     128.233     -90         0
----------------------------------------------------------------------------
1_PGC032            10    422973.2    480252.3     124.222     -90         0
----------------------------------------------------------------------------
1_PGC039            10    422950.6    480257.4     135.578     -90         
0----------------------------------------------------------------------------
1_PGC041            10    422960.6    480257.4     128.047     -90         0
----------------------------------------------------------------------------
1_PGC042            10    422965.7    480257.3     127.773     -90         0
----------------------------------------------------------------------------
1_PGC043            10    422970.6    480257.4     123.188     -90         0
----------------------------------------------------------------------------
1_PGC418            10    422972.5    480232.8     126.364     -90         0
----------------------------------------------------------------------------
1_PGC419            10    422977.5    480232.8     124.996     -90         0
----------------------------------------------------------------------------
1_PGC427            10    422965.0    480237.8     129.692     -90         0
----------------------------------------------------------------------------
1_PGC428            10    422969.9    480237.6     127.706     -90         0
----------------------------------------------------------------------------
1_PGC429            10    422975.0    480237.7     125.965     -90         0
----------------------------------------------------------------------------
1_PGC430            10    422980.0    480237.8     123.571     -90         0
----------------------------------------------------------------------------
1_PGC431            10    422985.0    480237.8     122.895     -90         0
----------------------------------------------------------------------------

Appendix B
- Assay Results for Peranggih Close Spaced RAB Drilling Campaign 2017
----------------------------------------------------------------------------
Hole ID  From (m)  To (m)    Au g/t   Hole ID    From (m)  To (m)  Au g/t
-----------------------------------   -----------------------------------
1_PGC005        0       1     0.394   1_PGC017          4       5   0.303
-----------------------------------   -----------------------------------
1_PGC005        1       2     1.203   1_PGC017          5       6   0.154
-----------------------------------   -----------------------------------
1_PGC005        2       3     0.257   1_PGC017          6       7   0.122
-----------------------------------   -----------------------------------
1_PGC005        3       4     1.438   1_PGC017          7       8   0.116
-----------------------------------   -----------------------------------
1_PGC005        4       5     0.697   1_PGC017          8       9   0.108
-----------------------------------   -----------------------------------
1_PGC005        5       6     0.460   1_PGC017          9      10   0.095
-----------------------------------   -----------------------------------
1_PGC005        6       7     0.351   1_PGC018          0       1   0.738
-----------------------------------   -----------------------------------
1_PGC005        7       8     0.089   1_PGC018          1       2   2.167
-----------------------------------   -----------------------------------
1_PGC005        8       9     1.194   1_PGC018          2       3   1.709
-----------------------------------   -----------------------------------
1_PGC005        9      10     2.935   1_PGC018          3       4   1.526
-----------------------------------   -----------------------------------
1_PGC006        0       1     0.361   1_PGC018          4       5   2.502
-----------------------------------   -----------------------------------
1_PGC006        1       2     0.385   1_PGC018          5       6   0.130
-----------------------------------   -----------------------------------
1_PGC006        2       3     1.553   1_PGC018          6       7   1.681
-----------------------------------   -----------------------------------
1_PGC006        3       4     2.640   1_PGC018          7       8   0.491
-----------------------------------   -----------------------------------
1_PGC006        4       5     3.702   1_PGC018          8       9   0.037
-----------------------------------   -----------------------------------
1_PGC006        5       6     2.744   1_PGC018          9      10   0.209
-----------------------------------   -----------------------------------
1_PGC006        6       7     3.093   1_PGC019          0       1   2.037
-----------------------------------   -----------------------------------
1_PGC006        7       8     4.687   1_PGC019          1       2   1.645
-----------------------------------   -----------------------------------
1_PGC006        8       9     0.055   1_PGC019          2       3   1.131
-----------------------------------   -----------------------------------
1_PGC006        9      10     0.101   1_PGC019          3       4   1.150
-----------------------------------   -----------------------------------
1_PGC007        0       1     3.269   1_PGC019          4       5   1.008
-----------------------------------   -----------------------------------
1_PGC007        1       2    11.440   1_PGC019          5       6   2.205
-----------------------------------   -----------------------------------
1_PGC007        2       3     1.194   1_PGC019          6       7   3.410
-----------------------------------   -----------------------------------
1_PGC007        3       4     1.299   1_PGC019          7       8   4.692
-----------------------------------   -----------------------------------
1_PGC007        4       5     1.192   1_PGC019          8       9   3.210
-----------------------------------   -----------------------------------
1_PGC007        5       6     1.952   1_PGC019          9      10   2.272
-----------------------------------   -----------------------------------
1_PGC007        6       7     3.392   1_PGC020          0       1   7.756
-----------------------------------   -----------------------------------
1_PGC007        7       8     2.340   1_PGC020          1       2   2.274
-----------------------------------   -----------------------------------
1_PGC007        8       9     1.933   1_PGC020          2       3   1.623
-----------------------------------   -----------------------------------
1_PGC007        9      10     1.387   1_PGC020          3       4   1.038
-----------------------------------   -----------------------------------
1_PGC008        0       1     1.599   1_PGC020          4       5   0.711
-----------------------------------   -----------------------------------
1_PGC008        1       2     3.483   1_PGC020          5       6   0.458
-----------------------------------   -----------------------------------
1_PGC016        0       1     0.155   1_PGC020          6       7   0.421
-----------------------------------   -----------------------------------
1_PGC016        1       2     0.105   1_PGC020          7       8   0.342
-----------------------------------   -----------------------------------
1_PGC016        2       3     0.740   1_PGC020          8       9   0.783
-----------------------------------   -----------------------------------
1_PGC016        3       4     0.118   1_PGC020          9      10   0.834
-----------------------------------   -----------------------------------
1_PGC016        4       5     0.197   1_PGC021          0       1   1.646
-----------------------------------   -----------------------------------
1_PGC016        5       6     0.286   1_PGC021          1       2   0.279
-----------------------------------   -----------------------------------
1_PGC016        6       7     0.254   1_PGC021          2       3   1.166
-----------------------------------   -----------------------------------
1_PGC016        7       8     0.133   1_PGC021          3       4   0.231
-----------------------------------   -----------------------------------
1_PGC016        8       9     0.033   1_PGC021          4       5   0.308
-----------------------------------   -----------------------------------
1_PGC016        9      10     0.094   1_PGC021          5       6   0.354
-----------------------------------   -----------------------------------
1_PGC017        0       1     0.880   1_PGC021          6       7   0.987
-----------------------------------   -----------------------------------
1_PGC017        1       2     0.815   1_PGC021          7       8   0.148
-----------------------------------   -----------------------------------
1_PGC017        2       3     0.110   1_PGC021          8       9   1.202
-----------------------------------   -----------------------------------
1_PGC017        3       4     0.441   1_PGC021          9      10   0.560
-----------------------------------   -----------------------------------


Appendix B
- Assay Results for Peranggih Close Spaced
RAB Drilling Campaign 2017
--------------------------------------------
Hole ID  Hole ID  From (m)  To (m)    Au g/t
--------------------------------------------
1_PGC005 1_PGC022        0       1     1.046
--------------------------------------------
1_PGC005 1_PGC022        1       2     0.269
--------------------------------------------
1_PGC005 1_PGC022        2       3     0.260
--------------------------------------------
1_PGC005 1_PGC022        3       4     0.173
--------------------------------------------
1_PGC005 1_PGC022        4       5     0.124
--------------------------------------------
1_PGC005 1_PGC022        5       6     0.279
--------------------------------------------
1_PGC005 1_PGC022        6       7     0.265
--------------------------------------------
1_PGC005 1_PGC022        7       8     0.199
--------------------------------------------
1_PGC005 1_PGC022        8       9     0.119
--------------------------------------------
1_PGC005 1_PGC022        9      10     0.097
--------------------------------------------
1_PGC006 1_PGC027        0       1     0.266
--------------------------------------------
1_PGC006 1_PGC027        1       2     1.006
--------------------------------------------
1_PGC006 1_PGC027        2       3     0.367
--------------------------------------------
1_PGC006 1_PGC027        3       4     0.355
--------------------------------------------
1_PGC006 1_PGC027        4       5     0.110
--------------------------------------------
1_PGC006 1_PGC027        5       6     5.651
--------------------------------------------
1_PGC006 1_PGC027        6       7     0.200
--------------------------------------------
1_PGC006 1_PGC027        7       8     0.100
--------------------------------------------
1_PGC006 1_PGC027        8       9     0.235
--------------------------------------------
1_PGC006 1_PGC027        9      10     0.250
--------------------------------------------
1_PGC007 1_PGC028        0       1     0.284
--------------------------------------------
1_PGC007 1_PGC028        1       2     0.252
--------------------------------------------
1_PGC007 1_PGC028        2       3     2.392
--------------------------------------------
1_PGC007 1_PGC028        3       4     0.640
--------------------------------------------
1_PGC007 1_PGC028        4       5     0.109
--------------------------------------------
1_PGC007 1_PGC028        5       6     0.297
--------------------------------------------
1_PGC007 1_PGC028        6       7     0.209
--------------------------------------------
1_PGC007 1_PGC028        7       8     0.215
--------------------------------------------
1_PGC007 1_PGC028        8       9     2.740
--------------------------------------------
1_PGC007 1_PGC028        9      10     1.645
--------------------------------------------
1_PGC008 1_PGC029        0       1     0.750
--------------------------------------------
1_PGC008 1_PGC029        1       2     0.574
--------------------------------------------
1_PGC016 1_PGC029        2       3     0.543
--------------------------------------------
1_PGC016 1_PGC029        3       4     0.260
--------------------------------------------
1_PGC016 1_PGC029        4       5     0.164
--------------------------------------------
1_PGC016 1_PGC029        5       6     0.220
--------------------------------------------
1_PGC016 1_PGC029        6       7     0.115
--------------------------------------------
1_PGC016 1_PGC029        7       8     0.074
--------------------------------------------
1_PGC016 1_PGC029        8       9     0.350
--------------------------------------------
1_PGC016 1_PGC029        9      10     0.253
--------------------------------------------
1_PGC016 1_PGC030        0       1     1.499
--------------------------------------------
1_PGC016 1_PGC030        1       2     0.797
--------------------------------------------
1_PGC017 1_PGC030        2       3     0.446
--------------------------------------------
1_PGC017 1_PGC030        3       4     0.507
--------------------------------------------
1_PGC017 1_PGC030        4       5     0.390
--------------------------------------------1_PGC017 1_PGC030        5       
6     0.640
--------------------------------------------

Appendix B (continued)

Assay Results for Peranggih Close Spaced RAB Drilling Campaign 2017
----------------------------------------------------------------------------
Hole ID   From (m)  To (m)   Au g/t   Hole ID   From (m)  To (m)   Au g/t
-----------------------------------   -----------------------------------
1_PGC030         6       7    0.374   1_PGC042         2       3    0.934
-----------------------------------   -----------------------------------
1_PGC030         7       8    0.087   1_PGC042         3       4    0.453
-----------------------------------   -----------------------------------
1_PGC030         8       9    0.121   1_PGC042         4       5    0.811
-----------------------------------   -----------------------------------
1_PGC030         9      10    0.068   1_PGC042         5       6    1.198
-----------------------------------   -----------------------------------
1_PGC031         0       1    0.690   1_PGC042         6       7    1.008
-----------------------------------   -----------------------------------
1_PGC031         1       2    0.839   1_PGC042         7       8    1.586
-----------------------------------   -----------------------------------
1_PGC031         2       3    1.229   1_PGC042         8       9    3.205
-----------------------------------   -----------------------------------
1_PGC031         3       4    1.295   1_PGC042         9      10    0.966
-----------------------------------   -----------------------------------
1_PGC031         4       5    4.061   1_PGC043         0       1    0.545
-----------------------------------   -----------------------------------
1_PGC031         5       6    0.192   1_PGC043         1       2    0.302
-----------------------------------   -----------------------------------
1_PGC031         6       7    2.164   1_PGC043         2       3    0.361
-----------------------------------   -----------------------------------
1_PGC031         7       8    4.235   1_PGC043         3       4    0.498
-----------------------------------   -----------------------------------
1_PGC031         8       9    0.070   1_PGC043         4       5    0.628
-----------------------------------   -----------------------------------
1_PGC031         9      10    0.129   1_PGC043         5       6    0.613


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Monument Mining Limited

TSX VENTURE SYMBOL: MMY
FRANKFURT SYMBOL: D7Q1

November 28, 2017

Monument Announces Encouraging Results from Recent Drilling at New Gold Field 
Peranggih Project


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Nov. 28, 2017) - Monument Mining 
Limited (TSX VENTURE:MMY)(FRANKFURT:D7Q1) "Monument" or the "Company" is 
pleased to report significant results from its recently completed drilling 
program at the Peranggih Gold Prospect, located approximately 10 km North of 
the Selinsing Gold Mine (Figure 1). A close spaced 5m x 5m Rotary Air Blast 
(RAB) drilling program together with previous exploration has successfully 
delineated a zone of higher grade gold material, indicating that the 
mineralization occurs in the same regional shearing structure hosting Selinsing 
and Buffalo Reef deposits.

Highlights of Significant Intercepts

The recent 2017 close spaced RAB drilling program was carried out at an 
historic mining site to test 150m strike length x 80m width of the 
mineralization. This allowed the accurate identification of several high grade 
gold (HG) zones surrounded by a main low grade (LG) halo. The significant drill 
intersections (Au greater than 2.0 g/t & greater than 5m length) within a more 
consistent high grade gold area are presented in Table 1.The full set of drill 
results for the holes intercepting this HG gold mineralization occurrence are 
listed in Appendix A and Appendix B.

The Peranggih Prospect has been identified as a new Gold Field that has the 
potential to host a significant mineralized hydrothermal breccia system.

Figure 1 - Local Geology of the Peranggih Area is available at the following 
address: http://media3.marketwire.com/docs/Figure1MMY.jpg

/T/

Table 1: Highlight of the best intercepts at Peranggih - Close Spaced RAB
Drilling in 2017
----------------------------------------------------------------------------
Drilled Width  approx. True
HOLE ID(i)         From(m)    To (m)           (m)     Width (m)      Au g/t
----------------------------------------------------------------------------
1_PGC006                 2         8           6.0           4.3        3.07
1_PGC007                 0        10          10.0           6.7        2.94
1_PGC019                 0        10          10.0           7.7        2.28
1_PGC020                 0         5           5.0           3.9        2.68
1_PGC428                 1        10           9.0           6.6        3.14
1_PGC429                 1        10           9.0           8.0        2.34
1_PGC430                 0        10          10.0           8.7        2.49
----------------------------------------------------------------------------
(i)all vertical holes

/T/

The low and high grade gold mineralization is hosted in both matrix supported 
and clast supported quartz breccia. Significant coarse free gold was observed 
hosted in the breccia matrix. The matrix is friable and loose material 
composing clay minerals and small rock fragments, as well as mixed ore and/or 
gangue minerals (Figure 2).

Figure 2 - Exposure of highly fractured quartz breccia on the old pit wall is 
available at the following address: 
http://media3.marketwire.com/docs/Figure2MMY.jpg

This leads to a nugget effect on the gold distribution throughout the deposit. 
The presence of well crystallized coarse free disseminated gold in the matrixes 
was not well recognized during the earlier exploration campaigns. This key 
finding had changed the perspective and approach facilitate better and more 
appropriate sampling and analysis methods to be applied to future exploration 
programs which include comparative work between traditional fire assay, screen 
fire assay as well as reconciliation of grade by way of bulk sampling.

The close spaced shallow drilling can be used as a cost effective tool to 
define shallow and broad gold mineralization within the breccia matrix that 
occur at this site

Peranggih

Peranggih was historically mined in the late 1980's and into the early 1990's 
by local artisanal miners. Gold was recovered by traditional sluicing and 
residual tailings and other evidence indicates substantial work was undertaken 
throughout this period.

In 2014 the company conducted exploration drilling with encouraging results, 
followed by soil sampling, trenching and other reconnaissance mapping to 
understand the extent and boundaries of the system at Peranggih. The recent 
work determined that the gold mineralization is associated with a hydrothermal 
breccia system which is distinct from the hydrothermal veins system that occurs 
at Selinsing and Buffalo Reef, but still related to the same regional shearing 
structuring.

Previous activities plus more recent exploration works, totaling 1,700m for 21 
trenches, 2,900m of Diamond Drilling (DD) and Reverse Circulation (RC) drilling 
for 35 drill holes, and 2,800m of close spaced RAB drilling for approximately 
300 drill holes (completed in 2017) have been used to outline an exploration 
target of 20,000 to 30,000 oz Au contained within 1 to 2 Mt @ 0.3 to 2.0 g/t 
Au. The potential tonnages and grades are conceptual in nature and are based on 
historical and recent drill and trench results that defined the approximate 
length, thickness, depth and grade of the portion of the internal resource 
estimate. There has been insufficient exploration to define a current resource, 
and the Company cautions that there is a risk that further exploration will not 
completely result in the delineation of a current mineral resource.

Sampling, assaying and cyanide leach test work to date shows that recoveries 
exceed 80% ranging up to 98%. The system extends over a distance of 
approximately 1.2 kilometers in length with varying widths of between 25 to 50 
meters with identified areas of high gold grade mineralization surrounded by a 
halo of lower grade mineralization. The system is open down dip and along 
strike.

Follow up Exploration Programs

Further exploration work primarily aims to carry out resource definition 
drilling around an area selected for bulk sample testwork. Regional exploration 
should also identify other target areas within the same Peranggih oxide system, 
eventually adding oxide mill feed sources to the Company.

The Company plans to mine a bulk sample of up to 50,000 tonnes, feed it to the 
existing Selinsing oxide gold processing plant to establish the average grade 
of the close spaced drilled area; and test the metallurgical performance at 
plant scale. This work can commence as soon as the access road has been 
prepared which is estimated to be in the beginning of 2018.

Roger Stangler, Chief Managing Geologist of the Company, MEng, MAusIMM, MAIG, 
has prepared, reviewed, supervised the preparation and approved the scientific 
and technical disclosure in this news release as a Qualified Person under 
NI43-101 standards.

About Monument

Monument Mining Limited (TSX VENTURE:MMY)(FRANKFURT:D7Q1) is an established 
Canadian gold producer that owns and operates the Selinsing Gold Mine in 
Malaysia. Its experienced management team is committed to growth and is 
advancing several exploration and development projects including the Mengapur 
Polymetallic Project, in Pahang State of Malaysia, and the Murchison Gold 
Projects comprising Burnakura, Gabanintha and Tuckanarra in the Murchison area 
of Western Australia. The Company employs approximately 190 people in both 
regions and is committed to the highest standards of environmental management, 
social responsibility, and health and safety for its employees and neighboring 
communities.

/T/

Robert F. Baldock, President and CEO
Monument Mining Limited
Suite 1580 -1100 Melville Street
Vancouver, BC V6E 4A6

/T/

FOR FURTHER INFORMATION visit the company web site at www.monumentmining.com.

"Neither TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release."

Forward-Looking Statement

This news release includes statements containing forward-looking information 
about Monument, its business and future plans ("forward-looking statements"). 
Forward-looking statements are statements that involve expectations, plans, 
objectives or future events that are not historical facts and include the 
Company's plans with respect to its mineral projects and the timing and results 
of proposed programs and events referred to in this news release. Generally, 
forward-looking information can be identified by the use of forward-looking 
terminology such as "plans", "expects" or "does not expect", "is expected", 
"budget", "scheduled", "estimates", "forecasts", "intends", "anticipates" or 
"does not anticipate", or "believes", or variations of such words and phrases 
or state that certain actions, events or results "may", "could", "would", 
"might" or "will be taken", "occur" or "be achieved". The forward-looking 
statements in this news release are subject to various risks, uncertainties and 
other factors that could cause actual results or achievements to differ 
materially from those expressed or implied by the forward-looking statements. 
These risks and certain other factors include, without limitation: risks 
related to general business, economic, competitive, geopolitical and social 
uncertainties; uncertainties regarding the results of current exploration 
activities; uncertainties in the progress and timing of development activities; 
foreign operations risks; other risks inherent in the mining industry and other 
risks described in the management discussion and analysis of the Company and 
the technical reports on the Company's projects, all of which are available 
under the profile of the Company on SEDAR at www.sedar.com.

Material factors and assumptions used to develop forward-looking statements in 
this news release include: expectations regarding the estimated cash cost per 
ounce of gold production and the estimated cash flows which may be generated 
from the operations, general economic factors and other factors that may be 
beyond the control of Monument; assumptions and expectations regarding the 
results of exploration on the Company's projects; assumptions regarding the 
future price of gold of other minerals; the timing and amount of estimated 
future production; the expected timing and results of development and 
exploration activities; costs of future activities; capital and operating 
expenditures; success of exploration activities; mining or processing issues; 
exchange rates; and all of the factors and assumptions described in the 
management discussion and analysis of the Company and the technical reports on 
the Company's projects, all of which are available under the profile of the 
Company on SEDAR at www.sedar.com. Although the Company has attempted to 
identify important factors that could cause actual results to differ materially 
from those contained in forward-looking statements, there may be other factors 
that cause results not to be as anticipated, estimated or intended. There can 
be no assurance that such statements will prove to be accurate, as actual 
results and future events could differ materially from those anticipated in 
such statements. Accordingly, readers should not place undue reliance on 
forward-looking statements. The Company does not undertake to update any 
forward-looking statements, except in accordance with applicable securities 
laws.

/T/

Appendix A
- Peranggih Close Spaced RAB Drilling Campaign 2017: collar coordinates in
Kertau MRSO Coordinate System

----------------------------------------------------------------------------
End of Hole
Hole ID      Depth (m)        East       North          RL     Dip   Azimuth
----------------------------------------------------------------------------
1_PGC005            10    422963.2    480242.3     130.438     -90         0
----------------------------------------------------------------------------
1_PGC006            10    422967.8    480242.3     130.179     -90         0
----------------------------------------------------------------------------
1_PGC007            10    422973.1    480242.3     124.445     -90         0
----------------------------------------------------------------------------
1_PGC008             2    422978.2    480242.3     123.833     -90         0
----------------------------------------------------------------------------
1_PGC016            10    422955.7    480247.3     132.874     -90         0
----------------------------------------------------------------------------
1_PGC017            10    422960.5    480247.3     130.778     -90         0
----------------------------------------------------------------------------
1_PGC018            10    422965.6    480247.3     129.522     -90         0
----------------------------------------------------------------------------
1_PGC019            10    422971.3    480247.3     125.017     -90         0
----------------------------------------------------------------------------
1_PGC020            10    422975.6    480247.3     124.231     -90         0
----------------------------------------------------------------------------
1_PGC021            10    422980.7    480247.3     123.698     -90         0
----------------------------------------------------------------------------
1_PGC022            10    422985.6    480247.4     122.141     -90         0
----------------------------------------------------------------------------
1_PGC027            10    422948.2    480252.4     135.437     -90         0
----------------------------------------------------------------------------
1_PGC028            10    422953.1    480252.3     134.800     -90         0
----------------------------------------------------------------------------
1_PGC029            10    422958.3    480252.3     130.241     -90         0
----------------------------------------------------------------------------
1_PGC030            10    422963.2    480252.3     129.090     -90         0
----------------------------------------------------------------------------
1_PGC031            10    422968.2    480252.3     128.233     -90         0
----------------------------------------------------------------------------
1_PGC032            10    422973.2    480252.3     124.222     -90         0
----------------------------------------------------------------------------
1_PGC039            10    422950.6    480257.4     135.578     -90         
0----------------------------------------------------------------------------
1_PGC041            10    422960.6    480257.4     128.047     -90         0
----------------------------------------------------------------------------
1_PGC042            10    422965.7    480257.3     127.773     -90         0
----------------------------------------------------------------------------
1_PGC043            10    422970.6    480257.4     123.188     -90         0
----------------------------------------------------------------------------
1_PGC418            10    422972.5    480232.8     126.364     -90         0
----------------------------------------------------------------------------
1_PGC419            10    422977.5    480232.8     124.996     -90         0
----------------------------------------------------------------------------
1_PGC427            10    422965.0    480237.8     129.692     -90         0
----------------------------------------------------------------------------
1_PGC428            10    422969.9    480237.6     127.706     -90         0
----------------------------------------------------------------------------
1_PGC429            10    422975.0    480237.7     125.965     -90         0
----------------------------------------------------------------------------
1_PGC430            10    422980.0    480237.8     123.571     -90         0
----------------------------------------------------------------------------
1_PGC431            10    422985.0    480237.8     122.895     -90         0
----------------------------------------------------------------------------

Appendix B
- Assay Results for Peranggih Close Spaced RAB Drilling Campaign 2017
----------------------------------------------------------------------------
Hole ID  From (m)  To (m)    Au g/t   Hole ID    From (m)  To (m)  Au g/t
-----------------------------------   -----------------------------------
1_PGC005        0       1     0.394   1_PGC017          4       5   0.303
-----------------------------------   -----------------------------------
1_PGC005        1       2     1.203   1_PGC017          5       6   0.154
-----------------------------------   -----------------------------------
1_PGC005        2       3     0.257   1_PGC017          6       7   0.122
-----------------------------------   -----------------------------------
1_PGC005        3       4     1.438   1_PGC017          7       8   0.116
-----------------------------------   -----------------------------------
1_PGC005        4       5     0.697   1_PGC017          8       9   0.108
-----------------------------------   -----------------------------------
1_PGC005        5       6     0.460   1_PGC017          9      10   0.095
-----------------------------------   -----------------------------------
1_PGC005        6       7     0.351   1_PGC018          0       1   0.738
-----------------------------------   -----------------------------------
1_PGC005        7       8     0.089   1_PGC018          1       2   2.167
-----------------------------------   -----------------------------------
1_PGC005        8       9     1.194   1_PGC018          2       3   1.709
-----------------------------------   -----------------------------------
1_PGC005        9      10     2.935   1_PGC018          3       4   1.526
-----------------------------------   -----------------------------------
1_PGC006        0       1     0.361   1_PGC018          4       5   2.502
-----------------------------------   -----------------------------------
1_PGC006        1       2     0.385   1_PGC018          5       6   0.130
-----------------------------------   -----------------------------------
1_PGC006        2       3     1.553   1_PGC018          6       7   1.681
-----------------------------------   -----------------------------------
1_PGC006        3       4     2.640   1_PGC018          7       8   0.491
-----------------------------------   -----------------------------------
1_PGC006        4       5     3.702   1_PGC018          8       9   0.037
-----------------------------------   -----------------------------------
1_PGC006        5       6     2.744   1_PGC018          9      10   0.209
-----------------------------------   -----------------------------------
1_PGC006        6       7     3.093   1_PGC019          0       1   2.037
-----------------------------------   -----------------------------------
1_PGC006        7       8     4.687   1_PGC019          1       2   1.645
-----------------------------------   -----------------------------------
1_PGC006        8       9     0.055   1_PGC019          2       3   1.131
-----------------------------------   -----------------------------------
1_PGC006        9      10     0.101   1_PGC019          3       4   1.150
-----------------------------------   -----------------------------------
1_PGC007        0       1     3.269   1_PGC019          4       5   1.008
-----------------------------------   -----------------------------------
1_PGC007        1       2    11.440   1_PGC019          5       6   2.205
-----------------------------------   -----------------------------------
1_PGC007        2       3     1.194   1_PGC019          6       7   3.410
-----------------------------------   -----------------------------------
1_PGC007        3       4     1.299   1_PGC019          7       8   4.692
-----------------------------------   -----------------------------------
1_PGC007        4       5     1.192   1_PGC019          8       9   3.210
-----------------------------------   -----------------------------------
1_PGC007        5       6     1.952   1_PGC019          9      10   2.272
-----------------------------------   -----------------------------------
1_PGC007        6       7     3.392   1_PGC020          0       1   7.756
-----------------------------------   -----------------------------------
1_PGC007        7       8     2.340   1_PGC020          1       2   2.274
-----------------------------------   -----------------------------------
1_PGC007        8       9     1.933   1_PGC020          2       3   1.623
-----------------------------------   -----------------------------------
1_PGC007        9      10     1.387   1_PGC020          3       4   1.038
-----------------------------------   -----------------------------------
1_PGC008        0       1     1.599   1_PGC020          4       5   0.711
-----------------------------------   -----------------------------------
1_PGC008        1       2     3.483   1_PGC020          5       6   0.458
-----------------------------------   -----------------------------------
1_PGC016        0       1     0.155   1_PGC020          6       7   0.421
-----------------------------------   -----------------------------------
1_PGC016        1       2     0.105   1_PGC020          7       8   0.342
-----------------------------------   -----------------------------------
1_PGC016        2       3     0.740   1_PGC020          8       9   0.783
-----------------------------------   -----------------------------------
1_PGC016        3       4     0.118   1_PGC020          9      10   0.834
-----------------------------------   -----------------------------------
1_PGC016        4       5     0.197   1_PGC021          0       1   1.646
-----------------------------------   -----------------------------------
1_PGC016        5       6     0.286   1_PGC021          1       2   0.279
-----------------------------------   -----------------------------------
1_PGC016        6       7     0.254   1_PGC021          2       3   1.166
-----------------------------------   -----------------------------------
1_PGC016        7       8     0.133   1_PGC021          3       4   0.231
-----------------------------------   -----------------------------------
1_PGC016        8       9     0.033   1_PGC021          4       5   0.308
-----------------------------------   -----------------------------------
1_PGC016        9      10     0.094   1_PGC021          5       6   0.354
-----------------------------------   -----------------------------------
1_PGC017        0       1     0.880   1_PGC021          6       7   0.987
-----------------------------------   -----------------------------------
1_PGC017        1       2     0.815   1_PGC021          7       8   0.148
-----------------------------------   -----------------------------------
1_PGC017        2       3     0.110   1_PGC021          8       9   1.202
-----------------------------------   -----------------------------------
1_PGC017        3       4     0.441   1_PGC021          9      10   0.560
-----------------------------------   -----------------------------------


Appendix B
- Assay Results for Peranggih Close Spaced
RAB Drilling Campaign 2017
--------------------------------------------
Hole ID  Hole ID  From (m)  To (m)    Au g/t
--------------------------------------------
1_PGC005 1_PGC022        0       1     1.046
--------------------------------------------
1_PGC005 1_PGC022        1       2     0.269
--------------------------------------------
1_PGC005 1_PGC022        2       3     0.260
--------------------------------------------
1_PGC005 1_PGC022        3       4     0.173
--------------------------------------------
1_PGC005 1_PGC022        4       5     0.124
--------------------------------------------
1_PGC005 1_PGC022        5       6     0.279
--------------------------------------------
1_PGC005 1_PGC022        6       7     0.265
--------------------------------------------
1_PGC005 1_PGC022        7       8     0.199
--------------------------------------------
1_PGC005 1_PGC022        8       9     0.119
--------------------------------------------
1_PGC005 1_PGC022        9      10     0.097
--------------------------------------------
1_PGC006 1_PGC027        0       1     0.266
--------------------------------------------
1_PGC006 1_PGC027        1       2     1.006
--------------------------------------------
1_PGC006 1_PGC027        2       3     0.367
--------------------------------------------
1_PGC006 1_PGC027        3       4     0.355
--------------------------------------------
1_PGC006 1_PGC027        4       5     0.110
--------------------------------------------
1_PGC006 1_PGC027        5       6     5.651
--------------------------------------------
1_PGC006 1_PGC027        6       7     0.200
--------------------------------------------
1_PGC006 1_PGC027        7       8     0.100
--------------------------------------------
1_PGC006 1_PGC027        8       9     0.235
--------------------------------------------
1_PGC006 1_PGC027        9      10     0.250
--------------------------------------------
1_PGC007 1_PGC028        0       1     0.284
--------------------------------------------
1_PGC007 1_PGC028        1       2     0.252
--------------------------------------------
1_PGC007 1_PGC028        2       3     2.392
--------------------------------------------
1_PGC007 1_PGC028        3       4     0.640
--------------------------------------------
1_PGC007 1_PGC028        4       5     0.109
--------------------------------------------
1_PGC007 1_PGC028        5       6     0.297
--------------------------------------------
1_PGC007 1_PGC028        6       7     0.209
--------------------------------------------
1_PGC007 1_PGC028        7       8     0.215
--------------------------------------------
1_PGC007 1_PGC028        8       9     2.740
--------------------------------------------
1_PGC007 1_PGC028        9      10     1.645
--------------------------------------------
1_PGC008 1_PGC029        0       1     0.750
--------------------------------------------
1_PGC008 1_PGC029        1       2     0.574
--------------------------------------------
1_PGC016 1_PGC029        2       3     0.543
--------------------------------------------
1_PGC016 1_PGC029        3       4     0.260
--------------------------------------------
1_PGC016 1_PGC029        4       5     0.164
--------------------------------------------
1_PGC016 1_PGC029        5       6     0.220
--------------------------------------------
1_PGC016 1_PGC029        6       7     0.115
--------------------------------------------
1_PGC016 1_PGC029        7       8     0.074
--------------------------------------------
1_PGC016 1_PGC029        8       9     0.350
--------------------------------------------
1_PGC016 1_PGC029        9      10     0.253
--------------------------------------------
1_PGC016 1_PGC030        0       1     1.499
--------------------------------------------
1_PGC016 1_PGC030        1       2     0.797
--------------------------------------------
1_PGC017 1_PGC030        2       3     0.446
--------------------------------------------
1_PGC017 1_PGC030        3       4     0.507
--------------------------------------------
1_PGC017 1_PGC030        4       5     0.390
--------------------------------------------1_PGC017 1_PGC030        5       
6     0.640
--------------------------------------------

Appendix B (continued)

Assay Results for Peranggih Close Spaced RAB Drilling Campaign 2017
----------------------------------------------------------------------------
Hole ID   From (m)  To (m)   Au g/t   Hole ID   From (m)  To (m)   Au g/t
-----------------------------------   -----------------------------------
1_PGC030         6       7    0.374   1_PGC042         2       3    0.934
-----------------------------------   -----------------------------------
1_PGC030         7       8    0.087   1_PGC042         3       4    0.453
-----------------------------------   -----------------------------------
1_PGC030         8       9    0.121   1_PGC042         4       5    0.811
-----------------------------------   -----------------------------------
1_PGC030         9      10    0.068   1_PGC042         5       6    1.198
-----------------------------------   -----------------------------------
1_PGC031         0       1    0.690   1_PGC042         6       7    1.008
-----------------------------------   -----------------------------------
1_PGC031         1       2    0.839   1_PGC042         7       8    1.586
-----------------------------------   -----------------------------------
1_PGC031         2       3    1.229   1_PGC042         8       9    3.205
-----------------------------------   -----------------------------------
1_PGC031         3       4    1.295   1_PGC042         9      10    0.966
-----------------------------------   -----------------------------------
1_PGC031         4       5    4.061   1_PGC043         0       1    0.545
-----------------------------------   -----------------------------------
1_PGC031         5       6    0.192   1_PGC043         1       2    0.302
-----------------------------------   -----------------------------------
1_PGC031         6       7    2.164   1_PGC043         2       3    0.361
-----------------------------------   -----------------------------------
1_PGC031         7       8    4.235   1_PGC043         3       4    0.498
-----------------------------------   -----------------------------------
1_PGC031         8       9    0.070   1_PGC043         4       5    0.628
-----------------------------------   -----------------------------------
1_PGC031         9      10    0.129   1_PGC043         5       6    0.613
-----------------------------------   -----------------------------------
1_PGC032         0       1    0.787   1_PGC043         6       7    0.594
-----------------------------------   -----------------------------------
1_PGC032         1       2    0.562   1_PGC043         7       8    4.846
-----------------------------------   -----------------------------------
1_PGC032         2       3    0.394   1_PGC043         8       9    5.916
-----------------------------------   -----------------------------------
1_PGC032         3       4    0.593   1_PGC043         9      10    2.479
-----------------------------------   -----------------------------------
1_PGC032         4       5    0.701   1_PGC418         0       1    0.273
-----------------------------------   -----------------------------------
1_PGC032         5       6    2.211   1_PGC418         1       2    0.314
-----------------------------------   -----------------------------------
1_PGC032         6       7    3.322   1_PGC418         2       3    0.624
-----------------------------------   -----------------------------------
1_PGC032         7       8    3.434   1_PGC418         3       4    3.490
-----------------------------------   -----------------------------------
1_PGC032         8       9    2.008   1_PGC418         4       5    2.880
-----------------------------------   -----------------------------------
1_PGC032         9      10    1.433   1_PGC418         5       6    1.550
-----------------------------------   -----------------------------------
1_PGC039         0       1    0.536   1_PGC418         6       7    1.490
-----------------------------------   -----------------------------------
1_PGC039         1       2    0.971   1_PGC418         7       8    1.460
-----------------------------------   -----------------------------------
1_PGC039         2       3    1.290   1_PGC418         8       9    0.480
-----------------------------------   -----------------------------------
1_PGC039         3       4    0.290   1_PGC418         9      10    0.420
-----------------------------------   -----------------------------------
1_PGC039         4       5    0.078   1_PGC419         0       1    0.235
-----------------------------------   -----------------------------------
1_PGC039         5       6    0.355   1_PGC419         1       2    0.032
-----------------------------------   -----------------------------------
1_PGC039         6       7    0.149   1_PGC419         2       3    2.120
-----------------------------------   -----------------------------------
1_PGC039         7       8    0.100   1_PGC419         3       4    0.177
-----------------------------------   -----------------------------------
1_PGC039         8       9    0.452   1_PGC419         4       5    4.340
-----------------------------------   -----------------------------------
1_PGC039         9      10    0.087   1_PGC419         5       6    2.840
-----------------------------------   -----------------------------------
1_PGC041         0       1    4.791   1_PGC419         6       7    1.690
-----------------------------------   -----------------------------------
1_PGC041         1       2    1.266   1_PGC419         7       8    3.410
-----------------------------------   -----------------------------------
1_PGC041         2       3    1.216   1_PGC419         8       9    2.370
-----------------------------------   -----------------------------------
1_PGC041         3       4    1.043   1_PGC419         9      10    1.910
-----------------------------------   -----------------------------------
1_PGC041         4       5    0.478   1_PGC427         0       1    0.300
-----------------------------------   -----------------------------------
1_PGC041         5       6    0.759   1_PGC427         1       2    0.750
-----------------------------------   -----------------------------------
1_PGC041         6       7    0.240   1_PGC427         2       3    0.895
-----------------------------------   -----------------------------------
1_PGC041         7       8    0.096   1_PGC427         3       4    1.286
-----------------------------------   -----------------------------------
1_PGC041         8       9    0.320   1_PGC427         4       5    0.144
-----------------------------------   -----------------------------------
1_PGC041         9      10    0.086   1_PGC427         5       6    0.174
-----------------------------------   -----------------------------------
1_PGC042         0       1    1.754   1_PGC427         6       7    0.243
-----------------------------------   -----------------------------------
1_PGC042         1       2    0.637   1_PGC427         7       8    0.331
-----------------------------------   -----------------------------------

Appendix B (continued)

Assay Results for Peranggih Close Spaced RAB
Drilling Campaign 2017
---------------------------------------------
Hole ID   Hole ID   From (m)  To (m)   Au g/t
---------------------------------------------
1_PGC030  1_PGC427         8       9    0.261
---------------------------------------------
1_PGC030  1_PGC427         9      10    0.426
---------------------------------------------
1_PGC030  1_PGC428         0       1    0.430
---------------------------------------------
1_PGC030  1_PGC428         1       2    1.030
---------------------------------------------
1_PGC031  1_PGC428         2       3    1.882
---------------------------------------------
1_PGC031  1_PGC428         3       4    4.973
---------------------------------------------
1_PGC031  1_PGC428         4       5    4.238
---------------------------------------------
1_PGC031  1_PGC428         5       6    9.180
---------------------------------------------
1_PGC031  1_PGC428         6       7    1.745
---------------------------------------------
1_PGC031  1_PGC428         7       8    1.620
---------------------------------------------
1_PGC031  1_PGC428         8       9    2.629
---------------------------------------------
1_PGC031  1_PGC428         9      10    0.922
---------------------------------------------
1_PGC031  1_PGC429         0       1    0.250
---------------------------------------------
1_PGC031  1_PGC429         1       2    0.500
---------------------------------------------
1_PGC032  1_PGC429         2       3    1.827
---------------------------------------------
1_PGC032  1_PGC429         3       4    7.948
---------------------------------------------
1_PGC032  1_PGC429         4       5    0.434
---------------------------------------------
1_PGC032  1_PGC429         5       6    3.620
---------------------------------------------
1_PGC032  1_PGC429         6       7    1.828
---------------------------------------------
1_PGC032  1_PGC429         7       8    1.387
---------------------------------------------
1_PGC032  1_PGC429         8       9    1.741
---------------------------------------------
1_PGC032  1_PGC429         9      10    1.755
---------------------------------------------
1_PGC032  1_PGC430         0       1    2.521
---------------------------------------------
1_PGC032  1_PGC430         1       2    0.678
---------------------------------------------
1_PGC039  1_PGC430         2       3    0.452
---------------------------------------------
1_PGC039  1_PGC430         3       4    1.884
---------------------------------------------
1_PGC039  1_PGC430         4       5    1.230
---------------------------------------------
1_PGC039  1_PGC430         5       6    3.280
---------------------------------------------
1_PGC039  1_PGC430         6       7    6.250
---------------------------------------------
1_PGC039  1_PGC430         7       8    3.110
---------------------------------------------
1_PGC039  1_PGC430         8       9    2.840
---------------------------------------------
1_PGC039  1_PGC430         9      10    2.630
---------------------------------------------
1_PGC039  1_PGC431         0       1    0.210
---------------------------------------------
1_PGC039  1_PGC431         1       2    0.450
---------------------------------------------
1_PGC041  1_PGC431         2       3    0.242
---------------------------------------------
1_PGC041  1_PGC431         3       4    0.388
---------------------------------------------
1_PGC041  1_PGC431         4       5    0.181
---------------------------------------------
1_PGC041  1_PGC431         5       6    0.288
---------------------------------------------
1_PGC041  1_PGC431         6       7    0.338
---------------------------------------------
1_PGC041  1_PGC431         7       8    0.296
---------------------------------------------
1_PGC041  1_PGC431         8       9    1.481
---------------------------------------------
1_PGC041  1_PGC431         9      10    0.693
---------------------------------------------
1_PGC041
----------
1_PGC041
----------
1_PGC042
----------
1_PGC042
----------

/T/

- 30 -

CONTACT INFO:

Richard Cushing
MMY Vancouver
+1-604-638-1661 x102
rcushing@monumentmining.com

or

Wolfgang Seybold
Axino GmbH
+49 711-82-09-7211
wolfgang.seybold@axino.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=600946561