Source	MARKET NEWS
Date	11/28/2017
Time	05:41:14 AM

Company	 Silver One Resources Inc.
Title	Drilling of Historic Leach Pads and Stockpiles a





    CDNX Symbol: SVE











Press Release





Drilling of Historic Leach Pads and Stockpiles at its CandelariaMine Project, 
Nevada --->@NEWS RELEASE
SILVER ONE RESOURCES INC ("SVE-V;SLVRF-0")
- Drilling of Historic Leach Pads and Stockpiles at its Candelaria
- Mine Project, Nevada

Silver One Resources Inc. ("Silver One") is pleased to announce
the commencement of drilling scheduled to begin November 28th, 2017 at
its Candelaria silver project in Nevada.  The proposed drill program
will consist of approximately   1,000 metres of sonic drilling on the
historic heap leach pads and stockpiled material left over from
previous operations. Samples will be sent for metallurgical testing to
evaluate silver-gold recoveries and potential extraction methods.

Boart Longyear, a highly qualified and experienced international
drilling company, will conduct the drilling with a track mounted drill
rig. Permits are in place to drill within 10 feet of the base liner and
includes a contingency plan to correct the accidental piercing of the
liner.

Silver One's President and CEO, Greg Crowe commented, "We look
forward to receiving the results of this drilling phase which could
represent a prime business opportunity moving forward. Past records
indicate that the leach pads and stockpiles contain a historic resource
of over 37 million tons and 4 million tons with silver grades of 1.29
ounces per ton (40 g/t Ag) and 0.75 ounces per ton (23 g/t Ag)
respectively. Assays of preliminary samples show that significant
amounts of silver are cyanide-soluble. Candelaria's historic silver
grades in leach pads and stockpiles are significantly higher than the
17 g/t silver cutoff grades of the Rochester mine held by Coeur Mining
located 220 kilometres north of Candelaria."

Candelaria was historically the highest-grade silver producer in
the state of Nevada, averaging over 1,250 g/t silver from high-grade
vein mining between the mid-1800s and the mid-1900s.  Open pit mining
operations were undertaken in the 1970s through 1998 by several
companies, including Nerco and Kinross.  Kinross closed the open pit
and leach operation in 1998 due to low silver prices.  Leaching of the
historic pads was not completed leaving a substantial amount of silver
unprocessed.  It is estimated that the property has produced over 68
million ounces of silver.

Preliminary Assays and Metallurgical Testing

Silver One geologists have collected eight samples from the heap
leach pads and 107 samples from the stockpiles. Samples from the leach
pads were collected from pits that were pre-dug to a depth of 40
centimetres and submitted for assays and bottle roll tests to confirm
grades and estimate silver recoveries.

Gold assays from the heap leach pads ranged from 0.1 to 0.3 g/mt
(0.14 g/mt average) while silver assays varied from 13 to 67 g/mt (47
g/mt average). The cyanide soluble gold ranged from 0% to 35% (17%
average) of the assayed gold.  The cyanide soluble silver ranged from
28% to 54% (42% average) of the assayed silver. Bottle roll tests on
composites are currently in progress with results expected December
2017.

The gold assays from the stockpiles ranged from 0.05 to 0.55 g/mt
(0.14 g/mt average) and the silver assays ranged from 9 to 138 g/mt and
average 34 g/mt.  No preliminary bottle roll tests are planned for the
stockpile material.  Metallurgical testing of stockpiles and leach pads
will be conducted on sonic drill samples.

Historical Resource Estimate -- Candelaria Project

SSR Mining Inc. (formerly, Silver Standard Resources Inc.)
acquired the Candelaria Project in 2001 and reported in a technical
report titled "Candelaria Project Technical Report" dated May 24, 2001
(filed on SEDAR on June 20, 2002), prepared by Pincock Allen & Holt,
the historical mineral resource estimate shown in the table below.  The
qualified person has not done sufficient work to classify the
historical estimate as a current mineral resource. Silver One is not
treating this historical estimate as current mineral resources.

//st

Candelaria Mine Project

Historical Resource Estimate

Area/Type    Classification      Tons      Factored Ag     Sol. Au
Grade         Grade
(optAgtotal)      (opt
Ausoluble)
Mount         Measured      3,391,000        4.44         0.004
Diablo

Indicated      10,231,185       2.84         0.003
Subtotal,      13,623,000       3.23         0.003
Measured +
Indicated

Mount         Inferred      5,191,000        2.12         0.003
Diablo

Northern                     9,162,000        2.26         0.002
Belle

Leach Pads                    37,328,000       1.29          ---
L.G.                       4,000,000        0.75          ---
Stockpiles

Subtotal.      55,681,000       1.49         0.002
Inferred





Area/Type    AqEq      Ag Ounces     Aq Equiv.
Grade      (Agtotal)      Ounces
(opt                   (AqEqtotal)
AgEqtotal)

Mount      4.67      15,054,000   15,838,000
Diablo

3.01      29,005,000   30,796,000

3.42      44,060,000   46,633,000

Mount      2.30      11,015,000   11,939,000
Diablo

Northern    2.37      20,661,000   21,714,000
Belle

Leach Pads   1.29      48,153,000   48,153,000

L.G.      0.75      3,000,000     3,000,000
Stockpiles

1.52      82,829,000   84,806,000



//et

Notes 1) Lode resources tabulated at a 0.5 opt Agsoluble
cutoff grades, with only Agtotal shown in this table. 2) Leach pads and
low grade stockpile resources tabulated for entire accumulation of
material. 3) Total silver grades factored from soluble silver grades
using regression formulas developed by Snowden. 4) Silver equivalent
grade includes the contribution from the gold grade (soluble) using an
Ag:Au equivalency ratio of 57.8:1. 5) Tonnages are short tons of 2,000
pounds. Precious metals are in troy ounces (oz) or troy ounces per
short ton (opt)

The historical mineral resource estimate used "measured mineral
resource", "indicated mineral resource" and "inferred mineral
resource", which are categories set out in NI 43-101. Accordingly,
Silver One considers these historical estimates reliable as well as
relevant as it represents key targets for exploration work by Silver
One. The data base for the historical resource estimate

(1)     on the Mount Diablo Deposit consisted of 538 drill holes
by previous owners and 10 drill holes by Silver Standard Resources Inc.
For drill holes that were twinned, the author used the lower of the two
values assigned to the original holes. The mineral resource estimate
used a kriging estimation method to establish mineralized        zones
with a cut-off grade of 0.5 opt Ag. Ordinary kriging was used to
interpolate grades in the block model.  The block models were set up
with block dimensions of 25 feet by 25 feet in plan and 10 feet in
height.  The maximum search range used in the higher-grade zone was 235
feet, in the lower grade zone it was 1,000 feet and in the background
zone it was 350 feet. Block models more than 300 feet from the nearest
composite only constituted 3 percent of the total number of estimated
blocks and were assigned to an inferred category,

(2)      on the Northern Belle Deposit consisted of 226 drill
holes by previous owners, of which a portion of these holes were
duplicated for the Mount Diablo Deposit database.  The mineral resource
estimate used a kriging estimation method to establish mineralized
zones with a cut-off grade of 0.5 opt Ag.  The mineral resource
estimate used multiple indicator kriging to interpolate grades in the
block model.  Block models were set up with block dimensions of 50 feet
by 50 feet in plan and 20 feet in height.   The maximum search range
used in the higher-grade zone was 85 feet, in the intermediate-grade
zone was 120 feet and the lower-grade zone was 140 feet and in the
lower undifferentiated material below the current pit topography was
260 feet.  Block models more than 300 feet from the nearest composite
only constituted 3 percent of the total number of estimated blocks and
were assigned to an inferred category;

(3)     on the Leach Pads consisted of 24,633,000 tons
located on Leach Pad 1 and 12,695,000 on Leach Pad 2.  The estimate for
Leach Pad 1 is based on the fact that silver production indicates 51.5%
of total silver was recovered by heap leaching operation, while 81.2%
of the soluble silver contact was recovered. Further, the estimate for
Leach Pad 2 is based on the fact that silver production indicates 42.4%
of total silver was recovered by heap leaching operation, while 71.3%
of the soluble silver content was recovered;

(4)     on the Low-Grade Stockpile is based on limited and
incomplete data and documentation.  Material placed on the on the stock
piles ranged from 0.5 to 0.65 opt Ag,

Qualified Person The technical content of this news release
has been reviewed and approved by Greg Crowe, P.Geo, President and CEO
of Silver One, and a Qualified Person as defined by National Instrument
43-101.

About Silver One Silver One is a silver focused exploration
company that holds an option to acquire a 100% interest in the past
producing Candelaria Silver Project, located in Nevada, from SSR Mining
Inc. (formerly, Silver Standard Resources Inc.) and holds a 100%
interest in three significant silver assets located in Mexico: Penasco
Quemado in the State of Sonora, La Frazada in the State of Nayarit, and
Pluton in the State of Durango. The Mexican mining assets were acquired
from First Mining Financing, which became a key shareholder resulting
from the transaction.



Silver One Resources Inc.
Monica Hamm
VP, Investor Relations
Phone: (604) 974-5274
Email: mhamm@silverone.com

Forward-Looking Statements

Information set forth in this news release contains
forward-looking statements that are based on assumptions as of the date
of this news release. These statements reflect management's current
estimates, beliefs, intentions and expectations. They are not
guarantees of future performance. Silver One cautions that all forward
looking statements are inherently uncertain and that actual performance
may be affected by a number of material factors, many of which are
beyond Silver One's control. Such factors include, among other things:
risks and uncertainties relating to Silver One's limited operating
history, ability to obtain sufficient financing to carry out its
exploration and development objectives on the Candelaria Project,
obtaining the necessary permits to carry out its activities and the
need to comply with environmental and governmental regulations.
Accordingly, actual and future events, conditions and results may
differ materially from the estimates, beliefs, intentions and
expectations expressed or implied in the forward-looking information.
Except as required under applicable securities legislation, Silver One
undertakes no obligation to publicly update or revise forward-looking
information.

NEITHER TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY       OF
THIS RELEASE.

TEL: 604-617-5421    SILVER ONE RESOURCES INC
FAX: 604-684-0642
E-mail: brad@bdcapital.com
Website: http://www.silverone.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1733100012TS11733100825-05403320171128