Source	MARKET NEWS
Date	11/29/2017
Time	07:29:22 AM

Company	 Juggernaut Exploration Ltd.
Title	Discovers New Zones With Channel Samples Grading





    CDNX Symbol: JUGR











Press Release




[200/News Release]JUGRVJUGGERNAUT EXPLORATION LTDNOV 29 2017  07:25 AM
Discovers New Zones With Channel Samples Grading 11.2 Grams PerTonne Gold 
Equivalent Over 4.6 Metres, 16.8 Grams Per Tonne GoldEquivalent Over 5 Metres, 
and 59 Grams Per Tonne Gold --->@NEWS RELEASE
JUGGERNAUT EXPLORATION LTD ("JUGR-V")
- Discovers New Zones With Channel Samples Grading 11.2 Grams
- Per Tonne Gold Equivalent Over 4.6 Metres, 16.8 Grams Per Tonne
- Gold Equivalent Over 5 Metres, and 59 Grams Per Tonne Gold
- Equivalent Over 2 Metres, in Outcrop on Empire

Juggernaut Exploration Ltd. (the "Company" or "Juggernaut") is
pleased to report initial channel and chip samples containing
polymetallic mineralization on its new Max Min and existing Metalworks,
Metallica and Olympus discoveries, located on the Empire property, 40
km northeast of Terrace British Columbia.
A highlight of the 2017 program was the discovery of the Max Min
zone. The best channel sample from the Max Min contained 11.15 grams
per tonne gold equivalent over 4.6 meters (including 4.8 grams per
tonne gold, 0.26 % copper, 3.73 % zinc, and 4.85 % lead). The channel
started and finished in mineralization due to snow cover and
mineralization remains open. Gold, copper, lead and zinc mineralized
samples in outcrop define a zone 170 by 100 metres in size which open
in all directions and to depth.
* The gold and polymetallic mineralization confirmed at the Max
Min, Metalworks, Metallic, Rockstar and Olympus targets, coupled with
the widespread porphyry dykes and extensive potassic and propylitic
alteration within the 5.5 km Inca Trend are consistent with
porphyry-style mineralization on the Empire Property.
* The extension of the Inca Trend to 5.5 kilometres during the
2017 program resulted from multiple new polymetallic discoveries in
just over a month of field work.
* Based on the positive 2017 results, the company has expanded the
claims block from 9852 hectares to 14,552 hectares.
2017 Highlights Include:
Max Min
* Channel sample containing 11.15 grams per tonne gold equivalent
including 4.8 grams per tonne gold, 0.26 % copper, 3.73 % zinc, and
4.85 % lead over 4.6 metres. The channel cut started and ended in
mineralization due to snow cover and the zone remains open-ended.
* Chip sample containing 59.02 grams per tonne gold equivalent
including 47.20 grams per tonne gold, 0.02 % copper, 5.39 % zinc, and
12.3 % lead over 2.0 metres.
* Gold and polymetallic mineralized samples with potassic
alteration over a zone measuring 170 by 100 m and open in all
directions.
* The Max Min zone is a drill ready target.
Metalworks
* Chip samples containing 16.8 grams per tonne gold equivalent
including 2.64 gram per tonne gold, 277 gram per tonne silver, 0.04 %
copper, 3.88 % zinc, and 11.95 % lead over 5 m. True thickness of this
zone is not known.
* The zone is characterized by extensive hydrothermal breccia,
potassic alteration and propylitic alteration.
* Exploration in 2017 has more than doubled the size of the zone
with gold mineralized samples from 95 by 85 metres in 2016 to 300 by
130 metres. The zone is open in all directions.
* The Metalworks zone is a drill ready target.
Olympus
* Chip sample containing 11.2 grams per tonne gold equivalent
(0.42 gram per tonne gold, 625 gram per tonne silver, 1.37 % copper,
0.22 % zinc, and 0.08 % lead).
* Outcrop grab samples containing up to 1.01 gram per tonne gold,
1185 gram per tonne silver, and 3.74 % copper from different samples.
Max Min Zone
The Max Min zone was discovered in late August 2017 due to ongoing
snowpack and glacier recession, exposing new mineralized bedrock. Max
Min is located 300 metres northwest of Metallica, 400 metres west of
Metalworks, and is part of the much larger, newly extended, 5.5 by 1.5
kilometre Inca Trend.
The high-grade polymetallic, gold mineralization, and potassic
alteration at Max Min suggest the presence of feeder zone for the
hydrothermal system at depth. The planned 2018 drill program will be
designed to test the source of the hydrothermal gold mineralization in
this key target area. In addition to drilling, ground IP, channel
sampling, prospecting and geological mapping is recommended to outline
the full geometry of the Max Min bedrock discovery. The rapid ongoing
snowpack and glacial recession has provided newly exposed outcrop every
year, all with strong discovery potential along the entire 5.5 km under
explored Inca Trend.
A total of 35.1 metres of channel cuts were made that ranged from
0.5 to 6.7 metres in length. Highlights include a channel sample
containing 11.15 grams per tonne gold equivalent (4.8 grams per tonne
gold, 0.26 % copper, 3.73 % zinc, and 4.85 % lead) over 4.6 metres.
This sample ended-in mineralization due to snow-cover at the time of
sampling. Six channel samples of a metre or less ranged from 11.65 to
58.72 grams per tonne gold equivalent (See Table 1).
//st

Table 1: Max Min Zone Assay Highlights

Sample     Type          Length         Gold Eq     Gold    Copper   Zinc
Lead
(metres) (1)   (gpt) (2)   (gpt)   %        %
%
W489803-8  Channel       4.6            11.15       4.80    0.26     3.73
4.85
W503171    Chip          3.4            9.80        7.43    0.22     0.72
2.35
W493000    Chip          2.0            59.02       47.20   0.02     5.39
12.3
W501110    Chip          2.0            28.72       13.30   0.63     11.4
8.74
W501111    Chip          2.0            24.19       12.95   0.77     5.90
8.64
W503310    Chip          2.0            21.88       13.55   0.20     5.78
5.59
W501207    Channel       0.5            58.72       56.4    0.08     0.72
2.65
W501203    Channel       0.5            50.06       38.1    0.02     7.66
9.60
W501204    Channel       0.5            31.17       30.4    0.01     0.51
0.57
W501206    Channel       0.6            38.38       36.9    0.02     0.12
2.21
W501210    Channel       1.0            22.90       10.3    1.25     7.66
7.27
W501211    Channel       1.0            11.67       3.85    0.29     4.62
6.02
W490533    Chip          0.5            9.48        8.82    0.00     0.22
0.79
W492999    Chip          0.2            18.80       18.70   0.06     0.00
0.00
W501178    Outcrop Grab                 19.18       13.55   0.02     3.07
5.18
W502670    Outcrop Grab                 27.93       12.55   9.13     0.00
0.14
W387652    Outcrop Grab                 14.91       7.69    0.08     4.70
5.50

(1)True thickness of mineralized zone not known. (2)AuEq based on Metal
Prices on Nov 14, 2017: Au $1273.4 oz; Cu $3.1115 lb; Pb $ 1.1347 lb; Zn
$1.4701 lb
//et

Twenty-four total chip samples were taken that range from below
detection limit to 59.02 grams per tonne gold equivalent (47.2 grams
per tonne gold, 0.02 % copper, 5.39 % zinc, and 12.3 % lead).
Twenty-four grab samples (Table 1) were taken that ranged from below
detection limit to 27.93 grams per tonne gold equivalent (12.55 grams
per tonne gold, 9.13 % copper, and 0.14 % lead), with six samples
ranging from 1.53 to 27.93 grams per tonne gold equivalent (1.23 gram
per tonne gold, 0.18 % copper and 12.55 gram per tonne gold, 9.13 %
copper, and 0.14 % lead, respectively).
The Max Min zone is currently limited in its northward extent by
rapidly receding glacial ice and snowpack; however where there are
islands of newly exposed outcrop, limited samples taken have returned
very promising results. Approximately three-hundred metres northwest of
Max Min, a 2 metre chip sample assaying 0.9 grams per tonne gold was
taken from an outcrop in the middle of the glacier. On the unexplored
northern flank of the glacier 0.3 and 0.5 metre chip samples assayed 6
and 1.2 grams per tonne gold, respectively. These extensions provide
excellent potential to expand the Max Min zone and further confirm the
discovery potential of the evolving Inca Trend.
The Inca Trend is hosted in volcanic, magmatic arc rocks of the
Stikine Terrane, which is a favorable geological setting for porphyry
systems in British Columbia. The thick sequence of volcanic rocks that
underlies the Inca Trend is intruded by numerous felsic and
intermediate porphyry dykes that strike broadly east-west. This
east-west trend is further emphasized by an extensive fracture set that
has provided structural controls on quartz-carbonate veining and
mineralization. The gold-silver-polymetallic mineralization coupled
with the extensive propylitic and potassic alteration along the Inca
Trend are consistent with the presence of a porphyry system at depth.
Metalworks Zone
The assay results from Metalworks have more the doubled the size
of zone with mineralized samples from 95 by 85 in 2016 metres to 300 by
130 metres in 2017 due to newly exposed bedrock along the fringes of
the rapidly receding glacial ice and snowpack. Metalworks remains open
in all directions.

//st
Table 2: Metalworks Assay Highlights

Sample   Type     Zone        Length (1)(metres)  Gold (2 )Eq   Gold
Silver   Copper   Zinc   Lead
(gpt)         (gpt)
(gpt)    %        %      %
W501090  Chip     Metalworks  5.00                16.8          2.64
277.0    0.04     3.88   11.95
W501041  Chip     Metalworks  2.00                12.8          0.02
517.0    3.51     0.02   0.00
W501083  Chip     Metalworks  2.00                8.53          0.12
30.40    0.05     7.48   3.27
W501043  Chip     Metalworks  1.00                9.17          0.04
484.0    0.67     0.71   1.65
W502559  Chip     Metalworks  1.00                4.21          0.04
248.0    0.52     0.00   0.00
W502925  Channel  Metalworks  1.00                6.05          3.53
6.90     0.03     1.41   2.07
W502514  Chip     Metalworks  0.50                2.48          1.51
9.90     0.09     0.10   0.99
W502510  Chip     Metalworks  0.50                6.32          0.20
126.0    0.44     2.90   2.31
W502778  Channel  Metalworks  0.30                16.6          4.43
68.8     0.90     6.95   7.00
W502792  Channel  Metalworks  0.30                4.26          2.79
18.4     0.15     0.43   1.03
W502776  Channel  Metalworks  0.30                8.25          2.43
25.3     0.41     3.19   3.72
W502789  Channel  Metalworks  0.30                2.39          1.10
9.00     0.22     0.43   0.76

(1)True thickness of mineralized zone not known.
(2)AuEq based on Metal Prices on Nov 14, 2017: Au $1273.4 oz; Cu $3.1115
lb; Pb $ 1.1347 lb; Zn $1.4701 lb

//et

Chip highlights (Table 2) include a 5 metre chip sample that
contained 16.76 grams per tonne equivalent gold (2.64 grams per tonne
gold, 277 grams per tonne silver, 3.88 % zinc, 11.95 % lead). The true
width of this zone is not known. A total of 27 total chip samples
(Table 2) were taken that ranged from below detection limit to 16.8
grams per tonne gold equivalent (2.64 grams per tonne gold, 277 grams
per tonne silver, 0.04 % copper, 3.88 % zinc, and 11.95 % lead). Seven
chip samples returned assays ranging from 2.48 to 16.8 grams per tonne
gold equivalent (1.51 grams per tonne gold, 9.9 grams per tonne silver,
0.09 % copper, 0.1 % zinc, 0.99 % lead and 2.64 grams per tonne gold,
277 grams per tonne silver, 0.04 % copper, 3.88 % zinc, and 11.95 %
lead, respectively).
Initial channel samples at Metalworks (Table 2) returned
highlights of 1 metre of 6.05 grams per tonne gold equivalent (3.53
grams per tonne gold, 6.9 grams per tonne silver, 1.41 % zinc, 2.07 %
lead).
Continued rapid snowpack and glacier recession should provide for
excellent new opportunities for discovery in 2018. With the expansion
of Metalworks in 2017 by ~200 metres, its boundary is now only ~750
metres south of Olympus, ~250 metres west of Metallica, and 400 metres
to Max Min, separated by rapidly receding glacial ice and snowpack.
These zones share a similar style of mineralization which is
predominantly hosted structurally above extensive hydrothermal
breccias. Other similarities include the same stratigraphic package of
rocks, potassic and propylitic alteration, and late porphyry dykes all
of which suggest shared porphyry feeder source of mineralization at
depth. Ground IP, mapping, prospecting and drilling is recommended to
outline the full geometry, along strike and to depth of the Metalworks
Zone.
Metallica Zone
The Metallica zone is located approximately 250 south of
Metalworks. Mineralization is hosted within a propylitically altered
feldspar porphyry unit and is comprised of two distinct types of
mineralization: (1) gently dipping, 20-30 cm wide quartz + Fe-carbonate
covellite  sphalerite veins, and (2) a silver-rich polymetallic massive
sulfide lens. Initial channel cuts from a massive sulphide lens
returned values of 22694 grams per tonne silver (729.6 oz per tonne),
26.4 % copper, 2.8 % zinc and a gold equivalent value of 348 grams per
tonne over 0.2 metres.
A quartz vein channel cut returned values of 6.15 grams per tonne
gold equivalent (3.74 grams per tonne gold, 83.4 grams per tonne
silver, and 0.74% copper) over 0.4 metres. Chip and channel samples
were collected in the gently-dipping (type 1) veins were cut in the
dip-slope of the veins and thus do not represent true thickness.
Twenty six total chip samples (Table 3) were taken that returned
assays ranging from below the detection limit up to 9.45 grams per
tonne gold equivalent (1.25 gram per tonne gold, 490 grams per tonne
silver, 0.9 % copper, 0.2 % zinc, and 0.02 % lead). Twenty grab samples
were taken that ranged in values from below detection limit up to 94.1
grams per tonne gold equivalent (0.32 gram per tonne gold, 6390 gram
per tonne silver, 5 % copper, 0.47 % zinc), with five samples ranging
from 3.96 to 94.1 grams per tonne equivalent gold (0.09 grams per tonne
gold, 200 grams per tonne silver, 0.72 % copper and 0.32 grams per
tonne gold, grams per tonne silver, 5 % copper, 0.47 % zinc,
respectively). This zone is also believed to be connected to a common
feeder system at depth.

//st
Table 3: Metallica Assay Highlights

Sample   Type     Zone       Length (1)(metres)  Gold Eq     Gold    Silver
Copper   Zinc   Lead
(gpt) (2)   (gpt)   (gpt)
%        %      %
W502571  Chip     Metallica  1.50                4.11        0.86    10
0.36     0.38   3.62
W503027  Channel  Metallica  1.30                3.91        1.18    104
0.75     0.12   0.00
W503044  Channel  Metallica  1.00                1.69        1.66    0.70
0.00     0.02   0.00
W503072  Channel  Metallica  0.80                24.0        0.37    1520
1.93     0.27   0.00
W503070  Channel  Metallica  0.60                5.75        1.39    267
0.44     0.09   0.00
W502569  Chip     Metallica  0.50                9.45        1.25    490
0.90     0.20   0.02
W503054  Channel  Metallica  0.50                4.17        1.58    105
0.65     0.13   0.00W503041  Channel  Metallica  0.40                
6.15        3.74    83.40
0.74     0.08   0.00
W503059  Channel  Metallica  0.20                348         0.01    22694
26.40    2.80   0.00
W501007  Grab     Metallica                      94.1        0.32    6390
5.00     0.47   0.00
W501006  Grab     Metallica                      35.0        0.20    1420
9.45     0.08   0.00
W501056  Grab     Metallica                      12.7        0.07    271
5.40     0.00   0.00
W499517  Grab     Metallica                      4.68        2.83    125
0.02     0.04   0.20
W494310  Grab     Metallica                      3.96        0.09    200
0.72     0.00   0.00

(1)chip and channel samples cut in-plane of a low angle vein and thus do
not represent true thickness. (2)AuEq based on Metal Prices on Nov 14,
2017: Au $1273.4 oz; Cu $3.1115 lb; Pb $ 1.1347 lb; Zn $1.4701 lb; Ag
$16.935 oz
//et

Olympus Zone
Mineralization at the Olympus zone is hosted in the same
stratigraphic unit as Metalworks and shares a similar geochemical
signature. Eight total chip samples (Table 4) were taken that range
from below detection limit up to 11.2 grams per tonne gold equivalent
(0.42 grams per tonne gold, 625 grams per tonne silver, 1.37 % copper,
0.22 % zinc, and 0.08 % lead), three samples ranged from 1.67 to 11.2
gram per tonne gold equivalent (0.84 grams per tonne gold, 45.1 grams
per tonne silver, 0.12 % copper, 0.02 % zinc, 0.01 % lead and 0.42
grams per tonne gold, 625 grams per tonne silver 1.37 % copper, 0.22 %
zinc, and 0.08 % lead, respectively).

//st

Table 4: Olympus Assay Highlights
Sample   Type  Zone     Length (1)(metres)  Gold Eq     Gold    Silver
Copper   Zinc   Lead
(gpt) (2)   (gpt)   (gpt)
%        %      %
W495213  Chip  Olympus  2                   11.2        0.42    625
1.37     0.22   0.08
W503312  Chip  Olympus  1                   1.99        1.88    3.90
0.02     0.03   0.00
W503305  Chip  Olympus  1                   1.67        0.84    45.1
0.12     0.02   0.01
W503307  Grab  Olympus                      22.0        0.71    1185
3.22     0.06   0.11
W501031  Grab  Olympus                      20.7        0.35    1050
3.74     0.10   0.03
W501104  Grab  Olympus                      12.0        1.01    718
0.83     0.04   0.05

(1)True thickness of mineralized zone not known.
(2)AuEq based on Metal Prices on Nov 14, 2017: Au $1273.4 oz; Cu $3.1115
lb; Pb $ 1.1347 lb; Zn $1.4701 lb
//et

Empire Property
In addition to porphyry style gold-silver-polymetallic
mineralization with potassic alteration, recent work and research in
the area by the BC geological survey identified
gold-silver-copper-lead-zinc mineralization in the region to be
consistent with transitional vein systems like the Snip mine. As part
of this same study the BC geological survey mapped a sequence of marine
Hazelton volcanic rocks (Quock formation pillow lavas and marine
fossils) on the northern portion of the Empire property and determined
are contemporaneous with the development of the Eskay rift to the west.
Therefore, the region also may have potential for epithermal
mineralization and Eskay Creek style mineralization.
Statements
Mr. Dan Stuart, Director, President & CEO of Juggernaut states:
"The Empire property has tremendous untapped potential, initial results
indicate it has the key markers to host a world class mineral
discovery. Welook forward to reporting additional results from both
Empire and Midas in the near future and to the 2018 drill campaign with
much anticipation. The Empire project is a very rare opportunity with
world class potential as demonstrated by both the support and interest
from institutions and miners alike, confirming the significance of this
and evolving new discoveries. We look forward to reporting the results
in the immediate future from the newly discovered Rock Star zone on
Inca Trend and the Material Metal and Babylon zones, also located on
the Empire Property. The company also looks forward to reporting
results from its Midas property and from the DSM project generator
syndicate when they become available."
Dr. Stefan Kruse, Chief Consulting Geologist stated: "Results to
date have farexceeded our expectations and we look forward to unlocking
the full potential of these exciting new discoveries contained within a
world class geological setting I strongly recommended a comprehensive
exploration and drill campaign for 2018."
For further information, new maps and photos of the Empire
property please go to www.juggernautexploration.com
Other
Stefan Kruse, Ph.D., P. Geo., Chief Geologist, is the qualified
person as defined by National Instrument 43- 101, for Juggernaut
Exploration projects, and supervised the preparation of, and has
reviewed and approved, the technical information in this release.
Further information regarding Juggernaut's Midas and Empire properties
can be sourced on-line at www.juggernautexploration.com, or by
contacting Dan Stuart at 778-233-0293.
All rock, channel and talus fine samples were crushed and
pulverized at ALS Canada Ltd.'s lab in Terrace, BC or in Reno Nevada.
ALS is either Certified to ISO 9001:2008 or Accredited to ISO
17025:2005 in all of its locations. The resulting sample pulps were
analyzed for gold by fire assay in Reno, Nevada or in Vancouver, BC.
The pulps were also assayed using multi-element aqua regia digestion at
ALS Canada Ltd.'s lab in Vancouver, BC. The silt samples were sieved
and assayed at ALS Canada Ltd.'s lab in Vancouver, BC. The coarse
reject portions of the rock, channel and talus fine samples, as well as
the pulps, were shipped to J2 Syndicate's storage facility in Terrace,
BC. The silt samples were disposed of after analysis. All samples were
analyzed using ALS Canada Ltd.'s assay procedure ME-ICP41, a 1:1:1 aqua
regia digestion with inductively-coupled plasma atomic emission
spectrometry (ICP-AES) or inductively-coupled plasma mass spectrometry
(ICP-MS) finish for 35 elements as well as the Au-AA24 lead-collection
fire assay fusion procedure with atomic absorption spectroscopy (AAS)
finish. Any results greater than 100 ppm for silver or 10,000 ppm
copper, lead and zinc were additionally assayed using ALS's OG46 method
particular to each element. This method used an HNO(3)-HCl digestion
followed by ICP-AES (or titrimetric and gravimetric analysis). Gold
values of greater than 10 ppm Au were assayed by the Au-GRA22 method
which includes a fire-assay fusion procedure with a gravimetric finish.
Blanks QA/QC samples were inserted into channels sample laboratory
batches. Additionally, a 10% sub-sample of pulp and reject material was
sent to Activation Laboratories in Ancaster Ontario, for
check-analysis.
The reader is cautioned that grab samples are spot samples which
are typically, but not exclusively, constrained to mineralization. Grab
samples are selective in nature and collected to determine the presence
or absence of mineralization and are not intended to be representative
of the material sampled.
Gold equivalent assays are based on metal prices (USD) on Nov 14,
2017: Au $1273.4 oz; Cu $3.1115 lb; Pb $1.1347 lb; Zn $1.4701 lb; Ag
$16.935 oz and are based on an assumption of 100% recovery.

On behalf of the Board of Directors,

"Dan Stuart"

Dan Stuart Director, President, and CEO

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release. Certain disclosure in this release may constitute
forward-looking statements that are subject to numerous risks and
uncertainties relating to Juggernaut's operations that may cause future
results to differ materially from those expressed or implied by those
forward-looking statements, including its ability to complete the
contemplated private placement. Readers are cautioned not to place
undue reliance on these statements. NOT FOR DISSEMINATION IN THE UNITED
STATES OR TO U.S. PERSONS OR FOR DISTRIBUTION TO U.S. NEWSWIRE
SERVICES. THIS PRESS RELEASE DOES NOT CONSTITUTE AN OFFER TO SELL OR AN
INVITATION TO PURCHASE ANY SECURITIES DESCRIBED IN IT.
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1733200030TS11733201294-07252120171129


[200/News Release]JUGRVJUGGERNAUT EXPLORATION LTDNOV 29 2017  07:25 
AMDiscovers New Zones With Channel Samples Grading 11.2 Grams PerTonne Gold 
Equivalent Over 4.6 Metres, 16.8 Grams Per Tonne GoldEquivalent Over 5 Metres, 
and 59 Grams Per Tonne Gold --->@NEWS RELEASE
JUGGERNAUT EXPLORATION LTD ("JUGR-V")
- Discovers New Zones With Channel Samples Grading 11.2 Grams
- Per Tonne Gold Equivalent Over 4.6 Metres, 16.8 Grams Per Tonne
- Gold Equivalent Over 5 Metres, and 59 Grams Per Tonne Gold
- Equivalent Over 2 Metres, in Outcrop on Empire

Juggernaut Exploration Ltd. (the "Company" or "Juggernaut") is
pleased to report initial channel and chip samples containing
polymetallic mineralization on its new Max Min and existing Metalworks,
Metallica and Olympus discoveries, located on the Empire property, 40
km northeast of Terrace British Columbia.
A highlight of the 2017 program was the discovery of the Max Min
zone. The best channel sample from the Max Min contained 11.15 grams
per tonne gold equivalent over 4.6 meters (including 4.8 grams per
tonne gold, 0.26 % copper, 3.73 % zinc, and 4.85 % lead). The channel
started and finished in mineralization due to snow cover and
mineralization remains open. Gold, copper, lead and zinc mineralized
samples in outcrop define a zone 170 by 100 metres in size which open
in all directions and to depth.
* The gold and polymetallic mineralization confirmed at the Max
Min, Metalworks, Metallic, Rockstar and Olympus targets, coupled with
the widespread porphyry dykes and extensive potassic and propylitic
alteration within the 5.5 km Inca Trend are consistent with
porphyry-style mineralization on the Empire Property.
* The extension of the Inca Trend to 5.5 kilometres during the
2017 program resulted from multiple new polymetallic discoveries in
just over a month of field work.
* Based on the positive 2017 results, the company has expanded the
claims block from 9852 hectares to 14,552 hectares.
2017 Highlights Include:
Max Min
* Channel sample containing 11.15 grams per tonne gold equivalent
including 4.8 grams per tonne gold, 0.26 % copper, 3.73 % zinc, and
4.85 % lead over 4.6 metres. The channel cut started and ended in
mineralization due to snow cover and the zone remains open-ended.
* Chip sample containing 59.02 grams per tonne gold equivalent
including 47.20 grams per tonne gold, 0.02 % copper, 5.39 % zinc, and
12.3 % lead over 2.0 metres.
* Gold and polymetallic mineralized samples with potassic
alteration over a zone measuring 170 by 100 m and open in all
directions.
* The Max Min zone is a drill ready target.
Metalworks
* Chip samples containing 16.8 grams per tonne gold equivalent
including 2.64 gram per tonne gold, 277 gram per tonne silver, 0.04 %
copper, 3.88 % zinc, and 11.95 % lead over 5 m. True thickness of this
zone is not known.
* The zone is characterized by extensive hydrothermal breccia,
potassic alteration and propylitic alteration.
* Exploration in 2017 has more than doubled the size of the zone
with gold mineralized samples from 95 by 85 metres in 2016 to 300 by
130 metres. The zone is open in all directions.
* The Metalworks zone is a drill ready target.
Olympus
* Chip sample containing 11.2 grams per tonne gold equivalent
(0.42 gram per tonne gold, 625 gram per tonne silver, 1.37 % copper,
0.22 % zinc, and 0.08 % lead).
* Outcrop grab samples containing up to 1.01 gram per tonne gold,
1185 gram per tonne silver, and 3.74 % copper from different samples.
Max Min Zone
The Max Min zone was discovered in late August 2017 due to ongoing
snowpack and glacier recession, exposing new mineralized bedrock. Max
Min is located 300 metres northwest of Metallica, 400 metres west of
Metalworks, and is part of the much larger, newly extended, 5.5 by 1.5
kilometre Inca Trend.
The high-grade polymetallic, gold mineralization, and potassic
alteration at Max Min suggest the presence of feeder zone for the
hydrothermal system at depth. The planned 2018 drill program will be
designed to test the source of the hydrothermal gold mineralization in
this key target area. In addition to drilling, ground IP, channel
sampling, prospecting and geological mapping is recommended to outline
the full geometry of the Max Min bedrock discovery. The rapid ongoing
snowpack and glacial recession has provided newly exposed outcrop every
year, all with strong discovery potential along the entire 5.5 km under
explored Inca Trend.
A total of 35.1 metres of channel cuts were made that ranged from
0.5 to 6.7 metres in length. Highlights include a channel sample
containing 11.15 grams per tonne gold equivalent (4.8 grams per tonne
gold, 0.26 % copper, 3.73 % zinc, and 4.85 % lead) over 4.6 metres.
This sample ended-in mineralization due to snow-cover at the time of
sampling. Six channel samples of a metre or less ranged from 11.65 to
58.72 grams per tonne gold equivalent (See Table 1).
//st

Table 1: Max Min Zone Assay Highlights

Sample     Type          Length         Gold Eq     Gold    Copper   Zinc
Lead
(metres) (1)   (gpt) (2)   (gpt)   %        %
%
W489803-8  Channel       4.6            11.15       4.80    0.26     3.73
4.85
W503171    Chip          3.4            9.80        7.43    0.22     0.72
2.35
W493000    Chip          2.0            59.02       47.20   0.02     5.39
12.3
W501110    Chip          2.0            28.72       13.30   0.63     11.4
8.74
W501111    Chip          2.0            24.19       12.95   0.77     5.90
8.64
W503310    Chip          2.0            21.88       13.55   0.20     5.78
5.59
W501207    Channel       0.5            58.72       56.4    0.08     0.72
2.65
W501203    Channel       0.5            50.06       38.1    0.02     7.66
9.60
W501204    Channel       0.5            31.17       30.4    0.01     0.51
0.57
W501206    Channel       0.6            38.38       36.9    0.02     0.12
2.21
W501210    Channel       1.0            22.90       10.3    1.25     7.66
7.27
W501211    Channel       1.0            11.67       3.85    0.29     4.62
6.02
W490533    Chip          0.5            9.48        8.82    0.00     0.22
0.79
W492999    Chip          0.2            18.80       18.70   0.06     0.00
0.00
W501178    Outcrop Grab                 19.18       13.55   0.02     3.07
5.18
W502670    Outcrop Grab                 27.93       12.55   9.13     0.00
0.14
W387652    Outcrop Grab                 14.91       7.69    0.08     4.70
5.50

(1)True thickness of mineralized zone not known. (2)AuEq based on Metal
Prices on Nov 14, 2017: Au $1273.4 oz; Cu $3.1115 lb; Pb $ 1.1347 lb; Zn
$1.4701 lb
//et

Twenty-four total chip samples were taken that range from below
detection limit to 59.02 grams per tonne gold equivalent (47.2 grams
per tonne gold, 0.02 % copper, 5.39 % zinc, and 12.3 % lead).
Twenty-four grab samples (Table 1) were taken that ranged from below
detection limit to 27.93 grams per tonne gold equivalent (12.55 grams
per tonne gold, 9.13 % copper, and 0.14 % lead), with six samples
ranging from 1.53 to 27.93 grams per tonne gold equivalent (1.23 gram
per tonne gold, 0.18 % copper and 12.55 gram per tonne gold, 9.13 %
copper, and 0.14 % lead, respectively).
The Max Min zone is currently limited in its northward extent by
rapidly receding glacial ice and snowpack; however where there are
islands of newly exposed outcrop, limited samples taken have returned
very promising results. Approximately three-hundred metres northwest of
Max Min, a 2 metre chip sample assaying 0.9 grams per tonne gold was
taken from an outcrop in the middle of the glacier. On the unexplored
northern flank of the glacier 0.3 and 0.5 metre chip samples assayed 6
and 1.2 grams per tonne gold, respectively. These extensions provide
excellent potential to expand the Max Min zone and further confirm the
discovery potential of the evolving Inca Trend.
The Inca Trend is hosted in volcanic, magmatic arc rocks of the
Stikine Terrane, which is a favorable geological setting for porphyry
systems in British Columbia. The thick sequence of volcanic rocks that
underlies the Inca Trend is intruded by numerous felsic and
intermediate porphyry dykes that strike broadly east-west. This
east-west trend is further emphasized by an extensive fracture set that
has provided structural controls on quartz-carbonate veining and
mineralization. The gold-silver-polymetallic mineralization coupled
with the extensive propylitic and potassic alteration along the Inca
Trend are consistent with the presence of a porphyry system at depth.
Metalworks Zone
The assay results from Metalworks have more the doubled the size
of zone with mineralized samples from 95 by 85 in 2016 metres to 300 by
130 metres in 2017 due to newly exposed bedrock along the fringes of
the rapidly receding glacial ice and snowpack. Metalworks remains open
in all directions.

//st
Table 2: Metalworks Assay Highlights

Sample   Type     Zone        Length (1)(metres)  Gold (2 )Eq   Gold
Silver   Copper   Zinc   Lead
(gpt)         (gpt)
(gpt)    %        %      %
W501090  Chip     Metalworks  5.00                16.8          2.64
277.0    0.04     3.88   11.95
W501041  Chip     Metalworks  2.00                12.8          0.02
517.0    3.51     0.02   0.00
W501083  Chip     Metalworks  2.00                8.53          0.12
30.40    0.05     7.48   3.27
W501043  Chip     Metalworks  1.00                9.17          0.04
484.0    0.67     0.71   1.65
W502559  Chip     Metalworks  1.00                4.21          0.04
248.0    0.52     0.00   0.00
W502925  Channel  Metalworks  1.00                6.05          3.53
6.90     0.03     1.41   2.07
W502514  Chip     Metalworks  0.50                2.48          1.51
9.90     0.09     0.10   0.99
W502510  Chip     Metalworks  0.50                6.32          0.20
126.0    0.44     2.90   2.31
W502778  Channel  Metalworks  0.30                16.6          4.43
68.8     0.90     6.95   7.00
W502792  Channel  Metalworks  0.30                4.26          2.79
18.4     0.15     0.43   1.03
W502776  Channel  Metalworks  0.30                8.25          2.43
25.3     0.41     3.19   3.72
W502789  Channel  Metalworks  0.30                2.39          1.10
9.00     0.22     0.43   0.76

(1)True thickness of mineralized zone not known.
(2)AuEq based on Metal Prices on Nov 14, 2017: Au $1273.4 oz; Cu $3.1115
lb; Pb $ 1.1347 lb; Zn $1.4701 lb

//et

Chip highlights (Table 2) include a 5 metre chip sample that
contained 16.76 grams per tonne equivalent gold (2.64 grams per tonne
gold, 277 grams per tonne silver, 3.88 % zinc, 11.95 % lead). The true
width of this zone is not known. A total of 27 total chip samples
(Table 2) were taken that ranged from below detection limit to 16.8
grams per tonne gold equivalent (2.64 grams per tonne gold, 277 grams
per tonne silver, 0.04 % copper, 3.88 % zinc, and 11.95 % lead). Seven
chip samples returned assays ranging from 2.48 to 16.8 grams per tonne
gold equivalent (1.51 grams per tonne gold, 9.9 grams per tonne silver,
0.09 % copper, 0.1 % zinc, 0.99 % lead and 2.64 grams per tonne gold,
277 grams per tonne silver, 0.04 % copper, 3.88 % zinc, and 11.95 %
lead, respectively).
Initial channel samples at Metalworks (Table 2) returned
highlights of 1 metre of 6.05 grams per tonne gold equivalent (3.53
grams per tonne gold, 6.9 grams per tonne silver, 1.41 % zinc, 2.07 %
lead).
Continued rapid snowpack and glacier recession should provide for
excellent new opportunities for discovery in 2018. With the expansion
of Metalworks in 2017 by ~200 metres, its boundary is now only ~750
metres south of Olympus, ~250 metres west of Metallica, and 400 metres
to Max Min, separated by rapidly receding glacial ice and snowpack.
These zones share a similar style of mineralization which is
predominantly hosted structurally above extensive hydrothermal
breccias. Other similarities include the same stratigraphic package of
rocks, potassic and propylitic alteration, and late porphyry dykes all
of which suggest shared porphyry feeder source of mineralization at
depth. Ground IP, mapping, prospecting and drilling is recommended to
outline the full geometry, along strike and to depth of the Metalworks
Zone.
Metallica Zone
The Metallica zone is located approximately 250 south of
Metalworks. Mineralization is hosted within a propylitically altered
feldspar porphyry unit and is comprised of two distinct types of
mineralization: (1) gently dipping, 20-30 cm wide quartz + Fe-carbonate
covellite  sphalerite veins, and (2) a silver-rich polymetallic massive
sulfide lens. Initial channel cuts from a massive sulphide lens
returned values of 22694 grams per tonne silver (729.6 oz per tonne),
26.4 % copper, 2.8 % zinc and a gold equivalent value of 348 grams per
tonne over 0.2 metres.
A quartz vein channel cut returned values of 6.15 grams per tonne
gold equivalent (3.74 grams per tonne gold, 83.4 grams per tonne
silver, and 0.74% copper) over 0.4 metres. Chip and channel samples
were collected in the gently-dipping (type 1) veins were cut in the
dip-slope of the veins and thus do not represent true thickness.
Twenty six total chip samples (Table 3) were taken that returned
assays ranging from below the detection limit up to 9.45 grams per
tonne gold equivalent (1.25 gram per tonne gold, 490 grams per tonne
silver, 0.9 % copper, 0.2 % zinc, and 0.02 % lead). Twenty grab samples
were taken that ranged in values from below detection limit up to 94.1
grams per tonne gold equivalent (0.32 gram per tonne gold, 6390 gram
per tonne silver, 5 % copper, 0.47 % zinc), with five samples ranging
from 3.96 to 94.1 grams per tonne equivalent gold (0.09 grams per tonne
gold, 200 grams per tonne silver, 0.72 % copper and 0.32 grams per
tonne gold, grams per tonne silver, 5 % copper, 0.47 % zinc,
respectively). This zone is also believed to be connected to a common
feeder system at depth.

//st
Table 3: Metallica Assay Highlights

Sample   Type     Zone       Length (1)(metres)  Gold Eq     Gold    Silver
Copper   Zinc   Lead
(gpt) (2)   (gpt)   (gpt)
%        %      %
W502571  Chip     Metallica  1.50                4.11        0.86    10
0.36     0.38   3.62
W503027  Channel  Metallica  1.30                3.91        1.18    104
0.75     0.12   0.00
W503044  Channel  Metallica  1.00                1.69        1.66    0.70
0.00     0.02   0.00
W503072  Channel  Metallica  0.80                24.0        0.37    1520
1.93     0.27   0.00
W503070  Channel  Metallica  0.60                5.75        1.39    267
0.44     0.09   0.00
W502569  Chip     Metallica  0.50                9.45        1.25    490
0.90     0.20   0.02
W503054  Channel  Metallica  0.50                4.17        1.58    105
0.65     0.13   0.00W503041  Channel  Metallica  0.40                
6.15        3.74    83.40
0.74     0.08   0.00
W503059  Channel  Metallica  0.20                348         0.01    22694
26.40    2.80   0.00
W501007  Grab     Metallica                      94.1        0.32    6390
5.00     0.47   0.00
W501006  Grab     Metallica                      35.0        0.20    1420
9.45     0.08   0.00
W501056  Grab     Metallica                      12.7        0.07    271
5.40     0.00   0.00
W499517  Grab     Metallica                      4.68        2.83    125
0.02     0.04   0.20
W494310  Grab     Metallica                      3.96        0.09    200
0.72     0.00   0.00

(1)chip and channel samples cut in-plane of a low angle vein and thus do
not represent true thickness. (2)AuEq based on Metal Prices on Nov 14,
2017: Au $1273.4 oz; Cu $3.1115 lb; Pb $ 1.1347 lb; Zn $1.4701 lb; Ag
$16.935 oz
//et

Olympus Zone
Mineralization at the Olympus zone is hosted in the same
stratigraphic unit as Metalworks and shares a similar geochemical
signature. Eight total chip samples (Table 4) were taken that range
from below detection limit up to 11.2 grams per tonne gold equivalent
(0.42 grams per tonne gold, 625 grams per tonne silver, 1.37 % copper,
0.22 % zinc, and 0.08 % lead), three samples ranged from 1.67 to 11.2
gram per tonne gold equivalent (0.84 grams per tonne gold, 45.1 grams
per tonne silver, 0.12 % copper, 0.02 % zinc, 0.01 % lead and 0.42
grams per tonne gold, 625 grams per tonne silver 1.37 % copper, 0.22 %
zinc, and 0.08 % lead, respectively).

//st

Table 4: Olympus Assay Highlights
Sample   Type  Zone     Length (1)(metres)  Gold Eq     Gold    Silver
Copper   Zinc   Lead
(gpt) (2)   (gpt)   (gpt)
%        %      %
W495213  Chip  Olympus  2                   11.2        0.42    625
1.37     0.22   0.08
W503312  Chip  Olympus  1                   1.99        1.88    3.90
0.02     0.03   0.00
W503305  Chip  Olympus  1                   1.67        0.84    45.1
0.12     0.02   0.01
W503307  Grab  Olympus                      22.0        0.71    1185
3.22     0.06   0.11
W501031  Grab  Olympus                      20.7        0.35    1050
3.74     0.10   0.03
W501104  Grab  Olympus                      12.0        1.01    718
0.83     0.04   0.05

(1)True thickness of mineralized zone not known.
(2)AuEq based on Metal Prices on Nov 14, 2017: Au $1273.4 oz; Cu $3.1115
lb; Pb $ 1.1347 lb; Zn $1.4701 lb
//et

Empire Property
In addition to porphyry style gold-silver-polymetallic
mineralization with potassic alteration, recent work and research in
the area by the BC geological survey identified
gold-silver-copper-lead-zinc mineralization in the region to be
consistent with transitional vein systems like the Snip mine. As part
of this same study the BC geological survey mapped a sequence of marine
Hazelton volcanic rocks (Quock formation pillow lavas and marine
fossils) on the northern portion of the Empire property and determined
are contemporaneous with the development of the Eskay rift to the west.
Therefore, the region also may have potential for epithermal
mineralization and Eskay Creek style mineralization.
Statements
Mr. Dan Stuart, Director, President & CEO of Juggernaut states:
"The Empire property has tremendous untapped potential, initial results
indicate it has the key markers to host a world class mineral
discovery. Welook forward to reporting additional results from both
Empire and Midas in the near future and to the 2018 drill campaign with
much anticipation. The Empire project is a very rare opportunity with
world class potential as demonstrated by both the support and interest
from institutions and miners alike, confirming the significance of this
and evolving new discoveries. We look forward to reporting the results
in the immediate future from the newly discovered Rock Star zone on
Inca Trend and the Material Metal and Babylon zones, also located on
the Empire Property. The company also looks forward to reporting
results from its Midas property and from the DSM project generator
syndicate when they become available."
Dr. Stefan Kruse, Chief Consulting Geologist stated: "Results to
date have farexceeded our expectations and we look forward to unlocking
the full potential of these exciting new discoveries contained within a
world class geological setting I strongly recommended a comprehensive
exploration and drill campaign for 2018."
For further information, new maps and photos of the Empire
property please go to www.juggernautexploration.com
Other
Stefan Kruse, Ph.D., P. Geo., Chief Geologist, is the qualified
person as defined by National Instrument 43- 101, for Juggernaut
Exploration projects, and supervised the preparation of, and has
reviewed and approved, the technical information in this release.
Further information regarding Juggernaut's Midas and Empire properties
can be sourced on-line at www.juggernautexploration.com, or by
contacting Dan Stuart at 778-233-0293.
All rock, channel and talus fine samples were crushed and
pulverized at ALS Canada Ltd.'s lab in Terrace, BC or in Reno Nevada.
ALS is either Certified to ISO 9001:2008 or Accredited to ISO
17025:2005 in all of its locations. The resulting sample pulps were
analyzed for gold by fire assay in Reno, Nevada or in Vancouver, BC.
The pulps were also assayed using multi-element aqua regia digestion at
ALS Canada Ltd.'s lab in Vancouver, BC. The silt samples were sieved
and assayed at ALS Canada Ltd.'s lab in Vancouver, BC. The coarse
reject portions of the rock, channel and talus fine samples, as well as
the pulps, were shipped to J2 Syndicate's storage facility in Terrace,
BC. The silt samples were disposed of after analysis. All samples were
analyzed using ALS Canada Ltd.'s assay procedure ME-ICP41, a 1:1:1 aqua
regia digestion with inductively-coupled plasma atomic emission
spectrometry (ICP-AES) or inductively-coupled plasma mass spectrometry
(ICP-MS) finish for 35 elements as well as the Au-AA24 lead-collection
fire assay fusion procedure with atomic absorption spectroscopy (AAS)
finish. Any results greater than 100 ppm for silver or 10,000 ppm
copper, lead and zinc were additionally assayed using ALS's OG46 method
particular to each element. This method used an HNO(3)-HCl digestion
followed by ICP-AES (or titrimetric and gravimetric analysis). Gold
values of greater than 10 ppm Au were assayed by the Au-GRA22 method
which includes a fire-assay fusion procedure with a gravimetric finish.
Blanks QA/QC samples were inserted into channels sample laboratory
batches. Additionally, a 10% sub-sample of pulp and reject material was
sent to Activation Laboratories in Ancaster Ontario, for
check-analysis.
The reader is cautioned that grab samples are spot samples which
are typically, but not exclusively, constrained to mineralization. Grab
samples are selective in nature and collected to determine the presence
or absence of mineralization and are not intended to be representative
of the material sampled.
Gold equivalent assays are based on metal prices (USD) on Nov 14,
2017: Au $1273.4 oz; Cu $3.1115 lb; Pb $1.1347 lb; Zn $1.4701 lb; Ag
$16.935 oz and are based on an assumption of 100% recovery.

On behalf of the Board of Directors,

"Dan Stuart"

Dan Stuart Director, President, and CEO

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release. Certain disclosure in this release may constitute
forward-looking statements that are subject to numerous risks and
uncertainties relating to Juggernaut's operations that may cause future
results to differ materially from those expressed or implied by those
forward-looking statements, including its ability to complete the
contemplated private placement. Readers are cautioned not to place
undue reliance on these statements. NOT FOR DISSEMINATION IN THE UNITED
STATES OR TO U.S. PERSONS OR FOR DISTRIBUTION TO U.S. NEWSWIRE
SERVICES. THIS PRESS RELEASE DOES NOT CONSTITUTE AN OFFER TO SELL OR AN
INVITATION TO PURCHASE ANY SECURITIES DESCRIBED IN IT.
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1733200030TS11733201294-07252120171129