Source	Marketwire
Date	11/30/2017
Time	04:00:25 PM

Company	 MUNDORO CAPITAL INC.
Title	Mundoro Drilling Confirms Extension of Alteration at Borsko in Serbia, 
Assays Pending





    CDNX Symbol: MUN











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Mundoro Capital Inc.

TSX VENTURE SYMBOL: MUN

November 30, 2017

Mundoro Drilling Confirms Extension of Alteration at Borsko in Serbia, Assays 
Pending


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Nov. 30, 2017) - Mundoro Capital 
Inc. (TSX VENTURE:MUN) (www.mundoro.com) ("Mundoro" or the "Company") is 
pleased to announce that the previously announced 3000 meter drill program at 
the Company's Borsko Jezero license ("Borsko") has been completed with 3990 
meters over four drill holes, Figure 1: Plan Map of Drillhole Locations. The 
core from the four drill holes has been cut and sampled with all assay results 
expected by mid-December 2017.

Borsko is one of the four licenses being sole funded by JOGMEC as part of the 
JOGMEC-Mundoro option agreement announced in August 2016. Borsko is located 
directly west of the Serbian state-operated producing mines, RTB Group's Borska 
Reka copper-gold porphyry mine and the Veliki Krivelj copper-gold porphyry 
mine, all located in the central portion of the Timok Magmatic Complex 
("Timok").

HIGHLIGHTS

/T/

--  Phase II drilling program was designed to further test for epithermal
high-sulphidation copper-gold mineralisation stepping out from the
alteration intersected in drill hole BJ-06 and BJ-07.
--  Drill holes 17-BJ-11 and 17-BJ-12 confirmed the extension of the
advanced argillic alteration 250 m to the northeast and 100 m to the
northwest, respectively.
--  Both drill holes also demonstrated the advanced argillic and argillic
zone remains open down plunge to the northwest beyond the vertical depth
of 1120 m.

/T/

Teo Dechev, CEO & President of Mundoro commented, "As a result of the drilling 
at Target 1 in Borsko in 2017, our exploration team has successfully found the 
right hydrothermal alteration environment that has the potential to host a 
copper-gold high-sulphidation epithermal system. The drilling has now extended 
the alteration zone and with downhole geophysical work to be completed by the 
end of this year, we will have geochemical and geophysical data as vectors to 
sulphide mineralization. The alteration and mineralization we have intercepted 
in the drill core thus far at Borsko provide support for the project's 
potential to host a copper-gold epithermal and porphyry system."

Dechev added, "Mundoro is also currently drilling at Zeleznik, another 
JOGMEC-Mundoro joint venture project, for a 4500 meter drill program over the 
West Zone and East Zone to further delineate the mineralization previously 
intersected in these two zones. Drilling is expected to be completed around 
year end with drill results expected in Q1-2018. "

Borsko Drill Program

Under this drill program, which began in early August 2017, the Company 
designed the drill program for four diamond drill holes with an average of 
depth of 750 m on Target 1. The projected depth of 750 m was designed to 
further test for epithermal high-sulphidation copper-gold mineralisation 
stepping out from the alteration intersected by previously released drill holes 
(BJ-06 and BJ-07) which began at approximately 580 m depth. Interpretation of 
the geology and alteration encountered at Borsko to date highlights the 
lithocap hosted in andesite as the prime target for epithermal 
high-sulphidation copper-gold mineralisation similar to that of the Bor (Tilva 
Rosh) and Cukaru Peki deposits in Timok (see Figure 1: Plan Map of Drillhole 
Locations) .

The Phase II drilling program confirmed the extension of the advanced argillic 
alteration zone at the depth of 600 m for at least 250 m to the east-northeast 
(ENE) and at least 100 m to the north-northwest (NNW), as exemplified by drill 
holes 17-BJ-11 and 17-BJ-12 respectively. The advanced argillic zone 
transitioned to argillic at depth and remains open down plunge to NNW beyond 
the vertical depth of 1120 m, where drill holes were terminated due to the 
drill rig capacity.

The advanced argillic altered andesites are moderate to strong pyritized, with 
locally exceeding 30% fine-grained sooty pyrite, and alternates with pervasive 
silica, vuggy silica, alunite and hydrothermal breccias, all of which are 
common features for the high-sulphidation epithermal systems (see pictures of 
core in Section A-A and Section B-B).

Mundoro considers the presence of fine-grained semi-massive pyrite 
mineralisation at Borsko as an important vector to copper-gold bearing sulphide 
mineralisation similar to that of the Bor (Tilva Rosh) and Cukaru Peki 
deposits. A documented feature of these known deposits in the region, is zoned 
mineralisation in massive sulphides from dominant pyrite to pyrite-chalcopyrite 
and to chalcopyrite-covellite copper ore mineralisation.

In order to locate and discriminate massive sulphide conductors that might 
correspond with the sulphide mineralisation, borehole electromagnetic (EM) 
Geophysics is planned to take place in November and December. The downhole EM 
survey is expected to provide information of depth, size, conductance, and 
orientation of a conductor in 3-Dimensions and assist in designing future drill 
programs at Borsko.

The Borsko drill program to date partly tested the first two of six targets 
generated by the 2016 exploration program. The targets were generated based on 
structural analysis carried out in the area, as well as, strong resistivity 
(CSAMT) geophysical anomalies that correspond with ground magnetic features and 
copper-gold in soil anomalies.

Comments on Individual Drillholes

17-BJ-11 and 17-BJ-12

Both, drill hole 17-BJ-11 (collared 530 m east-northeast of BJ-07) and drill 
hole 17-BJ-12 (collared 100 m north-northwest of BJ-07) intersected broad 
intervals, exceeding 400 m, of moderate to strong 
quartz-kaolinite-dickite-pyrite altered andesite right beneath a cover of 
agglomerate and confirmed the extension of the previously announced advanced 
argillic alteration further to the ENE and NNW, respectively. Intervals of 
cream-colored silica cut by irregular veinlets and patches of semi-massive 
pyrite, as well as, vuggy residual quartz and subsidiary alunite were observed. 
A significant interval for
159.4 m of hydrothermal breccia with fine-grained locally sooty pyrite 
mineralization and silica in matrix was intersected from 658.6 m at drill hole 
17-BJ-12. Both drill holes 17-BJ-11 and 17-BJ-12 were terminated in argillic 
altered andesite containing disseminated pyrite and anhydrite veins suggestive 
for down plunge extension of the alteration to the NNW.

17-BJ-09

Drill hole 17-BJ-09 was collared 400 m west-southwest of BJ-07, and planned as 
a step-out hole, intersect agglomerates from surface to end of the hole at 
depth of 749.9 m. At interval from 634 m to 686 m (52m) of patches of native 
copper were observed, suggestive for distal type of mineralisation to that of 
the main system of alteration intersected in BJ-07 and BJ-06 and 17-BJ-11 
(Section A-A). Hence this hole has been interpreted to be distal to the current 
system of interest for targeting and future drilling would focus on the 
alteration system towards the ENE and NNW.

17-BJ-10

Drill hole 17-BJ-10 was collared 400 m to the south-southeast of BJ-07 and 
intersect agglomerates with bands of andesite-basalt downwards to the end of 
the hole at 849 m, similar to those observed in drill holes BJ-07 and 17-BJ-12 
just above the lithocap. Horst-graben type of structures along east-west set of 
faults were interpreted and based on drill core measurement probably caused 
consecutive drops down of the blocks to the south. Due to such movements, drill 
hole 17-BJ-10 probably remains shallow in order to test the extension of the 
lithocap to the south. Drill hole 17-BJ-10 was collared on the same structural 
corridor as BJ-07 and 17-BJ-12 and was targeting similar geophysical anomaly as 
BJ-06 and BJ-07 (Section B-B).

Table 1 - Borsko Diamond Drill Hole Details: Key information for the above 6 
diamond drill holes, arranged by hole number, is reported below. Refer to 
drilling plan for location of holes and sections.

/T/

----------------------------------------------------------------------------
Hole ID               Azimuth     Dip   Elevation   Depth (m)        Section
----------------------------------------------------------------------------
BJ-06                     246     -65        471m      821.6m            A-A
----------------------------------------------------------------------------
BJ-07                    70.5     -85      546.3m     1301.9m    A-A and B-B
----------------------------------------------------------------------------
17-BJ-09                 68.1     -85      500.4m      749.9m            A-A
----------------------------------------------------------------------------
17-BJ-10                 72.2     -85      542.2m      849.1m            B-B
----------------------------------------------------------------------------
17-BJ-11                249.3     -70      470.3m     1190.8m            A-A
----------------------------------------------------------------------------
17-BJ-12                 58.5     -85      541.9m       1200m            B-B
----------------------------------------------------------------------------

/T/

Description of Target at Borsko

The Borsko license is located in the Timok Magmatic Complex which is one of the 
most prolific metallogenic domains in the Tethyan Belt. The geological units in 
this licence area consist of Upper Cretaceous volcano-sedimentary successions, 
predominantly andesite and pyroclastics. Target 1 at Borsko is approximately 4 
km west of the Bor mine and approximately 7 km northwest of the Cukaru Peki 
deposit which are both documented to host high sulphidation systems. The 
interpretation of Borsko geology along with models of known deposits in the 
district highlights the uppermost part of the lithocap, immediately below the 
less-altered volcanic sequence, as the prime target for any high-sulphidation 
copper-gold orebodies of Bor (Tilva Rosh) and Cukaru Peki type. Any such 
massive sulphide bodies are likely to lie within the footprint of the 
underlying porphyry copper-gold centre.

The 2017 drilling at Borsko shows that an advanced argillic lithocap underlies 
550 m of weak-altered agglomerate volcanic rocks, which were in existence at 
the time the advanced argillic alteration took place. The advanced argillic 
altered andesites at Borsko are moderate to strong pyritized and alternates 
with pervasive silica, vuggy silica, alunite and hydrothermal breccias, all of 
which are common features for the high-sulphidation epithermal systems.

Qualified Person

Technical information contained in this Press Release has been reviewed and 
approved by Mr. G. Magaranov, P. Geo., Qualified Person as defined by National 
Instrument 43-101.

Sampling and Analysis

Drill hole orientations were surveyed at approximately 30 metre intervals. 
Company personnel monitored the drilling, with cores delivered daily to the 
Company's core storage facility in the town of Bor, where it was logged, cut 
and sampled. Core recovery is recorded as 95-100% in most intervals, with the 
exception of the more intensely tectonized sections. The samples were collected 
in accordance with the Company's protocols that are compatible with accepted 
industry procedures and best practice standards. Most samples through the 
mineralized intervals were 1 metre in length, up to a maximum 2 metres. In 
sections of poorly mineralized or unaltered and unmineralised rocks one 2m 
sample was collected at every 15 meters core. The samples were submitted to ALS 
Laboratory in Bor, Serbia, for sample preparation and analysis. In addition to 
the laboratory's internal QA/QC procedures, the Company conducted its own QA/QC 
with the systematic inclusion of certified reference materials every 20 
samples, blank samples every 20 samples and field duplicates at every 25 
samples. Drill core samples are assayed using 50-grams charge for fire assay 
with atomic absorption finish and multi-element method MS 61 by ALS laboratory.

On behalf of the Company,

Teo Dechev, Chief Executive Officer, President and Director

About Mundoro Capital Inc.

Mundoro is a Canadian mineral exploration and development public company 
focused on building value for its shareholders through directly investing in 
mineral projects that have the ability to generate future returns for 
shareholders. The Company currently holds a diverse portfolio of projects in 
two European countries as well as an investment in a producing gold mine in 
Bulgaria and a feasibility stage gold project in China. The Company holds eight 
100% owned projects in Serbia, the four Timok North Projects are in option to 
JOGMEC, and the four Timok South Projects are being advanced by Mundoro. 
Mundoro's common shares trade on the TSX Venture Exchange under the symbol 
"MUN".

Caution Concerning Forward-Looking Statements

This News Release contains forward-looking statements. Forward-looking 
statements can be identified by the use of forward-looking words such as 
"will", "expect", "intend", "plan", "estimate", "anticipate", "believe" or 
"continue" or similar words or the negative thereof, and include the following: 
completion of the earn-in expenditures and options by JOGMEC; and completion of 
a definitive joint venture agreement by the parties. The material assumptions 
that were applied in making the forward looking statements in this News Release 
include expectations as to the mineral potential of the Timok North Properties, 
the Company's future strategy and business plan and execution of the Company's 
existing plans. We caution readers of this News Release not to place undue 
reliance on forward looking statements contained in this News Release, as there 
can be no assurance that they will occur and they are subject to a number of 
uncertainties and other factors that could cause actual results to differ 
materially from those expressed or implied by such forward-looking statements. 
These factors include general economic and market conditions, exploration 
results, commodity prices, changes in law, regulatory processes, the status of 
Mundoro's assets and financial condition, actions of competitors and the 
ability to implement business strategies and pursue business opportunities. The 
forward-looking statements contained in this News Release are expressly 
qualified in their entirety by this cautionary statement. The forward-looking 
statements included in this News Release are made as of the date of this News 
Release and the Board undertakes no obligation to publicly update such 
forward-looking statements, except as required by law. Shareholders are 
cautioned that all forward-looking statements involve risks and uncertainties 
and for a more detailed discussion of such risks and other factors that could 
cause actual results to differ materially from those expressed or implied by 
such forward-looking statements, refer to the Company's filings with the 
Canadian securities regulators available on www.sedar.com.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.
To view the figures associated with this release, please visit the following 
links:

http://media3.marketwire.com/docs/1105551_FIGURE-1.pdf

http://media3.marketwire.com/docs/1105551_FIGURE-2.pdf

http://media3.marketwire.com/docs/1105551_FIGURE-3.pdf

- 30 -

CONTACT INFO:

Mundoro Capital Inc.
Teo Dechev
CEO, President and Director
+1-604-669-8055

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=601046289