Source	MARKET NEWS
Date	11/30/2017
Time	04:14:30 PM

Company	 Mundoro Capital Inc.
Title	Drilling 
Confirms Extension Of Alteration At Bor





    CDNX Symbol: MUN











Press Release





MUNDORO CAPITAL INC ("MUN-V;MUNMF-0")
- Drilling Confirms Extension Of Alteration At Borsko In Serbia,
- Assays Pending

Mundoro Capital Inc. ("Mundoro" or the "Company") is pleased to
announce that the previously announced 3000 meter drill program at the
Company's Borsko Jezero license ("Borsko") has been completed with 3990
meters over four drill holes, Figure 1: Plan Map of Drillhole
Locations. The core from the four drill holes has been cut and sampled
with all assay results expected by mid-December 2017.

Borsko is one of the four licenses being sole funded by JOGMEC as
part of the JOGMEC-Mundoro option agreement announced in August 2016.
Borsko is located directly west of the Serbian state-operated producing
mines, RTB Group's Borska Reka copper-gold porphyry mine and the Veliki
Krivelj copper-gold porphyry mine, all located in the central portion
of the Timok Magmatic Complex ("Timok").

HIGHLIGHTS

//st

* Phase II drilling program was designed to further test for epithermal
high-sulphidation copper-gold mineralisation stepping out from the
alteration intersected in drill hole BJ-06 and BJ-07.
* Drill holes 17-BJ-11 and 17-BJ-12 confirmed the extension of the
advanced
argillic alteration 250 m to the northeast and 100 m to the northwest,
respectively.
* Both drill holes also demonstrated the advanced argillic and argillic
zone remains open down plunge to the northwest beyond the vertical
depth
of 1120 m.

//et

Teo Dechev, CEO & President of Mundoro commented, "As a result of
the drilling at Target 1 in Borsko in 2017, our exploration team has
successfully found the right hydrothermal alteration environment that
has the potential to host a copper-gold high-sulphidation epithermal
system. The drilling has now extended the alteration zone and with
downhole geophysical work to be completed by the end of this year, we
will have geochemical and geophysical data as vectors to sulphide
mineralization. The alteration and mineralization we have intercepted
in the drill core thus far at Borsko provide support for the project's
potential to host a copper-gold epithermal and porphyry system."
Dechev added, "Mundoro is also currently drilling at Zeleznik,
another JOGMEC-Mundoro joint venture project, for a 4500 meter drill
program over the West Zone and East Zone to further delineate the
mineralization previously intersected in these two zones. Drilling is
expected to be completed around year end with drill results expected in
Q1-2018. "

Borsko Drill Program

Under this drill program, which began in early August 2017, the
Company designed the drill program for four diamond drill holes with an
average of depth of 750 m on Target 1. The projected depth of 750 m was
designed to further test for epithermal high-sulphidation copper-gold
mineralisation stepping out from the alteration intersected by
previously released drill holes (BJ-06 and BJ-07) which began at
approximately 580 m depth. Interpretation of the geology and alteration
encountered at Borsko to date highlights the lithocap hosted in
andesite as the prime target for epithermal high-sulphidation
copper-gold mineralisation similar to that of the Bor (Tilva Rosh) and
&#268;ukaru Peki deposits in Timok (see Figure 1: Plan Map of Drillhole
Locations) .

The Phase II drilling program confirmed the extension of the
advanced argillic alteration zone at the depth of 600 m for at least
250 m to the east-northeast (ENE) and at least 100 m to the
north-northwest (NNW), as exemplified by drill holes 17-BJ-11 and
17-BJ-12 respectively. The advanced argillic zone transitioned to
argillic at depth and remains open down plunge to NNW beyond the
vertical depth of 1120 m, where drill holes were terminated due to the
drill rig capacity.

The advanced argillic altered andesites are moderate to strong
pyritized, with locally exceeding 30% fine-grained sooty pyrite, and
alternates with pervasive silica, vuggy silica, alunite and
hydrothermal breccias, all of which are common features for the
high-sulphidation epithermal systems (see pictures of core in Section
A-A and Section B-B).

Mundoro considers the presence of fine-grained semi-massive pyrite
mineralisation at Borsko as an important vector to copper-gold bearing
sulphide mineralisation similar to that of the Bor (Tilva Rosh) and
&#268;ukaru Peki deposits. A documented feature of these known deposits
in the region, is zoned mineralisation in massive sulphides from
dominant pyrite to pyrite-chalcopyrite and to chalcopyrite-covellite
copper ore mineralisation.

In order to locate and discriminate massive sulphide conductors
that might correspond with the sulphide mineralisation, borehole
electromagnetic (EM) Geophysics is planned to take place in November
and December. The downhole EM survey is expected to provide information
of depth, size, conductance, and orientation of a conductor in
3-Dimensions and assist in designing future drill programs at Borsko.

The Borsko drill program to date partly tested the first two of
six targets generated by the 2016 exploration program. The targets were
generated based on structural analysis carried out in the area, as well
as, strong resistivity (CSAMT) geophysical anomalies that correspond
with ground magnetic features and copper-gold in soil anomalies.

Comments on Individual Drillholes

17-BJ-11 and 17-BJ-12

Both, drill hole 17-BJ-11 (collared 530 m east-northeast of BJ-07)
and drill hole 17-BJ-12 (collared 100 m north-northwest of BJ-07)
intersected broad intervals, exceeding 400 m, of moderate to strong
quartz-kaolinite-dickite-pyrite altered andesite right beneath a cover
of agglomerate and confirmed the extension of the previously announced
advanced argillic alteration further to the ENE and NNW, respectively.
Intervals of cream-colored silica cut by irregular veinlets and patches
of semi-massive pyrite, as well as, vuggy residual quartz and
subsidiary alunite were observed. A significant interval for
159.4 m of hydrothermal breccia with fine-grained locally sooty
pyrite mineralization and silica in matrix was intersected from 658.6 m
at drill hole 17-BJ-12. Both drill holes 17-BJ-11 and 17-BJ-12 were
terminated in argillic altered andesite containing disseminated pyrite
and anhydrite veins suggestive for down plunge extension of the
alteration to the NNW.

17-BJ-09

Drill hole 17-BJ-09 was collared 400 m west-southwest of BJ-07,
and planned as a step-out hole, intersect agglomerates from surface to
end of the hole at depth of 749.9 m. At interval from 634 m to 686 m
(52m) of patches of native copper were observed, suggestive for distal
type of mineralisation to that of the main system of alteration
intersected in BJ-07 and BJ-06 and 17-BJ-11 (Section A-A). Hence this
hole has been interpreted to be distal to the current system of
interest for targeting and future drilling would focus on the
alteration system towards the ENE and NNW.

17-BJ-10

Drill hole 17-BJ-10 was collared 400 m to the south-southeast of
BJ-07 and intersect agglomerates with bands of andesite-basalt
downwards to the end of the hole at 849 m, similar to those observed in
drill holes BJ-07 and 17-BJ-12 just above the lithocap. Horst-graben
type of structures along east-west set of faults were interpreted and
based on drill core measurement probably caused consecutive drops down
of the blocks to the south. Due to such movements, drill hole 17-BJ-10
probably remains shallow in order to test the extension of the lithocap
to the south. Drill hole 17-BJ-10 was collared on the same structural
corridor as BJ-07 and 17-BJ-12 and was targeting similar geophysical
anomaly as BJ-06 and BJ-07 (Section B-B).

Table 1 - Borsko Diamond Drill Hole Details: Key information for
the above 6 diamond drill holes, arranged by hole number, is reported
below. Refer to drilling plan for location of holes and sections.

//st

Hole ID    Azimuth   Dip   Elevation   Depth (m)   Section

BJ-06      246       -65   471m        821.6m      A-A

BJ-07      70.5      -85   546.3m      1301.9m     A-A and B-B

17-BJ-09   68.1      -85   500.4m      749.9m      A-A

17-BJ-10   72.2      -85   542.2m      849.1m      B-B

17-BJ-11   249.3     -70   470.3m      1190.8m     A-A

17-BJ-12   58.5      -85   541.9m      1200m       B-B

//et

Description of Target at Borsko

The Borsko license is located in the Timok Magmatic Complex which
is one of the most prolific metallogenic domains in the Tethyan Belt.
The geological units in this licence area consist of Upper Cretaceous
volcano-sedimentary successions, predominantly andesite and
pyroclastics. Target 1 at Borsko is approximately 4 km west of the Bor
mine and approximately 7 km northwest of the Cukaru Peki deposit which
are both documented to host high sulphidation systems. The
interpretation of Borsko geology along with models of known deposits in
the district highlights the uppermost part of the lithocap, immediately
below the less-altered volcanic sequence, as the prime target for any
high-sulphidation copper-gold orebodies of Bor (Tilva Rosh) and
&#268;ukaru Peki type. Any such massive sulphide bodies are likely to
lie within the footprint of the underlying porphyry copper-gold centre.


The 2017 drilling at Borsko shows that an advanced argillic
lithocap underlies 550 m of weak-altered agglomerate volcanic rocks,
which were in existence at the time the advanced argillic alteration
took place. The advanced argillic altered andesites at Borsko are
moderate to strong pyritized and alternates with pervasive silica,
vuggy silica, alunite and hydrothermal breccias, all of which are
common features for the high-sulphidation epithermal systems.

Qualified Person

Technical information contained in this Press Release has been
reviewed and approved by Mr. G. Magaranov, P. Geo., Qualified Person as
defined by National Instrument 43-101.

Sampling and Analysis
Drill hole orientations were surveyed at approximately 30 metre
intervals. Company personnel monitored the drilling, with cores
delivered daily to the Company's core storage facility in the town of
Bor, where it was logged, cut and sampled. Core recovery is recorded as
95-100% in most intervals, with the exception of the more intensely
tectonized sections. The samples were collected in accordance with the
Company's protocols that are compatible with accepted industry
procedures and best practice standards. Most samples through the
mineralized intervals were 1 metre in length, up to a maximum 2 metres.
In sections of poorly mineralized or unaltered and unmineralised rocks
one 2m sample was collected at every 15 meters core. The samples were
submitted to ALS Laboratory in Bor, Serbia, for sample preparation and
analysis. In addition to the laboratory's internal QA/QC procedures,
the Company conducted its own QA/QC with the systematic inclusion of
certified reference materials every 20 samples, blank samples every 20
samples and field duplicates at every 25 samples. Drill core samples
are assayed using 50-grams charge for fire assay with atomic absorption
finish and multi-element method MS 61 by ALS laboratory.

On behalf of the Company,

Teo Dechev, Chief Executive Officer, President and Director

About Mundoro Capital Inc.

Mundoro is a Canadian mineral exploration and development public
company focused on building value for its shareholders through directly
investing in mineral projects that have the ability to generate future
returns for shareholders. The Company currently holds a diverse
portfolio of projects in two European countries as well as an
investment in a producing gold mine in Bulgaria and a feasibility stage
gold project in China. The Company holds eight 100% owned projects in
Serbia, the four Timok North Projects are in option to JOGMEC, and the
four Timok South Projects are being advanced by Mundoro. Mundoro's
common shares trade on the TSX Venture Exchange under the symbol "MUN".


Caution Concerning Forward-Looking Statements

This News Release contains forward-looking statements.
Forward-looking statements can be identified by the use of
forward-looking words such as "will", "expect", "intend", "plan",
"estimate", "anticipate", "believe" or "continue" or similar words or
the negative thereof, and include the following: completion of the
earn-in expenditures and options by JOGMEC; and completion of a
definitive joint venture agreement by the parties. The material
assumptions that were applied in making the forward looking statements
in this News Release include expectations as to the mineral potential
of the Timok North Properties, the Company's future strategy and
business plan and execution of the Company's existing plans. We caution
readers of this News Release not to place undue reliance on forward
looking statements contained in this News Release, as there can be no
assurance that they will occur and they are subject to a number of
uncertainties and other factors that could cause actual results to
differ materially from those expressed or implied by such
forward-looking statements. These factors include general economic and
market conditions, exploration results, commodity prices, changes in
law, regulatory processes, the status of Mundoro's assets and financial
condition, actions of competitors and the ability to implement business
strategies and pursue business opportunities. The forward-looking
statements contained in this News Release are expressly qualified in
their entirety by this cautionary statement. The forward-looking
statements included in this News Release are made as of the date of
this News Release and the Board undertakes no obligation to publicly
update such forward-looking statements, except as required by law.
Shareholders are cautioned that all forward-looking statements involve
risks and uncertainties and for a more detailed discussion of such
risks and other factors that could cause actual results to differ
materially from those expressed or implied by such forward-looking
statements, refer to the Company's filings with the Canadian securities
regulators available on www.sedar.com.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Mundoro Capital Inc.
Teo Dechev

TEL: +1-604-669-8055
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1733300074TS11733302729-16102020171130