Source	Marketwire
Date	10/04/2012
Time	06:00:10 AM

Company	 RHYOLITE RESOURCES LTD.
Title	Rhyolite Extends Gold Zone and Discovers VMS Target at Paxson





    CDNX Symbol: RYE











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRE


FOR: Rhyolite Resources Ltd.

TSX VENTURE SYMBOL: RYE

October 4, 2012

Rhyolite Extends Gold Zone and Discovers VMS Target at Paxson


VANCOUVER, BRITISH COLUMBIA--(Marketwire - Oct. 4, 2012) - Rhyolite Resources 
Ltd. (TSX VENTURE:RYE) ("Rhyolite" or the "Company") reports that updated assay 
data from a new infill sampling and quality assurance program has extended the 
mineralization in its most westerly and in its most easterly drill holes that 
tested the Shalosky gold zone on its wholly-owned Paxson gold property in 
eastern Alaska.

/T/

Shalosky 2012 Core Infill Program

---------------------------------------------------------------------------
To (m)              Weighted
Drill                              From       End of   Interval       Grade
Hole      Section  Azimuth  Dip      (m)     Hole(ii)        (m)  (g/t Gold)
---------------------------------------------------------------------------
WG11-12       870      330   70   106.5     187.0(ii)      80.5    1.5 (New)
---------------------------------------------------------------------------
Includes                          106.5        176.6       70.1         1.6
---------------------------------------------------------------------------
Includes                          143.2        157.9       14.7         3.1
---------------------------------------------------------------------------

---------------------------------------------------------------------------
WG11-02       940      350   65    87.6     138.7(ii)      51.1    1.8 (New)
---------------------------------------------------------------------------
Includes                           88.3        111.4       23.1         3.5
---------------------------------------------------------------------------
Includes                           90.4        103.6       13.2         5.4
---------------------------------------------------------------------------

---------------------------------------------------------------------------
WG11-13      1435      190   45   176.3     223.1(ii)      46.8    0.7 (New)
---------------------------------------------------------------------------
Includes                          178.9        189.0       10.1         2.1
---------------------------------------------------------------------------

Weighted Grade is based on 0.10 gram gold per tonne cut-off with the
inclusion of up to 10 per cent internal waste. All sub-intervals as
reported on November 8, 2011 were confirmed by the Quality Assurance
program. All intervals reported are downhole depth and core length, pending
additional drilling and more accurate determination of true thickness.

/T/

The results from the infill sampling suggest that the mineralization in the 
host schist may have stratigraphic controls as well as structural controls, in 
that the mineralization is now seen to continue beyond the limit of primary 
structures to the full limit of drilling in core holes WG11-02; WG11-12; and 
WG11-13. A complete summary of the remaining 2011 drilled intervals on the 
Shalosky zone incorporating the new quality assurance data reported above can 
be found at the end of this news release.

Surface sampling in 2012 identified a volcanic massive sulphide area located 6 
km northeast of the Shalosky gold zone. This occurrence dubbed HD-North is 
exposed in outcrop and appears to be 2 metres thick striking N30E and dipping 
45 degrees to the southeast. Sample 3629 is a 2 metre by 2 metre panel chip 
sample collected from the 2 metre by 4 metre outcrop area. Sample 3630 is a 
grab sample with subtle chalcopyrite banding and sample 3631 is a grab sample 
with prominent galena/sphalerite banding each collected from the same outcrop.

/T/

Base & Precious Metal assays from 2012 Outcrop Sampling

---------------------------------------------------------------------------
Sample #      Zinc (%)     Lead (%)   Copper (%)   Silver (g/t)   Gold (g/t)
---------------------------------------------------------------------------
3629             5.68         2.80         0.48           65.6         0.53
---------------------------------------------------------------------------
3630             4.73         0.60         0.42           23.6         0.35
---------------------------------------------------------------------------
3631             8.46         5.93         0.32          111.0         0.50
---------------------------------------------------------------------------

/T/

The Paxson property comprises 135 mineral claims for a total of 8,670 hectares 
(86.7 square kilometers). Rhyolite is currently seeking a partner to help 
advance the Paxson property.

/T/

Remaining 2011 Shalosky Diamond Drill Holes updated with Quality Assurance
assays

---------------------------------------------------------------------------
Drill                             From      To  Interval     Weighted Grade
Hole     Section  Azimuth  Dip      (m)     (m)       (m)         (g/t Gold)
---------------------------------------------------------------------------
WG11-01      940      350   45    56.1    77.1      21.0     2.0 (ii)((1.9))
---------------------------------------------------------------------------
Includes                          56.1    59.1       3.0     7.3 (ii)((7.2))
---------------------------------------------------------------------------
Includes                          70.1    71.8       1.7     7.0 (ii)((6.3))
---------------------------------------------------------------------------
And                               97.5    99.0       1.5     2.9 (ii)((2.7))
---------------------------------------------------------------------------

---------------------------------------------------------------------------
WG11-03      971      010   65   112.0   113.7       1.7     0.9 (ii)((0.9))
---------------------------------------------------------------------------
And                              118.2   120.2       2.0     2.0 (ii)((1.6))
---------------------------------------------------------------------------
And                              131.4   231.5     100.1     1.0 (ii)((1.0))
---------------------------------------------------------------------------
Includes                         193.0   210.8      17.8     1.9 (ii)((1.9))
---------------------------------------------------------------------------
Includes                         221.0   231.5      10.5     2.5 (ii)((2.5))
---------------------------------------------------------------------------

---------------------------------------------------------------------------
WG11-04      940      330   65    85.8    99.1      13.2     2.2 (ii)((2.2))
---------------------------------------------------------------------------
Includes                          85.8    91.0       5.2     4.4 (ii)((4.5))
---------------------------------------------------------------------------
Includes                          85.8    86.9       1.1   13.6 (ii)((13.7))
---------------------------------------------------------------------------

---------------------------------------------------------------------------
WG11-11      870      330   50    65.5    79.4      13.9     1.3 (ii)((1.0))
---------------------------------------------------------------------------
Includes                          76.9    78.8       1.9     5.0 (ii)((4.8))
---------------------------------------------------------------------------

All intervals reported are downhole depth and core length, pending
additional drilling and more accurate determination of true thickness.
(ii)(( )) represents original values reported on November 8, 2012.

/T/

The 2011 diamond drill results from the Hi-Low showing were not impacted by the 
infill or Quality Assurance program and remain as reported on August 29, 2011 
and November 8, 2011.

/T/

2011 Hi-Low Target Drill Results

---------------------------------------------------------------------------
Interval     Weighted Grade
Drill Hole         From (m)         To (m)         (m)(i)         (g/t Gold)
---------------------------------------------------------------------------
WG11-05               19.5           21.9            2.4                3.2
---------------------------------------------------------------------------
And                   26.9           54.3           27.4                1.9
---------------------------------------------------------------------------
Includes              38.7           52.3           13.6                3.4
---------------------------------------------------------------------------
Includes              40.2           43.0            2.8               14.2
---------------------------------------------------------------------------

---------------------------------------------------------------------------
WG11-06               31.7           37.2            5.5                4.0
---------------------------------------------------------------------------
Includes              35.0           37.2            2.2                8.6
---------------------------------------------------------------------------

(i) Downhole Widths - there has been insufficient drilling to determine
true widths.

/T/

Quality control/Quality assurance

In 2012, the infill samples were collected from intervals in the BTW-size drill 
core that were sawn longitudinally and half the drill core was sampled in 
standard intervals not exceeding 2.0 metres in length. Core samples were 
transported in security-sealed bags to the lab for analyses. All samples 
collected in 2012 were sent for gold fire assay and 48-element ICP analysis to 
ALS Chemex Labs. Samples were prepared in ALS Chemex's Fairbanks prep facility 
and then sent to Reno Nevada for analysis. Gold fire assays were on 30 gram 
pulp splits with an AA finish. One in every ten samples contains a control 
(blank or gold standard).

A total of 407 core samples from the 2011 diamond drill program were submitted 
for re-assay at no cost to Rhyolite because the control samples that were 
associated with select assay batches returned statistical variations. Within 
that group of 407 samples, 62 samples were ultimately determined to contain 
gold mineralization of 0.5 gram gold per tonne or more. Of these, 1/3 of the 
samples increased by more than 5% above the original assay; and for another 1/3 
the final accepted value was more than 5% lower than originally reported; and 
for the remaining 1/3 there was less than a 5% change. However, in the group 
whose original values were too low, the average increase was +48% compared to a 
-16% average for the group that went down.

Qualified Persons

The foregoing disclosure has been reviewed, compiled and is the responsibility 
of Richard A. Graham, P.Geol., President of Rhyolite and a "qualified person" 
for the purpose of NI 43-101.

ON BEHALF OF THE BOARD OF DIRECTORS OF RHYOLITE RESOURCES LTD.

Richard Graham, President and CEO

Forward-Looking Statement

Some statements in this report contain forward-looking information. These 
statements include, but are not limited to, statements with respect to future 
exploration, expenditures, transactions and financings. These statements 
address future events and conditions and, as such, involve known and unknown 
risks, uncertainties and other factors which may cause the actual results, 
performance or achievements of to be materially different from any future 
results, performance or achievements expressed or implied by the statements. 
Such factors include, among others, risks related to actual results of 
exploration activities, the timing and amount of expenditures and the 
completion of transactions and financings.

- 30 -

CONTACT INFO:

Rhyolite Resources Ltd.
Richard Graham, P.Geol.
President and CEO
604-488-8717
www.rhyoliteresources.com

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

MWDisclaimer
If you no longer want to receive announcements from us, please do 
not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=382989865