Source	MARKET NEWS
Date	10/30/2013
Time	05:43:23 AM

Company	 Silver Range Resources Ltd.
Title	Drill Results, Identifies Two New Mineralized Zo





    CDNX Symbol: SNG











Press Release	





Drill Results, Identifies Two New Mineralized Zones, And AppointsVice 
president Communications --->@NEWS RELEASE
SILVER RANGE RESOURCES LTD ("SNG-V;SLRRF-0")
- Drill Results, Identifies Two New Mineralized Zones, And
- Appoints Vice-president Communications

Silver Range Resources Ltd. ("Silver Range" or "the Company") is
pleased to announce results from exploration and drilling at its wholly
owned Silver Range Project located in Yukon Territory. The Silver Range
Project is situated 10 to 40 km north of the town of Faro, the former site
of large-scale lead-zinc-silver mining operations.

The 2013 exploration program included 1,156 m of diamond drilling in
seven exploration holes and one geotechnical hole, together with
prospecting and detailed mapping on silver-rich structural targets
surrounding the Company's core Keg Deposit. The bulk-tonnage Keg Deposit
contains 38.7 million ounces of silver, 675 million pounds of zinc, 228
million pounds of lead, and 131 million pounds of copper in inferred
resources (see further details below). Metallurgical results show that
mineralization responds very well to conventional copper/lead/zinc
flotation processing with excellent recoveries of payable metals.

Highlights of the 2013 exploration program include:

//st

A single exploration drill hole was completed at the Hammer Zone and
returned 337.00 g/t silver, 0.487% lead and 4.590% zinc over 0.49 m from
the Central Vein. Previous broadly-spaced drilling at the Hammer Zone
outlined a large high-grade epithermal system, with three subparallel,
silver-rich veins traced for strike lengths of up to 600 m and through a
vertical range of 280 m. All veins are open for extension along strike and
to depth;

Further drilling at the Owl Southwest Zone extended mineralization to the
northeast and downdip. Results from three completed drill holes include
152.4 g/t silver, 0.792% lead and 0.135% zinc over 2.61 m and 42.58 g/t
silver, 0.133% lead and 0.240% zinc over 11.18 m. Only two drill holes had
been previously completed at the Owl Southwest Zone, both of which returned
significant silver intersections including 5,370 g/t silver over 0.34 m and
432 g/t silver over 1.50 m; and

Silver-rich mineralization was discovered in two new areas of the property,
with rock samples returning 982 g/t silver, 4.180% lead and 9.730% zinc at
the Newton Zone and 504 g/t silver, 1.060% copper and 14.35% lead at the
Gauss Zone.

//et

Since 2010, exploration at the Silver Range project has identified 26
silver-bearing zones. Collectively, these prospects form two major
mineralized belts: the 17 km long Mount Mye Trend and the 70 km long Tay
Trend. Systematic grid drilling at one of the zones on the Tay Trend has
defined the Keg Deposit.

In 2013, three holes totaling 396.4 m were completed at the Owl
Southwest Zone, located 7.3 km northwest of the Keg Deposit. Drilling
tested the down-dip and strike extensions of mineralization identified in
2012, which included 5,370 g/t (156.63 oz/t) silver over 0.34 m in hole
OSW-12-001 (see news release dated October 25, 2012). Mineralization occurs
near the edge of an extensive upland marsh marked by a strong, open-ended
200 by 350 m soil geochemical anomaly, with values ranging from 10 to 208
g/t silver.

The 2013 drill program successfully extended the known mineralized
zone along strike to the northeast and down-dip. Hole OSW-13-005
intersected 2.61 m grading 152.4 g/t silver while hole OSW-006 returned
11.18 m grading 42.58 g/t silver. These 2013 holes are located 50 m along
strike and 50 m down dip, respectively, from the high-grade intercept in
OSW-12-001.

//st
Hole         From      To  Interval      Ag     Pb     Zn
(m)     (m)       (m)   (g/t)    (%)    (%)
OSW-13-005   31.52  34.13      2.61  152.40  0.792  0.135
OSW-13-006   71.13  82.31     11.18   42.58  0.133  0.240
Incl.        79.50  80.55      1.05  147.00  0.486  1.420
//et

//st

OSW-13-004 was collared ahead of the vein and returned no significant
intersections.

OSW-13-003 and OSW10-007 were lost at 119 m and 26 m, respectively, before
reaching their target depths.

//et

The Hammer Zone, a bonanza-grade silver-rich epithermal vein system
discovered in 2011, is located only 12 km from the Faro mine and mill site.
Broadly-spaced drilling in 2012 traced three subparallel veins for strike
lengths of up to 600 m and through a vertical range of 280 m.

One exploration drill hole (293 m in length) was completed at the
Hammer Zone in 2013. This hole intersected the Central Vein 110 m
vertically below surface and graded 337 g/t silver, 0.487% lead and 4.590%
zinc over 0.49 m. A second drill hole (68 m in length) was completed at the
Hammer Zone for environmental and geotechnical purposes. This hole was not
targeted to test any of the mineralized structures.

The Vent Zone,located 20 km east-southeast of the Keg Deposit, is
associated with a very strong, 600 by 400 m silver-arsenic-lead soil
anomaly. Two diamond drill holes totaling 280.0 m tested beneath a 2012
excavator trench that yielded 247 g/t silver and 1.30% lead across an 8 m
interval. While both diamond drill holes intersected structures thought to
be related to mineralization, no significant assays were returned. Both
holes unexpectedly cut shaly rocks which underlie the more brittle
pyroclastic rocks that host mineralization exposed in the trenches.

During 2013, field crews also conducted follow-up prospecting and
detailed mapping at 16 of the previously identified silver-bearing zones
(see Silver Range news release dated October 25, 2012) and eight previously
unprospected geochemical anomalies throughout the Silver Range project.
This work better defined the geological settings in areas of known
mineralization and discovered two new zones.

At the Newton Zone, located 17 km southeast of the Keg Main Zone,
silver-lead-zinc mineralization was identified in outcrop. A sample
collected from a 5 m wide fault exposed in bedrock along an east trending
linear feature yielded 30.44% zinc with 29.5 g/t silver. A near-source
float sample collected 800 m to the east along the same linear feature
produced 982 g/t silver with 4.180% lead and 9.730% zinc.

At the Gauss Zone, located 45 km southeast of the Keg Main Zone, two
silver-copper-lead showings were identified along a linear depression on a
northwest trending ridge. Two separate bedrock samples, located 1,700 m
apart along the linear depression, yielded 504 g/t silver, 1.060% copper
and 14.350% lead; and 44.1 g/t silver, 2.280% copper and 2.860% lead. Both
samples are associated with steeply dipping, northeast trending fracture
sets.

The 2013 surface work, combined with previous soil geochemical surveys
and prospecting, has identified several specific targets for future diamond
drilling.

Silver Range's Keg deposit contains an inferred resource of 39.76
million tonnes grading 30.25 g/t silver, 0.26% lead, 0.77% zinc and 0.15%
copper at a 16 g/t silver cut-off. For further details, see the technical
report entitled "Geology, Mineralization, Geochemical Surveys, Diamond
Drilling, Metallurgical Testing and Mineral Resources at the Keg Property"
dated December 19, 2012 and amended May 27, 2013 and filed on SEDAR.

In addition, the Company is pleased to announce the appointment of
Richard Drechsler as its Vice-President of Communications. In this
capacity, Mr. Drechsler will be the contact person for outside interest
groups, including First Nations and local communities. Mr. Drechsler will
continue to provide corporate communications and investor relations
services to shareholders and other interested parties. Mr. Drechsler
obtained a Bachelor of Science degree from the University of British
Columbia in 2007. He has worked in the mining/mineral exploration industry
since 2005 and has provided Silver Range Resources with investor relations
services since August 2011. In conjunction with this appointment, Mr.
Drechsler has been granted additional incentive stock options in respect of
25,000 shares exercisable at a price of $0.30 per share for a period of
five years. This option is subject to vesting provisions under which 25% of
the option will vest at the conclusion of each three months during the
first year of the term of the option.

Maps related to the Silver Range project can be viewed at
www.silverrangeresources.com. Work at the Silver Range project is being
conducted by Archer, Cathro & Associates (1981) Limited. Technical
information in this news release has been approved by Matthew R. Dumala, P.
Eng., a geological engineer with Archer Cathro and qualified person for the
purposes of National Instrument 43-101.

All analyses for rock and core samples from the 2013 program were
performed by ALS Minerals with sample preparation in Whitehorse and assays
and geochemical analyses in North Vancouver. Core samples are routinely
analyzed for gold by fire assay followed by atomic absorption (Au-AA24) and
48 other elements by inductively coupled plasma-mass spectrometry
(ME-MS61). Samples in mineralized intervals that exceed the detection
limits of the routine methods are assayed for silver, lead and zinc by
inductively coupled plasma-atomic emission spectroscopy (Ag/Pb/Zn - OG62).
Additionally core samples were analyzed for tin by pressed pellet x-ray
fluorescence spectroscopy (Sn-XRF05). Rigorous procedures are in place
regarding sample collection, chain of custody and data entry. Certified
assay standards, coarse reject duplicates, field duplicates and blanks are
routinely inserted into the sample stream to ensure integrity of the assay
process. All of the results reported have passed the QAQC screening.

ON BEHALF OF THE BOARD

W. Douglas Eaton, President and Chief Executive Officer
Neither the TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

TEL: (604) 688-2568  W. Douglas Eaton
President and C.E.O.
Silver Range Resources Ltd.

TEL: (604) 687-2522  Bruce A. Youngman, Chairman
Silver Range Resources Ltd.

TEL: (604) 687-2522  Richard Drechsler

TSX Venture closing price for SNG-V
Date: 2013/10/29
Closing Price: 0.12

TEL: (888) 688-2522  Corporate Communications
Silver Range Resources Ltd.
rdrechsler@silverrangeresources.com
www.silverrangeresources.com
____________________________________________________________
(c)2013 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1330200015TS11330200751-05422620131030