Source	Marketwire
Date	10/01/2014
Time	04:00:44 AM

Company	 SAVARY GOLD CORP.
Title	Savary Gold Drill Data Demonstrates Presence of Another Potentially Large, 
Gold Bearing System Further Emphasizing Exploration Potential of the Hounde 
South Property





    CDNX Symbol: SCA











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Savary Gold Corp.

TSX VENTURE SYMBOL: SCA

October 1, 2014

Savary Gold Drill Data Demonstrates Presence of Another Potentially Large, Gold 
Bearing System Further Emphasizing Exploration Potential of the Hounde South 
Property

Historic Holes Return 2.90 g/t Gold Over 21.0 Meters

TORONTO, ONTARIO--(Marketwired - Oct. 1, 2014) - Savary Gold Corp. (TSX 
VENTURE:SCA) ("Savary") announce newly documented results of historic drill 
intercepts on the Kueredougou West zone on the Hounde South property in 
southwestern Burkina Faso (see figure). The Hounde South property forms part of 
the recently announced joint venture between Savary (65%) and Sarama Resources 
Ltd (35%). Savary is the operator of the joint venture.

A summary of significant results(i) are as follows:

/T/

--  2.90 g/t gold over 22.0 metres - RC hole
--  1.75 g/t gold over 8.0 metres - RC hole
--  1.64 g/t gold over 20.0 meters - RC hole
--  1.42 g/t gold over 14.0 metres - RC hole
--  9.38 g/t gold over 2.0 meters - RC hole
--  1.91 g/t gold over 21.0 metres - RAB hole
--  1.73 g/t Au over 6.0 metres - RC hole

/T/

(i) These results are based on historic drill data that cannot be validated 
without re-drilling select holes as no reverse circulation chips are available 
for review. A summary of the assay composites are provided at the end of this 
release.

Don Dudek, President and CEO of Savary commented "These historic intercepts 
recently came to our attention during our continued review the property data 
with a goal toward developing a cost effective exploration program. These new 
results further emphasize what we perceive is the excellent exploration 
potential of the Hounde South property. To date we have not found the limits of 
any of the gold-bearing systems with the major gold-in-soil trends 
demonstrating the potential extent of individual mineralized trends. Thus it is 
with confidence that Savary, along with our partners Sarama look forward to 
validating these results with follow-up holes of our own, further testing and 
extending the known zones and the discovery of new centres of gold 
mineralization."

The Kueredougou West zone lies approximately 1.2 kilometres south of the 
furthest southern holes on the Kueredougou zone (see Figure) which returned 
drill intercepts of 12.80 g/t Au over 2.0 metres and 4.04 g/t Au over 5.0 
metres. Drilling has tested the zone, which consists of up to three modelled, 
moderate-east-plunging lenses of mineralization, to a maximum depth of 100 
metres along a 500 metre strike. True widths are estimated at approximately 90% 
of drill width. This zone, which was tested by seventeen reverse circulation 
holes, in 1999 and 2000 by Delta Gold, totalling 1,614 metres, is open in all 
directions and is either part of the Kueredougou mineralized system, which has 
been traced for approximately 2,900 metres (see Savary news release May 14, 
2014) or a parallel gold system, located 200 to 300 metres to the west. 
Gold-in-soil geochemical data with values ranging from a low of 50 ppb to a 
high of 1,888 ppb form a coherent anomaly approximately 5.6 kilometres long and 
up to 300 m wide. Other than reverse circulation drilling along a 500 metre 
portion of the gold-in-soil anomalous trend, the majority of the anomaly has 
not been tested. As well as providing context for the historic drill results 
presented in this release, the attached figure provides a summary snapshot of 
the extent of the drill defined gold systems, the resolution of the 0.5 - 1.5 
km wide gold-in-soil anomalous corridor, into three to four trends of better 
mineralization on the Hounde South portion of the property and the potential to 
extend the modelled gold zones by following the mineralized trends along the 
gold-in-soil anomalies. A summary of the drill results are presented in a table 
at the end of this release.

QP comments

The Kueredougou West gold zone results are based on data acquired from 
exploration companies that were previously active on the Hounde South property. 
This zone lies on strike with existing mineralization and is consistent in 
tenor with other gold zones on the property. However, in order to properly 
validate this occurrence, several twin drill holes will be required as the 
original reverse circulation drill chips and assay certificates are no longer 
available.

Drilling results are quoted as downhole intersections. True mineralisation 
width is expected to be approximately 90% of intersection length for holes 
drilled on 290 degrees azimuth sections, dipping at -60 degrees to the west and 
intersecting the north-north-east striking lenses, however the nature of some 
mineralised units is not well understood.

The reported composites for RC and RAB drilling were determined using a cut-off 
grade of 0.50g/t Au to select significant and anomalous intersections, with a 
maximum of 2m internal dilution being incorporated into the composite where 
appropriate. No top-cuts were applied to assay grades. Isolated mineralised 
intersections less than 2m in length have not been reported.

The nature of any quality assurance/quality control programs which may have 
been conducted as part of the original drilling program is not known.

Gold assays for the RC and RAB drilling were most likely determined by fire 
assay methods, however this cannot be confirmed.

RC drilling was generally designed using 290 degrees azimuth oriented holes, 
dipping at -60 degrees to the west, approximately 80-120m in length. RC drill 
cuttings were sampled over regular 1m intervals. RAB drill cuttings were 
sampled over regular 1m intervals.

About Savary Gold

Savary Gold is a Canadian exploration company, along with partner, Sarama 
Resources Limited, are focused on exploring the Hounde South and Serakoro 1 
Gold Properties in Burkina Faso. The properties are in the Birimian age Hounde 
Greenstone Belt, which hosts Semafo's Mana mine and additional gold deposits 
that are presently subject to extensive exploration efforts (including 
Endeavour Mining's Hounde Project, Roxgold Yaramoko Project and Sarama's South 
Hounde Project, which is adjacent to Savary Gold's property). For additional 
information please visit our website at www.savarygold.com and follow us on 
Facebook, Linked-In and Twitter: @SavaryGold.

Don Dudek, P.Geo., President and CEO of the Company and a qualified person 
under National Instrument 43-101, has reviewed and approved the scientific and 
technical information in this press release.

SAVARY GOLD CORP.

On behalf of the Board

Don Dudek, President & Chief Executive Officer

Cautionary Notes

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

This news release may contain forward-looking statements. These statements 
include statements regarding the historical drill intercepts and the results of 
historical data being indicative of the potential of the property. These 
statements are based on current expectations and assumptions that are subject 
to risks and uncertainties. Actual results could differ materially because of 
factors discussed in the management discussion and analysis section of our 
interim and most recent annual financial statements or other reports and 
filings with the TSX Venture Exchange and applicable Canadian securities 
regulations. We do not assume any obligation to update any forward-looking 
statements, except as required by applicable laws.

1999, 2000 Kueredougou West Assay Composites

/T/

----------------------------------------------------------------------------
Hole #                                    FROM        TO    LENGTH    Au_g/t
----------------------------------------------------------------------------
BRRC005                                   0.00     22.00     22.00      2.90
BRRC005                                  38.00     40.00      2.00      2.40
BRRC006                                   0.00      2.00      2.00      0.60
BRRC006                                  28.00     32.00      4.00      0.84
BRRC006                                  54.00     58.00      4.00      1.49
BRRC006                                  68.00     70.00      2.00      1.72
BRRC006                                  78.00     80.00      2.00      1.06
BRRC013                                  18.00     26.00      8.00      1.61
BRRC013                                  40.00     60.00     20.00      1.64
BRRC038                                  26.00     28.00      2.00      0.58
BRRC038                                  40.00     44.00      4.00      1.46
BRRC039                                  74.00     78.00      4.00      0.91
BRRC039                                 110.00    112.00      2.00      0.62
BRRC040                                   0.00      2.00      2.00      1.15
BRRC040                                  10.00     18.00      8.00      1.75
BRRC041                                   0.00      2.00      2.00      4.66
BRRC041                                  76.00     78.00      2.00      1.97
BRRC041                                  88.00     94.00      6.00      0.53
BRRC042                                   8.00     22.00     14.00      1.42
BRRC042                                  30.00     32.00      2.00      9.38
BRRC043                                  26.00     30.00      4.00      4.59
BRRC043                                  44.00     52.00      8.00      1.04
BRRC043                                  56.00     60.00      4.00      3.75
BRRC044                                   8.00     10.00      2.00      0.77
BRRC044                                  70.00     72.00      2.00      2.11
BRRC044                                  82.00     84.00      2.00      0.89
BRRC045                                  84.00     86.00      2.00      0.50
BRRC045                                  96.00     98.00      2.00      0.55
BRRC045                                 112.00    116.00      4.00      0.79
BRRC046                                  16.00     20.00      4.00      1.81
BRRC047                                  46.00     52.00      6.00      1.73
BRRC048                                  62.00     64.00      2.00      0.52
BRRC049                                   6.00     10.00      4.00      0.91
BRRC049                                  16.00     18.00      2.00      3.38
BRRC050                                  20.00     22.00      2.00      1.89
BRRC050                                  56.00     58.00      2.00      0.83
BRRC050                                  66.00     70.00      4.00      1.38
BRRC051                                  68.00     76.00      8.00      1.01
BGRB020(i)                                0.00     21.00     21.00      1.91

/T/

(i) Rotary Air Blast or RAB hole

To view the Figure associated with this release, please visit the following 
link: http://media3.marketwire.com/docs/970707.pdf

- 30 -

CONTACT INFO:

Savary Gold Corp.
Michael McAllister
Manager, Investor Relations
416-309-2134
info@savarygold.com
www.savarygold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=500946348