Source	Marketwire
Date	10/02/2014
Time	05:44:38 AM

Company	 SAN MARCO RESOURCES INC.
Title	San Marco Resources Inc.: CdM South Yields Signs of High Sulfidation 
Epithermal Gold Mineralization





    CDNX Symbol: SMN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: San Marco Resources Inc.

TSX VENTURE SYMBOL: SMN

October 2, 2014

San Marco Resources Inc.: CdM South Yields Signs of High Sulfidation Epithermal 
Gold Mineralization


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Oct. 2, 2014) - San Marco Resources 
Inc. (TSX VENTURE:SMN) ("San Marco" or "the Company") has discovered the 
presence of alteration patterns consistent with high sulfidation 
epithermal-type gold deposits at its CdM South concession in the Cuatro de Mayo 
Project, Sonora State, Mexico. Furthermore, stream sediment sampling, using the 
bulk leach extractable gold ("BLEG") technique, indicates the presence of gold 
coincident with this alteration.

In conjunction with its early reconnaissance work at CdM Central, San Marco 
geologists prospected at the CdM South concession where they discovered 
indications of high-sulfidation epithermal-style alteration including massive 
silicification and locally vuggy silica. Approximately 20% of the property was 
traversed, primarily along 3 creek drainages. Anomalous gold was detected in 
stream sediments over an 800 meter section of one stream in particular that 
occurs below highly silicified outcrops. Drainage flow indicates the origin of 
the gold is from the central area of the 3,336 hectare concession. In addition, 
fine gold was recovered locally from panning creek bed material. Although the 
Company's collection of rock chip samples was very limited due to the rainy 
season, in the northern area of CdM South, chip sampling of a highly altered 
silicified outcrop returned 0.43 g/t gold.

The CdM South concession lies approximately 20 km from both the La India and 
Mulatos gold operations (owned by Agnico Eagle and Alamos Gold respectively), 
each of which are producing gold from high sulfidation epithermal deposits. CdM 
South is approximately 50 km southwest of the CdM Central block of concessions 
and the El Valle shear zone, which was the subject of a separate San Marco news 
release issued on September 29, 2014. A map showing the location of concessions 
comprising the Cuatro de Mayo property is available at www.sanmarcocorp.com.

Robert Willis, CEO of San Marco states, "CdM South shows alteration patterns 
consistent with high sulfidation epithermal gold deposits, has returned 
anomalous gold in regional first-pass stream sediment sampling, and is in the 
vicinity of two operating mines producing gold from high sulfidation epithermal 
deposits. Our first pass evaluation of CdM South clearly indicates follow up 
work is warranted. This is the second highly prospective target we have 
identified within the CdM group of concessions over the last few months. San 
Marco has a top notch exploration team who continue to methodically field proof 
and prioritize targets."

Cuatro de Mayo Background

The Cuatro de Mayo property comprises 18,564 hectares in three claim areas 
located approximately 160 km east of Hermosillo, Mexico; CdM Central (seven 
concessions), CdM East, and CdM South (one concession each). Numerous gold, 
silver and base metal showings and historic workings are known to occur in the 
Cuatro de Mayo property and surrounding area. These showings represent a 
variety of deposit types including epithermal gold and silver, structurally 
controlled stratabound gold, CRD-type (mantos, skarns) silver-lead-zinc 
showings, and mesothermal silver showings. Additional details are provided on 
the Company's website www.sanmarcocorp.com and in San Marco's news release 
dated May 14, 2014.

About San Marco

San Marco Resources Inc. is a Canadian mineral exploration company with a 
current portfolio of four promising properties in mining-friendly Mexico and an 
aggressive project generation program focused on high-calibre, low-opportunity 
cost projects. San Marco has a committed management team with extensive 
experience in Mexico and a proven track record of building shareholder value.

National Instrument 43-101 Disclosure

The technical information contained in this document has been verified, and 
this news release has been approved, by San Marco's CEO, Robert D. Willis, P. 
Eng. a "Qualified Person" as defined in National Instrument 43-101, Standards 
of Disclosure for Mineral Projects of the Canadian Securities Administrators.

The CdM South stream sediment samples discussed in this document were assayed 
using the bull leach extractable gold ("BLEG") assay technique, which is well 
suited for first-pass evaluation for the presence of gold anomalies over a 
large area, but which does not recover gold tightly held in compounds or 
physically encased on other minerals. As such, BLEG assay results are generally 
far lower than those obtained by fire assay. The samples discussed herein were 
prepared for analysis at.ALS Chemex facilities in Hermosillo and analyzed using 
Au-AA12, MS41L and MEICP41iL mothods at ALS Chemex in North Vancouver. San 
Marco's sample collection, integrity, quality control and assurance procedures 
are in line with industry best practices and comply with National Instrument 
43-101 requirements.

Forward-Looking Information

Information set forth in this document includes forward-looking statements, 
such as: potential exploration plans and programs for the Cuatro de Mayo 
project. While these statements reflect management's current plans, projections 
and intents, by their nature, forward-looking statements are subject to 
numerous risks and uncertainties, some of which are beyond the control of San 
Marco Resources Inc. For instance, the execution of any exploration programs 
planned by the Company will be dependent upon the availability of both human 
and financial resources, both of which are presently limited. Readers are 
cautioned that the assumptions used in the preparation of such information, 
although considered reasonable at the time of preparation, may prove to be 
imprecise and, as such, undue reliance should not be placed on these 
forward-looking statements. San Marco's actual results, programs and financial 
position could differ materially from those expressed in or implied by these 
forward-looking statements.

Neither the TSX Venture Exchange nor the Investment Industry Regulatory 
Organization of Canada accepts responsibility for the adequacy or accuracy of 
this release.

- 30 -

CONTACT INFO:

San Marco Resources Inc.
Robert D. Willis
CEO
604-568-5951
604-813-2606
rwillis@sanmarcocorp.com

or

San Marco Resources Inc.
Barbara Henderson
Investor Relations Officer
604-568-5951
604-789-7689
bhenderson@sanmarcocorp.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=501153676