Source	Marketwire
Date	10/02/2014
Time	10:08:46 AM

Company	 NORTHERN ABITIBI MINING CORP.
Title	Exploration to Commence at Northern Abitibi's Ches Property, British 
Columbia





    CDNX Symbol: NAI











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Northern Abitibi Mining Corp.

TSX VENTURE SYMBOL: NAI

October 2, 2014

Exploration to Commence at Northern Abitibi's Ches Property, British Columbia


CALGARY, ALBERTA--(Marketwired - Oct. 2, 2014) - Northern Abitibi Mining Corp. 
("Northern Abitibi or the Company") (TSX VENTURE:NAI) is pleased to announce 
that exploration will commence shortly at the Ches property in Central British 
Columbia. An evacuation order for the area was issued in July due to a large 
uncontrolled wildfire over the Ches project area. This order has recently been 
lifted and Northern Abitibi exploration personnel can now access the area.

The Company will immediately start a field program consisting of mapping, soil 
and rock channel sampling, and excavator trenching to evaluate and expand known 
zones of mineralization previously exposed in logging road cuts on the property.

The Ches Property

The road accessible Ches Property is located 80 kilometres south of Burns Lake 
on the south side of Ootsa Lake. Mineralization consists of 
pyrrhotite-chalcopyrite-scheelite replacement (skarn) style mineralization in 
calcareous sedimentary rocks and quartz chalcopyrite-molybdenite-scheelite 
stockwork veining in fine grained siltstones. Historic Assessment Reports state 
average grades from surface sampling of 0.52% copper and 4.7 g/t silver over a 
zone 350 metres wide, and copper in soil geochemical anomalies up to 350 metres 
wide and 800 to 1500 metres long, and open along strike. Subsequent surface 
grab sampling reported in a 2009 Technical Report by Scarlet Resources Ltd. 
returned values up to 1% copper, 16 g/t silver, and 0.3% tungsten from the 
replacement-skarn style mineralization, and values up to 0.45% copper, 0.02% 
molybdenum, 7 g/t silver, and 0.1% tungsten from the stockwork zone. These 
mineralized zones have never been trenched or drill tested. The sampling 
results above are considered historic in nature, they have not been confirmed 
by Northern Abitibi, and should not be relied upon.

Dr. Shane Ebert, P. Geo. is the Qualified Person responsible for the 
preparation of this news release.

Shane Ebert, President/Director

The TSX Venture Exchange has neither approved nor disapproved of the contents 
of this press release.

Except for the historical and present factual information contained herein, the 
matters set forth in this news release, including words such as "expects", 
"projects", "plans", "anticipates" and similar expressions, are forward-looking 
information that represents management of Northern Abitibi's internal 
projections, expectations or beliefs concerning, among other things, future 
operating results and various components thereof or the economic performance of 
Northern Abitibi. The projections, estimates and beliefs contained in such 
forward-looking statements necessarily involve known and unknown risks and 
uncertainties, which may cause Northern Abitibi's actual performance and 
financial results in future periods to differ materially from any projections 
of future performance or results expressed or implied by such forward-looking 
statements. These risks and uncertainties include, among other things, those 
described in Northern Abitibi's filings with the Canadian securities 
authorities. Accordingly, holders of Northern Abitibi shares and potential 
investors are cautioned that events or circumstances could cause results to 
differ materially from those predicted. Northern Abitibi disclaims any 
responsibility to update these forward-looking statements.

- 30 -

CONTACT INFO:

Northern Abitibi Mining Corp.
Shane Ebert
1.250.964.2699

or

Northern Abitibi Mining Corp.
Jean Pierre Jutras
1.403.233.2636
www.naminco.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=501287411