Source	Marketwire
Date	10/08/2014
Time	05:30:21 AM

Company	 SAN MARCO RESOURCES INC.
Title	Trenching at Cuatro de Mayo Property Confirms Gold Mineralization and 
Extends Dimension at El Valle Shear Zone





    CDNX Symbol: SMN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: San Marco Resources Inc.

TSX VENTURE SYMBOL: SMN

October 8, 2014

Trenching at Cuatro de Mayo Property Confirms Gold Mineralization and Extends 
Dimension at El Valle Shear Zone


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Oct. 8, 2014) - San Marco Resources 
Inc. (TSX VENTURE:SMN) ("San Marco" or "the Company") is pleased to announce 
rock chip sampling results from four trenches recently completed at the El 
Valle shear zone on the Company's Cuatro de Mayo project in Sonora State, 
Mexico. This trench sampling has returned results of up to 0.55 g/t gold over 
24 metres.

Recent mapping along the El Valle shear zone has extended its known strike 
length to 800 metres, of which 400 metres has now been intermittently cross-cut 
and sampled. The systematic trenching recently completed has resulted in the 
discovery of a number of parallel, gold-bearing shears, which may coalesce with 
the main shear at depth. The El Valle shear zone is therefore open in all three 
dimensions. The trench sampling results reported below are comparable to those 
obtained from the Company's recently released creek sampling at El Valle (see 
news release dated September 29, 2014) and confirm the gold-bearing nature of 
the shear zone. Importantly, ICP results for secondary and pathfinder elements 
(particularly silver and mercury) indicates surface exposures at El Valle are 
quite high in the mineralized system and that both precious and base metal 
values may increase with depth. An El Valle trenching map is available at 
www.sanmarcocorp.com.

Robert Willis, CEO of San Marco states, "The El Valle area has quickly and 
efficiently developed into an exciting exploration target hosting oxide gold at 
surface. Shallowly dipping gold-bearing shear zones are a common feature in 
gold deposits in northwest Mexico, including the famous Megashear in western 
Sonora State. Similar structures that have returned grades in the range of 
those reported by San Marco today account for some of the most successful oxide 
heap leach operations currently in production in Sonora. The Company looks 
forward to undertaking additional work at this prospective target, which could 
include drilling, in order to assess the gold deposit potential at El Valle."

Tookie Angus, Chairman of San Marco adds, "The Cuatro de Mayo project is a 
highly prospective property that has provided early stage success for San 
Marco. The Company's focus on this project at this time is clearly warranted."

From south to north along the El Valle shear zone, sampling results to date 
include:

Creek 1 (previously released): 18.1 metres averaging 0.43 g/t gold including 
12.0 metres averaging 0.57 g/t gold near the western contact, and 14.2 metres 
averaging 0.90 g/t gold near the eastern contact. Approximately 10 metres of 
lower grade gold exists in the center section of the shear,

Trench 1: 25 metres averaging 0.40 g/t gold. This sample includes both cleaned 
bedrock exposure and intermittent areas of sub-crop/alluvium that report 
generally lower grades. Where exposed, the shear zone exhibits significant 
alteration and silicification around intense quartz veinlets.

Trench 2: 58 metres averaging 0.32 g/t gold, including 24 metres averaging 0.55 
g/t gold. This sample interval was completely within shear zone in bedrock 
exposed by trenching with no sub-crop/alluvium sections.

Trench 3: 22 metres averaging 0.21 g/t gold including 12 metres averaging 0.26 
g/t gold. A second shear structure containing anomalous gold (20 metres 
averaging 0.10 g/t gold) was discovered 32 metres to the east of this higher 
grade section. The trench was terminated in this second zone where an 
intermittently flooding creek prevented the backhoe from continuing. Bedrock 
was not reached in all zones along this trench and intermittent lower grade 
sections relate to samples collected from the bedrock/alluvium transitional 
zone.

Creek 2 (previously released): 9.1 metres averaging 1.0 g/t gold. Again, this 
sampling was truncated within the shear zone due to intermittent flooding 
within the creek. However, the shear zone was visually observed for an 
additional 30 metres eastward.

Trench 4: 22 metres averaging 0.21 g/t gold including 12 metres averaging 
0.32g/t gold. This trench was dug in order to test the hanging wall of the El 
Valle shear zone rather than to crosscut the main shear structure. A shear 
zone, which appears to be a sub-parallel or splay of the main shear, was 
encountered at the eastern end of this trench. Bedrock was not reached in all 
zones along this trench and intermittent lower grade sections relate to samples 
collected from the bedrock/alluvium transitional.

As expected, the surface width of the El Valle shear zone pinches and swells, 
and is locally cross cut by northeast-trending faults. The shear zone appears 
to dip shallowly to the northeast. Trenches 1 to 4 were excavated with a 
backhoe to a maximum depth of three metres (the limit of the backhoe). Due to 
variations in the overburden depth, some areas had to be hand trenched, and 
samples from these areas consist of sub-crop and alluvium rather than clean 
rock exposures. Gold values were typically lower, though still anomalous, in 
these sub-crop samples. The trench results above correspond to continuous 2 
metre rock chip samples, which periodically included sampling of the 
sub-crop/alluvium interface, and represent a portion of the total surface width 
of the shear zone.

About San Marco

San Marco Resources Inc. is a Canadian mineral exploration company with a 
current portfolio of four promising properties in mining-friendly Mexico and an 
aggressive project generation program focused on high-calibre, low-opportunity 
cost projects. San Marco has a committed management team with extensive 
experience in Mexico and a proven track record of building shareholder value.

National Instrument 43-101 Disclosure

The technical information contained in this document has been verified, and 
this news release has been approved, by San Marco's CEO, Robert D. Willis, P. 
Eng. a "Qualified Person" as defined in National Instrument 43-101, Standards 
of Disclosure for Mineral Projects of the Canadian Securities Administrators.

The samples discussed in this document were prepared for assay at ALS Chemex 
Lab in Mexico and assayed at their facility in Vancouver, BC. A 30 gram split 
is analyzed for gold, using the Au-AA23 method. Sample results greater than 10 
ppm are re-assayed, using AA23 fire assay and gravimetric finish. For silver, 
copper, lead and zinc, a multi-element, four acid digestion (ME -- ICP 61) 
method is used. For initial assays of silver greater than 100 ppm, copper, lead 
and zinc greater than 10,000 ppm (over limits), the OG62 method is used for 
re-analysis. San Marco's sample collection, integrity, and quality control and 
assurance procedures are in line with industry best practices and comply with 
National Instrument 43-101 requirements.

Forward Looking Information

Information set forth in this document includes forward-looking statements, 
such as: initial interpretation of geological observations; and, potential 
exploration plans and programs for the Cuatro de Mayo project. While these 
statements reflect management's current understanding, plans, projections and 
intents, by their nature, forward-looking statements are subject to numerous 
risks and uncertainties, some of which are beyond the control of San Marco 
Resources Inc. For instance, the execution of any exploration programs planned 
by the Company will be dependent upon the availability of both human and 
financial resources, both of which are presently limited. Furthermore, 
geological interpretations are open to revision as additional information 
becomes available. Readers are cautioned that the assumptions used in the 
preparation of such information, although considered reasonable at the time of 
preparation, may prove to be imprecise and, as such, undue reliance should not 
be placed on these forward-looking statements. San Marco's actual results, 
programs and financial position could differ materially from those expressed in 
or implied by these forward-looking statements.

Neither the TSX Venture Exchange nor the Investment Industry Regulatory 
Organization of Canada accepts responsibility for the adequacy or accuracy of 
this release.

- 30 -

CONTACT INFO:

San Marco Resources Inc.
Robert D. Willis
CEO
604-568-5951
604-813-2606
rwillis@sanmarcocorp.com

or

San Marco Resources Inc.
Barbara Henderson
Investor Relations Officer
604-568-5951
604-789-7689
bhenderson@sanmarcocorp.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=501806693