Source	Marketwire
Date	10/07/2014
Time	05:00:29 AM

Company	 SCORPIO GOLD CORPORATION
Title	Scorpio Gold's 2014 Drilling Continues to Upgrade the Mary LC Deposit, 
Mineral Ridge Project, Nevada





    CDNX Symbol: SGN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Scorpio Gold Corporation

TSX VENTURE SYMBOL: SGN

October 7, 2014

Scorpio Gold's 2014 Drilling Continues to Upgrade the Mary LC Deposit, Mineral 
Ridge Project, Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Oct. 7, 2014) - Scorpio Gold 
Corporation ("Scorpio Gold" or the "Company") (TSX VENTURE:SGN) reports further 
assay results from its 2014 drill program on the Mary LC deposit at the 70% 
owned Mineral Ridge project, located in Nevada.

On July 21, 2014, the Company reported an updated Life of Mine Plan ("LOM 
Plan") for the Mineral Ridge Operation, which includes the currently producing 
Drinkwater and Mary LC deposits and five adjacent satellite deposits. As of 
March 31, 2014, Probable Mineral Reserves for the Mary LC deposit totalled 
1,502,560 tons grading 0.061 ounces per ton (oz/ton) for 91,510 contained 
ounces gold. Probable Mineral Reserves are included within an Indicated Mineral 
Resource of 1,534,500 tons grading 0.063 oz/ton gold. Inferred Mineral 
Resources for the Mary LC deposit totalled 50,900 tons grading 0.061 oz/ton. 
Pre-stripping of the Mary LC pit commenced in the first quarter of 2014 and 
extraction of development ore was realized in the second quarter of 2014.

Infill and step-out drilling on the Mary LC deposit has continued since the 
March 31, 2014 cut-off date of the LOM Plan and is focused on increasing the 
total mineral resources, upgrading resource categories, lowering the strip 
ratio and potentially increasing the mineral reserve estimate for the Mary LC 
deposit. An additional 84 drill holes within and proximal to the Mary LC pit 
are planned to be completed by year end.

Highlights from the most recent phase of expansion drilling on the Mary LC, 
comprised of a total of 28 drill holes, include:

/T/

--  MR14887: 2.86 grams per tonne ("g/t") gold over 7.62 meters
--  MR14890: 2.47 g/t gold over 6.10 meters
--  MR14895: 2.89 g/t gold over 4.57 meters
--  MR141000: 3.08 g/t gold over 7.62 meters

/T/

Scorpio Gold's management considers the initial drilling results of the 
expansion drilling program on the Mary LC deposit to be positive, and 
anticipates that once the expansion drilling program is complete, the drill 
results will allow for a revised reserve and resource estimate on the Mary LC 
deposit.

A drill hole location map is available at: 
www.scorpiogold.com/i/maps/mr/MaryLC_DHplan.jpg

Table 1. Mary LC Deposit - Significant Drill Results

/T/

----------------------------------------------------------------------------
Hole             Azm   Dip  From    To Width   From     To Width  Gold  Gold
No.            (deg) (deg)  (ft)  (ft)  (ft)    (m)    (m)   (m) (OPT) (g/t)
----------------------------------------------------------------------------
MR14881            0   -90   145   150     5  44.20  45.72  1.52 0.051  1.76
----------------------------------------------------------------------------
175   180     5  53.34  54.86  1.52 0.051  1.73
----------------------------------------------------------------------------
MR14882            0   -90   145   150     5  44.20  45.72  1.52 0.077  2.62
----------------------------------------------------------------------------
MR14883            0   -90    20    25     5   6.10   7.62  1.52 0.038  1.31
----------------------------------------------------------------------------
110   120    10  33.53  36.58  3.05 0.036  1.23
----------------------------------------------------------------------------
MR14884            0   -90              No Significant Results
----------------------------------------------------------------------------
MR14885          225   -55              No Significant Results
----------------------------------------------------------------------------
MR14886            0   -90   235   240     5  71.63  73.15  1.52 0.012  0.41
----------------------------------------------------------------------------
MR14887            0   -90    85   110    25  25.91  33.53  7.62 0.083  2.86
----------------------------------------------------------------------------
MR14888          225   -55    55    60     5  16.76  18.29  1.52 0.010  0.34
----------------------------------------------------------------------------
70    75     5  21.34  22.86  1.52 0.138  4.73
----------------------------------------------------------------------------
85    95    10  25.91  28.96  3.05 0.013  0.45
----------------------------------------------------------------------------
MR14889            0   -90    70    75     5  21.34  22.86  1.52 0.016  0.55
----------------------------------------------------------------------------
110   115     5  33.53  35.05  1.52 0.039  1.34
----------------------------------------------------------------------------
MR14890          225   -55   100   120    20  30.48  36.58  6.10 0.072  2.47
----------------------------------------------------------------------------
MR14891            0   -90              No Significant Results
----------------------------------------------------------------------------
MR14892          225   -55              No Significant Results
----------------------------------------------------------------------------
MR14893            0   -90    25    30     5   7.62   9.14  1.52 0.011  0.38
----------------------------------------------------------------------------
75    85    10  22.86  25.91  3.05 0.021  0.70
----------------------------------------------------------------------------
MR14894          225   -55    10    15     5   3.05   4.57  1.52 0.011  0.38
----------------------------------------------------------------------------
65    80    15  19.81  24.38  4.57 0.019  0.64
----------------------------------------------------------------------------
330   335     5 100.58 102.11  1.52 0.041  1.41
----------------------------------------------------------------------------
375   380     5 114.30 115.82  1.52 0.029  0.99
----------------------------------------------------------------------------
MR14895          225   -55    95   110    15  28.96  33.53  4.57 0.084  2.89
----------------------------------------------------------------------------
MR14896            0   -90    50    55     5  15.24  16.76  1.52 0.059  2.02
----------------------------------------------------------------------------
MR14897            0   -90              No Significant Results
----------------------------------------------------------------------------
MR14898          225   -55              No Significant Results
----------------------------------------------------------------------------
MR14900            0   -90              No Significant Results
----------------------------------------------------------------------------
MR14992            0   -90    85    95    10  25.91  28.96  3.05 0.014  0.47
----------------------------------------------------------------------------
MR14993          225   -55              No Significant Results
----------------------------------------------------------------------------
MR14994            0   -90    20    45    25   6.10  13.72  7.62 0.021  0.73
----------------------------------------------------------------------------
65    85    20  19.81  25.91  6.10 0.032  1.10
----------------------------------------------------------------------------
MR14996            0   -90     0    10    10   0.00   3.05  3.05 0.030  1.01
----------------------------------------------------------------------------
MR14997            0   -90     0    10    10   0.00   3.05  3.05 0.034  1.15
----------------------------------------------------------------------------
45    60    15  13.72  18.29  4.57 0.031  1.05
----------------------------------------------------------------------------
MR14998            0   -90   235   260    25  71.63  79.25  7.62 0.036  1.23
----------------------------------------------------------------------------
MR14999            0   -90   245   265    20  74.68  80.77  6.10 0.036  1.22
----------------------------------------------------------------------------
295   300     5  89.92  91.44  1.52 0.014  0.47
----------------------------------------------------------------------------
MR141000         225   -55   180   185     5  54.86  56.39  1.52 0.035  1.19
----------------------------------------------------------------------------
205   230    25  62.48  70.10  7.62 0.090  3.08
----------------------------------------------------------------------------
245   250     5  74.68  76.20  1.52 0.016  0.53
----------------------------------------------------------------------------
MR141032           0   -90    35    40     5  10.67  12.19  1.52 0.021  0.70
----------------------------------------------------------------------------
210   235    25  64.01  71.63  7.62 0.042  1.44
----------------------------------------------------------------------------

/T/

All holes presented in Table 1 were completed by reverse circulation ("RC") 
drilling. True width is estimated at 80-100% of downhole width. Analytical 
results were performed by American Assay Laboratory Inc. in Sparks, Nevada, an 
ISO/IEC 17025:2005 accredited facility. External check assays to verify lab 
accuracy are routinely completed by ALS Chemex, an ISO 9001:2000 certified and 
ISO/IEC 17025:2005 accredited facility. Further details are presented in the 
Company's quality assurance and quality control program for the Mineral Ridge 
project at: www.scorpiogold.com/i/pdf/reports/QAQC-MR.pdf.

Red Cloud Fall Investor Showcase

Scorpio Gold's President, Steve Roebuck, will be presenting at the Red Cloud 
2nd Annual Fall Investor Showcase to be held on October 9, 2014 at the King 
Edward Hotel, 37 King St E Toronto, ON, 2nd Floor. Further information is 
available at: www.redcloudmining.com.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the producing Mineral Ridge gold mining 
operation located in Esmeralda County, Nevada with joint venture partner 
Waterton Global Value L.P. (30%), and Scorpio Gold is currently entitled to 
receive 80% of cash flow generated. Mineral Ridge is a conventional open pit 
mining and heap leach operation. The Mineral Ridge property is host to multiple 
gold-bearing structures, veins and lenses at exploration, development and 
production stages. Scorpio Gold also holds a 100% interest in the advanced 
exploration-stage Goldwedge property and processing facility in Manhattan, 
Nevada. The Company is assessing its exploration plans for the Goldwedge 
property as well as the potential for toll milling at the Goldwedge plant, 
which is currently permitted for 400 tons per day.

Scorpio Gold's President, Steve Roebuck, P.Geo., is a Qualified Person as 
defined by National Instrument 43-101 and has reviewed and approved the content 
of this release.

ON BEHALF OF THE BOARD

SCORPIO GOLD CORPORATION

Steve Roebuck, President

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

The Company relies on litigation protection for forward-looking statements. 
This news release contains forward-looking statements that are based on the 
Company's current expectations and estimates. Forward-looking statements are 
frequently characterized by words such as "plan", "expect", "project", 
"intend", "believe", "anticipate", "estimate", "suggest", "indicate" and other 
similar words or statements that certain events or conditions "may" or "will" 
occur, and include, without limitation, statements regarding the Company's 
plans with respect to the exploration, development and exploitation of its 
Mineral Ridge project, including pit expansion on the Mary LC deposit. Such 
forward-looking statements involve known and unknown risks, uncertainties and 
other factors that could cause actual events or results to differ materially 
from estimated or anticipated events or results implied or expressed in such 
forward-looking statements, including risks involved in exploration programs 
and those risk factors outlined in the Company's Management Discussion and 
Analysis as filed on SEDAR. Any forward-looking statement speaks only as of the 
date on which it is made and, except as may be required by applicable 
securities laws, the Company disclaims any intent or obligation to update any 
forward-looking statement, whether as a result of new information, future 
events or results or otherwise. Forward-looking statements are not guarantees 
of future performance and accordingly undue reliance should not be put on such 
statements due to the inherent uncertainty thereof.

- 30 -

CONTACT INFO:

Steve Roebuck, President
Tel: (819) 825-7618
Email: sroebuck@scorpiogold.com
Website: www.scorpiogold.com

or

Investor Relations:
Jim Macdonald, Torrey Hills Capital
Tel: (858) 456-7300
Email: jm@sdthc.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=501629053