Source	Marketwire
Date	10/07/2014
Time	07:06:39 AM

Company	 KHALKOS EXPLORATION INC.
Title	Khalkos Exploration Inc./Villebon: Gold Grade of 4.89 g/t Recovered by 
Gravimetric Process on 13-ton Rock Bulk Sample





    CDNX Symbol: KAS











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Khalkos Exploration Inc.

TSX VENTURE SYMBOL: KAS

October 7, 2014

Khalkos Exploration Inc./Villebon: Gold Grade of 4.89 g/t Recovered by 
Gravimetric Process on 13-ton Rock Bulk Sample


MONTREAL, QUEBEC--(Marketwired - Oct. 7, 2014) - Exploration Khalkos. 
("Khalkos") (TSX VENTURE:KAS) Management of Khalkos is pleased to announce the 
results of the bulk sampling undertaken on the zone Cere of the Villebon 
property. By gravimetric processing only, a recovery rate of gold of 82.5% was 
obtained. Sixty four grams of gold grading 83% Au, which is more than 2 ounces, 
were produced from the processing of the 13 tons with a calculated head grade 
of 4.89g Au/t.

It is worth mentioning that in most gold deposits in the Abitibi, the 
gravimetric recovery of gold rarely exceeds 60%. In addition, testing at URSTM 
(Unit of Research and Service in Mineral Technology) in Rouyn-Noranda on 
representative samples of the 13-ton bulk, combining gravity and cyanidation, 
gave an aggregated recovery rate of 97.9 %. All of these tests demonstrate 
excellent metallurgical quality of the gold mineralization present on the 
property Villebon which mostly can be treated easily and simply by gravimetry.

Khalkos also recently completed four short diamond drill holes totaling 262 
meters and verifying the lateral extension of just over 50 meters to the NE of 
the Cere zone. All holes intersected an altered shear zone with associated blue 
quartz veins grading from 0.11 g/t Au over 0.5 m. and 0.53 g/t Au over 3.4 m.

Recall that the first two drill holes (VB-14-07 and 08) on this shear 
intersected 17.1 g/t Au over 7.8 m. ; 17.5 g/t Au over 0.5 m. and 1.02 g/t Au 
over 6.1 m. (press release dated July 9, 2014). Only six short drill holes, 
totaling 365 m., have been undertaken so far on Cere zone. Untested geophysical 
anomalies are situated in the extension of this gold-bearing structure 
discovered by the team of Khalkos.

The results of the metallurgical report from Cere zone were prepared and 
validated by URSTM under the supervision of Jean Lelievre. M.Sc. Eng. This 
press release was prepared by Robert Gagnon, Geologist, President of Khalkos, 
Qualified Person under NI 43-101.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Robert Gagnon, President
(819) 825-2303
rgagnon@khalkos.com

or

Christian Guilbaud B.B.A
(514) 813-7862
cguilbaud@videotron.ca
Fax: (514) 510-7964
www.khalkos.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=501725609