Source	Marketwire
Date	10/07/2014
Time	07:46:26 AM

Company	 PROSPERO SILVER CORP.
Title	Prospero Silver Announces Initial San Luis Cordero Resource Estimate





    CDNX Symbol: PSL











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Prospero Silver Corp.

TSX VENTURE SYMBOL: PSL

October 7, 2014

Prospero Silver Announces Initial San Luis Cordero Resource Estimate


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Oct. 7, 2014) - Prospero Silver 
Corp. (TSX VENTURE:PSL) ("Prospero" or the "Company") is pleased to announce 
the initial NI-43-101 compliant resource estimate for the Santa Rosa vein and 
the Santa Rosa East skarn of its San Luis del Cordero property located in 
central Durango, Mexico. A total of 6,127 meters of diamond drill holes were 
incorporated into a database to calculate a resource along a 1,200 meter E-W 
segment of the Skarn Rim Zone (see Figure 1).

Highlights include:

/T/

--  The table below shows the estimated indicated and inferred resources for
both mineralized zones as of October 1st, 2014. Resources were
calculated using Inverse Distance cubed (ID3).
--  Resources are reported at a silver-equivalent cut-off grade of 85 g/t.
Metal prices: silver=$19/oz, copper= $3.00/lb, zinc=$0.90/lb.
--  The known mineralization is open in several directions and the property
has potential for new mineralized zones, which require additional
drilling, such as the Canal and La Puerta targets.

----------------------------------------------------------------------------
Zone       Class       TONNES  AgEq(3)    Ag   Cu   Zn         Ag       AgEq
g/t   g/t    %    %        ozs     Ozs(4)
----------------------------------------------------------------------------
Sta. Rosa  Indicated   31,500   1022.6 827.8 1.21 1.98    838,366  1,035,663
vein
----------------------------------------------------------------------------
Sta. Rosa  Indicated  631,125    200.8  86.1 0.76 1.02  1,747,094  4,075,335
East skarn
----------------------------------------------------------------------------
Total      Indicated  662,625    239.9 121.4 0.78 1.06  2,585,460  5,110,998
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Sta. Rosa  Inferred   218,437    955.4 716.4 1.12 3.62  5,031,291  6,710,075
vein
----------------------------------------------------------------------------
Sta. Rosa  Inferred 2,566,875    214.9  95.7 0.72 1.26  7,897,950 17,734.488
East skarn
----------------------------------------------------------------------------
Total      Inferred 2,785,312    273.0 144.4 0.75 1.45 12,929,241 24,444,562
----------------------------------------------------------------------------
(1) MineralResources are not Mineral Reserves because there are
insufficient studiesto demonstrate economic viability.
(2) Itcannot be assumed that all or any part of an Inferred Resource will
beupgraded to an Indicated or Measured Resource as a result of
continuedexploration.
(3) AgEq= Ag + (Cu% x 22.046 x Cu price x 31.103/Ag price + Zn% x
22.046xZnprice x 31.103/Ag price). Metal prices used in the formula:
silver =US$19/oz, copper = US$3.00/lb, Zn = US$0.90/lb.
(4) AgEq ozs= AgEq grams/31.103

/T/

Figure 2 exhibits the distribution of AgEq grade in the two mineralized zones.

Note: The Sta. Rosa East skarn zone in its western extension overlaps slightly 
the Sta. Rosa vein so the zones are shown separately in Figure 2.

The Company considers the project's immediate potential to add ounces of silver 
will be in the extensions of the known mineralized zones, namely A), west of 
the Santa Rosa vein, B), additional skarn lenses in the HW of the vein, and C) 
the eastern extension of the Sta. Rosa East skarn zone. The 2.5 km stretch of 
the NE striking eastern segment of the Skarn Rim Zone will also be a high 
priority drilling target. Having completed the initial resource, follow up 
programs will include drilling to upgrade and expand the existing Indicated and 
Inferred Resources, and initial metallurgical testwork. The Company also sees 
the need to review overall priorities for the property including focusing 
exploration and development efforts on the high grade vein resource.
Geology

The Sta. Rosa vein intersections vary in width from 2.10 meters to 2.62 meters 
and have an average true width of 1.99 meters with well-defined walls. The Sta. 
Rosa East skarn intersections vary in width from 2.19 meters to 30.59 meters 
with an average true width of 9.0 meters, with grade rather than structure 
generally defining the limits of mineralization.

3D modeling of the Sta. Rosa vein indicates the vein may be steeper than 
anticipated and that historic holes SL-00-2 and SL-00-3 were shut down before 
reaching the vein, suggesting the vein may continue at depth under hole 
SL-00-1. Additionally, holes SL-00-1, SL-00-2 and SL-00-3 intersected several 
mineralized skarn lenses up to 140 meters in the HW of the Sta. Rosa vein. 
These lenses may represent the upper parts of another mineralized skarn at 
greater depth and require deeper drilling to test this possibility.

The Sta. Rosa vein is open to the west and appears to be related to the shallow 
intersection of drill hole SSLC-13-24 (11.08 to 12.10 meters, 1.02 meters with 
115 g/t silver, 0.14% copper, 0.98% zinc), located 450 meters further west, if 
the vein changes to a more westerly strike along its western extension (Figures 
1, 2). The intersection of SSLC-13-24 is slightly below the contact with the 
Aurora limestones, in a position where the Sta. Rosa ore shoot is known to be 
lower grade (Figure 2).

The Sta. Rosa East skarn is open both to the east and at depth. There are 
insufficient holes at depth (PSLC-11-18, PSLC-11-12, SSLC-14-32 and SSLC-13-22) 
to establish clearly the degree of continuity of mineralization along its 
extension at depth. There is a 500 meter gap between holes PSLC-11-18 and 
SSLC-14-32 where a feeder zone could be present which requires additional 
drilling. A hanging wall skarn zone located at the eastern end of the main 
skarn zone has been traced by drill holes. This structure remains open along 
strike and down dip and requires additional drilling to confirm continuity and 
to define its extent.

Subsequent to the last drill program in 2014 and additional mapping, the Skarn 
Rim Zone is shown to envelope the intrusive complex in a "V" shape as shown in 
Figure 1. The initial focus has been on the 1,200 meter stretch between the 
Santa Rosa vein and the Sta. Rosa East skarn. Further attention and drilling 
will focus along the 2500 meter long NE striking eastern shoulder of the 
intrusive complex. This includes, at the northeast end, the La Puerta skarn, 
which outcrops as a continuous 800 meter length and remains unexplored. Hole 
SSLC-13-30 was stopped before reaching the La Puerta skarn indicating it is 
steeper than anticipated, and will require drilling pads closer to the outcrop 
to explore the skarn at depth. To the southwest, hole PSLC-17 was drilled in 
the Canal Target zone, had an intersection which showed elevated zinc values 
(4.14 meters with 96 g/t silver, 0.38% copper and 11.9% zinc), and is open in 
all directions.

"We are very pleased to get this initial resource estimate published. Having 
worked on SLC and neighboring projects for over 10 years we see considerable 
exploration potential in the district" said Tawn Albinson, President and CEO of 
the Company. "We see two types of mineralization, a high grade vein component 
that could potentially support an initial startup operation, as well as a 
higher tonnage lower grade skarn type component that could sustain a longer 
term operation. Our internal mission as a next step, is to expand the existing 
resources by focusing on high priority drill targets."

Tawn Albinson, M.Sc., President of the Company, is a Qualified Person, as 
defined in NI 43-101, and is responsible for the technical content of this 
press release. A quality control program is adopted to ensure best practices in 
the sampling and analysis of drill core. Samples are shipped in sealed bags to 
ALS-Chemex Laboratory preparation facilities in Chihuahua City (ISO 9001). 
Shipments include intermittent standards and blanks. Sample pulps are shipped 
to ALS-Chemex Laboratories in North Vancouver, B.C. for analysis. All samples 
were assayed by multielemental ME-ICP41, and gold by ICP21 (Inductively Induced 
Plasma-Atomic Emission Spectroscopy) which consists of a 30 gram fire assay 
with an ICP-AES finish. Silver, lead, zinc and copper values in excess of 100 
ppm, 1%, 1%, and 1% respectively were repeated with aqua regia digestion and 
with ICP-AES (Code OG46). T. Hodson, P. Geo, an independent qualified person as 
defined by NI 43-101, prepared the 2014 resources contained in this news 
release.

About Prospero Silver Corp.:

Prospero is a Canadian resource company with the majority of its staff based in 
Mexico and who work for its wholly owned subsidiary Minera Fumarola, SA de CV 
(Fumarola). Prospero's objective is to quickly evaluate the properties 
currently owned or optioned for their suitability to provide size potential 
and/or amenability for strategic joint ventures.

To view accompanying figures, visit the following link: 
http://media3.marketwire.com/docs/Propsero_Figures1and2.pdf

Forward-Looking Statement Cautions:

This news release contains certain "forward-looking statements" within the 
meaning of Canadian securities legislation, relating to the closing of a 
non-brokered Private Placement. Although the Company believes that such 
statements are reasonable, it can give no assurance that such expectations will 
prove to be correct. Forward-looking statements are statements that are not 
historical facts; they are generally, but not always, identified by the words 
"expects," "plans," "anticipates," "believes," "intends," "estimates," 
"projects," "aims," "potential," "goal," "objective," "prospective," and 
similar expressions, or that events or conditions "will," "would," "may," 
"can," "could" or "should" occur, or are those statements, which, by their 
nature, refer to future events. Factors that could cause actual results to 
differ materially from these forward looking statements include, but are not 
limited to, variations in the nature, quality and quantity of any mineral 
deposits that may be located, the Company's inability to obtain any necessary 
permits, consents or authorizations required for its planned activities, and 
the Company's inability to raise the necessary capital or to be fully able to 
implement its business strategies. The reader is referred to the Company's 
reports, publicly available through the Canadian Securities Administrators' 
System for Electronic Document Analysis and Retrieval (SEDAR) at www.sedar.com, 
including the risk factors discussed in Prospero's November 27, 2009 
prospectus. Except as required by securities laws and the policies of the TSX 
Venture Exchange, Prospero disclaims any intention or obligation to update or 
revise any forward-looking statement, whether as a result of new information, 
future events or otherwise.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Prospero Silver Corp.
William Murray
Chairman
(604) 288-7813

or

Kirk Gamley
Contact Financial
(604) 561-3642

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=501637603