Source	Marketwire
Date	10/15/2014
Time	06:00:12 AM

Company	 RYE PATCH GOLD CORP.
Title	Rye Patch Drills High-Grade Gold at Wilco





    CDNX Symbol: RPM











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Rye Patch Gold Corp.

TSX VENTURE SYMBOL: RPM
OTCQX SYMBOL: RPMGF
FRANKFURT SYMBOL: 5TN

October 15, 2014

Rye Patch Drills High-Grade Gold at Wilco


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Oct. 15, 2014) - Rye Patch Gold 
Corp. (TSX VENTURE:RPM)(OTCQX:RPMGF)(FRANKFURT:5TN) (the "Company" or "Rye 
Patch") is pleased to announce the results of its 2014 drilling campaign on the 
Wilco project located in Pershing County, Nevada along the Oreana trend in 
west-central Nevada.

HIGHLIGHTS:

/T/

--  Drilling established a high-grade corridor within the Colado resource
area which is open to the north, northwest, and southeast;

--  The continuity of high-grade gold in the Colado deposit extends 1,300
metres in a northwest direction and 500 metres in a northerly
orientation with the two zones coalescing to the south making a
"wishbone" shape;

--  A drillhole in Colado returned 22.9 metres grading 1.52 g/t Au;

--  Drilling in the Gap target established continuity between the Section
Line and the Colado resource areas including a high-grade intercept of
15.2 metres of 1.82 g/t Au; and

--  At the Rhyolite target, drillholes returned 12.2 metres grading 1.76 g/t
Au and 18.3 metres grading 1.41 g/g Au.

/T/

Rye Patch Gold US Inc. completed 13 reverse circulation drillings totaling 
2,103 metres (6,900 feet) in three target zones - Colado, Gap and Rhyolite. The 
drilling campaign returned positive results from the three target areas 
including the recognition of several high-grade gold zones.

At Colado, six drillholes totaling 726.9 metres were completed. Drillhole 
WR-120 was designed to test the intersection zone between a major northwest and 
north-northeast feeder faults that define a "Wishbone" shape to the high-grade 
zone. In drillhole WR-120, gold and silver mineralization start at 70 metres 
and returned 59 metres grading 1.07 g/t gold and 10 g/t silver including 22.9 
metres zone grading 1.52 g/t gold and 12.9 g/t silver. At the north margin of 
the resource area, drillholes WR-117 and WR-121 extended the mineralization for 
an additional 100 metres. Drillhole WR-117 encountered the zone and returned 
1.32 g/t gold over 9.1 metres starting at a depth of 105.2 metres.

The Colado high-grade zone has a "Wishbone" shape with a northwest and 
north-northeast oriented zone that intersect to the south. The northwest arm is 
1,300 metres by 85 metres while the northern arm is 510 metres by 115 metres in 
plan view. The zones are open to the north, northwest, and southeast. 
Additional drilling is being planned.

Table 1 summarizes significant result for RC drill holes WR-117 to WR-121 using 
a 0.3 g/t gold cutoff for intervals greater than 3 metres.

/T/


Table 1: Wilco Project - Colado Target, 2014 Drilling Results (cut off
0.3g/t)
----------------------------------------------------------------------------
Drillhole                   Total
AuEq   interval    From      To   Depth
Drillhole Target   Au g/t  Ag g/t  (1)g/t  (2)metres  metres  metres     (m)
----------------------------------------------------------------------------
WR-117    Colado     0.50     2.0    0.54       10.7    71.6    82.3   157.0
--------------------------------------------------------------------
WR-117    Colado     0.35     1.8    0.39        6.1    89.9    96.0
--------------------------------------------------------------------
WR-117    Colado     1.32     8.8    1.50        9.1   105.2   114.3
--------------------------------------------------------------------
Including        2.76    20.5    3.17        1.5   111.3   112.8
----------------------------------------------------------------------------
WR-118    Colado     0.59     1.4    0.62        7.6     7.6    15.2   147.8
--------------------------------------------------------------------
WR-118    Colado     0.37     1.2    0.39        4.6    54.9    59.4
--------------------------------------------------------------------
WR-118    Colado     0.56     5.3    0.67       41.1    71.6   112.8
--------------------------------------------------------------------
Including        1.17     8.4    1.34        9.1    82.3    91.4
--------------------------------------------------------------------
Including        2.40    17.5    2.75        1.5    89.9    91.4
--------------------------------------------------------------------
WR-118    Colado     0.41    10.2    0.61        9.1   118.9   128.0
----------------------------------------------------------------------------
WR-119    Colado     0.72     6.1    0.84       22.9    35.1    57.9   134.1
--------------------------------------------------------------------
WR-119    Colado     0.57     5.6    0.68        7.6    80.8    88.4
--------------------------------------------------------------------
WR-119    Colado     0.93    15.4    1.24       38.1    93.0   131.1
--------------------------------------------------------------------
Including        2.21     7.5    2.36        3.0   108.2   111.3
----------------------------------------------------------------------------
WR-120    Colado     0.41     1.6    0.44        4.6    24.4    29.0   152.4
--------------------------------------------------------------------
WR-120    Colado     1.07    10.0    1.27       59.4    70.1   129.5
--------------------------------------------------------------------
Including        1.52    12.9    1.78       22.9    93.0   115.8
--------------------------------------------------------------------
Including        3.39     7.8    3.55        3.0   102.1   105.2
----------------------------------------------------------------------------
WR-121    Colado                         NSA                           135.6
----------------------------------------------------------------------------
(1) AuEq is gold equivalent calculated using Ag:Au ratio of 50:1
(2) Drillhole Interval is not true thickness
NSA = No significant results

/T/

The Gap target area is located between the Section Line and Colado resource 
areas, within the two Whittle pits located one kilometre apart. Drill holes 
WR-116 and WR 122 completed at Gap suggest a connection and continuity between 
the two resource areas. Drillhole WR-116 encountered three stratabound mineral 
zones correlative with the upper mineralized zones at Section Line, suggesting 
also the continuity of the main mineralized horizon located at the siltstone 
and claystone geologic contact. The upper and lower zone contains anomalous 
mineralization (0.11 g/t gold over 10.7 metres and 0.2 g/t gold over 12.2 
metres). The middle zone started at 309.4 metres and consists of 4.6 metres 
grading 0.86 g/t gold and 9.3 g/t silver. A new geothermal area was also 
discovered by drillhole WR-116.

Drillhole WR-122 indicated the southwest continuity of the Colado resource into 
the Gap area. WR-122 penetrated an almost continuous zone of anomalous gold 
mineralization (greater than 0.1 g/t gold), and encountered two zones 
containing high-grade gold and silver. The zone started at 103.6 metres and 
returned 1.82 g/t gold and 22.2 g/t silver over 15.2 metres including two three 
metre zones with 2.89 g/t gold and 37.2 g/t silver and 5.06 g/t gold and 35.3 
g/t silver starting at 103.6 metres and 115.8 metres respectively. This 
promising mineralization is open toward southwest and warrants more drilling in 
the Gap target..

Table 2 summarizes significant result for RC drill holes WR-116 and WR-122 
using a 0.3 g/t gold cutoff for intervals greater than 3 metres.

/T/


Table 2: Wilco Project - Gap Target, 2014 Drilling Results (cut off 0.3g/t)
----------------------------------------------------------------------------
Drillhole                   Total
AuEq   interval    From      To   Depth
Drillhole Target   Au g/t  Ag g/t  (1)g/t  (2)metres  metres  metres     (m)
----------------------------------------------------------------------------
WR-116    Gap        0.86     9.3    1.05        4.6   309.4   313.9   361.2
----------------------------------------------------------------------------
WR-122    Gap        0.44    25.9    0.96        4.6    97.5   102.1   144.8
--------------------------------------------------------------------
WR-122    Gap        1.82    22.2    2.26       15.2   103.6   118.9
--------------------------------------------------------------------
Including        2.89    37.2    3.63        3.0   103.6   106.7
--------------------------------------------------------------------
Including        5.06    35.3    5.77        3.0   115.8   118.9
--------------------------------------------------------------------
WR-122    Gap        0.34     8.0    0.50        4.6   123.4   128.0
----------------------------------------------------------------------------
(1) AuEq is gold equivalent calculated using Ag:Au ratio of 50:1
(2) Drillhole Interval is not true thickness
NSA = No significant results

/T/

The Rhyolite Hill target is located north of the historical Willard pit and was 
preliminary tested with six drill holes totaling 1,015 metres. Two of these 
drillholes completed in the EW Draw pit (WR-123 and WR-124), extended gold 46 
metres toward the west. The high-grade is visually oxidised and looks similar 
to gold mineralization encountered at a shallow depth (45 m) under the pit 
floor. Drillhole WR-124 intersected a high-grade zone containing 18.3 metres 
containing 1.41 g/t Au. This mineralization is open toward north and west of 
the pit.

Drillholes WR-112 to WR-115 were designed to intercept the down deep extend of 
an area of strongly silicified and mineralized rhyolite, containing between 
2.1g/t Au and 7.46 g/t Au and 1.1g/t Ag and 31g/t Ag. This surface 
mineralization was initially interpreted as associated with a west dipping 
high-angle feeder fault, located at the western margin of the exposed rhyolite 
dome. None of the drillholes intercepted the rhyolite complex but intersected 
locally anomalous gold, with two intervals ranging between 0.15 g/t Au and 0.31 
g/t Au over 3 metres. Based on the results of this drilling the outcropping 
mineralization was reinterpreted as a low angle east dipping structural zone, 
located at the base of the rhyolite dome complex. A new drilling program will 
be design to test the volcanic dome and attempt to reconcile the 2.1 g/t Au and 
7.46 g/t Au surface anomaly.

Table 3 summarizes significant result for RC drill holes WR-112 to WR-115, 
WR-123 and WR-124 using a 0.3 g/t gold cutoff for intervals greater than 3 
metres.

/T/


Table 3: Wilco Project - Rhyolite Target, 2014 Drilling Results (cut off
0.3g/t)
----------------------------------------------------------------------------
Drillhole                Total
AuEq   interval   From     To  Depth
Drillhole Target      Au g/t  Ag g/t  (1)g/t  (2)metres metres metres    (m)
----------------------------------------------------------------------------
WR-112    Rhyolite                         NSA                         214.9
----------------------------------------------------------------------------
WR-113    Rhyolite                         NSA                         141.7
----------------------------------------------------------------------------
WR-114    Rhyolite                         NSA                         155.4
----------------------------------------------------------------------------
WR-115    Rhyolite                         NSA                         152.4
----------------------------------------------------------------------------
WR-123    Rhyolite      0.81     5.8    0.93        6.1   42.7   48.8   91.4
---------------------------------------------------------------------
WR-123    Rhyolite      1.76     6.2    1.88       12.2   56.4   68.6
----------------------------------------------------------------------------
WR-124    Rhyolite      0.90     8.0    1.06       36.6   77.7  114.3  114.3
---------------------------------------------------------------------
Including               1.41     7.3    1.56       18.3   86.9  105.2
----------------------------------------------------------------------------
(1) AuEq is gold equivalent calculated using Ag:Au ratio of 50:1
(2) Drillhole Interval is not true thickness
NSA = No significant results

/T/

"The Company is excited and pleased with the results of the Wilco drill 
program. The discovery of high-grade zones in the three target areas selected 
for drilling shows the property has additional upside potential and can 
continue to add value for our shareholders. The Company plans to follow up on 
these tremendous assay results and permitting is underway," stated Mr. William 
C. (Bill) Howald, President and CEO of the Company.

Rye Patch Gold US Inc. maintains a strict quality control program at all of its 
projects. All reverse circulation drill samples are submitted to American Assay 
with prep-blanks, assay blanks, and gold and silver standards. Rye Patch Gold 
inserts approximately one quality control or quality assurance samples for 
every ten samples submitted to the assay laboratory. The reverse circulation 
character samples are logged and photographed on site. American Assay collects 
the samples and transports them to their preparation and analytical facility 
located in Reno, Nevada. Gold analyses are conducted on 1-assay ton prepped 
samples with gold determined using industry standard fire assay methods with an 
ICP finish. Gold values above 10 g/t gold (over limits) are confirmed using 
fire assay with a gravimetric finish. Silver is analyzed using a two-acid 
digestion and an ICP finish. Silver values are re-analyzed with a four-acid 
digestion and ICP finish on all samples with gold values greater than a 0.2 g/t 
gold assay result. Silver values over 100 g/t silver are re-analyzed using 
volumetric dissolution.
Mr. William Howald, AIPG Certified Professional Geologist #11041, Rye Patch 
Gold's CEO and President, is a Qualified Person as defined under National 
Instrument 43-101. He has reviewed and approved the contents of this news 
release.

About Rye Patch Gold Corp.

Rye Patch Gold Corp. is a Tier 1, well-funded junior mining company with a 
royalty revenue stream from the operating Rochester silver mine and significant 
gold and silver resources, all located in the mining friendly state of Nevada, 
USA. The Company's seasoned management team is engaged in the acquisition, 
exploration, and development of quality resource-based gold and silver 
projects. Rye Patch Gold US Inc. controls over 75 square kilometres (30 sq. 
miles) of land, and has a 3.4 % Net Smelter Return (NSR) royalty from the 
Rochester silver mine along the Oreana trend located in west-central Nevada. 
The Company is aggressively developing gold and silver resources along this 
emerging trend, utilizing existing funds and cash flow from the NSR royalty, 
which is fully leveraged to the price of gold and silver. In east central 
Nevada, Rye Patch Gold US Inc. is exploring 66 square kilometres of exploration 
land along the prolific Cortez trend contiguous to Barrick's new Goldrush 
deposit. The Company has established gold and silver resource milestones and 
time frames in order to build a premier resource development company. For more 
information about the Company, please visit our website at www.ryepatchgold.com.

On behalf of the Board of Directors

William C. (Bill) Howald, CEO & President

This news release contains forward-looking statements, which address future 
events and conditions, which are subject to various risks and uncertainties. 
The Company's actual results, programs and financial position could differ 
materially from those anticipated in such forward-looking statements as a 
result of numerous factors, some of which may be beyond the Company's control. 
These factors include: the availability of funds; the financial position of Rye 
Patch; the timing and content of work programs; the results of exploration 
activities and development of mineral properties; the interpretation of 
drilling results and other geological data; the reliability of calculation of 
mineral resources (and, in respect of the Coeur Rochester mine 3.4% NSR, the 
reliability of calculation of Coeur's mineral resources and reserves); the 
reliability of calculation of precious metal recoveries; the receipt and 
security of mineral property titles; project cost overruns or unanticipated 
costs and expenses; fluctuations in metal prices; currency fluctuations; and 
general market and industry conditions.

Forward-looking statements are based on the expectations and opinions of the 
Company's management on the date the statements are made. The assumptions used 
in the preparation of such statements, although considered reasonable at the 
time of preparation, may prove to be imprecise and, as such, undue reliance 
should not be placed on forward-looking statements.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Rye Patch Gold Corp.
(604) 638-1588
Fax: (604) 638-1589
info@ryepatchgold.com
www.ryepatchgold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=502703154