Source	MARKET NEWS
Date	10/16/2014
Time	05:10:49 AM

Company	 Aben Resources Ltd.
Title	High Grade 
Tungsten Results At Justin Gold tungs





    CDNX Symbol: ABN











Press Release	





ABEN RESOURCES LTD ("ABN-V;ABNAD-0")
NORTH AMERICAN TUNGSTEN CORP LTD ("NTC-V;NATUF-0")
- High Grade Tungsten Results At Justin Gold-tungsten Project,
- Southeast Yukon

Aben Resources Ltd. is pleased to announce the re-assay results of
previous drill holes for Tungsten (W) at its 100% owned 18,314 acre
Justin gold-tungsten project. The project area is located in southeast
Yukon within the Tintina Gold Belt approximately 35 kilometers
southwest of the Cantung Mine and is accessed by an all-season road.

Justin gold-tungsten project location map:
http://www.abenresources.com/i/maps/ABN-Justin.jpg

Highlights:

//st

A total of 230 samples from 7 of 9 previously drilled POW zone holes, were
selected for tungsten specific analysis to provide a preliminary assessment
of the potential for economic tungsten mineralization.

Results from JN12016 returned 8.50 metres grading 0.39% WO(sub)3(/sub)
including 1.00 metre of 1.12% WO(sub)3(/sub)

Previous gold results from JN12016 returned 5.60 metres grading 4.12 grams
per tonne Au including 2.60 metres grading 8.20 grams per tonne Au

Results from JN12013 returned 28.90 metres grading 0.10% WO(sub)3(/sub)
beginning at surface, and 1.10 metres grading 1.15% WO(sub)3(/sub)

Previous gold results from JN12013 returned 7.40 metres grading 1.81 grams
per tonne Au including 2.20 metres grading 4.42 grams per tonne Au

Several high-priority exploration targets, defined by geophysics and
geochemistry exist within 2 km of known mineralization and remain
underexplored and untested by drilling. These areas offer significant
potential for expanding the current extent of mineralization and making
additional gold and tungsten discoveries.

//et

Summary of Exploration Activities:

The goal of the 2014 tungsten reconnaissance sampling was to make
a preliminary assessment of the property for economic W (tungsten)
mineralization and resample core, previously drilled, for W specific
analysis.

Justin Project 2014 trench location map:
http://www.abenresources.com/i/maps/ABN-Justin-2014-Trench-Locations-map.jp
g

Examination of drill core using short wave ultraviolet lamps in
2012 revealed visible scheelite (calcium tungstate) mineralization
disseminated within the POW Zone skarn and sheeted vein arrays. Review
of the 2011 - 2012 drill hole geochemical dataset indicated that
anomalous concentrations of tungsten () 200 ppm W) were reported in the
multi-element ICP analysis from several intervals within the POW zone
skarn. It is important to note that although multi-element ICP analysis
can indicate tungsten anomalies, it is not considered appropriate
quantitative analyses for the commodity since it can grossly
under-report actual quantities. The ICP W data, combined with the
Justin project being situated 35 km southwest of North American
Tungsten Corporation's world-class Cantung tungsten mine, helped the
Company recognize the importance of evaluating the project to determine
if significant quantities of tungsten could be identified.

Table 1:

//st
2014 WO3Analysis
DDH ID          From (m)     To (m)     Uncut Sample Results WO3%
JN11010           194.00     206.00       0.25 % WO3 over 12.00 m
including         195.00     200.00        0.45 % WO3 over 5.00 m
also including    196.00     200.00        0.48 % WO3 over 4.00 m
also including    197.00     200.00        0.53 % WO3 over 3.00 m
JN12013             4.10      33.00       0.10 % WO3 over 28.90 m
including          23.80      33.00        0.14 % WO3 over 9.20 m
&                  45.80      46.90         1.15% WO3 over 1.10 m
&                  88.70      90.80        0.46 % WO3 over 2.10 m
including          88.70      89.70        0.87 % WO3 over 1.00 m
JN12016           104.70     113.20        0.39 % WO3 over 8.50 m
including         104.70     107.30        0.62 % WO3 over 2.60 m
also including    106.30     107.30        1.12 % WO3 over 1.00 m
&                 110.10     113.20        0.50 % WO3 over 3.10 m
including         111.20     113.20        0.72 % WO3 over 2.00 m
also including    111.20     112.60        0.88 % WO3 over 1.40 m
JN12019           192.50     199.70        0.27 % WO3 over 7.20 m
including         194.20     199.70        0.32 % WO3 over 5.50 m
also including    197.80     199.40        0.52 % WO3 over 1.60 m
also including    197.80     198.30        1.18 % WO3 over 0.50 m
also including    199.40     199.70        1.27 % WO3 over 0.30 m
//et

Jim Pettit, President of Aben, stated: "We are very pleased with
these early stage results which suggest that there is strong potential
for delineating significant zones of both tungsten and gold
mineralization at the Justin property. The main goal of the 2011 & 2012
drilling was to focus on defining gold mineralization, which
subsequently discovered both gold and tungsten mineralization. This
serendipitous discovery of high grade tungsten mineralization adds a
new dimension to the project given its close proximity to the producing
Cantung Mine just up the Nahanni Range Road. With these new tungsten
results we now have a better understanding of the mineralized system
and can more efficiently explore for both gold and tungsten."

Cantung Tungsten-Copper Mine:

North American Tungsten Corporation Ltd., operator of the Cantung
tungsten-copper mine, recently released news (September 19, 2014)
indicating that Mineral Reserves at the deposit have increased
extending the mine life until at least 2017. The new Probable Mineral
Reserves are reported in the news release with a grand total of 1.81
million tons grading 0.81% WO(sub)3(/sub). Kurt Heikkila, Chariman and
CEO of North American Tungsten Corporation summarized the September 19,
2014 NR with the following statement: "Cantung will continue to be an
important source of tungsten for the world for years to come."

Management cautions that past results or discoveries on proximate
land are not necessarily indicative of the results that may be achieved
on the Justin property.

Qualified Person and Quality Assurance:

Michael (Mike) McCuaig, P.Geo., Justin Project geologist and a
Qualified Person as defined by National Instrument 43-101, has reviewed
and approved the technical information in this release.

All samples were submitted to ALS Minerals in Whitehorse for
preparation. Geochemical analysis was completed at ALS Minerals
Laboratory in Vancouver. The following analytical techniques were used
for all drill core samples: W-XRF05 for all samples ) 200 ppm W in the
ME-ICP41 analysis and W-XRF10 for all samples ) 5000 ppm W in the
W-XRF05 analysis. QAQC measures included insertion of external blanks
and standards into the sample stream for all rock chip/channel samples.
A minimum of one standard sample and one blank sample were inserted
into the sample stream every 20th sample.

All reported intersections were determined using uncut
WO(sub)3(/sub) % weighted average calculations. WO(sub)3(/sub) % values
were calculated using a conversion factor of 1.2611 ((W ppm/10,000) *
1.2611 = WO(sub)3(/sub) %). BC Energy & Mines. The company has not
determined the economic cut-off grade for WO(sub)3(/sub) mineralization
or the true thicknesses of drill hole intersections.

About Aben Resources:
Aben Resources Ltd. is a Canadian gold-silver-tungsten and uranium
exploration company with projects in the Yukon, NWT and Saskatchewan's
Athabasca Basin.

For further information on Aben Resources Ltd. (TSX VENTURE:ABN),
visit our Company's web site at www.abenresources.com.

ON BEHALF OF THE BOARD OF DIRECTORS

JAMES G. PETTIT, President

Neither TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This release includes certain statements that may be deemed to be
"forward-looking statements". All statements in this release, other
than statements of historical facts, that address events or
developments that management of the Company expects, are
forward-looking statements. Although management believes the
expectations expressed in such forward-looking statements are based on
reasonable assumptions, such statements are not guarantees of future
performance, and actual results or developments may differ materially
from those in the forward-looking statements. The Company undertakes no
obligation to update these forward-looking statements if management's
beliefs, estimates or opinions, or other factors, should change.
Factors that could cause actual results to differ materially from those
in forward-looking statements, include market prices, exploration and
development successes, continued availability of capital and financing,
and general economic, market or business conditions. Please see the
public filings of the Company at www.sedar.com for further information.




















TSX Venture closing price for ABN-V
Date: 2014/10/15
Closing Price: 0.05

TEL: 800-567-8181
FAX: 604-687-3119        Jim Pettit, President
info@abenresources.com   Don Myers, Corporate Communications
www.abenresources.com    Aben Resources Ltd.
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1428800006TS11428800502-05083820141016