Source	Marketwire
Date	10/16/2014
Time	04:00:20 AM

Company	 ABEN RESOURCES LTD.
Title	Aben Resources Reports High Grade Tungsten Results at Justin Gold-Tungsten 
Project, Southeast Yukon





    CDNX Symbol: ABN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Aben Resources Ltd.

TSX VENTURE SYMBOL: ABN
PINKSHEETS SYMBOL: ABNAF
FRANKFURT SYMBOL: E2L

October 16, 2014

Aben Resources Reports High Grade Tungsten Results at Justin Gold-Tungsten 
Project, Southeast Yukon


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Oct. 16, 2014) - Aben Resources 
Ltd. (TSX VENTURE:ABN)(PINKSHEETS:ABNAF)(FRANKFURT:E2L) is pleased to announce 
the re-assay results of previous drill holes for Tungsten (W) at its 100% owned 
18,314 acre Justin gold-tungsten project. The project area is located in 
southeast Yukon within the Tintina Gold Belt approximately 35 kilometers 
southwest of the Cantung Mine and is accessed by an all-season road.

Justin gold-tungsten project location map: 
http://www.abenresources.com/i/maps/ABN-Justin.jpg

Highlights:

/T/

--  A total of 230 samples from 7 of 9 previously drilled POW zone holes,
were selected for tungsten specific analysis to provide a preliminary
assessment of the potential for economic tungsten mineralization.
--  Results from JN12016 returned 8.50 metres grading 0.39% WO3 including
1.00 metre of 1.12% WO3
--  Previous gold results from JN12016 returned 5.60 metres grading 4.12
grams per tonne Au including 2.60 metres grading 8.20 grams per tonne Au
--  Results from JN12013 returned 28.90 metres grading 0.10% WO3 beginning
at surface, and 1.10 metres grading 1.15% WO3
--  Previous gold results from JN12013 returned 7.40 metres grading 1.81
grams per tonne Au including 2.20 metres grading 4.42 grams per tonne Au
--  Several high-priority exploration targets, defined by geophysics and
geochemistry exist within 2 km of known mineralization and remain
underexplored and untested by drilling. These areas offer significant
potential for expanding the current extent of mineralization and making
additional gold and tungsten discoveries.

/T/

Summary of Exploration Activities:

The goal of the 2014 tungsten reconnaissance sampling was to make a preliminary 
assessment of the property for economic W (tungsten) mineralization and 
resample core, previously drilled, for W specific analysis.

Justin Project 2014 trench location map: 
http://www.abenresources.com/i/maps/ABN-Justin-2014-Trench-Locations-map.jpg

Examination of drill core using short wave ultraviolet lamps in 2012 revealed 
visible scheelite (calcium tungstate) mineralization disseminated within the 
POW Zone skarn and sheeted vein arrays. Review of the 2011 - 2012 drill hole 
geochemical dataset indicated that anomalous concentrations of tungsten 
(greater than 200 ppm W) were reported in the multi-element ICP analysis from 
several intervals within the POW zone skarn. It is important to note that 
although multi-element ICP analysis can indicate tungsten anomalies, it is not 
considered appropriate quantitative analyses for the commodity since it can 
grossly under-report actual quantities. The ICP W data, combined with the 
Justin project being situated 35 km southwest of North American Tungsten 
Corporation's world-class Cantung tungsten mine, helped the Company recognize 
the importance of evaluating the project to determine if significant quantities 
of tungsten could be identified.

Table 1:

/T/

----------------------------------------------------------------------------
----------------------------------------------------------------------------
2014 WO3Analysis
----------------------------------------------------------------------------
----------------------------------------------------------------------------
DDH ID                From (m)    To (m)           Uncut Sample Results WO3%
----------------------------------------------------------------------------
----------------------------------------------------------------------------
JN11010                 194.00    206.00             0.25 % WO3 over 12.00 m
----------------------------------------------------------------------------
including               195.00    200.00              0.45 % WO3 over 5.00 m
----------------------------------------------------------------------------
also including          196.00    200.00              0.48 % WO3 over 4.00 m
----------------------------------------------------------------------------
also including          197.00    200.00              0.53 % WO3 over 3.00 m
----------------------------------------------------------------------------
----------------------------------------------------------------------------
JN12013                   4.10     33.00             0.10 % WO3 over 28.90 m
----------------------------------------------------------------------------
including                23.80     33.00              0.14 % WO3 over 9.20 m
----------------------------------------------------------------------------
and                      45.80     46.90               1.15% WO3 over 1.10 m
----------------------------------------------------------------------------
and                      88.70     90.80              0.46 % WO3 over 2.10 m
----------------------------------------------------------------------------
including                88.70     89.70              0.87 % WO3 over 1.00 m
----------------------------------------------------------------------------
----------------------------------------------------------------------------
JN12016                 104.70    113.20              0.39 % WO3 over 8.50 m
----------------------------------------------------------------------------
including               104.70    107.30              0.62 % WO3 over 2.60 m
----------------------------------------------------------------------------
also including          106.30    107.30              1.12 % WO3 over 1.00 m
----------------------------------------------------------------------------
and                     110.10    113.20              0.50 % WO3 over 3.10 m
----------------------------------------------------------------------------
including               111.20    113.20              0.72 % WO3 over 2.00 m
----------------------------------------------------------------------------
also including          111.20    112.60              0.88 % WO3 over 1.40 m
----------------------------------------------------------------------------
----------------------------------------------------------------------------
JN12019                 192.50    199.70              0.27 % WO3 over 7.20 m
----------------------------------------------------------------------------
including               194.20    199.70              0.32 % WO3 over 5.50 m
----------------------------------------------------------------------------
also including          197.80    199.40              0.52 % WO3 over 1.60 m
----------------------------------------------------------------------------
also including          197.80    198.30              1.18 % WO3 over 0.50 m
----------------------------------------------------------------------------
also including          199.40    199.70              1.27 % WO3 over 0.30 m
----------------------------------------------------------------------------
----------------------------------------------------------------------------

/T/

Jim Pettit, President of Aben, stated: "We are very pleased with these early 
stage results which suggest that there is strong potential for delineating 
significant zones of both tungsten and gold mineralization at the Justin 
property. The main goal of the 2011 & 2012 drilling was to focus on defining 
gold mineralization, which subsequently discovered both gold and tungsten 
mineralization. This serendipitous discovery of high grade tungsten 
mineralization adds a new dimension to the project given its close proximity to 
the producing Cantung Mine just up the Nahanni Range Road. With these new 
tungsten results we now have a better understanding of the mineralized system 
and can more efficiently explore for both gold and tungsten."

Cantung Tungsten-Copper Mine:

North American Tungsten Corporation Ltd., operator of the Cantung 
tungsten-copper mine, recently released news (September 19, 2014) indicating 
that Mineral Reserves at the deposit have increased extending the mine life 
until at least 2017. The new Probable Mineral Reserves are reported in the news 
release with a grand total of 1.81 million tons grading 0.81% WO3. Kurt 
Heikkila, Chariman and CEO of North American Tungsten Corporation summarized 
the September 19, 2014 NR with the following statement: "Cantung will continue 
to be an important source of tungsten for the world for years to come."

Management cautions that past results or discoveries on proximate land are not 
necessarily indicative of the results that may be achieved on the Justin 
property.

Qualified Person and Quality Assurance:

Michael (Mike) McCuaig, P.Geo., Justin Project geologist and a Qualified Person 
as defined by National Instrument 43-101, has reviewed and approved the 
technical information in this release.

All samples were submitted to ALS Minerals in Whitehorse for preparation. 
Geochemical analysis was completed at ALS Minerals Laboratory in Vancouver. The 
following analytical techniques were used for all drill core samples: W-XRF05 
for all samples greater than 200 ppm W in the ME-ICP41 analysis and W-XRF10 for 
all samples greater than 5000 ppm W in the W-XRF05 analysis. QAQC measures 
included insertion of external blanks and standards into the sample stream for 
all rock chip/channel samples. A minimum of one standard sample and one blank 
sample were inserted into the sample stream every 20th sample.

All reported intersections were determined using uncut WO3 % weighted average 
calculations. WO3 % values were calculated using a conversion factor of 1.2611 
((W ppm/10,000) (i) 1.2611 = WO3 %). BC Energy & Mines. The company has not 
determined the economic cut-off grade for WO3 mineralization or the true 
thicknesses of drill hole intersections.

About Aben Resources:

Aben Resources Ltd. is a Canadian gold-silver-tungsten and uranium exploration 
company with projects in the Yukon, NWT and Saskatchewan's Athabasca Basin.

For further information on Aben Resources Ltd. (TSX VENTURE:ABN), visit our 
Company's web site at www.abenresources.com.

ON BEHALF OF THE BOARD OF DIRECTORS

JAMES G. PETTIT, President

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

This release includes certain statements that may be deemed to be 
"forward-looking statements". All statements in this release, other than 
statements of historical facts, that address events or developments that 
management of the Company expects, are forward-looking statements. Although 
management believes the expectations expressed in such forward-looking 
statements are based on reasonable assumptions, such statements are not 
guarantees of future performance, and actual results or developments may differ 
materially from those in the forward-looking statements. The Company undertakes 
no obligation to update these forward-looking statements if management's 
beliefs, estimates or opinions, or other factors, should change. Factors that 
could cause actual results to differ materially from those in forward-looking 
statements, include market prices, exploration and development successes, 
continued availability of capital and financing, and general economic, market 
or business conditions. Please see the public filings of the Company at 
www.sedar.com for further information.

- 30 -

CONTACT INFO:

Aben Resources Ltd.
Jim Pettit
President
604-687-3376 or Toll Free: 800-567-8181
Fax: 604-687-3119

or

Aben Resources Ltd.
Don Myers
Corporate Communications
604-687-3376 / Toll Free: 800-567-8181
Fax: 604-687-3119
info@abenresources.com
www.abenresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=503000068