Source	MARKET NEWS
Date	10/20/2014
Time	04:03:06 AM

Company	 Endurance Gold Corporation
Title	Exploration 
Update On Pardo Jv; Samples 3.4 G/t





    CDNX Symbol: EDG











Press Release	





GINGURO EXPLORATION INC ("GEG-V")
ENDURANCE GOLD CORP ("EDG-V")
- Exploration Update On Pardo Jv; Samples 3.4 G/t Gold Over
- 25 Metres On Godzilla Zone

Ginguro Exploration Inc. ("Ginguro" or the "Company") released
assay results from the Godzilla Zone on the Pardo Joint Venture ("JV")
property, which is located approximately 65 km north-east of Sudbury,
Ontario.

Assays have now been received for six additional channel samples
taken at the recently discovered Godzilla Zone which previously
returned an average of 5.2 grams per tonne (g/t) gold over 140 metres
from Channel 14-34 (see press release dated Sept 2, 2014),. Channel
14-37, which was cut perpendicular to Channel 14-34, averaged 3.4 g/t
gold over 25 metres. Channels 14-38, 14-40 and 14-41, which were
shorter channels cut approximately 35 metres east of Channel 14-35 in
an overlying conglomerate, averaged 0.1g/t gold over 4 metres, 0.7 g/t
gold over 4 metres, and 0.7 g/t gold over 3 metres, respectively.
Channel 14-39 was cut perpendicular to Channel 14-34 and averaged 0.7
g/t over 13.5 metres and Channel 14-42, which was cut sub parallel to
Channel 14-34, averaged 0.7 g/t gold over 8 metres.

A total of 527 metres of channel sample were cut across the
Godzilla Zone. Assay results for 236.5 metres of channel samples remain
outstanding and are expected in the next few weeks. The exposed outcrop
area that contains the Godzilla Zone mineralization measures 175 metres
north-south by up to 125 metres east-west. The gold-bearing
conglomerate sampled at the Godzilla Zone appears to have an average
true thickness of approximately 4 metres.

Maps illustrating the geology and channel sample locations can be
found on the Company's website at www.ginguro.com.

Field crews are continuing the work of exploring new target areas
of the Pardo JV. The prospecting and geological work will continue
throughout the fall as long as weather permits.

The known gold mineralization within the near surface basal
conglomerate at Pardo now extends approximately 3 kilometres
north-south by approximately 1.1 kilometres east-west.

Due to the near flat lying nature of the sedimentary strata, it is
not always possible to cut samples across the gold-bearing strata.
Samples are usually collected either parallel or perpendicular to the
interpreted paleochannel direction. Therefore, the channel lengths
reported in this release represent the gold distribution over the
surface area sampled and do not represent true thicknesses of the
mineralized unit.

Ginguro is the operator of the Pardo JV and holds a 64.5%
ownership interest and Endurance Gold Corporation ("Endurance") owns a
35.5% ownership interest. Both Ginguro and Endurance are funding the
2014 program on a pro rata basis, based on ownership. As a result, it
is anticipated that Ginguro's ownership interest in the Pardo JV will
be unchanged at the completion of the current program.

About Ginguro
Ginguro Exploration Inc. is a mineral exploration company focused
on the advancement of its Pardo paleo-placer gold property, located in
Pardo Township in northern Ontario. To learn more about Ginguro
Exploration Inc., please visit: www.ginguro.com.

The Qualified Person responsible for the geological technical
content of this news release is Richard Murphy, P.Geo, President and
CEO of Ginguro Exploration Inc. Potential quantity and grade is
conceptual in nature. There has been insufficient exploration to define
a mineral resource on the Pardo property to date, and it is uncertain
if further exploration will result in the target being delineated as a
mineral resource. Samples are transported in security sealed bags for
preparation at AGAT Prep Lab located in Sudbury, Ontario. Prepped
samples are shipped for analysis to the AGAT Assay Laboratory in
Mississauga, Ontario. AGAT Laboratories Ltd. is an ISO 17025 registered
laboratory. The six channel samples summarized in this release and
channel 14-34 north reported earlier were assayed using a modified pulp
metallic assay procedure. The entire sample was crushed and pulverized
to 85% passing 100 mesh. The +100 mesh material was fluxed and assayed
in its entirety, while two 50 g aliquots of the -100 mesh undersize
pulp were cut out and fire assayed. Results were reported as a weighted
average of gold in the three fractions. Earlier reported samples for
channels 14-34 south, 14-35 and 14-36 were crushed in their entirety,
with a 1kg split then pulverized. Two 50 g aliquots of the pulp were
cut out and fire assayed. Results were reported as a weighted average
of gold in the fractions. In instances where the averages exceed 10
g/t, the sample is re-run with a gravimetric finish and the gravimetric
result is reported. For both techniques, the Company inserts a
certified reference standard or an analytical blank in every batch of
20 samples. Validation parametres are established in the database to
ensure quality control.

Statements in this release that are forward-looking statements are
subject to various risks and uncertainties concerning the specific
factors disclosed under the heading "Risk Factors" in the Corporation's
filings with Canadian securities regulators. Such information contained
herein represents management's best judgment as of the date hereof
based on information currently available. The Corporation does not
assume any obligation to update any forward-looking statements, save
and except as may be required by applicable securities laws.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

TSX Venture closing price for EDG-V
Date: 2014/10/16
Closing Price: 0.06

TEL: (705) 222-8800   Richard Murphy
info@ginguro.com      President and CEO
www.ginguro.com       Ginguro Exploration Inc.
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1429200002TS11429200302-04013720141020