Source	Marketwire
Date	10/20/2014
Time	05:09:02 AM

Company	 TROYMET EXPLORATION CORP.
Title	Troymet Reports Significant Skarn Zone Prospecting Results





    CDNX Symbol: TYE











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Troymet Exploration Corp.

TSX VENTURE SYMBOL: TYE

October 20, 2014

Troymet Reports Significant Skarn Zone Prospecting Results


CALGARY, ALBERTA--(Marketwired - Oct. 20, 2014) - Troymet Exploration Corp. 
(TSX VENTURE:TYE) ("Troymet" or the "Company") reports the results of a 
reconnaissance prospecting program conducted on the southern extension of the 
Skarn zone, on the Company's 100% owned Golden Eagle project in northern 
British Columbia. Prospecting has identified elevated to anomalous gold, 
silver, arsenic, bismuth, copper, mercury, antimony and tellurium values within 
an area of approximately 1,300 m x 900 m along the Paddy Fault system (map 
links provided below). The fault system, which controls the Skarn zone 
mineralization, is a major structural feature up to 500 m wide that has been 
traced for over 17 km.

The highest gold, bismuth and tellurium values are located in the head waters 
of creeks with anomalous gold-in-silts that drain eastwards. Elevated to 
anomalous silver, antimony and mercury values are also present. The geology 
comprises felsic intrusive (Cretaceous?) and Upper Triassic (Stuhini Group) 
mafic to intermediate volcanics. Mineralized samples exhibit bleaching, 
actinolite alteration, sulphidation, quartz and ankerite veining similar to the 
Skarn zone.

Copper, mercury (and silver) values are elevated to anomalous along the ridge 
that tracks the Paddy Fault south of the Skarn zone. Mineralized samples 
comprise quartz veins, quartz-ankerite veins, quartz-carbonate alteration, 
bleaching, actinolite alteration and sulphidization. The Paddy Fault marks the 
contact between mafic-intermediate-felsic volcanics (Stuhini Group) and 
sediments (Boundary Range Metamorphics).

Copper, arsenic, and mercury values are elevated to anomalous to the west, 
along with bismuth, antimony, silver and gold. Mineralized samples comprise 
quartz veins, quartz-ankerite veins, quart-carbonate alteration, bleaching and 
sulphidization.

Historic drilling in 1990 and 1997 was limited to an area 265 m long and 
intersections ranged from 2.12 g/t Au over 9.9 m to 7.64 g/t Au over 3.5m 
(further details are provided in a technical report available at: 
www.troymet.com/i/pdf/GE_TechRpt_Jul-12.pdf). Only visually obvious 
mineralization was assayed and no drill core exists today from this drilling. 
In 2011, Troymet drilled one hole (N11-06) to test the northern limit of the 
area of historic drilling. The hole collared in mineralization and intersected 
36.45 m grading 1.27 g/t gold (mineralization open; see cross-section link 
below). The upper portion of the gold intersection is also anomalous in silver, 
grading 4.05 g/t silver over 15.45 m. This intersection demonstrated the 
potential for high-grade, sub-cropping, bulk tonnage gold mineralization that 
was not recognized in the past.

The current prospecting results confirm the Skarn zone mineralization extends a 
significant distance to the south towards the Catfish zone, where gold-silver 
bearing veins occur in the head waters of creeks carrying anomalous 
gold-in-silt values. The Catfish zone is approx. 2.5 km south of the Skarn 
zone. This is a highly prospective area with a high discovery potential.

/T/

Map Links:
Gold: www.troymet.com/i/maps/GE_Au_Skarn.jpg
Silver: www.troymet.com/i/maps/GE_Ag_Skarn.jpg
Arsenic: www.troymet.com/i/maps/GE_As_Skarn.jpg
Bismuth: www.troymet.com/i/maps/GE_Bi_Skarn.jpg
Copper: www.troymet.com/i/maps/GE_Cu_Skarn.jpg
Mercury: www.troymet.com/i/maps/GE_Hg_Skarn.jpg
Antimony: www.troymet.com/i/maps/GE_Sb_Skarn.jpg
Tellurium: www.troymet.com/i/maps/GE_Te_Skarn.jpg
N11-06 cross-section: www.troymet.com/i/maps/GE_Section_N11-06.jpg

/T/

Casselman Geological Services Ltd. provided technical management of the field 
program for the Company. Rock samples were analyzed at ALS Chemex Labs Ltd. in 
Vancouver, BC, an ISO 9001:2000 accredited laboratory.

Kieran Downes, P. Geo., a Qualified Person as defined by National Instrument 
43-101, has reviewed and verified the technical information provided in this 
release.

TROYMET EXPLORATION CORP.

Kieran Downes, Ph.D., P.Geo., President, CEO & Director

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

This news release may contain certain forward-looking information. All 
statements included herein, other than statements of historical fact, are 
forward-looking information and such information involves various risks and 
uncertainties. In particular, this press release contains forward-looking 
information in respect of the shareholder approval of the Advance Notice 
By-law. There can be no assurance that such information will prove to be 
accurate, and actual results and future events could differ materially from 
those anticipated in such information. This forward-looking information 
reflects Troymet's current beliefs and is based on information currently 
available to Troymet and on assumptions Troymet believes are reasonable. These 
assumptions include, but are not limited to, the continued market acceptance of 
advance notice by-laws. Forward-looking information is subject to known and 
unknown risks, uncertainties and other factors that may cause the actual 
results, level of activity, performance or achievements of Troymet to be 
materially different from those expressed or implied by such forward-looking 
information. Such risks and other factors may include, but are not limited to: 
the early stage development of Troymet and its projects; general business, 
economic, competitive, political and social uncertainties; capital market 
conditions and market prices for securities, junior market securities and 
mining exploration company securities; commodity prices; the actual results of 
current exploration and development or operational activities; competition; 
changes in project parameters as plans continue to be refined; accidents and 
other risks inherent in the mining industry; lack of insurance; delay or 
failure to receive board or regulatory approvals; changes in legislation, 
including environmental legislation, affecting Troymet; timing and availability 
of external financing on acceptable terms; conclusions of economic evaluations; 
and lack of qualified, skilled labour or loss of key individuals. A description 
of other assumptions used to develop such forward-looking information and a 
description of other risk factors that may cause actual results to differ 
materially from forward-looking information can be found in Troymet's 
disclosure documents on the SEDAR website at www.sedar.com. Troymet does not 
undertake to update any forward-looking information except in accordance with 
applicable securities laws.

- 30 -

CONTACT INFO:

Troymet Exploration Corp.
Anthony Zelen
Investor Relations
1-888-456-4952 or  M. 1-778-388-5258
anthony@senergyir.com
www.troymet.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=503471618