Source	Marketwire
Date	10/22/2014
Time	05:45:05 AM

Company	 ROCKHAVEN RESOURCES LTD.
Title	Rockhaven Announces Exceptional Results from Deep Step-Out Drill Hole at 
Western BRX Zone - 16.29 g/t Gold and 1,435 g/t Silver (44.99 g/t Gold EQ) over 
1.37 m





    CDNX Symbol: RK











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Rockhaven Resources Ltd.

TSX VENTURE SYMBOL: RK

October 22, 2014

Rockhaven Announces Exceptional Results from Deep Step-Out Drill Hole at 
Western BRX Zone - 16.29 g/t Gold and 1,435 g/t Silver (44.99 g/t Gold EQ) over 
1.37 m


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Oct. 22, 2014) - Rockhaven 
Resources Ltd. (TSX VENTURE:RK) ("Rockhaven") is pleased to announce results 
from the final drill hole that tested the Western BRX Zone at its 100%-owned 
and road-accessible Klaza property, located in the Dawson Range Gold Belt of 
southern Yukon. Drilling in the Western BRX Zone has returned numerous 
high-grade gold and silver intercepts during the 2014 exploration season (see 
July 15th, July 22nd, July 29th and October 6th 2014 news releases). The final 
hole intersected high-grade precious and base metal mineralization 500 m 
down-dip from surface, further supporting the Carbonate Base Metal (CBM) Gold 
classification that has been proposed as the deposit model at the Klaza 
property.

News Release Highlights:

/T/

--  KL-14-238 returned 16.29 g/t gold, 1,435 g/t silver, 5.57% lead and
6.23% zinc over 1.37 m within an 18.5 m wide mineralized complex;
--  This is the deepest intercept obtained to date and clearly demonstrates
depth potential at Western BRX and other zones on the property; and,
--  Mineralization is consistent with the Carbonate Base Metal Gold model,
which predicts multiple zones with deep roots.

/T/

"The intercept in KL-14-238 is a game changer" stated Matt Turner, CEO of 
Rockhaven Resources. "It greatly increases the known depth extent of the 
precious metal-rich vein/breccia system and supports the CBM classification, 
making Klaza a truly unique high-grade deposit for the Northern Cordillera."

Western BRX Zone

The Western BRX Zone was the main target of the 2014 diamond drill program. A 
total of 9 excavator trenches and 40 diamond drill holes have traced 
mineralization over a 500 m strike length and from surface to a maximum depth 
of 500 m down-dip. Mineralized veins are emplaced adjacent to a feldspar 
porphyry dyke that is present throughout the zone. KL-14-238, the deepest hole 
completed to date at the Klaza property, intersected 16.29 g/t gold, 1,435 g/t 
silver, 5.57% lead and 6.23% zinc over 1.37 m within a complex of veins, 
breccias and dykes, which averaged 4.58 g/t gold EQ(i) over 18.50 m. The 
high-grade precious and base metal intercept at this depth demonstrates the 
exceptional down-dip potential of the Western BRX Zone. None of the earlier 
drill holes on this high-grade target extended below 310 m down-dip from 
surface. The complex of veins, breccias and dykes in KL-14-238 is the widest 
and strongest structure intercepted to date within the Western BRX Zone.

The complete results from hole KL-14-238 are shown in the table below. Maps, 
sections, core photos and assay results for work completed since 2010 can be 
viewed at Rockhaven's website at www.rockhavenresources.com.

/T/

----------------------------------------------------------------------------
From     To Interval   Gold Silver  Gold EQ  Lead  Zinc
Drill Hole Zone ID    (m)    (m)     (m)+  (g/t)  (g/t) (g/t)(i)   (%)   (%)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
KL-14-238  Western 502.44 520.94    18.50   2.19    120     4.58  0.49  0.68
BRX
----------         ---------------------------------------------------------
incl.              502.44 504.85     2.41   4.27   46.1     5.20  0.09  0.29
----------         ---------------------------------------------------------
incl.              519.57 520.94     1.37  16.29  1,435    44.99  5.57  6.23
----------------------------------------------------------------------------
+   Represents the intercepted length. True widths are estimated to be
approximately 80-90% of the interval.
(i) Gold equivalence (EQ) has been calculated using metal prices of $1200
per ounce gold and $24.00 per ounce silver, to be consistent with
earlier calculations and assumes 100% recoveries of both metals. Lead
and zinc assays were not used in the calculation of gold equivalence.

/T/

Carbonate Base Metal Gold Deposit Model

The Klaza property hosts CBM-style mineralization within multiple, sub-parallel 
vein and breccia zones. CBM's are a recently recognized sub-class of epithermal 
deposits that encompass a family of similar deposits located around the Pacific 
Rim. Multi-million ounce gold deposits classified as CBM include Barrick Gold's 
Porgera Mine (Papua New Guinea), Rio Tinto's formerly producing Kelian Mine 
(Indonesia) and Continental Gold's Buritica project (Columbia).

Klaza and other CBM deposits feature multiple precious metal-rich structures 
that are formed peripheral to mineralized porphyry systems. The presence of 
carbon dioxide gas within the mineralizing hydrothermal fluids is key in 
facilitating precious metal deposition over large vertical extents, often in 
excess of one kilometre. Gold and silver are generally well liberated in this 
type of deposits, and elevated levels of lead, zinc and copper are common.

Nine main mineralized structures and several subsidiary structures have been 
identified at the Klaza property within an area 4 km long and up to 2 km wide. 
The most extensively explored zones (BRX and Klaza) have been traced over 2.4 
km strike lengths and to a depth of 500 m down-dip. Recently completed 
geophysical surveys suggest there is good potential for more discoveries within 
known areas of mineralization, and in undrilled areas along strike and further 
into the hanging wall and footwall of the system.

Within high-grade parts of the zones, deportment and quantitative mineralogy 
studies show that gold largely occurs as native gold or electrum, with a high 
degree of liberation. Silver mainly occurs with pyrargyrite, tetrahedrite and 
electrum, which are also well liberated from gangue and non-ore sulphide 
minerals. Copper mineralization is strongest near the porphyry centre in the 
eastern portion of the property, while lead and zinc contents dramatically 
increase in distal parts of the system. Highly elevated lead and zinc assays 
are often associated with high-grade gold and silver results.

All analyses for rock and core samples from the 2014 program were performed by 
ALS Minerals with sample preparation in Whitehorse and assays and geochemical 
analyses in North Vancouver. Core samples are routinely analyzed for gold by 
fire assay followed by atomic absorption (Au-AA24) and 48 other elements by 
inductively coupled plasma-mass spectrometry (ME-MS61). Samples that exceed the 
detection limits of the routine methods are assayed for silver, copper, lead 
and zinc by inductively coupled plasma-atomic emission spectroscopy 
(Ag/Cu/Pb/Zn - OG62) and gold by gravimetric analysis (Au-GRA22). Rigorous 
procedures are in place regarding sample collection, chain of custody and data 
entry. Certified assay standards, coarse reject duplicates, field duplicates 
and blanks are routinely inserted into the sample stream to ensure integrity of 
the assay process. All of the results reported have passed the QAQC screening.

The 2014 program was managed by Archer, Cathro & Associates (1981) Limited 
(Archer Cathro). Technical information in this news release has been approved 
by Matthew R. Dumala, P.Eng., a geological engineer with Archer Cathro and 
qualified person for the purpose of National Instrument 43-101.

Rockhaven is a well-funded company focused on growth through exploration of its 
wholly-owned projects. For additional information concerning Rockhaven or its 
various exploration projects please visit Rockhaven's website at 
www.rockhavenresources.com.

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE.

- 30 -

CONTACT INFO:

Rockhaven Resources Ltd.
Matthew Turner
CEO and Director
604-688-2568
mturner@rockhavenresources.com
www.rockhavenresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=503778709