Source	Marketwire
Date	10/22/2014
Time	05:00:13 AM

Company	 SCORPIO GOLD CORPORATION
Title	Scorpio Gold Accelerates Exploration Program and Intersects 0.9 g/t Gold 
over 47 Metres on the NW Brodie Trend, Mineral Ridge Project, Nevada





    CDNX Symbol: SGN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Scorpio Gold Corporation

TSX VENTURE SYMBOL: SGN

October 22, 2014

Scorpio Gold Accelerates Exploration Program and Intersects 0.9 g/t Gold over 
47 Metres on the NW Brodie Trend, Mineral Ridge Project, Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Oct. 22, 2014) - Scorpio Gold 
Corporation ("Scorpio Gold" or the "Company") (TSX VENTURE:SGN) is pleased to 
report that a third reverse circulation ("RC") drill rig has mobilized to site 
to expand the 2014 exploration and satellite deposit drilling program at its 
70% owned Mineral Ridge project, located in Nevada.

The 2014 exploration and satellite deposit drilling program has been highly 
successful with 340 RC holes completed to date, totalling more than 34,000 
meters (111,500 feet). The program has been expanded to include a further 150 
RC holes totalling approximately 18,300 meters (60,000 feet).

An additional 2,939 meters (9,643 feet) of drilling was completed in 20 HQ 
(approx. 63 mm diameter) oriented diamond drill core holes. The drill core is 
providing for a better understanding of the lithology and structural geology as 
well as the styles and geological controls to mineralization on a property-wide 
scale.

Peter J. Hawley, CEO, reports, "A significant drop in RC and core drilling 
costs during the year has allowed us to increase the overall 2014 drill program 
under the current budget. By adding a third RC drill rig, we can accelerate the 
program and push hard on priority targets such as the NW Brodie trend."

The expanded 2014 drill program will concentrate in several areas, including:

/T/

--  Infill and down dip extension on the Mary LC deposit

--  Infill drilling on the Brodie deposit

--  Step out drilling along the NW Brodie trend

--  Delineation of pit outlines on the Bluelite and Solberry deposits

/T/

This accelerated drill program is directed at converting previously designated 
waste areas into mineable material, upgrading inferred mineralized blocks 
within the Mary LC deposit, and further defining the NW Brodie trend. The 
overall objective of the program is to increase and upgrade the mineral 
resource and reserve estimates that were presented in the Company's updated 
Life of Mine Plan ("LOM Plan") for Mineral Ridge, which includes the currently 
producing Drinkwater and Mary LC pits and five adjacent satellite deposits (as 
reported in the Company's July 21, 2014 news release).

NW Brodie Trend

The Company is pleased to report additional assay results from the NW Brodie 
trend, a semi-continuous mineralized corridor that extends between the Brodie 
and Bluelite deposits. This area lies well outside of currently defined 
resources and modelled pit outlines. The company's management believes that 
results to date are very promising and may potentially allow for building a new 
resource in this area.

Highlights from this latest phase of RC drilling on the NW Brodie trend include:

/T/

--  MR141101: 0.90 grams per tonne ("g/t") gold over 47.24 meters

--  MR141103: 3.36 g/t gold over 9.14 meters

--  MR141144: 1.97 g/t gold over 10.67 meters

--  MR141144: 3.14 g/t gold over 10.67 meters

--  MR141146: 1.22 g/t gold over 4.57 meters

--  MR141147: 2.44 g/t gold over 6.10 meters

/T/

A drill hole location map is available at: 
www.scorpiogold.com/i/maps/mr/BrodieNW_DHplan.jpg

Table 1. NW Brodie Trend - Significant Drill Results

/T/

----------------------------------------------------------------------------
Hole         Azm   Dip  From    To   Width    From      To Width  Gold  Gold
No.        (deg) (deg)  (ft)  (ft)    (ft)     (m)     (m)   (m) (OPT) (g/t)
----------------------------------------------------------------------------
MR14960        0   -90   150   155       5   45.72   47.24  1.52 0.014  0.48
----------------------------------------------------------------------------
260   265       5   79.25   80.77  1.52 0.041  1.41
----------------------------------------------------------------------------
290   295       5   88.39   89.92  1.52 0.012  0.41
----------------------------------------------------------------------------
440   460      20  134.11  140.21  6.10 0.029  0.98
----------------------------------------------------------------------------
MR141101       0   -90   205   210       5   62.48   64.01  1.52 0.010  0.33
----------------------------------------------------------------------------
275   430     155   83.82  131.06 47.24 0.026  0.90
----------------------------------------------------------------------------
incl.                    410   430      20  124.97  131.06  6.10 0.058  1.98
----------------------------------------------------------------------------
MR141102       0   -90   190   195       5   57.91   59.44  1.52 0.048  1.66
----------------------------------------------------------------------------
225   230       5   68.58   70.10  1.52 0.019  0.64
----------------------------------------------------------------------------
315   325      10   96.01   99.06  3.05 0.022  0.76
----------------------------------------------------------------------------
350   365      15  106.68  111.25  4.57 0.013  0.43
----------------------------------------------------------------------------
MR141103       0   -90   175   180       5   53.34   54.86  1.52 0.012  0.41
----------------------------------------------------------------------------
285   295      10   86.87   89.92  3.05 0.013  0.43
----------------------------------------------------------------------------
305   310       5   92.96   94.49  1.52 0.019  0.65
----------------------------------------------------------------------------
320   325       5   97.54   99.06  1.52 0.012  0.41
----------------------------------------------------------------------------
380   410      30  115.82  124.97  9.14 0.098  3.36
----------------------------------------------------------------------------
450   455       5  137.16  138.68  1.52 0.021  0.72
----------------------------------------------------------------------------
MR141104       0   -90   235   255      20   71.63   77.72  6.10 0.028  0.95
----------------------------------------------------------------------------
330   335       5  100.58  102.11  1.52 0.037  1.27
----------------------------------------------------------------------------
MR141144       0   -90   135   140       5   41.15   42.67  1.52 0.010  0.33
----------------------------------------------------------------------------
180   185       5   54.86   56.39  1.52 0.026  0.87
----------------------------------------------------------------------------
200   215      15   60.96   65.53  4.57 0.049  1.69
----------------------------------------------------------------------------
230   240      10   70.10   73.15  3.05 0.025  0.86
----------------------------------------------------------------------------
255   260       5   77.72   79.25  1.52 0.015  0.51
----------------------------------------------------------------------------
295   300       5   89.92   91.44  1.52 0.014  0.47
----------------------------------------------------------------------------
320   355      35   97.54  108.20 10.67 0.058  1.97
----------------------------------------------------------------------------
365   400      35  111.25  121.92 10.67 0.092  3.14
----------------------------------------------------------------------------
440   445       5  134.11  135.64  1.52 0.034  1.18
----------------------------------------------------------------------------
MR141146       0   -90   195   200       5   59.44   60.96  1.52 0.027  0.91
----------------------------------------------------------------------------
205   210       5   62.48   64.01  1.52 0.010  0.35
----------------------------------------------------------------------------
295   300       5   89.92   91.44  1.52 0.017  0.58
----------------------------------------------------------------------------
320   335      15   97.54  102.11  4.57 0.036  1.22
----------------------------------------------------------------------------
355   365      10  108.20  111.25  3.05 0.036  1.24
----------------------------------------------------------------------------
385   390       5  117.35  118.87  1.52 0.012  0.39
----------------------------------------------------------------------------
410   415       5  124.97  126.49  1.52 0.024  0.81
----------------------------------------------------------------------------
MR141147       0   -90   100   110      10   30.48   33.53  3.05 0.021  0.72
----------------------------------------------------------------------------
120   125       5   36.58   38.10  1.52 0.010  0.34
----------------------------------------------------------------------------
175   180       5   53.34   54.86  1.52 0.059  2.02
----------------------------------------------------------------------------
220   225       5   67.06   68.58  1.52 0.010  0.35
----------------------------------------------------------------------------
260   280      20   79.25   85.34  6.10 0.034  1.16
----------------------------------------------------------------------------
305   325      20   92.96   99.06  6.10 0.071  2.44
----------------------------------------------------------------------------
365   370       5  111.25  112.78  1.52 0.016  0.55
----------------------------------------------------------------------------
425   435      10  129.54  132.59  3.05 0.022  0.74
----------------------------------------------------------------------------
440   445       5  134.11  135.64  1.52 0.017  0.57
----------------------------------------------------------------------------
455   465      10  138.68  141.73  3.05 0.025  0.84
----------------------------------------------------------------------------

/T/

All holes presented in Table 1 were completed by reverse circulation (RC) 
drilling. True width is estimated at 80-100% of downhole width. Analytical 
results were performed by American Assay Laboratory Inc. in Sparks, Nevada, an 
ISO/IEC 17025:2005 accredited facility. External check assays to verify lab 
accuracy are routinely completed by ALS Chemex, an ISO 9001:2000 certified and 
ISO/IEC 17025:2005 accredited facility. Further details are presented in the 
Company's quality assurance and quality control program for the Mineral Ridge 
project at: www.scorpiogold.com/i/pdf/reports/QAQC-MR.pdf.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the producing Mineral Ridge gold mining 
operation located in Esmeralda County, Nevada with joint venture partner 
Waterton Global Value L.P. (30%), and Scorpio Gold is currently entitled to 
receive 80% of cash flow generated. Mineral Ridge is a conventional open pit 
mining and heap leach operation. The Mineral Ridge property is host to multiple 
gold-bearing structures, veins and lenses at exploration, development and 
production stages. Scorpio Gold also holds a 100% interest in the advanced 
exploration-stage Goldwedge property and processing facility in Manhattan, 
Nevada. The Company is assessing its exploration plans for the Goldwedge 
property as well as the potential for toll milling at the Goldwedge plant, 
which is currently permitted for 400 tons per day.

Scorpio Gold's President, Steve Roebuck, PGeo, is a Qualified Person as defined 
by National Instrument 43-101 and has reviewed and approved the content of this 
release.

ON BEHALF OF THE BOARD

SCORPIO GOLD CORPORATION

Peter J. Hawley, CEO

Website: www.scorpiogold.com

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

The Company relies on litigation protection for forward-looking statements. 
This news release contains forward-looking statements that are based on the 
Company's current expectations and estimates. Forward-looking statements are 
frequently characterized by words such as "plan", "expect", "project", 
"intend", "believe", "anticipate", "estimate", "suggest", "indicate" and other 
similar words or statements that certain events or conditions "may" or "will" 
occur, and include, without limitation, statements regarding the Company's 
plans with respect to the exploration, development and exploitation of its 
Mineral Ridge project, including the completion or potential results of the 
additional RC drilling planned in 2014 and the potential addition of new 
mineral resources along the NW Brodie trend. Such forward-looking statements 
involve known and unknown risks, uncertainties and other factors that could 
cause actual events or results to differ materially from estimated or 
anticipated events or results implied or expressed in such forward-looking 
statements, including risks involved in mineral exploration and development 
programs and those risk factors outlined in the Company's Management Discussion 
and Analysis as filed on SEDAR. Any forward-looking statement speaks only as of 
the date on which it is made and, except as may be required by applicable 
securities laws, the Company disclaims any intent or obligation to update any 
forward-looking statement, whether as a result of new information, future 
events or results or otherwise. Forward-looking statements are not guarantees 
of future performance and accordingly undue reliance should not be put on such 
statements due to the inherent uncertainty thereof.

- 30 -

CONTACT INFO:

Scorpio Gold Corporation
Steve Roebuck
President
(819) 825-7618
sroebuck@scorpiogold.com
www.scorpiogold.com

or

Investor Relations:
Jim Macdonald
Torrey Hills Capital
(858) 456-7300
jm@sdthc.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=503837023