Source	Marketwire
Date	10/22/2014
Time	01:11:38 PM

Company	 RIVERSIDE RESOURCES INC.
Title	Riverside and Partner Morro Bay Announce Drill Results From the San Rafael 
Silver-Gold Mine Area at the Penoles Project, Durango, Mexico





    CDNX Symbol: RRI











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Riverside Resources Inc.

TSX VENTURE SYMBOL: RRI
PINKSHEETS SYMBOL: RVSDF
FRANKFURT SYMBOL: R99

October 22, 2014

Riverside and Partner Morro Bay Announce Drill Results From the San Rafael 
Silver-Gold Mine Area at the Penoles Project, Durango, Mexico


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Oct. 22, 2014) - Riverside 
Resources Inc. ("Riverside" or the "Company") (TSX 
VENTURE:RRI)(PINKSHEETS:RVSDF)(FRANKFURT:R99) is pleased to announce drill 
results from the San Rafael historic mine area ("San Rafael") at the Penoles 
Project (the "Project") in Durango, Mexico. This most recent round of drilling 
focused on stepping out beyond the already known gold body at El Capitan and 
high-grade silver vein system at Jesus Maria, with the first five drill holes 
now completed 2 kilometres to the east at San Rafael. Drill result intervals 
included (DDH-14-01) 3.08 metres of 1.19 g/t gold and 79.2 g/t silver, and 
(DDH-14-05) 8.90 metres of 0.63 g/t gold and 101 g/t silver. The drilling 
intersected key mineralized structural veins and starts to confirm strike and 
depth continuity of gold and silver mineralization in multiple structural zones 
and warrants a further follow up drilling and exploration program. This initial 
work phase was designed to confirm the presence of mineralized veins and 
structures at the San Rafael mine area, and was successful within 5-10m of the 
estimated location.

The Penoles Project is host to multiple mineralized vein systems, fault zone 
structures, poly-metallic skarns, and silicified low-temperature gold-rich 
volcaniclastics. The mineralization commonly has high grades of gold and silver 
with varying amounts of lead and zinc. Approximately 86 diamond drill holes 
totaling more than 10,000 metres have now been completed at the Project. 
Initial partner funded drill programs focused on the El Capitan zone, which is 
up to 70 metres thick, 700 metres long, and extends at least 200 metres down 
dip with over 30 drill holes and remains open for further expansion potential. 
Exploration continued beyond El Capitan with 30 holes and approximately 3,115 
metres of drilling completed at the Jesus Maria historic mine area in 2013. At 
least three mineralized zones have been identified at Jesus Maria including 
poly-metallic replacement bodies, gold-silver veins, and breccia bodies. The 
mineralized horizon in the Jesus Maria zone is at least 1400 metres long, up to 
50 metres thick and extends at least 200 metres down dip. Further drilling 
could extend this zone significantly. In addition to El Capitan and Jesus 
Maria, this most recent drilling has now extended exploration to include the 
historic workings at San Rafael. See the table below for highlighted drill 
results hitting multiple sub-parallel Ag-Au veins:

Table 1.1 Summary of Mineralized Intervals in the 2014 San Rafael Drilling 
Program

/T/

From        To    Sample        Au        Ag
Drill Hole                       (m)       (m)    Length       g/t       g/t
----------------------------------------------------------------------------
SR-DDH-14-01                   66.95     69.25       2.3      0.09      99.8
----------------------------------------------------------------------------
SR-DDH-14-01                  190.32     193.4      3.08      1.19      79.2
----------------------------------------------------------------------------
SR-DDH-14-01                   193.4     205.3      11.9      0.06      48.0
----------------------------------------------------------------------------
SR-DDH-14-01                   214.3     223.7       9.4      0.06      46.9
----------------------------------------------------------------------------
SR-DDH-14-03                    94.9      96.1       1.2      0.04      50.1
----------------------------------------------------------------------------
SR-DDH-14-04                    55.7      57.7         2      0.03      63.0
----------------------------------------------------------------------------
SR-DDH-14-05                   123.3     126.7       3.4      0.10      53.0
----------------------------------------------------------------------------
SR-DDH-14-05                   146.8    155.65       8.9      0.63     101.0
----------------------------------------------------------------------------
SR-DDH-14-05                   174.4       179       4.6      0.33      44.9
----------------------------------------------------------------------------

/T/

(i)True widths are estimated to be 90% of reported core lengths

To view cross sections of drill holes DDH-14-01 and DDH-14-05 please follow 
this link: http://goo.gl/XNwykx.

About the Penoles Project:

The Penoles Project is located in the Durango silver-gold belt in north-central 
Mexico and is currently owned 100% by Riverside. The recently completed drill 
program was conducted pursuant to a commitment by Morro Bay Resources Ltd. 
("Morro Bay") to perform $500,000 of exploration work on the property during 
the fall of 2014. Morro Bay can complete its option to earn an initial 
51-per-cent interest in the property by paying Morro Bay can complete its 
option to earn an initial 51-per-cent interest in the property by paying 
USD$1.25-million in cash to Riverside and paying CAD$850,000 (CAD$750,000 of 
which may be paid by delivery of Morro Bay shares) no later than December 31, 
2014. For more information see Riverside press release dated January 23, 2014.

There are approximately eleven targets on the Penoles Project, including the El 
Capitan Gold Zone, the Pinchanzo Zone (see Riverside press release dated May 
23, 2012), potential west extensions of El Capitan (referred to as the West 
Extension), the previously mined Jesus Maria and San Rafael Ag-Au-Pb-Zn mines 
areas. The district is highly prospective with active mining operations nearby 
and has proven to be a cost effective region where projects can be efficiently 
developed towards production.

Qualified Person and QA/QC:

The scientific and technical data contained in this news release pertaining to 
the Penoles Project was reviewed by Greg Myers, PhD, P. Geo. - VP Exploration, 
a non-independent qualified person to Riverside Resources, who is responsible 
for ensuring that the geologic information provided in this news release is 
accurate and who acts as a "qualified person" under National Instrument 43-101 
Standards of Disclosure for Mineral Projects.

All drill cores were placed in numbered boxes and transported to the project's 
secure core facilities by the drill contractor. Following detailed core logging 
all core was cut using a diamond bladed core saw under the direct supervision 
of Riverside's geologic staff with half of the core kept on site in the 
original core boxes. All drill samples were sealed in numbered plastic bags and 
transported to Inspectorate America Assay labs facility in Durango City for 
prep work and analyzed at their facilities in Reno, NV, USA. Inspectorate 
America is certified for the provision of assays and geochemical analysis 
(ISO:9001-2008). All samples were prepared using standard industry preparation 
methods followed by fire assay analysis and four acid complete digestion for 
trace elements. All samples with greater than 10 g/t Au or 100 g/t silver were 
additionally tested by fire assay with a gravimetric finish. The Company has 
included appropriate industry certified standards and blanks within the drill 
core sample stream in addition to the standards and duplicates included as part 
of the Inspectorate QA/QC program.

About Riverside Resources Inc.:

Riverside is a well-funded prospect generation team of focused, proactive 
precious and base metal discoverers with the breadth of knowledge to dig much 
deeper. The Company currently more than $3,500,000 in the treasury and 
approximately 37,000,000 shares outstanding. The Company's model of growth 
through partnerships and exploration uses the prospect generation business 
approach to own resources, while partners share in de-risking projects en route 
to discovery. Riverside has additional properties available for option with 
more information available on the Company's website at www.rivres.com.

ON BEHALF OF RIVERSIDE RESOURCES INC.

Dr. John-Mark Staude, President & CEO

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Riverside Resources Inc.
John-Mark Staude
President & CEO
(778) 327-6671
Fax: (778) 327-6675
info@rivres.com
www.rivres.com

or

Riverside Resources Inc.
Joness Lang
VP, Corporate Development
(877) RIV-RES1
Fax: (778) 327-6675
jlang@rivres.com
www.rivres.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=503998795