Source	Marketwire
Date	10/28/2014
Time	05:00:39 AM

Company	 KAMINAK GOLD CORPORATION
Title	Kaminak Drilling Expands Kona North Discovery at Coffee: 3.12g/t Au Over 
29m





    CDNX Symbol: KAM











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Kaminak Gold Corporation

TSX VENTURE SYMBOL: KAM

October 28, 2014

Kaminak Drilling Expands Kona North Discovery at Coffee: 3.12g/t Au Over 29m


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Oct. 28, 2014) - Kaminak Gold 
Corporation (TSX VENTURE:KAM) today announced positive results from follow up 
drilling at Kona North, a new gold discovery at the development track Coffee 
Gold Project in the Yukon. The Kona North discovery returned 3.55 grams per 
tonne gold (g/t Au) over 28m in its first hole (announced September 2, 2014), 
and mineralization has now been traced over a minimum strike length of 240m. A 
total of 1,600m of drilling across 8 additional drill holes were completed as 
part of a second phase exploration drilling program at Kona North this fall, 
bringing the total number of holes and metres drilled at Kona North to 10 and 
2,000 metres, respectively. All holes intercepted mineralization with estimated 
true widths of between 5m and 25m. Mineralization appears to be associated with 
a broadly east-west trending structural corridor that remains open along strike 
in both directions and to depth. Oxidization is variable, but appears well 
developed near surface extending to an average depth of 40 metres below 
surface. Additional drilling is scheduled for Kona North early in 2015 with the 
aim of delineating a near surface oxide resource for consideration and 
potential inclusion in the Coffee Feasibility study, now underway.

Kaminak recently announced the results from a preliminary economic assessment 
(PEA) at Coffee demonstrating a robust, high-margin, rapid pay-back, 11-year 
open pit mining project using a US$1250/oz gold price. The Coffee Feasibility 
study commenced mid-2014 with a targeted completion date of end 2015.

Highlights

/T/

--  Kona North Step-Out Drilling
--  3.12g/t Au over 28.95m from 64m downhole (CFR657)
--  4.85g/t Au over 16m from 118m downhole and 2.90g/t Au over 22m from
163m downhole (CFD435)
--  6.99g/t Au over 9.14m from 97.54m downhole (CFR654).

/T/

Exploration Drilling Results

Kona North consists of a 1.5km x 0.5km gold-in-soil anomaly peaking at 1.6g/t 
Au, which straddles the contact between Permian gneisses and schists (host 
rocks to Latte-Supremo) and the Cretaceous Coffee Creek Granite. The 
gold-in-soil anomaly is coincident with topographic and magnetic lineaments 
interpreted to represent the extensions of the WNW striking Latte and ENE 
striking Americano structures and a possible third NNW trending structure. The 
highest tenor gold-in-soils occur at the interpreted intersection zone of the 
three structures. To date, drilling has extended the bedrock mineralization at 
Kona North over a strike length of at least 240 metres, and it remains open 
along strike to the east and west. The gold-in-soil anomaly is slightly offset 
from the underlying bedrock mineralization due to down-slope colluvial creep. 
Therefore the earlier drilling, prior to the discovery of Kona North, was 
located too far north. Additional drilling is planned for early 2015 to test 
along the full 1.5km gold-in-soil trend.

To date, gold mineralization at Kona North is primarily hosted in granite in 
the hanging-wall to the contact with Permian basement rocks. Mineralization 
comprises disseminated sulphide and stockwork sulphide veinlets accompanied by 
strong silicification and clay alteration. Oxide (90-100% oxidized) and Upper 
Transition (50-90% oxidized) mineralization extends to an average depth of 40 
metres below surface, below which mineralization is Lower Transition and 
Sulphide facies. Drill intercepts to date support a broadly east-west striking, 
moderate to steeply south dipping mineralized envelope, which exhibits pinch 
and swell as observed at other gold zones at Coffee. Overall thickening of the 
mineralized corridor on 579,525E may be due to multiple stacked mineralized 
structures at the intersection of the Americano and Latte trends, and/or at the 
intersection of the NW striking structure with the east-west corridor. 
Follow-up drilling in 2015 will target the near surface Oxide and Upper 
Transition zones with the objective to extend mineralization along strike and 
to further test the geometry of the thicker zone of mineralization around 
579,525E.

Drilling Results

/T/


--------------------------------------------------------------------------
Weighted
Average
Drill        From          To       Width       grade
Prospect              Hole         (m)         (m)      (m)(i)    (g/t Au)
--------------------------------------------------------------------------
Kona North         CFD0435          77          80           3        3.00
--------------------------------------------------------------------------
Kona North         CFD0435         118         134          16        4.85
--------------------------------------------------------------------------
Kona North         CFD0435         163         185          22        2.90
--------------------------------------------------------------------------
Kona North         CFD0435         214         218           4        1.39
--------------------------------------------------------------------------
Kona North         CFD0440         125         128           3        4.95
--------------------------------------------------------------------------
Kona North         CFD0440         134         147          13        1.04
--------------------------------------------------------------------------
Kona North         CFD0440         162         164           2        2.92
--------------------------------------------------------------------------
Kona North         CFR0654       97.54      106.68        9.14        6.99
--------------------------------------------------------------------------
Kona North         CFR0655      176.78       184.4        7.62        0.92
--------------------------------------------------------------------------
Kona North         CFR0656       28.96       33.53        4.57        2.94
--------------------------------------------------------------------------
Kona North         CFR0656      105.16      118.87       13.71        1.10
--------------------------------------------------------------------------
Kona North         CFR0656      129.54      132.59        3.05        1.76
--------------------------------------------------------------------------
Kona North         CFR0657       64.01       92.96       28.95        3.12
--------------------------------------------------------------------------
Kona North         CFR0660      153.92       158.5        4.58        1.08
--------------------------------------------------------------------------
Kona North         CFR0661       62.48       73.15       10.67        1.28
--------------------------------------------------------------------------

(i)True width estimated at approximately 2/3 down-hole length.

/T/

All maps, sections and assay sheets associated with this news release can be 
viewed by clicking the following link: 
http://kaminak.com/news_releases/2014/index.php?&content_id=603

Field Program Updates: Feasibility and Environment

As recently announced (28 July, 2014), in conjunction with the closing of a 
$13.52M private placement (23 July, 2014), the Company has commenced a 
Feasibility Study on the Coffee Gold Project. Drilling and related field 
programs have been extended into the fall of 2014 with the objective to 
complete critical path and long lead time work programs. Three RC percussion 
drills are still turning on the property, undertaking resource delineation 
infill drilling. Environmental and heritage baseline studies and engineering 
studies into the optimal route and design of the access road are also advancing 
as planned.

The Company is debt-free and fully-financed to complete its 2014 objectives.

QA / QC

Kaminak's disclosure of a technical or scientific nature in this press release 
has been reviewed and approved by Tim Smith, P.Geo., Vice President Exploration 
of Kaminak Gold Corporation, who serves as a Qualified Person under the 
definition of National Instrument 43-101. Quality assurance and quality control 
procedures include the systematic insertion of blanks and standards into the 
drill sample string. Samples are placed in sealed bags and shipped directly to 
the ALS Minerals preparatory laboratory in Whitehorse prior to gold fire assay.

On behalf of the Board of Directors of Kaminak

Eira Thomas, President and CEO

Kaminak Gold Corporation

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accept 
responsibility for the adequacy or accuracy of this release.

Caution Concerning Forward-Looking Statements

Certain disclosures in this release, including management's assessment of the 
future potential of the Coffee Project and future exploration programs, 
constitute forward-looking statements that are subject to numerous risks, 
uncertainties and other factors relating to Kaminak's operations as a mineral 
exploration company that may cause future results to differ materially from 
those expressed or implied in such forward-looking statements, including risks 
as to the completion of the plans and projects. Readers are cautioned not to 
place undue reliance on forward-looking statements. Except as required by law, 
Kaminak expressly disclaims any intention or obligation to update or revise any 
forward-looking statements, whether as a result of new information, future 
event, or otherwise.

The Company has not made a production decision, and the Company's strategic 
plan to develop a stand-alone heap leach operation is subject to the results of 
its Feasibility Study. Further, if and when the Company makes any production 
decision, it will disclose the basis of such decision in accordance with the 
requirements of National Instrument 43-101 Standards of Disclosure for Mineral 
Projects ("NI 43-101").

Cautionary Note concerning estimates of Inferred and Indicated Resources:

This news release uses the terms "Inferred Resources" and "Indicated 
Resources", which have a great amount of uncertainty as to their existence, and 
great uncertainty as to their economic and legal feasibility. It cannot be 
assumed that all or any part of an Inferred and/or Indicated Mineral Resource 
will ever be upgraded to a higher category. Under Canadian rules, estimates of 
Inferred Resources may not form the basis of feasibility or other economic 
studies. Kaminak advises U.S. investors that while this term is recognized and 
required by Canadian regulations, the U.S. Securities and Exchange Commission 
does not recognize it. U.S. investors are cautioned not to assume that part or 
all of an Inferred and Indicated resource exists, or is economically or legally 
minable.

- 30 -

CONTACT INFO:

Kaminak Gold Corporation
Tony Reda
Vice President of Corporate Development
Toll Free: 1.844.646.4520 or Direct: 604.646.4534
info@kaminak.com
www.kaminak.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=504533752