Source	Marketwire
Date	10/28/2014
Time	08:06:06 AM

Company	 ATAC RESOURCES LTD.
Title	ATAC Advances Carlin-Type Gold Targets in the Anubis Area, Rackla Gold 
Project - Yukon





    CDNX Symbol: ATC











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: ATAC Resources Ltd.

TSX VENTURE SYMBOL: ATC

October 28, 2014

ATAC Advances Carlin-Type Gold Targets in the Anubis Area, Rackla Gold Project 
- Yukon


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Oct. 28, 2014) - ATAC Resources 
Ltd. ("ATAC") (TSX VENTURE:ATC) is pleased to provide an update on exploration 
conducted in the Anubis area within the Nadaleen Trend of ATAC's 100% owned 
1,700 sq/km Rackla Gold Project, Yukon Territory.

Highlights:

/T/

--  Trenching and geochemical sampling has outlined a cumulative strike
length of 8 km of elevated pathfinder element+gold response in
overburden and bedrock along favourable northwest-trending extensional
faults;

--  The anomalies and elevated gold response are strongest where major and
secondary faults intersect;

--  The geochemical anomalies occur with well-developed Carlin-type
hydrothermal alteration and the associated fault zones are considered to
be feeder fault systems;

--  The overall 18 sq/km geochemical footprint of the Anubis area, together
with peripheral occurrences of high-grade silver-lead-gold
mineralization at the Corona and Zodiac targets, suggests a very large
Carlin-type system; and,

--  Within this system, ten priority exploration targets have been
identified for follow-up drilling.

/T/

"The systematic 2014 exploration program was very successful in achieving 
ATAC's objective of tracing known gold bearing faults and identifying new 
mineralized crosscutting faults over the largely untested regional-scale 
mineralizing system that underlies the Nadaleen Trend," stated Julia Lane, 
ATAC's Rackla Gold Project Manager. "As with many Carlin-type deposits in 
Nevada, understanding mineralizing structures and where they interact with 
receptive calcareous host rocks is a critical step before targeting drill 
holes. The focused 2014 exploration program at Anubis generated a large amount 
of exploration data that will be compiled in the coming months to prioritize 
drill targets."

During 2014 ATAC completed an extensive surface exploration program at the 18 
sq/km Anubis area, which is located 10 km west of the Osiris cluster of gold 
zones - the primary focus of ATAC's exploration since 2011. The Anubis area 
hosts over ten gold exploration targets, including the Anubis discovery 
outcrop, where prospecting grab sample assays ranged from below detection to 
139 g/t gold. Subsequent drilling beneath the discovery outcrop returned 8.51 m 
of 19.85 g/t gold (OS-12-001). The Anubis area displays many of the same 
structural controls and mineralizing characteristics as the Osiris area and is 
now considered ATAC's second district-scale Carlin-type gold target within the 
broader 50 km long Nadaleen Trend.

2014 exploration work in the Anubis area consisted of systematic prospecting, 
mapping, excavator trenching and overburden auger drilling. The goal was to 
evaluate the distribution of gold mineralization and pathfinder element 
anomalies within and adjacent to two major northwest-trending extensional 
faults. Excavator trenching and overburden drilling were specifically used to 
locate the bedrock source of subdued gold-in-soil response typically associated 
with Carlin-type mineralization in areas of shallow overburden. The 2014 
program at the Anubis area resulted in the completion of 1,050 m of trenching, 
50 overburden drill holes and the collection of 172 soil samples and 786 rock 
samples.

The 2014 program results have enabled ATAC to: (i) better define geochemical 
anomalies and track the geochemical response back to areas of bedrock 
alteration; (ii) trace known faults; and (iii) identify new intersecting 
structures that are the potential feeder systems for mineralizing fluids. 
Excavator trenching along the Anubis fault was particularly successful in 
identifying areas of complex faulting that are enveloped by zones of 
hydrothermal alteration. Trenching of host limestone and calcareous shale 
returned gold values from below detection up to 2.30 g/t gold over 5 m. The 
identification of these structures in relation to geochemical anomalies and 
characteristic Carlin-type alteration is a critical milestone for developing 
drill targets. Now that the hydrothermal footprint has been outlined, the next 
step will be targeted drilling to test the intersection of feeder fault systems 
with favourable host rock units, such as the Anubis area silty limestones.

Updated maps and figures of the Anubis area can be found on ATAC's website at 
www.atacresources.com.

QA/QC

Samples were forwarded to ALS Minerals in Whitehorse where they were fine 
crushed before a 250 gram split was pulverized to better than 85% passing 75 
microns. Pulps were then analyzed at ALS Minerals in North Vancouver. Gold 
analyses were by the Au-AA26 procedure that involves fire assay preparation 
using a 50 gram charge with an atomic absorption spectroscopy finish while 49 
other elements were determined by the ME-MS61m procedure that involves a four 
acid digestion followed by inductively coupled plasma mass spectrometry and 
inductively coupled plasma atomic emission spectroscopy. Samples that exceeded 
the detection limit of the routine methods are assayed for silver, lead and 
zinc by the Ag/Pb/Zn - OG62 method involving inductively coupled plasma-atomic 
emission spectroscopy.

Rigorous procedures are in place regarding sample collection, chain of custody 
and data entry. Certified assay standards, duplicate samples and blanks are 
routinely inserted into the sample stream to ensure integrity of the assay 
process. All of the samples included in this news release have passed the QA/QC 
procedures as described above.

The technical information in this news release has been approved by Julia Lane, 
P.Geo., the Rackla Gold Project manager and a geologist with Archer, Cathro & 
Associates (1981) Limited, and a qualified person for the purposes of National 
Instrument 43-101.

About ATAC

ATAC is a Yukon-based exploration company focused on developing Canada's only 
Carlin-type gold district at its 100% owned Rackla Gold Project. Recent work on 
the 1,700 sq/km project has resulted in a positive Preliminary Economic 
Assessment for the Tiger Deposit, drilling of multiple high-grade Carlin-type 
gold zones and the identification of numerous early-stage gold exploration 
targets. The Rackla Gold Project has no underlying royalties or third-party 
interests. ATAC is well financed with approximately $20 million in its treasury.

On behalf of Management and the Board of Directors of ATAC Resources Ltd.

Graham Downs, CEO

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE.

This news release may contain forward looking statements based on assumptions 
and judgments of management regarding future events or results that may prove 
to be inaccurate as a result of exploration and other risk factors.

- 30 -

CONTACT INFO:

ATAC Resources Ltd.
Vanessa Pickering
Manager, Corporate Communications
604-687-2522 ext. 260
vpickering@atacresources.com
www.atacresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=504634712