Source	MARKET NEWS
Date	10/28/2014
Time	08:18:36 AM

Company	 ATAC Resources Ltd.
Title	Advances 
Carlin type Gold Targets In The Anubis





    CDNX Symbol: ATC











Press Release	





ATAC RESOURCES LTD ("ATC-V;ATADF-0")
- Advances Carlin-type Gold Targets In The Anubis Area, Rackla
- Gold Project - Yukon

ATAC Resources Ltd. ("ATAC") is pleased to provide an update on
exploration conducted in the Anubis area within the Nadaleen Trend of
ATAC's 100% owned 1,700 sq/km Rackla Gold Project, Yukon Territory.

Highlights:

//st

Trenching and geochemical sampling has outlined a cumulative
strike length of 8 km of elevated pathfinder element+gold response in
overburden and bedrock along favourable northwest-trending extensional
faults;

The anomalies and elevated gold response are strongest where
major and secondary faults intersect;

The geochemical anomalies occur with well-developed Carlin-type
hydrothermal alteration and the associated fault zones are considered to be
feeder fault systems;

The overall 18 sq/km geochemical footprint of the Anubis area,
together with peripheral occurrences of high-grade silver-lead-gold
mineralization at the Corona and Zodiac targets, suggests a very large
Carlin-type system; and,

Within this system, ten priority exploration targets have been
identified for follow-up drilling.

//et

"The systematic 2014 exploration program was very successful in
achieving ATAC's objective of tracing known gold bearing faults and
identifying new mineralized crosscutting faults over the largely
untested regional-scale mineralizing system that underlies the Nadaleen
Trend," stated Julia Lane, ATAC's Rackla Gold Project Manager. "As with
many Carlin-type deposits in Nevada, understanding mineralizing
structures and where they interact with receptive calcareous host rocks
is a critical step before targeting drill holes. The focused 2014
exploration program at Anubis generated a large amount of exploration
data that will be compiled in the coming months to prioritize drill
targets."

During 2014 ATAC completed an extensive surface exploration
program at the 18 sq/km Anubis area, which is located 10 km west of the
Osiris cluster of gold zones - the primary focus of ATAC's exploration
since 2011. The Anubis area hosts over ten gold exploration targets,
including the Anubis discovery outcrop, where prospecting grab sample
assays ranged from below detection to 139 g/t gold. Subsequent drilling
beneath the discovery outcrop returned 8.51 m of 19.85 g/t gold
(OS-12-001). The Anubis area displays many of the same structural
controls and mineralizing characteristics as the Osiris area and is now
considered ATAC's second district-scale Carlin-type gold target within
the broader 50 km long Nadaleen Trend.

2014 exploration work in the Anubis area consisted of systematic
prospecting, mapping, excavator trenching and overburden auger
drilling. The goal was to evaluate the distribution of gold
mineralization and pathfinder element anomalies within and adjacent to
two major northwest-trending extensional faults. Excavator trenching
and overburden drilling were specifically used to locate the bedrock
source of subdued gold-in-soil response typically associated with
Carlin-type mineralization in areas of shallow overburden. The 2014
program at the Anubis area resulted in the completion of 1,050 m of
trenching, 50 overburden drill holes and the collection of 172 soil
samples and 786 rock samples.

The 2014 program results have enabled ATAC to: (i) better define
geochemical anomalies and track the geochemical response back to areas
of bedrock alteration; (ii) trace known faults; and (iii) identify new
intersecting structures that are the potential feeder systems for
mineralizing fluids. Excavator trenching along the Anubis fault was
particularly successful in identifying areas of complex faulting that
are enveloped by zones of hydrothermal alteration. Trenching of host
limestone and calcareous shale returned gold values from below
detection up to 2.30 g/t gold over 5 m. The identification of these
structures in relation to geochemical anomalies and characteristic
Carlin-type alteration is a critical milestone for developing drill
targets. Now that the hydrothermal footprint has been outlined, the
next step will be targeted drilling to test the intersection of feeder
fault systems with favourable host rock units, such as the Anubis area
silty limestones.

Updated maps and figures of the Anubis area can be found on ATAC's
website at www.atacresources.com.

QA/QC

Samples were forwarded to ALS Minerals in Whitehorse where they
were fine crushed before a 250 gram split was pulverized to better than
85% passing 75 microns. Pulps were then analyzed at ALS Minerals in
North Vancouver. Gold analyses were by the Au-AA26 procedure that
involves fire assay preparation using a 50 gram charge with an atomic
absorption spectroscopy finish while 49 other elements were determined
by the ME-MS61m procedure that involves a four acid digestion followed
by inductively coupled plasma mass spectrometry and inductively coupled
plasma atomic emission spectroscopy. Samples that exceeded the
detection limit of the routine methods are assayed for silver, lead and
zinc by the Ag/Pb/Zn - OG62 method involving inductively coupled
plasma-atomic emission spectroscopy.

Rigorous procedures are in place regarding sample collection,
chain of custody and data entry. Certified assay standards, duplicate
samples and blanks are routinely inserted into the sample stream to
ensure integrity of the assay process. All of the samples included in
this news release have passed the QA/QC procedures as described above.

The technical information in this news release has been approved
by Julia Lane, P.Geo., the Rackla Gold Project manager and a geologist
with Archer, Cathro & Associates (1981) Limited, and a qualified person
for the purposes of National Instrument 43-101.

About ATAC

ATAC is a Yukon-based exploration company focused on developing
Canada's only Carlin-type gold district at its 100% owned Rackla Gold
Project. Recent work on the 1,700 sq/km project has resulted in a
positive Preliminary Economic Assessment for the Tiger Deposit,
drilling of multiple high-grade Carlin-type gold zones and the
identification of numerous early-stage gold exploration targets. The
Rackla Gold Project has no underlying royalties or third-party
interests. ATAC is well financed with approximately $20 million in its
treasury.

On behalf of Management and the Board of Directors of ATAC
Resources Ltd.

Graham Downs, CEO

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
RELEASE.

This news release may contain forward looking statements based
on assumptions and judgments of management regarding future events or
results that may prove to be inaccurate as a result of exploration and
other risk factors.

TSX Venture closing price for ATC-V
Date: 2014/10/27
Closing Price: 0.51

TEL: 604-687-2522 ext 260      Vanessa Pickering
vpickering@atacresources.com   Manager, Corporate Communications
www.atacresources.com          ATAC Resources Ltd.
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1430000022TS11430001660-08172820141028