Source	Marketwire
Date	10/29/2014
Time	12:13:04 PM

Company	 BRIXTON METALS CORPORATION
Title	Brixton Metals Establishes an Inferred Resource of 21.5 Million Ounce 
Silver Equivalent on Limited Drilling





    CDNX Symbol: BBB











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Brixton Metals Corporation

TSX VENTURE SYMBOL: BBB

October 29, 2014

Brixton Metals Establishes an Inferred Resource of 21.5 Million Ounce Silver 
Equivalent on Limited Drilling


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Oct. 29, 2014) - Brixton Metals 
Corporation (TSX VENTURE:BBB) (the "Company" or "Brixton") is pleased to 
announce its independent maiden resource estimate of 21.5 million ounces of 
silver equivalent as an inferred resource at its 100% owned Thorn project 
located in northwestern B.C. SRK Consulting (Canada) Inc. (SRK), has prepared 
the inferred resource estimate in a National Instrument 43-101 ("NI 43-101") 
technical report (that will be filed on SEDAR within 45 days) based on 
approximately 15,160 metres of drilling. The resource estimate combines three 
mineralized zones; Oban, Talisker and Glenfiddich.

Highlights of 2014 Results

/T/

--  The 3 zones combined total 21.5Moz AgEq of inferred resource
--  All mineralized zones remain open for expansion
--  Most of the inferred resource is open pit material
--  The sediment-hosted gold discovery, not part of the current resource, in
2014 provides significant upside potential
--  Abundant high-grade gold-silver targets remain to be tested

/T/

Chairman and CEO of Brixton Metals, Gary Thompson, stated: "We are excited to 
have completed our first resource estimate at the Thorn project. This inferred 
resource is based on limited drilling and importantly, all mineralized zones 
remain open for expansion. In addition, during 2014, Brixton discovered a 
sediment hosted-gold zone which represents a large scale gold target as 
previously stated in the Company's News Release dated July 29, 2014 and in 
general has had a high rate of discovery on the project." Mr. Thompson further 
stated that, "The Company currently has approximately $1.2 million in working 
capital."

Table 1.1: Inferred Mineral Resource Statement, Thorn Project, British 
Columbia, SRK Consulting (Canada) Inc., October 28, 2014.

/T/

----------------------------------------------------------------------------
In-Situ Grade
----------------------------------------------------------------------------
Grade  Grade  Grade  Grade  Grade  Grade
Tonnage    AgEq     Ag     Au     Cu     Pb     Zn
Deposit                    x 1000   (g/t)  (g/t)  (g/t)    (%)    (%)    (%)
----------------------------------------------------------------------------
Oban         In-Pit         3,700  105.07  50.82   0.40     NA   0.31   0.58
---------------------------------------------------------------
Underground      500  113.84  50.51   0.46     NA   0.37   0.67
----------------------------------------------------------------------------
Glenfiddich  In-Pit         1,100   57.78  16.01   0.48   0.13     NA     NA
----------------------------------------------------------------------------
Talisker     In-Pit         2,100   73.77  15.29   0.75   0.13     NA     NA
----------------------------------------------------------------------------
Total          7,400   89.75  35.54   0.51   0.13   0.32   0.59
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Contained Metal
----------------------------------------------------------------------------
Metal
AgEq  Metal  Metal  Metal  Metal  Metal
Tonnage    Oz x  Ag Oz  Au Oz Cu Lbs Pb Lbs Zn Lbs
Deposit                    x 1000    1000 x 1000 x 1000 x 1000 x 1000 x 1000
----------------------------------------------------------------------------
Oban         In-Pit         3,700  12,500  6,000     50     NA 25,200 47,500
---------------------------------------------------------------
Underground      500   1,900    800     10     NA  4,100  7,600
----------------------------------------------------------------------------
Glenfiddich  In-Pit         1,100   2,100    600     20  3,200     NA     NA
----------------------------------------------------------------------------
Talisker     In-Pit         2,100   5,000  1,000     50  6,100     NA     NA
----------------------------------------------------------------------------
Total          7,400  21,500  8,400    130  9,300 29,300 55,100
----------------------------------------------------------------------------

1.  The in-pit portion is reported at a dollar equivalent cut-off value of
US $15 per tonne within a Whittle shell and $50 per tonne for an
underground portion of the Oban deposit. The Whittle shells were
designed based on a slope angle of 55 degrees and 90% recovery for all
metals. The block models are 10 x 10 x 10 m, 5 x 10 x 5 m, and 5 x 10 x
5 m for Oban, Glenfiddich, and Talisker respectively. The Whittle shell
for Oban does not include Copper. The Whittle shells for Glenfiddich and
Talisker do not include Lead or Zinc.
2.  Dollar and Silver Equivalents are based on US $20 Silver, $1200 Gold, $3
Copper, $1 Lead, and $1 Zinc, with metal recoveries of 90%. Copper is
not included in the Oban estimates. Lead and zinc are not included in
the Glenfiddich and Talisker estimates.

/T/

The resource model is based on 35 historical drill holes and 64 recent drill 
holes completed by Brixton. Most of the drilling by Brixton has concentrated on 
the Oban Zone with the majority of this taking place during the 2012-2013 
exploration programmes. Of the total drilling, 11,000 metres was directed to 
the Oban deposit, 2,160 metres was within the Talisker Zone and 2,000 metres in 
the Glenfiddich Zone.

SRK states in conclusion, "that the Thorn Project has future potential for 
developing additional mineral resources. A careful drill program could identify 
additional inferred mineral resources and possibly upgrade some of the inferred 
resources to an indicated category."

SRK recommends the following:

/T/

--  Continued specific gravity sampling.
--  Continued careful monitoring of QA/QC sample results.
--  Additional drilling to extend the open pit resource for the Oban Zone,
especially to the south east.
--  Additional drilling to extend the Glenfiddich and Talisker Zones.
--  Metallurgical testing for all zones with the focus on the Oban Zone.

/T/

SRK has classified the mineral resources into the Inferred category (Table 
1.1). For both the Talisker and Glenfiddich zones, the drill hole spacing, at 
approximately 75 metres, is too widely spaced to support resource 
classification higher than inferred. In addition, a part of the resource in 
those two deposits is based on historic drilling, for which there is no 
documentation of sampling practices or analytical quality control procedures. 
For all zones, including the Oban deposit, there has not been metallurgical 
work to determine metal recoveries. In particular, and with requisite 
metallurgical testwork, SRK believes that a portion of the Oban resource could 
upgrade in classification to indicated in the future. Until completing 
additional exploration work, the Company cannot guarantee that any such upgrade 
will occur.

A copy of the NI-43-101 technical report shall be made available on the 
Company's website and SEDAR profile at www.sedar.com upon receipt.

The technical report was prepared in accordance with NI 43-101 Standards of 
Disclosure for Mineral Projects and Form 43-101F1 by Tessa Scott under the 
supervision of Marek Nowak, P.Eng. APEGBC#119958 of SRK, an independent 
Qualified Person as defined by NI 43-101, who has also reviewed and approved 
this news release.

About Brixton Metals and its Thorn Project

Brixton is an exploration company focused on the advancement of high-grade 
precious metal assets to feasibility. Brixton's Thorn project hosts a district 
scale Triassic to Cretaceous volcanoplutonic complex with several styles of 
mineralization related to porphyry and epithermal environments. Targets include 
sediment hosted gold, high-grade silver-gold-lead-zinc-bearing diatreme-breccia 
zones, high-grade gold-silver-copper veins and porphyry copper-gold-silver. The 
28,000-hectare Thorn Project is located in the Sutlahine River area of 
northwestern British Columbia, Canada, approximately 105 km ENE from Juneau, AK.

Brixton Metals Corporation shares trade on the TSX-V under the ticker symbol 
BBB. For more information about Brixton please visit our website at 
www.brixtonmetals.com.

On Behalf of the Board of Directors

Mr. Gary R. Thompson, Chairman and CEO

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Information set forth in this news release may involve forward-looking 
statements under applicable securities laws. Forward-looking statements are 
statements that relate to future, not past, events. In this context, 
forward-looking statements often address expected future business and financial 
performance, and often contain words such as "anticipate", "believe", "plan", 
"estimate", "expect", and "intend", statements that an action or event "may", 
"might", "could", "should", or "will" be taken or occur, or other similar 
expressions. All statements, other than statements of historical fact included 
herein including, without limitation, statements regarding the proposed 
exploration, sampling and drilling at Thorn and statements concerning the 
anticipated results of such exploration work, are forward looking statements. 
By their nature, forward-looking statements involve known and unknown risks, 
uncertainties and other factors which may cause our actual results, performance 
or achievements, or other future events, to be materially different from any 
future results, performance or achievements expressed or implied by such 
forward-looking statements. Such factors include, among others, the following 
risks: the need for additional financing; operational risks associated with 
mineral exploration; fluctuations in commodity prices; title matters; and the 
additional risks identified in the annual information form of the Company or 
other reports and filings with the TSX-V and applicable Canadian securities 
regulators. Forward-looking statements are made based on management's beliefs, 
estimates and opinions on the date that statements are made and the Company 
undertakes no obligation to update forward-looking statements if these beliefs, 
estimates and opinions or other circumstances should change, except as required 
by applicable securities laws. Investors are cautioned against attributing 
undue certainty to forward-looking statements.

- 30 -

CONTACT INFO:

Brixton Metals Corporation
Mr. Gary R. Thompson
Chairman and CEO
604-630-9707
info@brixtonmetals.com
www.brixtonmetals.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=504858618