Source	MARKET NEWS
Date	10/29/2014
Time	12:38:09 PM

Company	 Brixton Metals Corporation
Title	Establishes 
An Inferred Resource Of 21.5 Million





    CDNX Symbol: BBB











Press Release	





BRIXTON METALS CORP ("BBB-V")
- Establishes An Inferred Resource Of 21.5 Million Ounce Silver
- Equivalent On Limited Drilling

Brixton Metals Corporation (the "Company" or "Brixton") is pleased
to announce its independent maiden resource estimate of 21.5 million
ounces of silver equivalent as an inferred resource at its 100% owned
Thorn project located in northwestern B.C. SRK Consulting (Canada) Inc.
(SRK), has prepared the inferred resource estimate in a National
Instrument 43-101 ("NI 43-101") technical report (that will be filed on
SEDAR within 45 days) based on approximately 15,160 metres of drilling.
The resource estimate combines three mineralized zones; Oban, Talisker
and Glenfiddich.

Highlights of 2014 Results

//st

The 3 zones combined total 21.5Moz AgEq of inferred resource

All mineralized zones remain open for expansion

Most of the inferred resource is open pit material

The sediment-hosted gold discovery, not part of the current resource, in
2014 provides significant upside potential

Abundant high-grade gold-silver targets remain to be tested

//et

Chairman and CEO of Brixton Metals, Gary Thompson, stated: "We are
excited to have completed our first resource estimate at the Thorn
project. This inferred resource is based on limited drilling and
importantly, all mineralized zones remain open for expansion. In
addition, during 2014, Brixton discovered a sediment hosted-gold zone
which represents a large scale gold target as previously stated in the
Company's News Release dated July 29, 2014 and in general has had a
high rate of discovery on the project." Mr. Thompson further stated
that, "The Company currently has approximately $1.2 million in working
capital."

Table 1.1: Inferred Mineral Resource Statement, Thorn Project,
British Columbia, SRK Consulting (Canada) Inc., October 28, 2014.

//st



In-Situ Grade
---------------------------------------------------------------------------
-
Grade  Grade  Grade  Grade  Grade
Grade
Tonnage    AgEq     Ag     Au     Cu     Pb
Zn
Deposit                    x 1000   (g/t)  (g/t)  (g/t)    (%)    (%)
(%)
---------------------------------------------------------------------------
-
Oban         In-Pit         3,700  105.07  50.82   0.40     NA   0.31
0.58

---------------------------------------------------------------
Underground      500  113.84  50.51   0.46     NA   0.37
0.67
---------------------------------------------------------------------------
-
Glenfiddich  In-Pit         1,100   57.78  16.01   0.48   0.13     NA
NA
---------------------------------------------------------------------------
-
Talisker     In-Pit         2,100   73.77  15.29   0.75   0.13     NA
NA
---------------------------------------------------------------------------
-
Total          7,400   89.75  35.54   0.51   0.13   0.32
0.59
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
Contained Metal
---------------------------------------------------------------------------
-
Metal
AgEq  Metal  Metal  Metal  Metal
Metal
Tonnage    Oz x  Ag Oz  Au Oz Cu Lbs Pb Lbs Zn
Lbs
Deposit                    x 1000    1000 x 1000 x 1000 x 1000 x 1000 x
1000
---------------------------------------------------------------------------
-
Oban         In-Pit         3,700  12,500  6,000     50     NA 25,200
47,500

---------------------------------------------------------------
Underground      500   1,900    800     10     NA  4,100
7,600
---------------------------------------------------------------------------
-
Glenfiddich  In-Pit         1,100   2,100    600     20  3,200     NA
NA
---------------------------------------------------------------------------
-
Talisker     In-Pit         2,100   5,000  1,000     50  6,100     NA
NA
---------------------------------------------------------------------------
-
Total          7,400  21,500  8,400    130  9,300 29,300
55,100
---------------------------------------------------------------------------
-

//et

//st
1.  The in-pit portion is reported at a dollar equivalent cut-off value of
US $15 per tonne within a Whittle shell & $50 per tonne for an underground
portion of the Oban deposit. The Whittle shells were designed based on a
slope angle of 55 degrees & 90% recovery for all metals. The block models
are 10 x 10 x 10 m, 5 x 10 x 5 m, & 5 x 10 x 5 m for Oban, Glenfiddich, &
Talisker respectively. The Whittle shell for Oban does not include Copper.
The Whittle shells for Glenfiddich & Talisker do not include Lead or Zinc.
2.  Dollar & Silver Equivalents are based on US $20 Silver, $1200 Gold, $3
Copper, $1 Lead, & $1 Zinc, with metal recoveries of 90%. Copper is not
included in the Oban estimates. Lead & zinc are not included in the
Glenfiddich & Talisker estimates.

//et

The resource model is based on 35 historical drill holes and 64
recent drill holes completed by Brixton. Most of the drilling by
Brixton has concentrated on the Oban Zone with the majority of this
taking place during the 2012-2013 exploration programmes. Of the total
drilling, 11,000 metres was directed to the Oban deposit, 2,160 metres
was within the Talisker Zone and 2,000 metres in the Glenfiddich Zone.

SRK states in conclusion, "that the Thorn Project has future
potential for developing additional mineral resources. A careful drill
program could identify additional inferred mineral resources and
possibly upgrade some of the inferred resources to an indicated
category."

SRK recommends the following:

//st

Continued specific gravity sampling.

Continued careful monitoring of QA/QC sample results.

Additional drilling to extend the open pit resource for the Oban Zone,
especially to the south east.

Additional drilling to extend the Glenfiddich and Talisker Zones.

Metallurgical testing for all zones with the focus on the Oban Zone.

//et

SRK has classified the mineral resources into the Inferred category
(Table 1.1). For both the Talisker and Glenfiddich zones, the drill
hole spacing, at approximately 75 metres, is too widely spaced to
support resource classification higher than inferred. In addition, a
part of the resource in those two deposits is based on historic
drilling, for which there is no documentation of sampling practices or
analytical quality control procedures. For all zones, including the
Oban deposit, there has not been metallurgical work to determine metal
recoveries. In particular, and with requisite metallurgical testwork,
SRK believes that a portion of the Oban resource could upgrade in
classification to indicated in the future. Until completing additional
exploration work, the Company cannot guarantee that any such upgrade
will occur.

A copy of the NI-43-101 technical report shall be made available
on the Company's website and SEDAR profile at www.sedar.com upon
receipt.
The technical report was prepared in accordance with NI 43-101
Standards of Disclosure for Mineral Projects and Form 43-101F1 by Tessa
Scott under the supervision of Marek Nowak, P.Eng. APEGBC#119958 of
SRK, an independent Qualified Person as defined by NI 43-101, who has
also reviewed and approved this news release.

About Brixton Metals and its Thorn Project

Brixton is an exploration company focused on the advancement of
high-grade precious metal assets to feasibility. Brixton's Thorn
project hosts a district scale Triassic to Cretaceous volcanoplutonic
complex with several styles of mineralization related to porphyry and
epithermal environments. Targets include sediment hosted gold,
high-grade silver-gold-lead-zinc-bearing diatreme-breccia zones,
high-grade gold-silver-copper veins and porphyry copper-gold-silver.
The 28,000-hectare Thorn Project is located in the Sutlahine River area
of northwestern British Columbia, Canada, approximately 105 km ENE from
Juneau, AK.

Brixton Metals Corporation shares trade on the TSX-V under the
ticker symbol BBB. For more information about Brixton please visit our
website at www.brixtonmetals.com.

On Behalf of the Board of Directors

Mr. Gary R. Thompson, Chairman and CEO

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Information set forth in this news release may involve
forward-looking statements under applicable securities laws.
Forward-looking statements are statements that relate to future, not
past, events. In this context, forward-looking statements often address
expected future business and financial performance, and often contain
words such as "anticipate", "believe", "plan", "estimate", "expect",
and "intend", statements that an action or event "may", "might",
"could", "should", or "will" be taken or occur, or other similar
expressions. All statements, other than statements of historical fact
included herein including, without limitation, statements regarding the
proposed exploration, sampling and drilling at Thorn and statements
concerning the anticipated results of such exploration work, are
forward looking statements. By their nature, forward-looking statements
involve known and unknown risks, uncertainties and other factors which
may cause our actual results, performance or achievements, or other
future events, to be materially different from any future results,
performance or achievements expressed or implied by such
forward-looking statements. Such factors include, among others, the
following risks: the need for additional financing; operational risks
associated with mineral exploration; fluctuations in commodity prices;
title matters; and the additional risks identified in the annual
information form of the Company or other reports and filings with the
TSX-V and applicable Canadian securities regulators. Forward-looking
statements are made based on management's beliefs, estimates and
opinions on the date that statements are made and the Company
undertakes no obligation to update forward-looking statements if these
beliefs, estimates and opinions or other circumstances should change,
except as required by applicable securities laws. Investors are
cautioned against attributing undue certainty to forward-looking
statements.

Brixton Metals Corporation
TSX Venture closing price for BBB-V
Date: 2014/10/27
Closing Price: 0.12

TEL:     604-630-9707 Mr. Gary R. Thompson, Chairman and CEO
E-mail:  info@brixtonmetals.com
Website: www.brixtonmetals.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1430100037TS11430102149-12360220141029